## Slide 1: Way Forward on Fragmented Carriers in Rel-19
RP-240498
3GPP TSG RAN Meeting #103
Maastricht, The Netherlands, 18th – 21st March, 2024
Agenda Item 9.1.4.1
Source: TELUS, Bell Mobility, Nokia, Nokia Shanghai Bell, Telstra, T-Mobile USA, US Cellular, Spark NZ Ltd, Southern Linc, AT&T, Verizon Wireless, CableLabs, Samsung, Apple, Ericsson, CHTTL, Intel

## Slide 2: Motivation
Today, fragmented carriers in the same band consume multiple Rx chains, thus limiting the Carrier Aggregation (CA) capabilities
The maximum number of component carriers (CCs) in a CA combo is mostly limited by the number and capabilities of the analog Rx chains in the UEs
This limitation prevents operators from fully utilizing their fragmented spectrum holdings in a single CA combo
A multi-company proposal was submitted to RAN#102[1] and RAN4#110[2] indicating this is a solution that would have global impact.
Observation: Fragmented carriers in the same band consume multiple Rx chains, thus limiting the CA capabilities
Proposal: Study the use of fewer Rx chains than carrier fragments in a band
[1] RP-233374, “Fragmented carriers in the DL”, TELUS, Bell Mobility, Telstra, Nokia, Nokia Shanghai Bell, AT&T, US Cellular
[2] R4-2402309: “Study on effective utilization of fragmented FR1 carriers in the DL”, TELUS, Bell Mobility, Telstra, Nokia, Nokia Shanghai Bell, AT&T, US Cellular

## Slide 3: Scope
Objectives:
  Identify methods for reducing number of UE Rx chains (e.g. 1 or 2) needed for single DL band of ≤ 100 MHz (frequency span) containing two non-contiguous CCs within a CA combination for the inter-operator co-located scenario, considering:
    Which RF requirements could be adjusted for the inter-operator co-located scenario, e.g. Existing UE RF requirements such as ACS
    The ability to semi-statically switch hardware resources (i.e., Rx chains) between bands
    6 dB power imbalance between the two non-contiguous CCs
    Impacts on DL performance
    Means for a UE to inform the network of new CA configuration it can support with adjusted RF requirements
RAN4 led item with minimal RAN2 impact and no RAN1 impact is foreseen
Timescale:
  Start Q3 2024
  Target completion Q2 2025
Note: When the study is complete, consider normative work to define core requirements using the identified solution