## Slide 1: Moderator Summary on Rel-19 SBFD Discussions
3GPP RAN1 Chair
RP-240783

## Slide 2: Issue#1: Mechanism for adjacent channel CLI
Moderator Proposal1: Modify the Rel-19 SBFD WID objective on CLI handling as follows:
------------ Unchanged part omitted ----------------
Specify enhancements for CLI handling [RAN1, RAN2, RAN3]:
  Support gNB-to-gNB co-channel CLI handling scheme(s) (the detailed schemes are to be down-selected from those in TR38.858 by RAN1#117)
  Support UE-to-UE co-channel CLI handling scheme(s) (the detailed schemes are to be down-selected from those in TR38.858 by RAN1#117)
  Note: Without dedicated optimization for dynamic/flexible TDD.
Specify BS RF requirements for SBFD operation at gNB [RAN4]
Specify applicable RRM core requirements for co-channel CLI handling mechanisms [RAN4]
Specify other RRM core requirements for SBFD operation, if identified [RAN4]
Note: RAN3 will not specify enhancements to network signalling to support inter-operator coordination for CLI handling

## Slide 3: Issue#2: Legacy UL symbol
Moderator: RAN1 is currently in the process of discussing this issue (as highlighted in yellow part below)
Agreement from RAN1#116
For SBFD-aware UE transmission and reception in the SBFD symbols configured in DL and/or flexible in TDD-UL-DL-ConfigCommon,
UL transmissions within UL usable PRBs are allowed
  FFS SSB symbols
DL receptions within DL usable PRBs are allowed
UL transmissions outside UL usable PRBs are not allowed
DL receptions outside DL usable PRBs are not allowed
  This restriction is not applicable for CLI measurement
CLI measurement behaviours for SBFD-aware UE are discussed in agenda item 9.3.3.
RAN1 to discuss SBFD aware UE behaviors in SBFD symbols with interaction with legacy TDD slot configuration indications via TDD-UL-DL-ConfigDedicated and SFI in DCI format 2_0
DCI format 2_0 cannot be used to revert SBFD symbol to non-SBFD symbol
Moderator proposal2: No action in RAN necessary.

## Slide 4: Appendix (1/2)
(RP-240270) Proposal 2: Rel-19 WID should be revised with the following:
Specify enhancements for CLI handling [RAN1, RAN2, RAN3, RAN4]:
  Support gNB-to-gNB co-channel CLI handling scheme(s) (the detailed schemes are to be down-selected from those in TR38.858 by RAN1#117)
  Support UE-to-UE co-channel CLI handling scheme(s) (the detailed schemes are to be down-selected from those in TR38.858 by RAN1#117)
  Further, support CLI handling scheme(s) to also include adjacent channel interference
  Note: Without dedicated optimization for dynamic/flexible TDD
Specify BS RF requirements for SBFD operation at gNB [RAN4]
Specify applicable RRM core requirements for co-channel and adjacent channel CLI handling mechanisms [RAN4]

## Slide 5: Appendix (2/2)
(RP-240480) Proposal 1: Update WID objective and assumptions related to UL subband as follows:
Specify UE transmission, reception and measurement behavior and procedures in SBFD symbols and/or non-SBFD symbols for SBFD aware UE [RAN1, RAN2]
    Transmission and reception behaviours on SBFD subbands configured in DL and/or flexible symbol indicated by TDD-UL-DL-ConfigCommon
      UL transmissions within UL subband only
      DL receptions within DL subband(s) only, except for CLI measurement by the UE outside of the DL subbands
Note: When flexible symbols are used, it is not expected that any legacy Uplink symbol is converted to Downlink/SBFD symbols. Legacy Uplink symbol indicates a symbol that is indicated as Uplink by legacy signaling such as ConfigCommon, TDD-UL-DL-ConfigDedicated and/or dynamic SFI indication.
One UL subband for SBFD operation in an SBFD symbol (excluding legacy UL symbol/slot) within a TDD carrier.
NOTE: legacy UL symbol/slot includes all UL symbols are indicated as UL to any serving UE(s) via slot formation signaling such as TDD-UL-DL-ConfigCommon, DL-ConfigDedicated, and group common slot format-indicators (SFI).