Third Generation Partnership Project

DRAFT Meeting Report v1.1.0

for

3GPP TSG CT WG 1

Meeting #54

Zagreb, Croatia 23rd – 27th June 2008

Hosted by

Ericsson Nikola Tesla , Zagreb

Chairman: 	Atle Monrad, Ericsson atle.monrad@ericsson.com

Vice Chairman: 	Georg Mayer, Nokia georg.mayer@nokia.com

Vice Chairman: 	Chen-Ho Chin, Samsung chenho.chin@samsung.com

3GPP Support:	Andrijana Brekalo, ETSI MCC. andrijana.brekalo@etsi.org

Table of contents

Table of contents	2

1 	Opening	4

2	Agenda & Reports	4

3	Input Liaison statements	4

4	Work organisation	21

4.2	Other adm. Issues	21

5	Corrections to old releases	21

5.1	Rel-4 and older	21

6	Release 5	21

6.1	Work Item: IMS-CCR	21

6.2	All other Rel-5 WIs	22

7	Release 6 work items	22

7.1	Work Items: IMS2 PRESNC, SEC1-SC	22

7.2	All other Rel-6 WIs	23

8	Release 7 work items	23

8.1	Work Item: PCC	23

8.2	Emergency Call Enhancements for IP& PS Based Calls – stage 3	24

8.2.1	Work Item: EMC1 - Emergency Call Enhancements for IP& PS Based Calls – stage 3 IMS part; IMS documents (24.229)	24

8.2.2	Work Item: EMC1 - Emergency Call Enhancements for IP& PS Based Calls – stage 3 access part; Access documents (24.008 and 24.234)	26

8.3	Work Item: ServID	26

8.4	Work Item: MTSI	26

8.5	Work Item: IMSProtoc	26

8.6	Work Item: GRUU	27

8.7	Work Item: SDoUE	27

8.8	Work Items: EVGCS, IVGCS and VGCSflex	27

8.9	Work Item: VCC	27

8.10	Work Items: CSICS CSItermS	27

8.11	Work Item:I SMSIP	27

8.12	Work Items: FBI, FBI-pcbl	27

8.13	Work Item: NSP-CR	28

8.14	Other Rel-7 work items	28

8.14.1	All other IMS-related WIs	28

8.14.2	All other Non-IMS-related WIs	28

9	Release 8	28

9.1	Release 8 documents for information	28

9.2	SAE issues	30

9.2.1	Work Items: SAES - Stage 3 SAE impact on services, network functions and capabilities; Stage 2 & 3 for Network selection procedures	30

9.2.2	Work Items: SAES - SAE for LTE access (mainly TS 24.301)	34

9.2.3	Work Items: SAES - TS 24.302.	47

9.2.4	Work Items: SAES - TS 24.303	52

9.2.5	Work Items: SAES - TS 24.304.	55

9.2.6	Work Items: SAES-CSFB	55

9.3	Work Item: PRIOR-MM	57

9.4.1	Study Item: MRFC	57

9.4.2	Work Item: MRFC_TS	57

9.5	Work Item: UUSIW	57

9.6	Work Item: PktCbl-Intw, PktCbl-Deploy, PktCbl-Sec	57

9.7	Work Item: ETWS	58

9.8	Work Item: EData	59

9.9	Work Item: EVA	59

9.10	Personal Network Management - Stage 2 and Stage 3 issues	59

9.10.1	Work Item: PNM Stage 2	59

9.10.2	Work Item: PNM Stage 3	60

9.11	Work Item: IMSProtoc2	61

9.12	Work Item: Overlap	63

9.13	TISPAN R1 and R2 maintenance and 3GPP and 3GPP2  re-documentation	64

9.13.1	Work Item: MAINT_R1	64

9.13.2	Work Item: MAINT_R2	66

9.13.3	Work Item: REDOC_TIS-C1	66

9.13.4	Work Item: REDOC_3GPP2	68

9.14	Work Item: NBA	69

9.15	Work Item: PPACR-CT1	69

It was commented that the CR introduce some clarification which was not specified by stage 1. It was proposed to introduce reference to RFC specification.	70

9.16	IMS supplementary services	70

9.16.1	Work Item: CCBS-CCNR	70

9.16.2	Work Item: CW-IMS	71

9.16.3	Work Item: FA	71

9.16.4	Work Item: CAT-SS	71

9.17	Work Item: OAM8-Trace	72

9.18	Work Item:  IWLANNSP	73

9.19	Work Item: IWLAN_Mob	73

9.20	Work Item: IMS_Corp	74

9.21	Work Item: ICSRA	76

9.22	Work Item: IMS-Cont	79

9.23	81

9.23.1	All other IMS-related WIs	81

9.23.2	All other Non-IMS-related WIs	82

10	Output Liaison Statements	85

11	Late and misplaced documents	88

12	A.O.B.	90

13	Closing	90

Annex A	Participants list	91

Annex B	Output documents (Agreed CRs, WIDs, LS OUT)	95

Annex C	Document List (CT1-54)	100

# 1 	Opening

The meeting was opened on Monday 23rd June at 9:00 in Hotel Westin Zagreb.

On behalf of the host Ericsson Nikola Tesla Company, Mr. Lorenco Damjanic gave a welcome speech and wished to all the delegates nice time in Zagreb and successful meeting.

# 2	Agenda & Reports

It was agreed that documents requested by the deadline for requests and submitted until the deadline for documents submission should not be treated as late document.

C1-082120	Agenda

Type:		Agenda

Source: 	CT1 chairman

Discussion:

Status:	NOTED

# 3	Input Liaison statements

C1-082198	LS on documentation of TISPAN Rel-2 in 3GPP

Type:		LS IN

Source: 	TSG SA

Discussion:	It was agreed by the SA #40 not to add any new functionality to 400-series and 500-series TISPAN R1 and R2 re-documentation specifications.

This decision means that the work on the still outstanding services for which stage 1 requirements and work items do already exist (NBA, overlap, CW, CCBS/CCNR, IMS_Corp) can continue in the common IMS specifications that will continue to later releases but TSG SA requests not to duplicate the outcome of that work in the already frozen specifications.

3GPP website also documents these decisions at: http://www.3gpp.org/specs/TISPAN-IMS-transfer.htm

TSG SA kindly requests all groups to treat the TISPAN re-documentation TSs in 400-series and 500-series as already frozen so that only essential corrections are allowed and not to make any alignment CRs to add new functionality from stage 1 or 2 towards the later stages.

Status:	NOTED

C1-082199	Reply to LS from TSG-RAN on decision for NW interface option for ETWS support

Type:		LS IN

Source: 	TSG SA

Discussion:	TSG SA reviewed LS from TSG RAN on possible architecture for the support of ETWS elements in the RAN.

It was agreed to task SA WG2 to analyse this proposal and determine whether any other alternative could be used or not. TSG-SA has granted a Rel-8 exception to SA2 for this exercise.

TSG SA WG2 is also asked to inform as soon as possible TSG CT WG1 and TSG RAN WG2 and TSG RAN WG3 of the consequence of their decision.

It is recognized that the other possibility relying on the direct interface in between the CB Centre and eNode B might create some difficulties in terms of addressing the proper eNode Bs.

If a positive answer can be given to the alternative described by TSG-RAN, it is also noted that the CT working groups may base their work on the already specified TS 25.419 in order to speed up their work (e.g. defining the proper envelop to encapsulate messages inside the most appropriate transport layer that CT would specify and re-use this application layer between the CB Centre and the MME).

TSG SA kindly asks SA2 to review the ETWS architecture proposal by TSG-RAN and provide feedback to CT1, RAN2, and RAN3 at their earliest convenience.

Status:	NOTED

C1-082200	LS on multiple solutions for VoIP call continuity

Type:		LS IN

Source: 	TSG SA

Discussion:	SA indicates that it is preferred to have a single solution for VoIP call continuity (SR-VCC).

Status:	NOTED

C1-082201	LS on handling of local emergency calls numbers dialled whilst in IMS

Type:		LS IN

Source: 	TSG SA WG2

Discussion:	C1-082334 and C1-082335 are related CRs.

C1-082183 is a discussion document on IMS Emergency Services gap analysis.

The LS will be discussed in the IMS parallel session.

Background:

SA2 has agreed the attached change request which modifies the behaviour of the in the case where the user has dialled a local emergency number which is not recognized by the UE while the UE is registered in IMS.

At present SA2 believe that when the UE is redirected to the CS domain, it is instructed to set up an emergency call (the SA2 technical specifications only indicate that the CS domain is used for emergency services). This will result in the UE being connected to the default PSAP rather than to the requested PSAP.

SA2 has modified the behaviour in Release 7 and would like to ask CT1 to determine any impacts to CT1 and decide whether such change should be applied only to Release 7 and Release 8 or if instead the change should be applied also to earlier releases.

Status:	NOTED

C1-082202	LS on IM Credentials

Type:		LS IN

Source: 	TSG SA

Discussion:	SA#40 has approved the attached CR SP-080268 as part of work related to 3GPP2 input to Common IMS.

The CR introduces, among other things, the concept of IM Credentials.

In order to complete the work with 3GPP2 input to Common IMS, it is kindly asked that CT1 and SA2 make the appropriate changes in TS 24.229 and TS 23.228 to align these specifications with TS 33.203.

Status:	NOTED

C1-082203	LS on “IMS initiated and controlled PSS and MBMS User Service” Architecture

Type:		LS IN

Source: 	TSG SA WG4 MBS S

Discussion:	SA4 posed questions to stage 2 groups on the WI “IMS initiated and controlled PSS and MBMS User Service”

Status:	NOTED

C1-082204	LS on CS fallback for 1xRTT CS domain access

Type:		LS IN

Source: 	TSG SA WG2

Discussion:	SA2 posed questions to RAN2 and CT4 on CS fallback functionality for 1xRTT access.

Status:	NOTED

C1-082205	LS on Earthquake and Tsunami Warning System

Type:		LS IN

Source: 	TSG SA WG2

Discussion:	SA2 has documented details of their preferred solution for ETWS in TR23.828 v.0.2.0. This TR is being sent to SA plenary in June 2008 for approval. SA2 expect that the TR is to be used as a guideline for specification work in the relevant WGs.

Status:	NOTED

C1-082206	LS on Active mode paging in E-UTRAN

Type:		LS IN

Source: 	TSG SA WG2

Discussion:	TSG SA2 would like to inform TSG RAN2 and CT1 about the outcome of discussions related to delivery of paging indication for CS fallback.

In case of the terminating CS Services to an UE, a mechanism to deliver a paging indication for CS services to the UE is required to indicate CS fallback to an active UE. This indicator guides the UE to perform CS Fallback specific operation.

Paging of active UE’s is needed for the CS fallback feature. To enable paging of active mode UE’s the MME shall check if there is active S1 connections before executing the normal paging procedure. If an active S1 connection exists for the UE this connection will be reused to convey the paging message to the UE.

With this solution for active mode paging it seems that the MME can send the active mode paging as a NAS message, transparent to the eNB.

Status:	NOTED

C1-082207	Response LS on the need for TAU in connected mode

Type:		LS IN

Source: 	TSG SA WG2

Discussion:

Status:	NOTED

C1-082208	Reply LS on Enhancements for SRNS Relocation

Type:		LS IN

Source: 	TSG SA WG2

Discussion:

Status:	NOTED

C1-082209	Reply LS on adding UE Capability as a SPT

Type:		LS IN

Source: 	TSG SA WG2

Discussion:	SA2 would like to thank CT1 for their LS on "Adding UE capability as a SPT".  SA2 has agreed a CR to remove the requirement from the Release 8 version of their specification.

Status:	NOTED

C1-082210	Reply LS on working assumptions for the scope of responsibility for optimized handover specification

Type:		LS IN

Source: 	TSG SA WG2

Discussion:	SA2 agrees with the working assumptions stated in the document:

1) for the handover direction from E-UTRAN to HRPD no NAS signalling is involved, and

2) for the handover direction from HRPD to E-UTRAN, apart from a possible new value for the attach type in the Attach Request message, there are no impacts on the NAS protocol, assuming that the signalling transport of NAS messages via the S101 interface is provided by the AS via the same service access point as the signalling transport via the S1 interface.

Just as a clarification, SA2 would like to inform CT1 that the indicator present in the Attach Request messages, referred to in #2 above, is not specific for HRPD to E-UTRAN HO, but provided by the UE in attach request message during any non-3GPP to 3GPP access system HO.

Status:	NOTED

C1-082211	Reply LS on Resource mapping at handover between EPS and 2G/3G

Type:		LS IN

Source: 	TSG SA WG2

Discussion:	CT1 asked SA2 about the value range of the EPS Bearer ID and the maximum number of active EPS Bearers. Furthermore, CT1 inquired about the solution for handling the mapping of EPS Bearers in case the EPS Bearer value range exceeds that of the NSAPI

In response to this query, SA2 would like to inform CT1, that the value range and mapping of the EPS Bearer Identity to the NSAPI has been resolved in the latest approved version of TS 23.401 (version 8.1.0, section 5.2.1 “EPS bearer identity”)

- For inter-RAT mobility between E-UTRAN and GERAN/UTRAN a one to one mapping between and the EPS Bearer and the PDP Context is specified.

When mapping EPS Bearers to PDP Contexts and vice versa, the same identity value shall be used for the EPS Bearer identity and the NSAPI/RAB ID. The value ranges of the EPS Bearer Identity and the NSAPI are therefore equivalent.

Status:	NOTED

C1-082212	Reply LS on NGCN issues and proposed workshop

Type:		LS IN

Source: 	TSG SA WG2

Discussion:	C1-082246 is the RIM's related discussion document.

Status:	NOTED

C1-082213	LS on UE Radio Capabilities

Type:		LS IN

Source: 	TSG SA WG2

Discussion:	This LS is related to response LSs in C1-082255 and C1-082234.

SA2 and RAN-groups discuss the need for provision of UE capabilities to NAS.

Status:	NOTED

C1-082214	LS on IMS Emergency Registration

Type:		LS IN

Source: 	TSG SA WG2

Discussion:	C1-082179, C1-082180, C1-082181 and C1-082183 are related documents.

C1-082371 is also contribution related to this topic.

SA2 has tried to address the SA1 requirements for emergency calls, and in particular the requirement related to call back and also related to the usage of the Directory number/MSISDN for emergency call.

As a conclusion of the discussion, a number of actions have been identified as way forward. As part of this, SA2 decided to eliminate the use of the Emergency Public User Identity (E-IMPU) and instead use an emergency registration indicator for Rel.7 and Rel.8. This change is regarded as an essential correction.

Due to the timing, SA2 realize that CT1 will need to find a solution reasonably quickly. But the alternative would be to use a less attractive solution where the E-IMPU is retained. The decision of eliminating the E-IMPU is conditional, based on the assumption that CT1 will be able to find a simple solution to solve this within a reasonable timeframe.

SA2 asks CT1 to:

- consider eliminating the use of the E-IMPU and instead using an emergency indicator in the registration request.  If the indicator can be defined within a short period, then SA2 will adopt this solution.

- advise SA2 and CT4 of your decision so impacted specifications can be updated, if needed, per CT1’s decision.

Status:	NOTED, Reply LS in C1-082540

C1-082215	Reply LS on request for recommendations (on IEEE 802.11u approach)

Type:		LS IN

Source: 	TSG SA WG2

Discussion:	TSG SA WG2 would like to inform CT1/SA1 that they have received the LS S2-083210 from IEEE 802.11u, including a summary of IEEE 802.11u, “Interworking with External Networks” and requesting recommendations in this area.

SA2 was under the view that CT1 and SA1 normally perform specification changes in the area of Network Selection. CT1 are then kindly asked to help in the query by answering IEEE 802.11u questions included in LS S2-083210. Consequently, SA2 also believe that this is up to CT1 to decide to perform stage 3 changes in this area.

CT1 is kindly asked to answer the questions from IEEE 802.11u included in the LS S2-083210 to help and progress in this area.

There is related CR from RIM in C1-082471.

Status:	NOTED, Reply LS is in C1-082541

C1-082221	SA1 answer to Relation between EPS Services and GPRS Services

Type:		LS IN

Source: 	TSG SA WG1

Discussion:	This is the reply from SA1 on service related questions on the relationship of EPS services with GPRS. In particular it was asked if, from a services point of view, these services should be considered independent – having different subscriptions – or should be considered the same packet service, with potential access restrictions to one or the other access system.

It was commented that the attached CR is not the latest one.

Status:	NOTED

C1-082222	LS on Unauthenticated PS emergency calls

Type:		LS IN

Source: 	TSG SA WG1

Discussion:

Status:	NOTED

C1-082223	Reply LS on CSG requirements for UTRA/E-UTRA

Type:		LS IN

Source: 	TSG SA WG1

Discussion:

Status:	NOTED

C1-082224	SA1 answer on " SAE interworking with Pre-REL8 system "

Type:		LS IN

Source: 	TSG SA WG1

Discussion:	During the discussion at SA1#40, SA1 decided that the use case agreed at the last SA1 meeting (SA1#39) (i.e. a user from a pre-release 8 operator receives E-UTRAN access while roaming in a Rel-8 EPS network) is not the primary, but a valid, use case as this use case received support from one operator among the operators present at SA1#40.

All operators present at SA1#40 were interested in the new use case when an operator makes a stepwise upgrade of HSS/AUC to Rel-8 EPS to its own PLMN, and consider this to be the primary use case.

Therefore, SA1 would like all other groups to primarily consider the stepwise upgrade use case. Also, as a secondary consideration, the original use case identified above with roaming subscribers shall be taken into account. Note that the earlier expressed requirements about "no impact"/"limited impact" does not apply to the stepwise upgrade use case. If the roaming use case requires changes on top of the solution for the stepwise use-case for these changes the "no impact"/"limited impact" requirement still applies.

Therefore SA1 asks the other groups to revisit earlier discarded solutions; however, this should not delay the work for Rel-8.

SA1 would like to emphasize that the solution is needed in Rel-8 and can, if necessary, accept UTRAN level security for a limited time.

SA1 would like to ask the working groups involved in this discussion to take the above into consideration.

CT4 has outlined various solutions in one of the previous meetings. The document will be resubmitted to this meeting.

This will be discussed in Joint meeting with CT4 on Thursaday at 8:00.

Status:	NOTED

C1-082225	LS on ODB barring categories for EPS

Type:		LS IN

Source: 	TSG SA WG1

Discussion:

Status:	NOTED

C1-082226	Reply LS on Progress of eCall requirements

Type:		LS IN

Source: 	TSG SA WG1

Discussion:	SA1 clarifies some service requirements on eCall. CT1 can progress the work based on SA1 reply.

Status:	NOTED

C1-082227	LS on "MSG Answer to Progress of eCall requirements"

Type:		LS IN

Source: 	TSG SA WG1

Discussion:	SA1 clarifies that the "eCall only mode" refers to a terminal behaviour in relation to a specific configuration and is not intended to be related to any special (x)SIM type.

Status:	NOTED

C1-082228	SA1 answer to Support of pre-Rel-8 USIMs in EPS

Type:		LS IN

Source: 	TSG SA WG1

Discussion:	SA1 would like to thank CT1 for their LS S1-080511 (=C1-081424). In this LS CT1 drew our attention to the fact that no requirement in stage 1 can be found that mandates the support of pre-Rel-8 USIMs in E-UTRAN capable UEs.  SA1 answers the related questions as follows:

Q1: Can SA1 confirm CT1's understanding that pre-Rel-8 USIMs need to be supported in EPS ?

Answer: Yes. (see attached CR)

On a related question concerning Home NodeBs:

Q2: It is CT1's understanding that Rel-8 and onwards USIMs will contain additional files for EPS, and new files could be introduced for the purpose of storing some EPS Mobility Management parameters such as temporary identities or last visited registered TAI.
CT1's assumption is that in order to handle both pre-Rel-8 USIMs and Rel-8 and onwards USIMs, a solution needs to be implemented so that EPS Mobility Management parameters are stored in non-volatile memory in the UE when a pre-Rel-8 USIM is used, and are stored in the USIM when a Rel-8 USIM is used.
Can SA1 confirm the expected UE behaviour for Home NodeBs as indicated above?

Answer: It is SA1's understanding that for purposes such as the one indicated above additional files on the USIM will be needed. To be able to use USIMs that do not contain these files (e.g. pre Rel-8), the solution proposed by CT1 to store them in non-volatile memory in the ME seems to be a possible work-around. However, if such files exist in the USIM they should have preference.

Status:	NOTED

C1-082229	Ls on Adding and removing media during a multimedia service session

Type:		LS IN

Source: 	TSG SA WG1

Discussion:	SA1 confirms to RAN5 that add&remove of media is possible.

Status:	NOTED

C1-082230	Reply LS on Applicability of Multimedia Priority Service

Type:		LS IN

Source: 	TSG SA WG1

Discussion:	SA1 clarifies that MPS apply to media as well as signalling.

Status:	NOTED

C1-082231	LS on PPAC clarifications

Type:		LS IN

Source: 	TSG SA WG1

Discussion:	SA1 thanks CT1 for their LS on PPAC clarification.

SA1 understands that PPAC functionality will be specified in stage 3 for UTRAN only and therefore we corrected TS 22.011 in order to restrict the scope of PPAC in release 8 for UTRAN so we align with stage 3 work.

Is any further work on this needed in any CT1-specification?

In addition to UTRAN it is needed to handle PPAC in E UTRAN.

Status:	NOTED

C1-082232	LS on HSPA VoIP Continuity Solution

Type:		LS IN

Source: 	TSG RAN

Discussion:	The LS expresses concerns from RAN on multiple solutions for VoIP session continuity in Rel-8.

Status:	NOTED

C1-082233	LS on decision for NW interface option for ETWS support

Type:		LS IN

Source: 	TSG RAN

Discussion:

Status:	NOTED

C1-082234	Response LS on UE Radio Capabilities

Type:		LS IN

Source: 	TSG RAN

Discussion:	RAN kindly asks SA and SA2 to take note of the RAN decision on using AS procedure as the only procedure for transfer of LTE UE AS capability and that RAN would hence recommend not to adopt the NAS procedure as proposed in the attached SA2 CR.

Status:	NOTED

C1-082235	LS on add/remove media

Type:		LS IN

Source: 	TSG RAN WG5

Discussion:	RAN5 asks SA1 whether add&remove of media is possible.

Status:	NOTED, Reply in C1-082544

C1-082236	LS on SDP connection information

Type:		LS IN

Source: 	TSG RAN WG5

Discussion:	According to examples in TR 24.930, the SDP type connection information ("c") is present in session level but not in the media description.

RAN5 kindly asks CT WG1 to

- clarify/confirm the mandatory requirements for SDP connection information (“c=” ) within the media description

- provide guidance for interpretation on requirements for the SDP contents in TR 24.930 with respect to TS 24.229.

Status:	NOTED, Reply in C1-082545

C1-082237	LS on RTCP bandwidth modifiers for MTSI

Type:		LS IN

Source: 	TSG RAN WG5

Discussion:	RAN5 kindly asks CT WG1

-	to clarify whether or not they find TS 26.114 to be in conflict with TS 24.229 for the usage of RS, RR and AS modifiers for MTSI.

-	to give further guidance about the correct usage of those modifiers for MTSI if any kind of conflict is identified

-	to contact SA WG4 in case a conflict is identified between the specifications mentioned above

Status:	NOTED, Reply in C1-082546

C1-082238	Reply LS on reply LS on Paging Permission with Access Control (PPAC)

Type:		LS IN

Source: 	TSG RAN WG3

Discussion:	RAN3 comes to a conclusion that it is not necessary to have changes in RANAP to support PPAC.

Information on access class barring for PPAC may be treated/conveyed in the same manner as those barring information, before PPAC is defined.

Status:	NOTED

C1-082239	LS on Enhancements for SRNS Relocation

Type:		LS IN

Source: 	TSG RAN WG3

Discussion:	RAN3 would like to inform CT1 that RAN3 has agreed the DL NAS PDU handling as per Solution 2 in section 6.2 in the endorsed RAN3 internal TR as a scheme for the enhanced relocation for the WI: Enhancements for SRNS Relocation.

Especially as a solution for DL NAS Handling during the relocation, RAN3 has agreed to take an approach which Source RNC forwards the received DL NAS messages to Target RNC, which is different solution with LTE X2 HO that the source eNB sends the MME Non Delivery Notification with the DL NAS message.

RAN3 kindly requests CT1 to review the agreed scheme in TR. If no problems are seen then RAN3 kindly asks CT1 to analyse the impact CT1 might see on the outlined solution.

Status:	NOTED, Reply LS is in C1-082547

C1-082240	Reply LS on the necessity of Location Reporting procedure in S1

Type:		LS IN

Source: 	TSG RAN WG3

Discussion:

Status:	NOTED

C1-082241	LS on Data forwarding for Inter 3GPP-RAT HO from E-UTRAN to UMTS/GERAN

Type:		LS IN

Source: 	TSG RAN WG3

Discussion:

Status:	NOTED

C1-082242	LS on HSPA VoIP to WCDMA/GSM CS continuity

Type:		LS IN

Source: 	TSG RAN WG2

Discussion:	At TSG RAN #39 meeting, a new Rel-8 WI has been started, i.e, HSPA VoIP to WCDMA/GSM CS continuity and is scheduled to be finalized at RAN #41 meeting (Sep/2008).

RAN2 has discussed some solutions, at RAN2#61bis and RAN2#62, which are based on the multi-RAB capability of UMTS system (see attached document in R2-082474). The baseline solution assumes that the UE indicates to the RNC it is "HSPA VCC capable" as a UE capability during RRC connection setup. This capability would be based on IMS policy with regard to call anchoring: for this, UE should receive this policy during the IMS registration i.e. indication whether a voice call that is setup through IMS will be anchored or not.  If this UE capability is indicated by the UE, UTRAN would consider all HSPA VoIP calls as HSPA VCC capable.

Question1: Does CT1/SA2 foresee any problem in this assumption?

Another enhancement of the baseline solution proposes that after successful NAS Service Request procedure, RNC intercepts CC:Setup message to defer the actual CS voice bearer setup. And only when the real HO is decided, RNC forwards the CC:Setup message to MSC. By doing this, the radio efficiency can be improved.

Question2: RAN 2 kindly asks whether the existing MSC can cope with this kind of scenario and what could be the impact to CN nodes in general.

Status:	NOTED, Reply in C1-082548

C1-082243	LS on UTRA R8 hNB requirements

Type:		LS IN

Source: 	TSG RAN WG2

Discussion:	In RAN#39 a WI on “Support of UTRA HNB” has been agreed with the aim to adopt the CSG approach for UTRAN HNB in Rel-8.

In this context RAN-WG2 discussed the attached document R2-082203, which proposes UE white-list to be managed based on a combination of manual hNB cell selection and MM-protocols (i.e. LA update/accept/reject).

In these proposals the UE would display all HNBs in range and the user would be allowed to trigger the selection of such a HNB. The CSG would be added to the UE CSG white-list when accept is received and removed when reject is received as part of the LAU/RAU procedures.

It was discussed whether this proposal was contradictory to the requirement of  home E-NodeB white-list from SA1.

RAN-WG2 kindly asks CT1 whether the changes to the NAS protocol to handle LTE  CSG white-list management would also be available for UTRAN HNBs.

In GERAN white and black lists are discussed. It may happen that RAN and GERAN select different solutions. Some consistent solution should be found in both groups.

There is a new WI proposal in this meeting that may have an impact on outgoing LS. Related document is C1-082323.

Status:	NOTED, Reply in C1-082549

C1-082244	LS on per UE frequency restriction

Type:		LS IN

Source: 	TSG RAN WG2

Discussion:

Status:	NOTED

C1-082245	Reply LS on NAS–AS interaction for dependent procedures

Type:		LS IN

Source: 	TSG RAN WG2

Discussion:	RAN2 would like to thank CT1 for the reply LS on NAS–AS interaction for dependent procedures and would like to inform that based on the input from CT1, RAN has chosen to specify NAS-AS interaction for dependent procedures according to option 2, i.e. concatenation of NAS message with RRC will always be used with dependent AS and NAS message and concatenation is only allowed for procedures with dependent AS and NAS messages.  The only dependent procedure is the bearer establishment/modification procedure and any associated NAS message. No concatenation of NAS and AS messages is allowed for the uplink(although one exception exists: RRC CONNECTION SETUP COMPLETE and SERVICE REQUEST)

However, RAN2 would like to clarify RAN2’s understanding of the handling for simultaneous multiple bearer establishment procedure where the eNB rejects some bearers, but accepts at least one of the bearers. In that case, if a single NAS message is used for all bearers, it would be necessary to send the complete NAS message to the UE including the NAS information about the rejected bearers, together with all AS configuration for all admitted bearers. RAN2 believes that this issue will also be applicable for the Attach Accept if the Attach Accept were to contain NAS information for the default and additional dedicated bearers.

In case of simultaneous multiple bearer establishment, one alternative proposed in RAN2 is to concatenate separate NAS message along with the AS configuration of each bearer, depending on CT1 decision. Another alternative proposed is to specify that the UE should only establish bearers for which it has received both NAS and AS information.

NEC has a contribution related to LS in C1-082422, discussing two proposed solutions.

Status:	Forwarded to CT1-55, originally reply LS was foreseen in C1-082550

C1-082246	LS on Connection recovery by NAS

Type:		LS IN

Source: 	TSG RAN WG2

Discussion:	RAN2 kindly asks CT1 to consider standardising the NAS connection recovery procedures including inter-RAT recovery.

Status:	NOTED, Reply in C1-082551

C1-082247	LS on reservation of an MMEC value

Type:		LS IN

Source: 	TSG RAN WG2

Discussion:

Status:	NOTED

C1-082248	Reply LS on UE specific paging DRX

Type:		LS IN

Source: 	TSG RAN WG2

Discussion:	RAN2 has further progressed the default paging DRX, and has decided to provide the system information modification period as a multiple of the default paging DRX. The system information modification period needs to be a cell specific parameter, and thus RAN2 has agreed to also provide the default paging DRX as a cell specific parameter.

Status:	NOTED

C1-082249	Reply LS on Earthquake and Tsunami Warning System

Type:		LS IN

Source: 	TSG RAN WG2

Discussion:	RAN2 kindly asks CT1, SA1, SA2 and SA3 to take into account the RAN2 decisions regarding ETWS support in Release 8 E-UTRAN, and to also provide feedback for the questions indicated in this LS.

Status:	NOTED, Reply in C1-082552

C1-082250	Reply LS on S1 Overload Control and on security for service request message

Type:		LS IN

Source: 	TSG RAN WG2

Discussion:	During RAN2 #62 meeting, RAN2 discussed the establishment cause values in RRC Connection Request message and would like to inform the conclusion to other groups.

As RAN3 correctly understands, eNB does not look into NAS service request to know the purpose of the RRC connection. However, Establishment cause information element in the RRC Connection Request message will convey the corresponding information. For the information to other groups, RAN2 agreed the following values for Establishment cause IE:

- Emergency call

- High priority access AC 11-15

- MT access

- MO signalling

- MO data

- 3 spares

Status:	NOTED

C1-082251	LS regarding GAN Iu mode security

Type:		LS IN

Source: 	TSG GERAN WG2

Discussion:

Status:	NOTED

C1-082252	LS on Latency Reduction support for non RTTI capable MSs

Type:		LS IN

Source: 	TSG GERAN

Discussion:	CRs attached to this LS are split of to C1-082531 and C1-082532.

Status:	NOTED

C1-082253	Response LS on replacement of in-band tones within Group Calls

Type:		LS IN

Source: 	TSG GERAN

Discussion:	TCRT consider to replace in-band tones with control plane signalling.

Status:	NOTED

C1-082254	LS on documentation of TISPAN Rel-2 in 3GPP

Type:		LS IN

Source: 	TSG CT

Discussion:	3GPP CT kindly asks 3GPP SA to consider the text on TSG CT's proposal to provide a viable maintenance track to TISPAN Rel-2 and give guidance on how to consistently incorporate functionality from TISPAN Rel-2 into 3GPP Common IMS from Release 8 and onwards across all the relevant TSG WGs.

It was commented that for NBA only a maintenance is needed.

Status:	NOTED

C1-082255	ReplyLS on UE Radio Capabilities

Type:		LS IN

Source: 	TSG CT

Discussion:	TSG CT thanks SA2 for their liaison, and the opportunity to comment on the proposal to send UE Radio Capability information in MME attach and TAU procedures.

Several comments were made on the proposal and TSG CT would like to point out that:

- According to TSG CT information, TSG RAN WG2 already has an Access Stratum procedure for the transfer of LTE UE AS capability. TSG RAN #40 has also decided to recommend the use of this AS procedure instead of a NAS procedure.

- Due to meeting schedules the CT Working Groups have not yet had any chance to comment on the SA2 LS or its attached CR.

- Concerns were also expressed regarding the additional workload for CT1 that the SA2 proposal would represent.

- Even though conveying AS information in NAS messages is seen as technically feasible, it reduces the protocol layer integrity.

Based on the existence of the RAN AS procedure, and discussions at CT #40, TSG CT advises against sending the UE radio capability information in MME messages.

TSG CT kindly asks TSG SA to consider the above position when discussing the approval of the change request S2-084434 attached to the original SA2 liaison statement S2-084436.

Status:	NOTED

C1-082256	Reply LS on Enhancements for SRNS Relocation

Type:		LS IN

Source: 	TSG CT WG4

Discussion:

Status:	NOTED

C1-082257	LS on CAT in the 3GPP CS domain

Type:		LS IN

Source: 	TSG CT WG4

Discussion:

Status:	Forwarded to CT1-55, Reply was foreseen in C1-082553

C1-082258	LS on CT impacts for eCALL Data WI

Type:		LS IN

Source: 	TSG CT WG4

Discussion:

Status:	NOTED

C1-082259	LS on “Changes to the format of TMGI”

Type:		LS IN

Source: 	TSG CT WG4

Discussion:

Status:	NOTED

C1-082260	LS on CT-wide WID on enhancement of multimedia interworking between IM CN subsystem and Circuit Switched network

Type:		LS IN

Source: 	TSG CT WG3

Discussion:

Status:	NOTED

C1-082261	LS on Rejection of TFT filters

Type:		LS IN

Source: 	TSG CT WG3

Discussion:

Status:	NOTED

C1-082262	LS to 3GPP CT3, CT4, CT1, SA1 and SA2 status on Overlap Work

Type:		LS IN

Source: 	ETSI TISPAN WG3

Discussion:	TISPAN WG3 informs CT3 about the status of Overlap.

Status:	NOTED

C1-082476	LS on CS Fallback

Type:		LS IN

Source: 	RAN2

Discussion:	At RAN2 RRC Adhoc meeting in June 2008, RAN2 discussed CS fallback (CS FB) procedures and signalling details. During the discussion, RAN2 encountered a few questions and RAN2 would like to have answers from SA2 and CT1 for the further work.

CT1 can give some comments to question 2 and 4 where CT1 could contribute in order to not to be in conflict with possible answers from SA2.

For question 1, SA2 answer is needed.

Status:	NOTED, Reply in C1-082554

C1-082527	LS on Tracking Area Update in RRC Connected

Type:		LS IN

Source: 	TSG RAN WG2

Discussion:	RAN2 discussed a principle, whether it is NAS or AS that should trigger the unconditional TAU.

RAN2 has identified two possible solutions:

1) Include 2 bits possibly in handover command where 1 bit should be used to indicate to the UE to trigger TAU only if TAI read from broadcast channel of a cell UE has entered at HO is not in the list of TAI in the UE (as in IDLE) and second bit would be used to indicate to the UE to trigger TAU unconditionally (which could be used for mobility based MME change when the Idle mode behavior is not applicable or for load re-balancing).

RAN2 observed that with any AS based solution to trigger an unconditional TAU, the eNB would need to have the knowledge when to trigger TAU unconditionally (that is, at MME change).

RAN2 noted that eNB does not have the knowledge about the TA of the UE and hence cannot set a bit to a UE to unconditionally trigger a TAU when crossing the TA list. Thus two mechanisms are needed to trigger TAU in connected mode to meet all the requirements.

In case of load balancing, eNB triggered intra cell HO would result in L2 reset which imposes short data interruption over the radio. Further, a combination of S1 based Handover with intra-cell Handover will need to be supported to handle load rebalancing.

2) UE always behaves as in IDLE mode (i.e., UE reads TA from SIB in connected mode after HO) and, in addition for the purpose of load rebalancing, NAS triggers TAU transparent to the eNB.

For this alternative, it is unclear what NAS message is used to trigger TAU.

RAN2 discussed whether it is acceptable for the UE to always behave as in IDLE and not have the flexibility to configure the eNB to trigger the UE to perform a TAU in connected mode every time the UE moves out of its TA list. According to the current version of TS 36.331, triggering TAU in connected mode upon reading system information is not allowed. However, from RAN2’s point of view, we haven’t found any issue.

RAN 2 asks SA2 to answer following questions:

-	Which of the above alternatives SA2 sees as preferred for the purpose of TAU in RRC Connected?

-	In case alternative 1) is selected, what is the trigger for the eNB to set a bit that triggers unconditional TAU in the UE?

Status:	NOTED

C1-082529	NGCN issues and proposed workshop

Type:		LS IN

Source: 	ETSI TISPAN WG2

Discussion:

Status:	NOTED

C1-082537	LS on Reply to LS S3-080489 = C4-081222 on SAE interworking with Pre-REL8 system

Type:		LS IN

Source: 	TSG CT WG4

Discussion:

Status:	NOTED

C1-082538	LS on E-UTRAN Identifiers

Type:		LS IN

Source: 	TSG RAN WG3

Discussion:	This LS contains RAN3 feedback on E-UTRAN identifiers

Status:	NOTED

C1-082646	Reply LS on "SAE interworking with Pre-REL8 system"

Type:		LS IN

Source: 	TSG SA WG3

Discussion:	This LS should preferably have a common CT1 / CT4 reply

The LS will be presented in CT1 for endorsement but will be sent from CT4.

Status:	forwarded to CT1-55

C1-082678	NGCN issues and proposed WS

Type:		LS IN

Source: 	TSG SA WG3

Discussion:

Status:	NOTED

C1-082696	Actions upon out of credit condition

Type:		LS IN

Source: 	TSG CT WG3

Discussion:

Status:	NOTED

C1-082708	LS on IMS CAT

Type:		LS IN

Source: 	3GPP SA WG2

Discussion:

Status:	NOTED

# 4	Work organisation

## 4.2	Other administrative issues

The IMS Emergency workshop in Phoenix in October is not needed as CT1 has regular meeting and is busy with preparing contribution for that meeting. It was commented that CT1 does not need any dedicated days for this workshop, but it would be useful if SA2 informs CT1 about the agenda and foreseen work that is intended to be done there, so that CT1 delegates still have the possibility to join the workshop if they see the need.

This workshop concerns more IETF and SA2 and they should finish their part of work in 2008.. From protocol perspective the workshop would be needed in 2009.

It should be still possible for CT1 delegates to attend the workshop, which means that workshop should not be the week before CT1 meeting or during CT1 meeting. This will be left to SA2 to find a solution but it was agreed that CT1 does not need additional rooms during CT1 meeting in Phoenix.

C1-082528	Latest version of the Work Plan

Type:		Work Plan

Source: 	MCC

Discussion:

Status:	The document will be discussed by e-mail due to lack of the time during CT1-54

C1-082533	DISC, Administration of 3GPP Namespace Identification (NID)

Type:		Discussion

Source: 	CT1 Chairman

Discussion:

Status:	NOTED, the proposal was agreed

# 5	Corrections to old releases

## 5.1	Rel-4 and older

# 6	Release 5

## 6.1	Work Item: IMS-CCR

C1-082143	Annex A: Correction of SDP connection information

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:

Status:	WITHDRAWN

C1-082263	Correction on identifiers distinguishing the dialog

Type:		CR, 24.229

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	The CR was discussed in IMS parallel session.

Status:	REVISED TO C1-082605 which is AGREED

C1-082264	Correction on identifiers distinguishing the dialog

Type:		CR, 24.229

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	The CR was discussed in IMS parallel session.

The only change needed is to write "values of tags"

Status:	REVISED TO C1-082606 which is AGREED

## 6.2	All other Rel-5 WIs

# 7	Release 6 work items

## 7.1	Work Items: IMS2 PRESNC, SEC1-SC

C1-082138	Removal of draft-ietf-simple-common-policy-caps

Type:		CR, 24.141

Source: 	LM Ericsson

Discussion:	The CR was discussed in IMS parallel session.

Status:	REVISE TO C1-082607 which is revised to C1-082774 which is postponed.

C1-082139	Removal of draft-ietf-simple-pres-policy-caps

Type:		CR, 24.141

Source: 	LM Ericsson

Discussion:

Status:	WITHDRAWN

C1-082144	Annex A: Correction of SDP connection information

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:

Status:	REVISED TO C1-082609 which is AGREED

C1-082145	Annex A: Correction of SDP connection information

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:

Status:	REVISED TO C1-082610 which is AGREED

C1-082146	Annex A: Correction of SDP connection information

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:	Related to LS from RAN5 in C1-082236 and CT1 reply in C1-082545.

Status:	REVISED TO C1-082611 which is AGREED

C1-082612	Annex A: Correction of SDP connection information

Type:		CR, 24.403

Source: 	LM Ericsson

Discussion:	This is a NEW CR against 24.403 – parallel CR to C1-082609

Status:	AGREED

C1-082613	Annex A: Correction of SDP connection information

Type:		CR, 24.503

Source: 	LM Ericsson

Discussion:	This is a NEW CR against 24.503 – parallel CR to C1-082609

Status:	AGREED

C1-082614	Removal of draft-ietf-simple-pres-policy-caps

Type:		CR, 24.430 Rel-7

Source: 	LM Ericsson

Discussion:	This is a NEW CR against 24.430 (R7) – parallel CR to C1-082607.

Status:	WITHDRAWN

C1-082615	Removal of draft-ietf-simple-pres-policy-caps

Type:		CR, 24.430 Rel-8

Source: 	LM Ericsson

Discussion:	This is a NEW CR against 24.430 (R8) – parallel CR to C1-082607.

Status:	WITHDRAWN

C1-082616	Removal of draft-ietf-simple-pres-policy-caps

Type:		CR, 24.141

Rel-6

Source: 	LM Ericsson

Discussion:	This is a NEW CR against 24.141 (R6) – parallel CR to C1-082607.

Status:	REVISED TO C1-082775 which is POSTPONED

C1-082617	Removal of draft-ietf-simple-pres-policy-caps

Type:		CR, 24.141,Rel-7

Source: 	LM Ericsson

Discussion:	This is a NEW CR against 24.141 (R7) – parallel CR to C1-082607.

Status:	REVISED TO C1-082776 which is POSTPONED

## 7.2	All other Rel-6 WIs

# 8	Release 7 work items

## 8.1	Work Item: PCC

## 8.2	Emergency Call Enhancements for IP& PS Based Calls – stage 3

### 8.2.1	Work Item: EMC1 - Emergency Call Enhancements for IP& PS Based Calls – stage 3 IMS part; IMS documents (24.229)

C1-082179	Replacement of Emergency IMPU

Type:		Discussion

Source: 	LM Ericsson

Discussion:	Related Liaison Statements are in C1-082201, C1-082214.

CRs related to solution as proposed in C1-082179 are in C1-082180 and C1-082181.

Proposal in this document is a new communication service value for emergency is defined. In practice it means:

When an UE make an emergency registration it will include the emergency ICSI value in the contact header.

When the UE makes an emergency call it includes in the P-Preferred Service with emergency value.

The S-CSCF uses the emergency ICSI value in the Contact header and the P-	Preferred-Service header to trigger the specific behaviour in the S-CSCF for emergency that is required for the S-CSCF.

The E-CSCF includes the emergency ICSI value in the P-Asserted-Service header when it send the initial request to an IBCF.

Status:	NOTED

C1-082180	Replacement of Emergency IMPU

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:

Status:	POSTPONED

C1-082181	Replacement of Emergency IMPU

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:

Status:	POSTPONED

C1-082183	IMS Emergency Services gap analysis

Type:		Discussion

Source: 	Alcatel-Lucent/Milo Orsic

Discussion:	This discussion paper is related to C1-082179 and related CRs and LSs mentioned in discussion part of C1-082179.

Four problems were identified:

1) Identification of emergency registration

2) Identification of emergency call from the UE (in INVITE request)

3) Identification of emergency call towards the UE (in response to INVITE request, as UE was not aware that it sets up a emergency call)

4) Identification of a call back

It was agreed, that the emergency Public User ID can be removed (based on the question asked by SA2 in LS C1-082214. Though it was not agreed, how the emergency Public User ID could be replaced.

It was agreed that at least problem 1) and 4) should use the same mechanism for solution.

It is still not clear, whether a specific solution for 2) is needed and if, whether this solution should be the same as for 1) and 4)

It is still not clear whether the solution for 3) should be the same as 1) and 4).

It was indicated by some companies, that more granularity of information on the type of emergency call might be needed at least for problem 3).

Qualcomm volunteered to organize a conference call on this issue during the time to the next meeting.

Status:	NOTED

C1-082334	Correction to emergency service request

Type:		CR, 24.229

Source: 	Research in Motion

Discussion:

Status:	POSTPONED

C1-082335	Correction to emergency service request

Type:		CR, 24.229

Source: 	Research in Motion

Discussion:

Status:	POSTPONED

C1-082370	P-CSCF notification of non UE detectable emergency calls

Type:		Discussion

Source: 	Qualcomm Europe

Discussion:

Status:	NOTED

C1-082371	Identifying PSAP callbacks

Type:		Discussion

Source: 	Qualcomm Europe

Discussion:	Discussion papers related to the Emergency Service Identification issue are C1-082179, C1-082183 and C1-082371 (reply in C1-082540).

Related Liaison Statements are in C1-082201 and C1-082214.

CRs related to solution as proposed in C1-082179 are in C1-082180 and C1-082181.

Status:	NOTED

C1-082453	Discussion document on Correction to emergency service request

Type:		Discussion

Source: 	Research in Motion

Discussion:

Status:	NOTED

### 8.2.2	Work Item: EMC1 - Emergency Call Enhancements for IP& PS Based Calls – stage 3 access part; Access documents (24.008 and 24.234)

## 8.3	Work Item: ServID

## 8.4	Work Item: MTSI

C1-082265	Introduction of terms "multimedia telephony participant" and "multimedia telephony application server"

Type:		CR, 24.173

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	Consequences if not approved need to be updated. "See sub clause 4.3" needs to be put either into brackets or behind a comma.

Status:	REVISED TO C1-082618 which is AGREED

C1-082266	Introduction of terms "multimedia telephony participant" and "multimedia telephony application server"

Type:		CR, 24.173

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	The same comment as for C1-082618 apply.

Status:	REVISED TO C1-082619 which is AGREED

## 8.5	Work Item: IMSProtoc

C1-082140	Correction of DHCP reference

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:

Status:	WITHDRAWN

C1-082141	Correction of DHCP reference

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:	WI to be changed to IMSProtoc2.

Status:	REVISED TO C1-082620 which is AGREED

C1-082267	Addition of AVPF support and SDP capability negotiation mechanism

Type:		CR, 24.229

Source: 	Alcatel-Lucent / Keith Drage

Discussion:

Status:	AGREED

C1-082268	Addition of AVPF support and SDP capability negotiation mechanism

Type:		CR, 24.229

Source: 	Alcatel-Lucent / Keith Drage

Discussion:

Status:	AGREED

## 8.6	Work Item: GRUU

## 8.7	Work Item: SDoUE

## 8.8	Work Items: EVGCS, IVGCS and VGCSflex

## 8.9	Work Item: VCC

## 8.10	Work Items: CSICS CSItermS

## 8.11	Work Item:I SMSIP

## 8.12	Work Items: FBI, FBI-pcbl

C1-082269	Profile corrections for outbound

Type:		CR, 24.229

Source: 	Alcatel-Lucent / Keith Drage

Discussion:

Status:	AGREED

C1-082270	Profile corrections for outbound

Type:		CR, 24.229

Source: 	Alcatel-Lucent / Keith Drage

Discussion:

Status:	AGREED

C1-082626	Update outbound reference

Type:		CR, 24.229, Rel-8

Source: 	Qualcomm Europe

Discussion:	This is mirror CR of C1-081627. WI is FBI-Pcbl, category A.

Status:	AGREED

C1-082627	Update outbound reference

Type:		CR, 24.229,Rel-7

Source: 	Qualcomm Europe

Discussion:	This is Rel-7 CR, Cat F, WI FBI-Pcbl. The mirror CR is in C1-082626.

Status:	AGREED

## 8.13	Work Item: NSP-CR

## 8.14	Other Rel-7 work items

### 8.14.1	All other IMS-related WIs

No documents provided.

### 8.14.2	All other Non-IMS-related WIs

C1-082173	Stage 2 alignment related to Network bearer control

Type:		CR, 24.008

Source: 	Ericsson

Discussion:	What are the possible values for Bearer Control Mode?

Cover page shall be corrected - reason for change should say that CT1 will treat this CR as essential correction due to SA2 decision.

Status:	REVISED TO C1-082640 which is POSTPONED

C1-082174	Stage 2 alignment related to Network bearer control

Type:		CR, 24.008

Source: 	Ericsson

Discussion:

Status:	REVISED TO C1-082641 which is POSTPONED

C1-082531	“Latency Reduction support for non RTTI capable MSs”

Type:		CR, 24.008

Source: 	Nortel

Discussion:	It was proposed to remove the note and make it as normative text.

Linkage to GERAN specifications should be removed.

Status:	REVISED TO C1-082642 which is AGREED

C1-082532	“Latency Reduction support for non RTTI capable MSs”

Type:		CR, 24.008

Source: 	Nortel

Discussion:	The same change applies as for previous CR.

Status:	REVISED TO C1-082643 which is AGREED

# 9	Release 8

## 9.1	Release 8 documents for information

C1-082271	Summary of current IETF documents on SIPPING

Type:		INFO

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	No significant change to any 3GPP dependencies, however note the appearance of draft-dawes-sipping-debug-event and draft-dawes-sipping-debug-id which are intended to ultimately be 3GPP dependencies. Peter Dawes would appreciate comment on these documents.

Status:	NOTED

C1-082272	Summary of current IETF documents on SIP

Type:		INFO

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	Presentation notes: Outbound has now advanced to -15 and Dean is preparing the proto writeup of this document. A couple of essential correction documents have now completed WGLC (draft-sparks-sip-invfix,

draft-ietf-sip-ipv6-abnf-fix) - these are essentially complete and we need to look at incorporating them into our profile. A call is currently out regarding the support of draft-dotson-sip-mutual-auth as a WG charter item. If companies are interested in this 3GPP dependency then please respond.

Status:	NOTED

C1-082273	Summary of current IETF documents on MMUSIC

Type:		INFO

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	No significant change to any 3GPP dependencies.

Status:	NOTED

C1-082274	Summary of current IETF documents on SIMPLE

Type:		INFO

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	draft-ietf-simple-partial-pidf-format, draft-ietf-simple-partial-notify, draft-ietf-simple-partial-publish, draft-ietf-simple-prescaps-ext have all been IESG approced and are now in the RFC editor's queue.

draft-ietf-simple-xml-patch-ops which is a dependency of these documents has also been approved so these should all progress rapidly to publication and RFC number assignment now.

Status:	NOTED

C1-082275	Summary of current IETF documents on XCON

Type:		INFO

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	Framework document is now published as RFC 5239.

Status:	NOTED

C1-082276	Summary of current IETF documents on GEOPRIV

Type:		INFO

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	Presentation notes: Waiting for a decision on draft-peterson-geopriv-retransmission (and this needs a revised version of that document) by WG before draft-ietf-sip-location-conveyance can proceed.

Status:	NOTED

C1-082277	Summary of current IETF documents on ECRIT

Type:		INFO

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	Presentation notes: No significant change to any 3GPP dependencies.

Status:	NOTED

C1-082278	Summary of current IETF documents on MEDIACTRL

Type:		INFO

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	draft-ietf-mediactrl-ivr-control-package is now a WG item

Status:	NOTED

C1-082279	Summary of current IETF documents on BLISS

Type:		INFO

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	No significant change to any 3GPP dependencies.

Status:	NOTED

## 9.2	SAE issues

### 9.2.1	Work Items: SAES - Stage 3 SAE impact on services, network functions and capabilities; Stage 2 & 3 for Network selection procedures

C1-082407	Reference version of TR 24.801, v 1.0.0

Type:		TR

Source: 	Nokia Siemens Networks

Discussion:

Status:	NOTED

C1-082121	Pseudo CR on PLMN selection, Introduction of TA

Type:		CR, 24.801

Source: 	T-Mobile

Discussion:

Status:	REVISED TO C1-082555 which is AGREED

C1-082151	Pseudo-CR on multi system PLMN selection

Type:		CR, 24.801

Source: 	Nokia

Discussion:	It is proposed to add RAT codes for CDMA 1xRTT and HRPD and to split the already existing E-UTRAN RAT code to E-UTRAN FDD and E-UTRAN TDD.

It is intended that while using the new RAT codes for selecting the candidate PLMN during PLMN selection procedure, once the candidate highest priority PLMN and RAT has been selected, then the actual registration procedures defined for the selected RAT shall be followed. So this change only affects the PLMN selection in the scope of 3GPP TS 23.122 and none of the subsequent procedures are affected.

HPLMN list on USIM shall be considered.

Status:	REVISED TO C1-082556 which is AGREED

C1-082152	Detailed pseudo CR on multi system PLMN selection

Type:		CR, 24.801

Source: 	Nokia

Discussion:	It was commented that the scope of TS 24.801 has too many details now if changes from this CR are included.

SIM should be replaced by UICC. It was replied that in definition section it is specified that 24.801 makes no distinction between SIM and USIM.

'3GPP2 access technology' should be replaced by appropriate term.

The scope of the TR is the scope of the TS 23.122 actually and will be put in one of the annexes in order to become the part of the TS later.

Status:	REVISED TO C1-082557 which is AGREED

C1-082171	Initiation of Security mode control procedure

Type:		CR, 24.801

Source: 	Ericsson

Discussion:	From the document it can be seen that at least a stand-alone Security mode control procedure is needed.

A combination of Security mode control procedure and Attach and TAU procedures could be possible to optimize the request of new key sets in attach and TAU procedures without a major effort.

If also the combination of Security mode control procedure and Attach and TAU procedures to support the SA2 wish for “on-the-fly” change of security algorithm this will however have more impact on the current CT1 definitions of NAS security.

To summarize there are three identified ways to initiate Security mode control procedure and CT1 needs to agree on the preferred option:

1) Only support a stand-alone Security mode control procedure;

2) Support a stand-alone Security mode control procedure and a Security mode control procedure combined with Attach and TAU procedures where the Attach accept and TAU accept messages are fully security protected;

3) Support a stand-alone Security mode control procedure and a Security mode control procedure combined with Attach and TAU procedures where the Attach accept and TAU accept messages are partially unprotected.

It is the proposal of this draft CR to choose option 1) and for the time being take note of the chosen option by adding a statement of this to the 3GPP TR 24.801.

NEC contribution in C1-082423 supports option 1 (contribution provided for the TS).

Status:	POSTPONED, Related LS out to SA2 is in C1-082558

C1-082172	Pseudo-CR on Mapping between GUTI and P-TMSI

Type:		CR, 24.801

Source: 	Ericsson

Discussion:	Related discussion document and the CR are in C1-082397 and C1-082398.

Status:	WITHDRAWN

C1-082323	Pseudo-CR on Option C for CSG deployments

Type:		CR

Source: 	Telecom Italia

Discussion:	During the SA plenary #38 a set of Stage 1 requirements on the HeNB CSG have been agreed in the document SP-080188. In the TR 24.801 there are two deployment scenarios documented in the chapter 10.12. This document tries to identify an additional Option C not competing with the other two, but collecting aspects from the two options already existing. If an agreement can be found on the new Option C the related CRs can be proposed for the next CT1 meeting in Budapest.

It was commented that there is a WI for SA2 and ongoing discussion on this topic. CT1 should avoid to make decision until SA2 discussion brings some conclusions on the topic this week in Montreal.

Solution c) is a compromise way forward. Some clarifications for option c) should be added.

C1-082355 is a proposed change to TS 24.301 (source: Qualcomm). It was proposed to address this change directly to Telecom Italia to incorporate it to the change request to the TR.

Status:	REVISED TO C1-082559 which is revised further to C1-082792. C1-082792 is AGREED

C1-082397	On temporary mobile identity handling at Intersystem change to 2G/3G for supporting ISR

Type:		Discussion

Source: 	Vodafone

Discussion:	It was commented that update status of GUTI and "update-needed" are not clear.

Related document is also C1-082491.

C1-082488 is also related discussion paper from Huawei.

Status:	NOTED

C1-082398	Temporary mobile identity handling at Intersystem change to 2G/3G for supporting ISR

Type:		CR, 24.801

Source: 	Vodafone

Discussion:

Status:	REVISED TO C1-082658 which is revised to C1-082717 which is AGREED

C1-082430	Corrections and additions to interaction between EMM and GMM following GMM unsuccessful procedures

Type:		CR, 24.801

Source: 	NEC/Yannick

Discussion:	In reply LS C1-082221/S1-080771 SA1 confirms that there is only one subscription for packet services, applying for both GPRS and EPS services. Also, SA1 indicates that “it is SA1's understanding that no special subscription for EPS is necessary. Cause “GPRS services not allowed in this PLMN” applies to GERAN/UTRAN and E-UTRAN.”

This contribution proposes to remove the related editor’s note in TR 24.801.

This contribution also proposes a description for the impacts on EMM due to attach/combined attach rejected by the network, as well as service request procedure rejected by the network.

It is also proposed that for cause #12, #13 and #15 there is interaction between EMM and GMM.

Corrections to styles needed in the text of the document.

Status:	REVISED TO C1-082560 which is AGREED

It was commented that after September plenary CRs should be created to move changes from the TR to TSs. It is proposed to have consistent approach towards all TSs until September plenary.

C1-082488	Discussion on the impacts of ISR function

Type:		Discussion

Source: 	Huawei

Discussion:	The principle is identical in this and Vodafone's document. The issue is which condition may be used to trigger this method.

Offline discussion is encouraged to merge those two papers into one common paper.

Status:	NOTED

C1-082489	Update the description of the ISR function for TR24.801

Type:		CR, 24.801

Source: 	Huawei

Discussion:

Status:	REVISED TO C1-082715 which is AGREED

C1-082491	Removed FFS about mapping GUTI to P-TMSI/RAI

Type:		CR, 24.801

Source: 	Huawei

Discussion:	It was questioned if mapping of parameters will be defined in 23.401 or 23.003. Currently it is part of the annex. Related document is also C1-082658.

Status:	REVISED TO C1-082716 which is AGREED

C1-082514	EPS as IP-CAN

Type:		CR, 24.229

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	EPS creates a new IP-CAN for which a new annex is required in 24.229. Note that while this can be substantially based on Annex B, the terminology is significantly different and therefore a new annex is proposed. Other changes are also required to support this IP-CAN.

Some editorial corrections shall be done, input to be provided offline.

Status:	REVISED TO C1-082680 which will be postponed and discussed offline until the next meeting.

C1-082525	Proposed WID for CT1 aspects of SRVCC

Type:		WID

Source: 	Nokia Siemens Networks

Discussion:	The objective of this work item is to enhance the relevant 3GPP protocol specifications to support the following aspects:

- Procedures to support call control state synchronization between UE and network when SRVCC is executed from PS to CS domain (i.e., change from SIP to TS 24.008 CC state machine, including a change from CC state Null to Active)

- indication of SRVCC capabilities

- indication of supported CS voice codecs for handover preparation with the target cell

This work item shall consider any necessary enhancements to the UE and the network to enable the objective.

It was questioned whether SA2 has made a decision on supported codecs - whether there will be default codec in use or there will be codec negotiation.

This is CT1 WI, CT4 has separate WI covering CT4 tasks.

It was questioned whether no changes are needed to 24.229 as the WI indicates.

Motorola, Telecom Italia and Vodafone shall be added as supporting companies. All affected specifications should be added (24.301 to be added).

Status:	REVISED TO C1-082561 which is AGREED

C1-082526	Proposed Update to WID for CT4 aspects of Evolved Packet System

Type:		WID for INFO

Source: 	Nokia Siemens Networks

Discussion:

Status:	NOTED

### 9.2.2	Work Items: SAES - SAE for LTE access (mainly TS 24.301)

C1-082408	Reference version of TS 24.301, v 0.3.0

Type:		TS

Source: 	Nokia Siemens Networks

Discussion:

Status:	NOTED

C1-082123	Optimized Handover Impacts to NAS

Type:		Discussion

Source: 	Nortel Networks

Discussion:

Status:	NOTED

C1-082124	S101 mode NAS Signalling Connection

Type:		CR, 24.301

Source: 	Nortel Networks

Discussion:	The terminology used in this document was questioned. We should specify more generic S101 mode, but more specific in definition of trusted non-3GPP access. Should HRPD be specified also in definition of S101 mode? It should be specified that S101 mode points to HRPD.

How to get non-3GPP stack if we are in the cell that does not support HO?

Status:	REVISED TO C1-082571 which is revised to C1-082794 which is AGREED

C1-082125	Optimized Handover Execution

Type:		CR, 24.301

Source: 	Nortel Networks

Discussion:	This contribution provides text to allow for the TAU during the execution phase of an optimized handover.

Status:	AGREED

C1-082126	Using S101 NAS Signalling Connection

Type:		CR, 24.301

Source: 	Nortel Networks

Discussion:	The document describes how the S101 mode NAS Signalling Connection is used.

Status:	AGREED

C1-082132	EMM-DEREGISTERED when in HRPD

Type:		CR, 24.301

Source: 	Nortel Networks

Discussion:	This contribution provides text to clarify that the UE should transition to EMM-DEREGISTERED when moving from E-UTRAN to HRPD.

It was questioned whether 'non 3GPP cell' is necessary to be specified in following bullet:

"-if the cell selected is a non-3GPP cell that does not support S101 mode to S1 mode handover, the sub state shall be NO-CELL-AVAILABLE."

It was not seen necessary to repeat HRPD reference in CT1 specification as it is sufficiently defined in stage 2. It would be sufficient to refer to definition of S101 reference point. Stage 3 should be defined as generic as possible.

Status:	REVISED TO C1-082795 which is AGREED

C1-082162	EPS bearer context

Type:		Discussion

Source: 	Ericsson

Discussion:	The issue is not clear from SA2 point of view.

Status:	NOTED

C1-082163	Pseudo-CR on EPS bearer context

Type:		CR, 24.301

Source: 	Ericsson

Discussion:

Status:	POSTPONED

C1-082164	Pseudo-CR on optional parameters in PDN connectivity request

Type:		CR, 24.301

Source: 	Ericsson

Discussion:	The proposed changes are added to clarify the usage of the optional parameters in PDN connectivity request.

The contraversial subclause is 8.3.1.2 (PDN address allocation). PDN address allocation is defined in 9.9.4.6.

Status:	REVISED TO C1-082572 which is AGREED

C1-082165	Pseudo-CR on Authentication procedure abnormal cases

Type:		CR, 24.301

Source: 	Ericsson

Discussion:	In sub clause 5.4.2.6 description of timers 3418 and 3420should be added.

Notes should be numbered as there are more than one note in the sub clauses.

Status:	REVISED TO C1-082573 which is AGREED

C1-082166	Pseudo-CR on IPv6 prefix delegation

Type:		CR, 24.301

Source: 	Ericsson

Discussion:	This CR removew the possibility for the UE of requesting additional prefixes via DHCPv6 from the Rel-8 version of 3GPP TS 23.401, to align stage 3 and stage 2.

In sub clause 6.2.1 cleanups are needed.

Some clauses that are voided will be removed as they are at the end of the clause.

Status:	REVISED TO C1-082574 which is AGREED

C1-082167	EPS bearer context synchronization at service request

Type:		CR, 24.301

Source: 	Ericsson

Discussion:

Status:	WITHDRAWN

C1-082168	Pseudo-CR on NAS Sequence Number Handling

Type:		CR, 24.301

Source: 	Ericsson

Discussion:	Related proposal is in C1-082413.

Correct handling of NAS COUNTs and in particular the sequence number part is crucial for EPS security. Incorrect handling could lead to loss of confidentiality and/or possibilities for faked/replayed messages. In particular, except for possible identical retransmission, the same NAS COUNT must never be used to process more than a single message protected under a given NAS security context. This contribution discusses the principles that should be used and proposes additional text to 24.301.

The contribution should be improved based on comments given by Nokia Siemens Networks (changes to clause 4 and 5)

Suggested algorithms in the annexes that could be used should be discussed offline.

Wording and structuring should be improved in sub clause 4.x.2, as well it should be checked against real requirements.

There are some principles in 4.x.2 that should be decided ,but not left to implementation (The receiver typically maintains a list (“window”) of recently received and authenticated NAS COUNT values.). There should be more description of algorithm Replay protection.

Status:	REVISED TO C1-082575 which is REVISED TO C1-082796.

C1-082796 which is revised to C1-082807 which is AGREED.

C1-082169	Pseudo-CR on TAU in connected mode

Type:		CR, 24.301

Source: 	Ericsson

Discussion:	This contributions proposes an alignment with stage 2 whereby a UE in connected mode only performs the tracking area update procedure when triggered from the lower layers after receiving an indication from the eNodeB.

It was commented by NEC that it is premature to include any option in CT1 specification as the discussion on the topic is still ongoing in SA2 . It was suggested to discuss first NEC contribution in C1-082421. It is related to incoming LS in C1-082527

It was confirmed by other companies that we should wait SA2 decision.

Status:	POSTPONED

C1-082170	Pseudo-CR on Order of integrity protection and ciphering

Type:		CR, 24.301

Source: 	Ericsson

Discussion:	In the current version of TS 24.301 it is not yet specified in which order integrity protection and ciphering shall be applied. This contributions studies the alternatives and proposes a way forward.

The order of the information elements could be changed. Partial cyphering of messages should be avoided.

Status:	WITHDRAWN

C1-082175	Coding of the TAI list IE

Type:		CR, 24.301

Source: 	Nokia

Discussion:	Table 9.9.3.6.1contains the text in bold style which should be normal.

In 9.9.3.X compression is mentioned but it is missing the indication how the compression occurs and how identified compression is being used.

9.9.3.x  says: The coding the information element allows short lists to be sent in plain mode without compression and large lists to be sent with compression.

It should be avoided to specify only large list in sentence above.

Status:	REVISED TO C1-082576 which is revised to C1-082797 which is AGREED.

C1-082176	ESM information in Attach messages

Type:		CR, 24.301

Source: 	Nokia

Discussion:	CT1 has agreed to implement a method to fulfil requirement in stage 2, but has not agreed the method to be used. Two different methods have been presented in CT1; a method basing on ESM message container IE in attach messages and a method basing on EPS NAS message concatenation.

This CR discusses those two possible methods and describes in more detail the method basing on ESM message container IE.

It was commented that additional concatenation methods should not be defined.

Status:	REVISED TO C1-082577 which is AGREED

C1-082185	UE Security Capabilities IE

Type:		CR, 24.301

Source: 	Alcatel-Lucent / Frank Alfano

Discussion:	This contribution adds information element definitions to Sub-Clause 9.9.3 of 24.301 v0.3.0.

It was commented that key derivation functions should be included in UE security capabilities. Same security alg apply on access stratum (RAN2 indicated in the LS in previous meeting). There is nothing received from SA3 on this.

9.9.3.x says that the purpose of the NAS security algorithms information element is to indicate which algorithms shall be used for ciphering and integrity protection.

It was questioned if this sentence should be more inoformative, i.e. if the use of 'shall' is appropriate.

Status:	REVISED TO C1-082578 which is AGREED

C1-082186	Tracking area request message update

Type:		CR, 24.301

Source: 	Alcatel-Lucent / Frank Alfano

Discussion:	This contribution is to change the definition of the Tracking Area Update request message. The objective is to have a mandatory UE identifier at the beginning of the message.

Subclause 8.2.26.x should be marked with revision marks.

Status:	POSTPONED

C1-082193	Update of UE requested PDN connectivity procedure

Type:		Discussion document

Source: 	Marvell

Discussion:	Since new parameter (Request type) is added to the message (PDN connectivity request), it should be described in actuall message not only in the procedure.

Status:	REVISED TO C1-082579 which is AGREED

C1-082280	CR to 24.301: Completion of timer T3402 procedures

Type:		CR, 24.301

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	In 5.5.1.2.4, it was commented that following sentence is not necessary: "If timer T3402 is currently running, the UE shall stop timer T3402."

It was commented that when timer expires it triggers tracking area update.

Status:	REVISED TO C1-082580 which is AGREED

C1-082281	CR to 24.301: Download of timer T3402

Type:		CR, 24.301

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	'May' to be changed to 'can'.

Status:	REVISED TO C1-082581 which is revised to C1-082791 which is AGREED.

C1-082282	CR to 24.301: Completion of timer T3411 procedures

Type:		CR, 24.301

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	A review of the procedures for timer T3402 indicates some omissions. This contribution attempt to complete those requirements.

This is alignment with 24.008

Status:	AGREED

C1-082291	Discussion about re-connection problem(R2-082895)

Type:		Discussion

Source: 	NTT DoCoMo

Discussion:	This paper proposes that UE should reestablish bearer when AS re-establishment is unsuccessful, regardless of existence of U-plane signal.

Concerns were raised whether the problem described could be resolved by the related CRs (C1-082292 – 94)

This will be included in outgoing LS C1-082551.

Lower Layer Failure, like Radio Link Failure, should be differentiated from other link failures that can happen.

Status:	NOTED, Reply LS to RAN2 in C1-082551 on the connection recovery can include also aspects indicated in this discussion. Related CRs are postponed.

C1-082292	Service Request Modification for Connection Recovery

Type:		CR, 24.301

Source: 	NTT DoCoMo

Discussion:

Status:	POSTPONED

C1-082293	TAU with active flag for Connection Recovery

Type:		CR, 24.301

Source: 	NTT DoCoMo

Discussion:

Status:	POSTPONED

C1-082294	Modification of Service Request for Connection Recovery

Type:		CR, 24.008

Source: 	NTT DoCoMo

Discussion:

Status:	POSTPONED

C1-082295	Discussion on requirements for USIM from CT1 point of view

Type:		Discussion

Source: 	NTT DoCoMo

Discussion:

Status:	NOTED

C1-082296	Proposal of normative annex which describes about newly introduced EPS parameters

Type:		CR, 24.301

Source: 	NTT DoCoMo

Discussion:	CT1 supported to continue with Alcatel-Lucent document, by removing change from Attach request message. In annex x the rewording is proposed.

Status:	REVISED TO C1-082586 which is AGREED, CR will be attached to related LS in C1-082713 (revision of C1-082508).

C1-082336	Flexible concatenation of ESM messages during attach

Type:		Discussion

Source: 	Panasonic

Discussion:	The current assumption for initial attach is that default bearer context is established at the same time as EMM-attach procedures. This is done by concatenation of EMM & ESM messages during initial attach. While this may seem to reduce the round trip time to achieve default bearer establishment after attach, it introduces many problems such as longer time to achieve basic attach and increased error dependency of ESM and EMM layers.

In this paper, it is intended to discuss these two problems and propose that this concatenation should be optional rather than mandatory.

Status:	NOTED

C1-082337	P-CR: Flexible concatenation of ESM messages during attach

Type:		CR, 24.301

Source: 	Panasonic

Discussion:

Status:	POSTPONED

C1-082339	Clarification of UE requested PDN disconnection procedure

Type:		CR, 24.301

Source: 	ETRI

Discussion:

Status:	WITHDRAWN

C1-082340	Clarification of UE requested bearer resource release procedure

Type:		CR, 24.301

Source: 	ETRI

Discussion:

Status:	WITHDRAWN

C1-082351	MTU signalling over NAS

Type:		CR, 24.301

Source: 	Qualcomm Europe

Discussion:

Status:	REVISED TO C1-082587 which is POSTPONED

C1-082353	Impact of CSG Access Control on NAS Procedures

Type:		CR, 24.301

Source: 	Qualcomm Europe

Discussion:

Status:	POSTPONED

C1-082354	On mapping between PDP context and EPS bearer context

Type:		CR, 24.301

Source: 	Qualcomm Europe

Discussion:

Status:	POSTPONED

C1-082355	Paging in Mixed Deployments

Type:		CR, 24.301

Source: 	Qualcomm Europe

Discussion:	It is proposed to agree to the following changes to 3GPP TS 24.301-0.3.0 to optimize the paging load in the presence of a mixed deployment of HeNBs and eNBs

- Allow the TAI list in the TRACKING AREA UPDATE ACCEPT message returned by the MME to include global cell identifiers (GCI) as well as TAIs.

Designate a special TAC to indicate that this HeNB or eNB only pages based on GCI.

Status:	POSTPONED

C1-082356	Registration in Mixed Deployments

Type:		CR, 24.301

Source: 	Qualcomm Europe

Discussion:

Status:	WITHDRAWN

C1-082358	Inclusion of R8 QoS in ESM messages

Type:		TS, 24.301

Source: 	Qualcomm Europe

Discussion:

Status:	REVISED TO C1-082588 which is AGREED

C1-082399	Sub-states update

Type:		CR, 24.301

Source: 	Vodafone

Discussion:	Spelling mistake to be corrected.

Status:	REVISED TO C1-082589 which is AGREED

C1-082409	Definition of the Service Request message.

Type:		CR, 24.301

Source: 	Nokia Siemens Networks

Discussion:	In table 9.3.1 'in this version of the protocol' is used. It was agreed earlier not to use this expression in the TS.

Status:	REVISED TO C1-082633 which is AGREED

C1-082410	Coding of the Attach result and Attach type information element

Type:		CR, 24.301

Source: 	Nokia Siemens Networks

Discussion:

Status:	REVISED TO C1-082634 which is AGREED

C1-082411	Coding of the TAI information element

Type:		CR, 24.301

Source: 	Nokia Siemens Networks

Discussion:	There are several occurrences of description of location area in the description.

MNC digits are not in right order in the table, but this order is taken from existing TS.

Changes done in 8.2.26.1 should be applied also in 8.2.26.3.

Status:	REVISED TO C1-082635 which is AGREED

C1-082412	Coding of the PDN type and PDN address information element

Type:		CR, 24.301

Source: 	Nokia Siemens Networks

Discussion:

- In 6.2.2 editor's notes can be removed.

- In 8.3.16.1 PDN address is added and there is no description of this IE

- 6.5.1.2 PDP type IE description needs rewording.

- The text in 8.3.6.10 should be reduced, they should say only how the IE is used, not talk about the content.

- PD type to be change to PDN type.

Status:	REVISED TO C1-082636 which is AGREED. Cleanup to be done for the next meeting.

C1-082413	Principles of NAS COUNT and NAS sequence number handling

Type:		Discussion

Source: 	Nokia Siemens Networks

Discussion:	The related proposal is in C1-082168.

During the last few meetings, CT1 has established some working assumptions about the handling of the parameters NAS COUNT and NAS sequence number. Some decisions, e.g. about the size of the parameters, have already been documented in TR 24.801 or TS 24.301, but so far no complete description has been given. This contribution tries to provide such a description.

If the NAS counter reaches the maximum value what is the way to do re-authentication? That part of the description is missing.

There are lot of similarities with proposal in C1-082168. It was proposed to continue with revision of C1-082168, remove all controversial issues and solve them with Editor's notes in order to progress on this topic.

Status:	NOTED

C1-082415	Correction of the Detach type IE

Type:		CR, 24.301

Source: 	Nokia Siemens Networks

Discussion:

Status:	AGREED

C1-082421	CR 24.301: TAU in connected mode

Type:		CR, 24.301

Source: 	NEC/Caroline

Discussion:

Status:	POSTPONED

C1-082422	CR 24.301 : Multiple EPS bearer contexts activation

Type:		CR, 24.301

Source: 	NEC/Caroline

Discussion:	Further to RAN2#62 reply LS on NAS-AS interaction for dependent procedures was sent where RAN2 proposes two options depending on whether CT1 makes a decision on NAS messages concatenation:

- Concatenate separate NAS message along with the AS configuration of each bearer (let’s call this, option 1, in this case the NAS messages are not concatenated)

- Establish bearers for which both NAS and AS information are received (let’s call this, option 2, in this case the NAS messages are concatenated)

After looking into the pros and cons of each alternative, this contribution proposes to adopt alternative 2 to simplify UE specification and implementation.

The group has agreed not to use combined scheme for the NAS transport. Concatenation of the NAS messages will not be used.

Status:	POSTPONED

C1-082423	CR 24.301 : Attach or TAU combined with Security Mode Control procedure

Type:		CR, 24.301

Source: 	NEC/Caroline

Discussion:	As Ericsson's contribution on the same topic was postponed, it is proposed to postpone this document as well.

Status:	POSTPONED

C1-082424	CR 24.301 : UE requested PDN connectivity procedure

Type:		CR, 24.301

Source: 	NEC/Caroline

Discussion:

Status:	REVISED TO C1-082689 which is POSTPONED

C1-082425	CR 24.301 : Default EPS bearer context activation not accepted by the UE

Type:		CR, 24.301

Source: 	NEC/Caroline

Discussion:

Status:	REVISED TO C1-082690 which is revised to C1-082802 to correct styles and formatting. C1-082802 is AGREED.

C1-082426	CR 24.301 : Dedicated EPS bearer context activation not accepted by the UE

Type:		CR, 24.301

Source: 	NEC/Caroline

Discussion:	First change to be cancelled to comply with 24.008. In sub clause 6.4.2.4 more cause codes to be added according to information in the TR.

Status:	REVISED TO C1-082718 which is revised to C1-082819 which is AGREED.

C1-082427	CR 24.301 : EPS bearer context modification not accepted by the UE

Type:		CR, 24.301

Source: 	NEC/Caroline

Discussion:	Cause code values shall include the complete list from the TR.

Some part of the introduced text will be cancelled as it will be moved to another place.

Status:	REVISED TO C1-082719 which is AGREED

C1-082431	Clarification for network initiated detach with re-attach required

Type:		CR, 24.301

Source: 	NEC/Yannick

Discussion:	This contribution proposes to clarify the UE behaviour when the network initiated detach is triggered with detach type set to re-attach required.

It was proposed to use the existing connection to be used for MME re-balancing.

This actually depends on what is the use case for re-attach required. There is one use case described in TS23.236 for Iu-flex (load balancing).

There was too many opened questions, therefore it is proposed to postpone the document untill there is understanding why re-attach required is usefull.

Status:	POSTPONED

C1-082432	Definition for EMM cause IE and updates for the handling of EMM reject causes

Type:		CR, 24.301

Source: 	NEC/Yannick

Discussion:

Status:	AGREED

C1-082480	EPS bearer QoS delivery on NAS level

Type:		CR, 24.301

Source: 	Panasonic

Discussion:

Status:	WITHDRAWN, merged with C1-082588

C1-082484	Discussion on the impact of multiple PLMN identities encoded in TAI list

Type:		CR, 24.301

Source: 	Huawei

Discussion:	Second change to be removed.

In the first change it should be specified in a generic way how the registered PLMN shall be derived. PLMN identity in the GUTI indicates the current registered PLMN.

Status:	REVISED TO C1-082720 which is AGREED

C1-082485	remove the FFS about "EPS bearer context status"

Type:		CR, 24.301

Source: 	Huawei

Discussion:	This includes removal of FFS indication.

Status:	AGREED

C1-082486	Discussion on the FFS of unsuccessful TAU procedure

Type:		CR, 24.301

Source: 	Huawei

Discussion:	The first change should be kept in the CR (removing editor's note under cause code #10), but all other changes should be reverted.

Status:	REVISED TO C1-082721 which is revised to C1-082820 which is AGREED

C1-082487	Update the description for UE requested ESM procedure

Type:		CR, 24.301

Source: 	Huawei

Discussion:

Status:	AGREED

C1-082490	Update the description of the ISR function for TS24.301

Type:		CR, 24.301

Source: 	Huawei

Discussion:

Status:	REVISED TO C1-082722 which is AGREED

C1-082492	The abnormal case for PDN connection procedure

Type:		CR, 24.301

Source: 	Huawei

Discussion:

Status:	REVISED TO C1-082723 which is AGREED

C1-082493	the abnormal case for service request procedure

Type:		CR, 24.301

Source: 	Huawei

Discussion:	Wording to be improved.

Status:	REVISED TO C1-082724 which is AGREED

C1-082497	P-CR on Abnormal cases on the network side for attach procedure

Type:		CR, 24.301

Source: 	ZTE

Discussion:	Numbering of bullets should be corrected during the CR implementation.

Similar editors note as in C1-082495.

Status:	REVISED TO C1-082726 which is AGREED

C1-082498	P-CR on Abnormal cases on the network side for TAU procedure

Type:		CR, 24.301

Source: 	ZTE

Discussion:	Figures of the signalling procedures should be moved to an appropriate place in the general section or at the top of the normal procedure.. It was agreed by the meeting to leave it to CR implementation issue.

Status:	REVISED TO C1-082725 which is AGREED

C1-082499	P-CR on Abnormal cases on the network side for GUTI reallocation procedure

Type:		CR, 24.301

Source: 	ZTE

Discussion:	Below the note UE to be replaced by GUTI.

Editor's note to be added in 5.4.1.5

Status:	REVISED TO C1-082727 which is AGREED

C1-082500	P-CR on PCO request procedure

Type:		CR, 24.301

Source: 	ZTE

Discussion:	In 5.4.6 includes actually mobility management procedure. In this section only session management procedures should be defined. New timer in session management to be introduced, or suitable existing timer to be used.

Status:	REVISED TO C1-082728 which is AGREED

C1-082501	P-CR on Ciphered PCO transfer flag

Type:		CR, 24.301

Source: 	ZTE

Discussion:	Changes to attach procedure to be removed.

Status:	REVISED TO C1-082729 which is AGREED

C1-082502	P-CR on Abnormal cases for UE requested PDN disconnection procedure

Type:		CR, 24.301

Source: 	ZTE

Discussion:

Status:	POSTPONED

C1-082503	P-CR on Abnormal cases for Dedicated EPS bearer context activation procedure

Type:		CR, 24.301

Source: 	ZTE

Discussion:

Status:	POSTPONED

C1-082510	Separate ESM messages for default and dedicated bearers

Type:		Discussion

Source: 	Motorola

Discussion:

Status:	AGREED

C1-082511	Update result and Update type information element

Type:		Draft CR

Source: 	NSN, Motorola

Discussion:	Editor's note to be removed. Table number to be corrected in 8.2.26.1.

Status:	REVISED TO C1-082702 which is AGREED

C1-082515	CR to 24.301: Download of timer T3412

Type:		CR, 24.301

Source: 	Alcatel-Lucent / Keith Drage

Discussion:

Status:	REVISED TO C1-082790 which is REVISED TO C1-082816 which is AGREED

### 9.2.3	Work Items: SAES - TS 24.302.

C1-082133	Baseline version of TS 24.302 v0.4.0

Type:		Draft TS

Source: 	Rapporteur

Discussion:

Status:	NOTED

C1-082134	Notes on conference call of 5th Jun 2008 on TS 24.302

Type:		Report

Source: 	Samsung/Chen-Ho

Discussion:

Status:	NOTED

C1-082135	P-CR: Restructuring and adding procedural text to sub clause 5.1 for Access Network discovery and selection

Type:		CR, 24.302

Source: 	Samsung/Chen-Ho

Discussion:	Now that 23.402 for ANDSF is functionally frozen and the UE and the ANDSF interactions in terms of discovery and selection of NW is clearer, subclauses 5.1, 5.1.1, 5.1.2 and 5.1.3 needs to be adjusted accordingly.

Proposed changes are:

a)	Discovery and Selection (of NWs), can be partitioned into 
	1st)	triggers that cause UE to commuincate with ANDSF to discover available ANs
	2nd)	discovering the available ANs
	3rd)	checking for presence of those ANs (and this is a radio specific procedure)
	4th)	selection of ANs

b)	Wordings/rewordings are chosen to distinguish between available access networks (ie. information provided by ANDSF) and access networks that are actually present.

First note in 5.1.2.1 shall be modified, related to use of operator's policies in order to  determine whether the information of available access networks known to the UE is out-of-date.

It was questioned what is the meaning of 'if the UE can communication with the ANDSF' in sub clause 5.1.2.2.

It is commented that wording 'By this signalling to the ANDSF and the information on available access networks provided by the ANDSF the UE discovers the available access networks' should be replaced by wording 'based on information provided through signalling ...'

Status:	REVISED TO C1-082562 which is revised to C1-082804.

C1-082804 is AGREED.

C1-082136	P-CR: Restructuring sub clause 6.8 and adding signalling procedure text

Type:		CR, 24.302

Source: 	Samsung/Chen-Ho

Discussion:	After the CRs agreed at CT1#53, it is proposed to better align the subclauses that describes commuincations between UE and ANDSF over the S14.

It was commented that editor's note that is now in UE procedures subclause should be moved to subclause 6.8.2.

In 6.8.2.2, push model should not be triggered by UE messages.

The CR is improving a structure of the document - a lot of bullet points and editor's notes have been just moved to other place.

Status:	REVISED TO C1-082563 which is AGREED

C1-082137	P-CR: Deciding if non-3GPP IP access is trusted or untrusted

Type:		CR, 24.302

Source: 	Samsung/Chen-Ho

Discussion:	Whilst the Stage 2 CR given in S2-084128 has clarified how the UE knows whether a certain non-3GPP IP access is trusted or untrusted, the manner by which the UE knows whether a non-3GPP IP access network is trusted or untrusted is still left open in Stage 3.

This P-CR proposes Stage 3 text for UE deciding on whether a non-3GPP IP access is trusted or untrusted.

Related papers are in C1-082404, C1-082504, C1-082416.

It was proposed to withdraw some of the proposals on the same topic and continue with one document as a base for further revisions.

C1-082404 is withdrawn. Samsung agreed to withdraw C1-082137 and to move part of changes to C1-082416. C1-082504 is withdrawn.

C1-082416 will be taken as a base for further revisions.

Status:	WITHDRAWN

C1-082161	Communication protocol between the UE and the ANDSF

Type:		Discussion document

Source: 	Ericsson

Discussion:

This contribution analyses the latest stage 2 requirements on the ANDSF (i.e. 3GPP TS 23.402 [2]) and describes the OMA Device Management (DM) protocol suggested to be used as the protocol for communication between the UE and the ANDSF, as well as discusses its benefits.

Using OMA DM , the server can request location information from terminal and provide terminal with information that match with the location information.

It was agreed that following aspects are important for the protocol (for MIH):

Support of Push

Support of Pull

Security

Location and Time line

This needs to be documented for the next meeting in the TR, for both solutions. It was proposed to give simple flows to show how to support push and pull to see the benefit of using each solution.

Status:	REVISED TO C1-082565 which is AGREED

C1-082187	Pseudo-CR on 24.302 Authentication and authorization for accessing EPC via a trusted non-3GPP access network

Type:		CR, 24.302

Source: 	Alcatel-Lucent / Frank Alfano

Discussion:	This contribution proposes modifications to the text in clause 6.4 of 3GPP TS 24.302 dealing with UE authentication and authorization when accessing an EPC via a trusted non-3GPP access network.

Identity management section is the only area of technical change in the document.

In 6.4.2.2 the first deletion of the text is something that should wait for SA3 decision first.

Status:	REVISED TO C1-082567 which is AGREED

C1-082191	IP Mobility Mode selection

Type:		Discussion document

Source: 	Marvell

Discussion:	In the CT1 meeting #54, CT1 agreed on EAP-AKA based mechanism for indication for IP mobility mode selection. This document specifies the details of this mechanism by specifying the attributes used for this purpose. This document also cleans up some of the text in section 6.3 based on comments received during the last meeting.

Corrections to structure of the document and styles needed:

- figures and tables should be created as appropriate using table numbers and references.

- hanging paragraphs should be avoided

- wrong styles should be corrected

- second sentence of the value description is not needed, it was included for clarification

- NSN and Marwell documents do not interfere and could go forward independently

Status:	REVISED TO C1-082568. Detailed coding shall be for further study. This should be included in editor's note, as well as indication that registration with IANA is needed. C1-082568 is postponed as the agreement could not be reached.

C1-082192	On Multiple PDN support

Type:		Discussion document

Source: 	Marvell

Discussion:	TS 24.302 currently does not cover aspects of Multiple PDN support on non-3GPP access. This documents introduces a section on Multiple PDN connectivity support in TS 24.302

It was commented that it is out of scope of 3GPP to define this kind of messages. It is access specific.

Status:	REVISED TO C1-082569 which is AGREED

C1-082338	Access Network Identity in TS 24.302

Type:		Discussion document

Source: 	Nokia Siemens networks, Nokia

Discussion:	It was commented that the need for parameter should be clarified. Both CT1 and CT4 should be aware of the use of the new parameter.

Status:	REVISED TO C1-082688 which is AGREED

C1-082360	Use DNS for ANDSF selection

Type:		CR, 24.302

Source: 	Qualcomm Europe

Discussion:

Status:	POSTPONED

C1-082404	Trust relationship detection

Type:		CR, 24.302

Source: 	Ericsson

Discussion:	Related documents are in C1-082137, C1-082416 and C1-082504.

Status:	WITHDRAWN

C1-082416	Detection of trusted/untrusted non-3GPP access network

Type:		CR, 24.302

Source: 	Panasonic

Discussion:	The main points of this contribution are as follows:

- If the trusted/untrusted information discovered during 3GPP-based access authentication is different from the pre-configured trusted/untrusted information, then the UE relies on the dynamic trust relationship discovery during 3GPP-based access authentication.  Further the UE updates its internal database about pre-configured trusted/untrusted information.

- If the UE does not perform 3GPP-based access authentication and the pre-configured information is not correct, the information about trusted/untrusted non-3GPP access network is conveyed to the UE from ePDG or P-GW via the IKEv2 messages for IPsec tunnel establishment or via DSMIP BA messages in case DSMIP bootstrapping was already performed.

Changes to 3GPP TS 24.302, v0.4.0 are proposed.

Most of the time UE knows if the access is trusted or untrusted.

Status:	REVISED TO C1-082564 which is POSTPONED

C1-082437	MIH Protocol for communication between UE and ANDSF

Type:		CR, 24.302

Source: 	Intel

Discussion:	This discussion paper presents the requirements that the protocol for communication between the UE and the ANDSF should fulfil. These requirements, among other things, indicate that information has to be extensible, both push and pull mechanisms need to be supported, and the transport options should allow information exchange in a secure way. Further it should be possible to limit information being made available to the UE through smart queries and the work needs to be completed within 3GPP in a timely manner to meet Release-8 timelines. It then describes how IEEE 802.21 Information Service and MIH protocol can satisfy all the requirements including the time line.

It is proposed to select the MIH protocol, for inter-system mobility policy and access network discovery information between UE and ANDSF.

The benefit of this proposal should be shown using flows.

Status:	REVISED TO C1-082566 which is further revised to C1-082793. C1-082793 is AGREED.

C1-082439	Location Information during Network Discovery

Type:		CR, 24.302

Source: 	Intel

Discussion:	On receipt of the request message the ANDSF sends a response to the UE. The response includes information about available access networks. The ANDSF provides the following information about available access networks:

1)	Type of Access network (e.g. WLAN, WiMAX);

2)	Access Network Identifier (e.g. SSID of WLAN network);

3)	The PLMN(s) it provides access to; and

4)	A preference value indicating the serving operator’s preference to access a particular access network.

5) Location (3GPP Cell Ids where the access network coverage is available)

Bullet 5 is added. It was questioned what is the behaviour when UE is in non-3GPP network. If the UE is on WLAN, keeping 3GPP off, UE does not know anything about the cell identity.

Some more offline discussion is encouraged.

Status:	POSTPONED

C1-082440	WiMAX System Information from ANDSF

Type:		CR, 24.302

Source: 	Intel

Discussion:	This contribution proposes information about the WiMAX system that needs to be provided by the ANDSF.

It was agreed that editor's note saying that the exact information provided for each access network is FFS, should not be deleted.

There should be a general framework first defined in form of the table, to define similarities between different access networks.

It was questioned if NSP (Network Service Provider) can be considered as network operator.

Status:	REVISED TO C1-082712 Added text in 5.1.x on WiMAX System Information should not be normative.

C1-082712 is revised to C1-082809 which is AGREED.

C1-082469	ANDSF indication of services supported

Type:		CR, 24.302

Source: 	Research in Motion

Discussion:

Status:	POSTPONED

C1-082470	ANDSF Operator differentiated text field

Type:		CR, 24.302

Source: 	Research in Motion

Discussion:	The purpose of this document is to describe necessary use case for the network to provide a generic container (free format text field) capability from the ANDSF to the UE to assist a subscriber when they are using a manual network discovery mechanism.

Status:	AGREED

C1-082504	P-CR on Trusted and Untrusted Accesses

Type:		CR, 24.302

Source: 	ZTE

Discussion:

Status:	WITHDRAWN

C1-082518	IPMS Indication in Authentication

Type:		Discussion

Source: 	Nokia Siemens Networks, Nokia

Discussion:

Status:	REVISED TO C1-082692 which is revised to C1-082803 which is AGREED.

### 9.2.4	Work Items: SAES - TS 24.303

C1-082122	DSMIP6 Detach

Type:		CR, 24.303

Source: 	Nortel Networks

Discussion:	Changes on changes should be fixed during the implementation.

Status:	AGREED

C1-082153	Multiple authentications for DSMIPv6 bootstrapping

Type:		CR, 24.303

Source: 	TeliaSonera

Discussion:	This Draft CR introduces multiple authentication exchanges capability to DSMIPv6 IKEv2 based bootstrapping procedures.

Status:	REVISED TO C1-082693 which is AGREED

C1-082154	Clarification of DSMIPv6 Handover Procedure

Type:		CR, 24.303

Source: 	Ericsson

Discussion:

Status:	REVISED TO C1-082694 which is AGREED

C1-082155	Field and Message Details for Initial BU and BA

Type:		CR, 24.303

Source: 	Ericsson

Discussion:	C1-062156 can possibly be incorporated into this document.

Status:	REVISED TO C1-082695 which is revised to C1-082808. Heading styles are incorrect and they should be corrected as part of CR implementation. All messages to be included in one normative annex.

C1-082808 is AGREED

C1-082156	Field and Message Details for Re-Registration

Type:		CR, 24.303

Source: 	Ericsson

Discussion:

Status:	WITHDRAWN, content merged with C1-082695

C1-082157	Field and Message Details for Handover BU and BA

Type:		CR, 24.303

Source: 	Ericsson

Discussion:

Status:	WITHDRAWN, content merged with C1-082695

C1-082158	Field and Message Details for DSMIPv6 Detach using BU and BA

Type:		CR, 24.303

Source: 	Ericsson

Discussion:

Status:	WITHDRAWN, content merged with C1-082695

C1-082159	Field and Message Details for HA Switch

Type:		CR, 24.303

Source: 	Ericsson

Discussion:

Status:	WITHDRAWN, content merged with C1-082695

C1-082160	Field and Message Details for BRI/ BRA and corrections

Type:		CR, 24.303

Source: 	Ericsson

Discussion:

Status:	WITHDRAWN, content merged with C1-082695

C1-082361	Definition of HA APN for HA discovery

Type:		CR, 24.303

Source: 	Qualcomm Europe

Discussion:	Stage 2 specifies that it is not mandatory that 'the UE shall use the HA-APN', therefore 'shall' is not appropriate here.

Status:	REVISED TO C1-082697 which is AGREED

C1-082362	Clarifications on values and error codes in BU and BA

Type:		CR, 24.303

Source: 	Qualcomm Europe

Discussion:

Status:	REVISED TO C1-082698 which is AGREED

C1-082364	Clarification on HoA and HNP assignment

Type:		CR, 24.303

Source: 	Qualcomm Europe

Discussion:

Status:	AGREED

C1-082365	Clarification on DSMIPv6 and PMIPv6 interactions

Type:		CR, 24.303

Source: 	Qualcomm Europe

Discussion:

Status:	REVISED TO C1-082699 which is AGREED

C1-082366	HA discovery mechanisms and respective applicability scenarios

Type:		CR, 24.303

Source: 	Qualcomm Europe

Discussion:	Reference in 5.1.2.1.6 to be corrected.

Status:	REVISED TO C1-082700 which is AGREED

C1-082367	Encoding of the target PDN information in IKEv2

Type:		CR, 24.303

Source: 	Qualcomm Europe

Discussion:

Status:	POSTPONED

C1-082368	Clarification on the usage of F flag in BA

Type:		CR, 24.303

Source: 	Qualcomm Europe

Discussion:

Status:	AGREED

C1-082452	DSMIPv6 back home

Type:		CR, 24.303

Source: 	Ericsson

Discussion:

Status:	WITHDRAWN

### 9.2.5	Work Items: SAES - TS 24.304.

C1-082310	Reference version TS 24.304 v0.4.0

Type:		TS

Source: 	Motorola

Discussion:

Status:	NOTED

C1-082311	MIPv4 Security Aspects

Type:		CR, 24.304

Source: 	Motorola

Discussion:	There are some editorial comments given offline.

Status:	REVISED TO C1-082686 which is AGREED

C1-082312	MIPv4 multiple PDN connectivity

Type:		CR, 24.304

Source: 	Motorola

Discussion:	The only change is to add editor's note to the new reference. Some comments received offline also.

Status:	REVISED TO C1-082687 which is AGREED

### 9.2.6	Work Items:	SAES-CSFB

C1-082216	Pseudo-CR on Combined Attach for CS Fallback

Type:		CR, 24.301

Source: 	NTT DoCoMo

Discussion:	The removal of editor's note and the change in the table Table 8.2.4.1 can be kept in the revision of this document. Other changes are covered by other contribution and should be cancelled.

Status:	REVISED TO C1-082701 which is AGREED

C1-082217	Pseudo-CR on Update type for CS Fallback

Type:		CR, 24.301

Source: 	NTT DoCoMo

Discussion:	These changes are covered by C1-082511.

Editor's note can be removed. Table number '8.2.263.1' should be corrected.

Status:	WITHDRAWN

C1-082218	Pseudo-CR on Combined TAU procedure for CS Fallback

Type:		CR, 24.301

Source: 	NTT DoCoMo

Discussion:	EPS specific timer should be changed to MM timer .

Status:	REVISED TO C1-082703 which is AGREED

C1-082219	Pseudo-CR on Service request procedure for CS Fallback

Type:		CR, 24.301

Source: 	NTT DoCoMo

Discussion:

Status:	REVISED TO C1-082705 which is AGREED

C1-082220	Pseudo-CR on Paging procedure for CS Fallback

Type:		CR, 24.301

Source: 	NTT DoCoMo

Discussion:	First sentence of the change should be more general. UE specific actions should be taken out of the changes. Editor's note should be deleted.

Status:	REVISED TO C1-082706 which is REVISED TO C1-082811.

C1-082811 is AGREED.

C1-082433	SGs interface specification

Type:		CR, 24.801

Source: 	NEC/Yannick

Discussion:	This document details the procedures required for SGs, based on their equivalent Gs procedure. Also, this document proposes to capture in TR 24.801 the protocol architecture for SGs. This document proposes the creation of a dedicated Technical Specification for SGs interface procedures and messages.

It was proposed to point to CT4 TS 29.202, to description about SCTP.

Status:	REVISED TO C1-082707 which is AGREED

C1-082434	Updated WID on stage 3 for CS Fallback in EPS

Type:		WID

Source: 	NEC/Yannick

Discussion:	The objective of this work is to specify stage3 capabilities and functionalities to meet the requirements as defined in TS23.272.

The following is expected to be specified:

- combined EPS/IMSI attach and tracking area update procedures based on similar mechanisms as those used by the combined GPRS attach and routing area update procedures from 3GPP TS 24.008, in order to register the UE to the CS domain for future Fallback from E-UTRAN access to 2G/3G CS domain access,

- IMSI or combined EPS/IMSI detach procedure, both UE and network initiated, based on similar mechanisms as those used by the GPRS detach procedure from 3GPP TS 24.008,

- the CS fallback related capability for the UE to receive the CS paging request via EPS and respond to this paging via the GERAN/UTRAN, or to request a CS call in E-UTRAN and establish the call in GERAN/UTRAN,

- the procedures for supporting Mobile originating and Mobile terminating SMS in EPS,

- the procedures required for the support of CS fallback to 1xRTT,

- procedures on the SGs interface between the MME and the MSC, based on the Gs interface procedures.

Status:	REVISED TO C1-082709 which is AGREED

C1-082435	Proposed skeleton for new TS "Mobility Management Entity (MME) - Visitors Location Register (VLR) SGs interface specification"

Type:		TS

Source: 	NEC/Yannick

Discussion:	This document contains a proposal for the skeleton for new TS 29.xyz “Mobility Management Entity (MME) - Visitors Location Register (VLR) SGs interface specification”.

Yannick Lair volunteered for rapporteurship of this TS.

Status:	AGREED

C1-082436	Proposed scope for new TS "Mobility Management Entity (MME) - Visitors Location Register (VLR) SGs interface specification"

Type:		New TS 29.

Source: 	NEC/Yannick

Discussion:	The scope of the document should contain a sentence explaining to what document is applicable.

It was commented that stage 2 TS refers to MSC server in the title.

Status:	REVISED TO C1-082710 which is AGREED.

C1-082494	Update the description of CS fallback

Type:		CR, 24.801

Source: 	Huawei

Discussion:

Status:	REVISED TO C1-082704 which is AGREED

C1-082495	NAS message related to CS fallback

Type:		CR, 24.801

Source: 	Huawei

Discussion:

Status:	POSTPONED

## 9.3	Work Item: PRIOR-MM

### 9.4.1	Study Item: MRFC

### 9.4.2	Work Item: MRFC_TS

## 9.5	Work Item: UUSIW

This WI is dependent on current work in sipping group in IETF. Companies are invited to contribute to sipping group in IETF to progress the draft that is in progress.

## 9.6	Work Item: PktCbl-Intw, PktCbl-Deploy, PktCbl-Sec

C1-082129	Add reference to draft-dotson-sip-mutual-auth

Type:		CR, 24.229

Source: 	Ericsson/Sean

Discussion:

Status:	REVISED TO C1-082621 which is AGREED

C1-082420	Annex K Updates

Type:		CR, 24.229

Source: 	CableLabs

Discussion:

Status:	REVISED TO C1-082622 which is AGREED

C1-082623	Cleanup of P-CSCF procedures for inclusion of "tls-yes" and "tls-pending"

Type:		CR, 24.229

Source: 	Ericsson/Sean

Discussion:	This is revision of C1-082127 and the document is moved from agenda item 9.11 to 9.6. WI is changed to "PktCbl-Sec".

Status:	AGREED

## 9.7	Work Item:	ETWS

C1-082194	Introduction to the solution for ETWS for UTRAN

Type:		Discussion

Source: 	NTT DoCoMo

Discussion:

Status:	NOTED

C1-082195	Chages to CBS for the realisation of ETWS.

Type:		CR, 23.041

Source: 	NTT DoCoMo

Discussion:

Status:	REVISED TO C1-082654. Editor's note has incorrect style. In first change, new changes should be shown with revision marks. Revision marks should not be in cover page. Curly quotes to be replaced by correct ones. C1-082654 is revised to C1-082812 which is revised to C1-082817.

C1-082817 is AGREED.

C1-082196	Additions to the protocol aspects of CBS for the realisation of ETWS

Type:		CR, 23.041

Source: 	NTT DoCoMo

Discussion:	3 changes are proposed to the protocol aspect of CBS for the realization of ETWS. All changes are based on the solution decided in TR 23.828.

The UE should use the information provided for security purposes. It should not be specified in details how the information is used or provided.

Status:	REVISED TO C1-082655 which is revised to C1-082813 which is AGREED

C1-082197	Changes to the radio message format aspect of CBS for the realisation of ETWS

Type:		CR, 23.041

Source: 	NTT DoCoMo

Discussion:	Changes are proposed to the radio message format of CBS in order to realise ETWS.

The proposed change to Clause 9.4.1.2.1 intends to use parts of Message Code of Serial Number parameter for to instruct mobile terminals to alert the users in case of emergency message transmission.

The proposed change to Clause 9.4.1.2.2 intends to allocate Message Identifier for emergency types relevant to ETWS.  This uses a part of the ID range reserved for the future extension.

Status:	REVISED TO C1-082656 which is revised to C1-082814 to fix same editorial problems as in previous two documents.

As styles are still not used correctly, C1-082814 has to be revised to C1-082818, which is AGREED.

It was noted that message identifier is identified by CBS forum. We should make sure that values we allocate are not duplicated.

## 9.8	Work Item: EData

C1-082347	Avoidance of mobility management signalling for eCall only terminals

Type:		CR, 24.008

Source: 	Qualcomm Europe

Discussion:

Status:	REVISED TO C1-082644 which is revised to C1-082711.

C1-082711 is revised to C1-082815 which is AGREED.

C1-082348	Support of expedited location updating for an eCall only UE

Type:		CR, 24.008

Source: 	Qualcomm Europe

Discussion:	The CR adds a new “pending emergency call” flag to the Location Updating Type IE which can be set to indicate a pending emergency call when a location update occurs.

It was commented that the possibility of location update needed shall be verified.

It was clarified that LU was not needed, thus the CR would not be needed.

Status:	POSTPONED

## 9.9	Work Item: EVA

## 9.10	Personal Network Management - Stage 2 and Stage 3 issues

### 9.10.1	Work Item: PNM Stage 2

### 9.10.2	Work Item: PNM Stage 3

C1-082400	Latest version of TS24.259

Type:		INFO

Source: 	Vodafone

Discussion:

Status:	NOTED

C1-082401	On using XCAP for PNM

Type:		Discussion

Source: 	Vodafone

Discussion:	The conventions and basic rules of the XML schema and the HTTP URIs in accordance with IETF RFC4825 for supporting the PN configuration were introduced, along with a couple of examples showing how such conventions and rules work.

It is encouraged that CT1 approve the conventions, ensuring the further works on modifying the PN-configuration procedures and the example signalling flows in 3GPP TS 24.259 relying on these conventions and rules can be followed.

Status:	NOTED

C1-082402	PNM XML schema update

Type:		CR, 24.259

Source: 	Vodafone

Discussion:	It is up to SA1 to decide whether PNM is an supplementary service.

Editorial corrections to be done.

Status:	REVISED TO C1-082637 which is AGREED

C1-082403	XCAP for PN configuration

Type:		CR, 24.259

Source: 	Vodafone

Discussion:	It was commented that there is overlap in this specification with TS 24.523.

Alignment for Presence with OMA needs to be maintained. Also, alignments with our own specifications is needed, where rules on how to use XCAP is described. TS 24.259 should not overlap with TS 24.623

Status:	REVISED TO C1-082638 which is AGREED

C1-082467	Correction of PN access control procedure

Type:		CR, 24.259

Source: 	Research in Motion

Discussion:

Status:	AGREED

C1-082468	Some cleanup of PNM Signalling flows

Type:		CR, 24.259

Source: 	Research in Motion

Discussion:	Two editor's notes are resolved and cleanup to diagram was done.

Status:	AGREED

C1-082505	PN UE Redirection Signalling flow Update

Type:		CR, 24.259

Source: 	ZTE

Discussion:	This paper provides the PN UE redirection signalling flow update in CS domain.

Offline discussion needed to find another approach which will work. This approach was not seen as appropriate.

Status:	REVISED TO C1-082639 which is not handled

## 9.11	Work Item: IMSProtoc2

C1-082127	Cleanup of P-CSCF procedures for inclusion of "tls-yes" and "tls-pending"

Type:		CR, 24.229

Source: 	Ericsson/Sean

Discussion:	WI to be changed to "PktCbl-Sec".

Status:	REVISED TO C1-082623 and moved to agenda item 9.6.

C1-082142	Reference correction

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:

Status:	AGREED

C1-082147	Target refresh correction

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:

Status:	REVISED TO C1-082624 which is POSTPONED

C1-082148	Backward compatibility issue with P-Access-Network-Info ABNF extension

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:

Status:	REVISED TO C1-082625 which is AGREED

C1-082149	Discussion on indication of early dialog termination

Type:		CR, Discussion

Source: 	LM Ericsson

Discussion:

Status:	NOTED

C1-082150	Discussion on STUN/TURN server discovery

Type:		CR, Discussion

Source: 	LM Ericsson

Discussion:

Status:	WITHDRAWN

C1-082283	Annex K editorial changes

Type:		CR, 24.229

Source: 	Alcatel-Lucent / Keith Drage

Discussion:

Status:	WITHDRAWN, merged with C1-082622

C1-082349	Allow Multiple Registrations in Rel 8

Type:		CR, 24.229

Source: 	Qualcomm Europe/Roozbeh

Discussion:

Status:	POSTPONED

C1-082369	Resource allocation based on session information in SDP offer at the terminating network

Type:		CR, Discussion

Source: 	Qualcomm Europe

Discussion:	It was indicated by several companies that this issue needs to be discussed in SA2 first.

Status:	POSTPONED

C1-082372	Multiple registration

Type:		Discussion

Source: 	Qualcomm Europe

Discussion:

Three methods to implement multiple registrations have been presented in this paper.

Method 1: Outbound

Method 2: Registering multiple IP addresses-new mechanism (with IETF)

Method3:Use of Multiple Private ID

Method two (whatever sub-solution is used there) requires additional IETF work for communications between the UE and the network. If till the CT1#55 meeting (Budapest in August 2008) no progress is made on this within IETF, Solution 2 will not make the Rel-8 timeframe and therefore will not be considered within a possible vote on the appropriate solution.

If no solution can be decided on until the next plenary meeting (September 2008), a vote on plenary level between the discussed solutions might become necessary. For each of these solutions CRs showing the complete technical solution need to be agreed / technically endorsed at the next CT1 (Budapest) meeting and need to be available at the plenary meeting.

Status:	NOTED

C1-082374	Update outbound reference

Type:		CR, 24.229

Source: 	Qualcomm Europe

Discussion:	WI changed to FBI-Pcbl, category to be changed to A.

Status:	REVISED TO C1-082626 and moved from agenda item 9.11 to agenda item 8.12.

C1-082388	Discussion on specific SIP error response for different S-CSCF assignment

Type:		Discussion

Source: 	Huawei

Discussion:

Status:	NOTED

C1-082389	Error Response for Different S-CSCF Assignment

Type:		CR, 24.229

Source: 	Huawei

Discussion:	A related CR in CT4 is needed to updated the Cx procedures. This CT4 CR has not been submitted yet, it needs to be agreed before the next CT plenary meeting in order for this CR to go forward.

Status:	REVISED TO C1-082628 which is revised to C1-082770 which is AGREED.

C1-082417	Discussion document on SDP enhancements

Type:		Discussion

Source: 	CableLabs, Nortel

Discussion:

Status:	NOTED, proposed outgoing LS is in C1-082418

C1-082419	SDP Enhancements to support resource allocation

Type:		CR, 24.229

Source: 	CableLabs, Nortel

Discussion:

Status:	REVISED TO C1-082630 which is POSTPONED

C1-082524	Alignment of IP-CAN specific annexes

Type:		CR, 24.229

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	The document is moved to this agenda item from late documents. Hidden character needs to be made visible.

Status:	REVISED TO C1-082755 which is revised to C1-082778 which is AGREED.

C1-082629	Clarification of abnormal handling of de-registration

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:	Moved from late documents.

Status:	POSTPONED

C1-082530	Discussion on indication of keep-alive support

Type:		CR, Discussion

Source: 	Ericsson

Discussion:	Moved from late documents.

Delegates are encouraged to support this new draft on the IETF SIP mailing list. The reception of the document was positive within CT1.

Status:	NOTED

## 9.12	Work Item: Overlap

C1-082405	Overview on Overlap signalling an the resuming changes

Type:		Discussion document

Source: 	Deutsche Telekom, T-Mobile

Discussion:

Status:	NOTED

C1-082406	ANNEX N for Overlap Signalling

Type:		CR, 24.229

Source: 	Deutsche Telekom, T-Mobile

Discussion:

Status:	POSTPONED

## 9.13	TISPAN R1 and R2 maintenance and 3GPP and 3GPP2  re-documentation

### 9.13.1	Work Item: MAINT_R1

C1-082182	Correction to the communication diversion service

Type:		CR, 24.404

Source: 	LM Ericsson

Discussion:	Reason for change to be improved, correct WI acronym and introduce reference to related CT3 CRs.

Status:	REVISED TO C1-082738 which is AGREED

C1-082313	Correction to the communication diversion service

Type:		CR, 24.504

Source: 	LM Ericsson

Discussion:

Status:	REVISED TO C1-082739 which is AGREED

C1-082328	Correction of notification service activation

Type:		CR, 24.404

Source: 	Research in Motion

Discussion:

Status:	POSTPONED

C1-082329	Correction of notification service activation

Type:		CR, 24.504

Source: 	Research in Motion

Discussion:

Status:	POSTPONED

C1-082330	Correction of notification service activation

Type:		CR, 24.604

Source: 	Research in Motion

Discussion:	New work item is REDOC_TIS-C1 ,category is F. The CR should be treated in 9.13.3.

Status:	REVISED TO C1-082731 which is AGREED

C1-082331	Correction of subscription options

Type:		CR, 24.404

Source: 	Research in Motion

Discussion:	This should be category F CR. WI and release to be corrected accordingly and reason for change to be improved.

Status:	REVISED TO C1-082732 which is AGREED.

C1-082332	Correction of subscription options

Type:		CR, 24.504

Source: 	Research in Motion

Discussion:	This should be category F CR. WI and release to be corrected accordingly and reason for change to be improved.

Status:	REVISED TO C1-082733 which is AGREED.

C1-082333	Correction of subscription options

Type:		CR, 24.604

Source: 	Research in Motion

Discussion:	This should be category F CR. WI and release to be corrected accordingly and reason for change to be improved.

Status:	REVISED TO C1-082734 which is AGREED

C1-082341	Deletion of unnecessary usage of announcement

Type:		CR, 24.428

Source: 	NTT

Discussion:

Status:	AGREED

C1-082342	Deletion of unnecessary usage of announcement

Type:		CR, 24.528

Source: 	NTT

Discussion:

Status:	AGREED

C1-082343	Deletion of unnecessary usage of announcement

Type:		CR, 24.628

Source: 	NTT

Discussion:

Status:	AGREED

C1-082344	Value of "No reply timer" for CDIV

Type:		CR, 24.404

Source: 	NTT

Discussion:

Status:	REVISED TO C1-082735 which is AGREED

C1-082345	Value of "No reply timer" for CDIV

Type:		CR, 24.504

Source: 	NTT

Discussion:

Status:	REVISED TO C1-082736 which is AGREED

C1-082346	Value of "No reply timer" for CDIV

Type:		CR, 24.604

Source: 	NTT

Discussion:

Status:	REVISED TO C1-082737 which is AGREED

### 9.13.2	Work Item: MAINT_R2

### 9.13.3	Work Item: REDOC_TIS-C1

C1-082131	Clarification of B2BUA and Proxy roles for AS

Type:		CR, 24.604

Source: 	Ericsson/Sean

Discussion:	The NOTE should include the following words: "and CDIV according to the requirements in this document" – the NOTE should also be added to sub clause 4.5.2.7.

Status:	REVISED TO C1-082740 which is revised to C1-082779. C1-082779 is AGREED.

C1-082297	Pseudo-CR on miscellaneous cleanups and corrections to the reference version

Type:		CR, 24.647

Source: 	Ericsson, Nortel

Discussion:

Status:	AGREED

C1-082298	Correction of reference

Type:		CR, 24.605

Source: 	Ericsson / Atle

Discussion:

Status:	AGREED

C1-082299	Correction of minors mistakes in signalling flows

Type:		CR, 24.606

Source: 	Ericsson / Atle

Discussion:

Status:	AGREED

C1-082300	Removal of normative statements in NOTEs

Type:		CR, 24.607

Source: 	Ericsson / Atle

Discussion:

Status:	AGREED

C1-082301	Correction of Activation/deactivation of HOLD

Type:		CR, 24.610

Source: 	Ericsson / Atle

Discussion:

Status:	AGREED

C1-082302	Removal of text from voided sub clause

Type:		CR, 24.616

Source: 	Ericsson / Atle

Discussion:

Status:	AGREED

C1-082303	Editorial fixes for the flows

Type:		CR, 24.628

Source: 	Ericsson / Atle

Discussion:

Status:	AGREED

C1-082304	Removal of normative statement in a NOTE

Type:		CR, 24.629

Source: 	Ericsson / Atle

Discussion:

Status:	AGREED

C1-082305	Alignment of user configuration

Type:		CR, 24.654

Source: 	Ericsson / Atle

Discussion:

Status:	REVISED TO C1-082741 which is AGREED

C1-082315	Network requirements for OIP and OIR

Type:		CR, 24.607

Source: 	Nokia Siemens Networks

Discussion:

Status:	REVISED TO C1-082742 which is AGREED

C1-082316	Tidyup xsd

Type:		CR, 24.623

Source: 	Nokia Siemens Networks

Discussion:

Status:	REVISED TO C1-082743 which is AGREED

C1-082327	Correction of terminology

Type:		CR, 24.604

Source: 	Research in Motion

Discussion:

Status:	AGREED

C1-082381	Miscellaneous clean-up corrections

Type:		CR, 24.610

Source: 	Qualcomm Europe

Discussion:	Subclause 4.5.1 to be removed as this change has been done in another document already.

Status:	REVISED TO C1-082744 which is AGREED

### 9.13.4	Work Item: REDOC_3GPP2

C1-082284	Removal of redundant references

Type:		CR, 24.141

Source: 	Alcatel-Lucent / Keith Drage

Discussion:

Status:	AGREED

C1-082350	Add Timestamp in Register Request

Type:		CR, 24.229

Source: 	Qualcomm Europe/Roozbeh

Discussion:

Status:	REVISED TO C1-082745

New sections in the Annex to be added also to the other access specific annexes and mark them there as void.

RIM stated their view that this CR causes a cdma2000 specific variant of the S-CSCF and so in this particular regard we did not achieve common IMS.

C1-082745 is revised to C1-082810 to correct numbering of sub clauses. C1-082810 is AGREED.

C1-082375	Allow SIP based user configuration mechanism for configuring supplementary services

Type:		CR, 24.173

Source: 	Qualcomm Europe

Discussion:	The issue of parallel usage of the two specified configuration mechanisms (either XCAP or feature codes) was discussed and not resolved. An editors note will be added, stating, that the parallel usage is for further study.

Status:	REVISED TO C1-082746 which is revised to C1-082768.

C1-082768 is AGREED.

C1-082376	Allow SIP based user configuration mechanism for configuring supplementary services

Type:		CR, 24.604

Source: 	Qualcomm Europe

Discussion:

Status:	REVISED TO C1-082747 which is revised to C1-082769 which is AGREED

C1-082377	Allow SIP based user configuration mechanism for configuring supplementary services

Type:		CR, 24.607

Source: 	Qualcomm Europe

Discussion:

Status:	REVISED TO C1-082748 which is AGREED

C1-082378	Allow SIP based user configuration mechanism for configuring supplementary services

Type:		CR, 24.608

Source: 	Qualcomm Europe

Discussion:

Status:	REVISED TO C1-082749 which is AGREED

C1-082379	Allow SIP based user configuration mechanism for configuring supplementary services

Type:		CR, 24.611

Source: 	Qualcomm Europe

Discussion:

Status:	REVISED TO C1-082750 which is AGREED

C1-082380	Allow SIP based user configuration mechanism for configuring supplementary services

Type:		CR, 24.654

Source: 	Qualcomm Europe

Discussion:

Status:	REVISED TO C1-082751 which is AGREED

C1-082382	Introduction of IMC in support of common IMS

Type:		CR, 24.229

Source: 	Qualcomm Europe

Discussion:

Status:	POSTPONED

C1-082447	Pseudo-CR on miscellaneous cleanups and corrections to the reference version of 24.238.

Type:		Draft CR

Source: 	Nortel Networks, Ericsson

Discussion:

Status:	AGREED

## 9.14	Work Item: NBA

## 9.15	Work Item: PPACR-CT1

C1-082286	PPAC_UE behaviour (For UTRAN)

Type:		Discussion

Source: 	NTT DoCoMo

Discussion:

Proposal:

Current descriptions in TS24.008 are not sufficient to describe UE behavior described in Figure 1 and Figure 2. Therefore those descriptions are needed in TS24.008.  With this clarification of overall UE behaviour it is proposed to ask CT1 agreement for future work based on this.

It is then proposed to add in TS24.008:

- Descriptions to MM/GMM state when PPAC indicator is available in SIB3.

- Descriptions about follow-on-request parameter when location/registration procedures executed.

- Descriptions to abnormal cases.

In this section it should be described more how baring status of the cell is determined, and the description should be limited to this.

Any combination of access class control is possible, but if we include all this in description of specific scenarios it will be too much. Therefore more generic explanation should be found to describe possible combinations.

Status:	NOTED

C1-082287	PPAC for UTRAN:introduction

Type:		CR, 24.008

Source: 	NTT DoCoMo

Discussion:	The CR proposes clarification on Paging Permission with Access Control in sub clause 4.1.1.5.1.

It was commented that the CR introduce some clarification which was not specified by stage 1. It was proposed to introduce reference to RFC specification.

The term 'Paging permission' is misleading, it should refer to permission to respond to paging, therefore it is better to leave only a reference to RFC specification.

First paragraph is not needed as it does not provide any new information that is not provided in previous sub clause.

Part of change in second paragraph also repeats information that is already mentioned in 23.122.

The only new information in new sub clause is the name of the feature. Reference to existing specification should be used to point to the feature.

Status:	REVISED TO C1-082645 which is WITHDRAWN. Work will be performed offline to progress this work at CT1-55.

C1-082288	PPAC for UTRAN:general_mobility_management

Type:		CR, 24.008

Source: 	NTT DoCoMo

Discussion:	Offline discussion is encouraged before the next meeting.

Status:	WITHDRAWN

C1-082289	PPAC for UTRAN:follow-on request parameters

Type:		CR, 24.008

Source: 	NTT DoCoMo

Discussion:

Status:	WITHDRAWN

C1-082290	PPAC for UTRAN:abnormal_cases

Type:		CR, 24.008

Source: 	NTT DoCoMo

Discussion:

Status:	WITHDRAWN

## 9.16	IMS supplementary services

### 9.16.1	Work Item: CCBS-CCNR

C1-082306	Pseudo-CR on miscellaneous cleanups and corrections to the reference version

Type:		CR, 24.642

Source: 	Ericsson / Atle

Discussion:

Status:	REVISED TO C1-082632 which is AGREED

C1-082386	TS 24.642 CCBS/NR proposal for signalling flow

Type:		Discussion

Source: 	Deutsche Telekom

Discussion:

Status:	REVISED TO C1-082543

C1-082543 is revised to C1-082660 which is AGREED.

### 9.16.2	Work Item: CW-IMS

C1-082307	Pseudo-CR on miscellaneous cleanups and corrections to the reference version

Type:		CR, 24.615

Source: 	Ericsson / Atle

Discussion:

Status:	AGREED

C1-082387	TS 24.615 CW proposal for signalling flow

Type:		Discussion

Source: 	Deutsche Telekom

Discussion:

Status:	REVISED TO C1-082661 which is further revised to C1-082780.

C1-082780 is AGREED.

### 9.16.3	Work Item: FA

C1-082448	Pseudo-CR on miscellaneous cleanups and corrections to the reference version of 24.239

Type:		Draft CR

Source: 	Nortel Networks, Ericsson

Discussion:

Status:	AGREED

C1-082449	Pseudo-CR on AS procedures for FA service

Type:		Draft CR

Source: 	Nortel Networks

Discussion:	The rapporteur is asked to change "section" to "subclause" in the appropriate places.

Status:	REVISED TO C1-082662 which is AGREED

### 9.16.4	Work Item: CAT-SS

C1-082442	Proposed skeleton for new TS 24.182 "IP Multimedia Subsystem (IMS) Customized Alerting Tones (CAT); Protocol specification"

Type:		Skeleton for New TS

Source: 	Nortel Networks

Discussion:

Status:	AGREED

C1-082443	Pseudo-CR on stage 3 CAT scope and general description

Type:		Draft CR

Source: 	Nortel Networks

Discussion:	The rapporteur is asked to remove the "-" between "multi" and "media".

Status:	REVISED TO C1-082663 which is AGREED

C1-082444	Pseudo-CR on CAT operational requirements

Type:		Draft CR

Source: 	Nortel Networks

Discussion:	The rapporteuer is asked to add the abbreviation "MRF" in clause 3.

Status:	REVISED TO C1-082664 which is AGREED

C1-082445	Pseudo-CR on CAT signalling procedures

Type:		Draft CR

Source: 	Nortel Networks

Discussion:

Status:	REVISED TO C1-082665 which is further revised to C1-082771. Sublause 4.5.1 needs to be changed according to the changes provided in C1-082769 in subclause 4.5.0.

C1-082771 is AGREED.

C1-082446	Pseudo-CR on CAT interactions with other services

Type:		Draft CR

Source: 	Nortel Networks

Discussion:

Status:	AGREED

## 9.17	Work Item: OAM8-Trace

C1-082473	Adding P-Debug-ID to SIP Profile Tables

Type:		CR, 24.229

Source: 	Vodafone

Discussion:

Status:	REVISED TO C1-082752 which is AGREED

C1-082474	Subscribing to the debug event package

Type:		CR, 24.229

Source: 	Vodafone

Discussion:

Status:	REVISED TO C1-082753 which is revised to C1-082781. Subclause 5.2.3a needs to be renamed to 5.2.3A and all version numbers of internet drafts need to be removed from the main body of the spec (not from clause 2).

C1-082781 is AGREED.

C1-082475	Parameters for IMS Service Level Trace

Type:		CR, 24.323

Source: 	Vodafone

Discussion:	Editors Note in Annex A needs to be added, stating that the DDF needs to be updated with the changes in this CR.

Status:	REVISED TO C1-082754 which is AGREED

## 9.18	Work Item: 	IWLANNSP

C1-082472	Implementation error of CR 0052

Type:		CR, 24.234

Source: 	Research in Motion

Discussion:

Status:	AGREED

## 9.19	Work Item:	IWLAN_Mob

C1-082455	Reference version of the TS 24.327, v0.1.1

Type:		Draft TS

Source: 	Orange

Discussion:

Status:	NOTED

C1-082456	Attach for I-WLAN mobility: UE procedures

Type:		Draft CR, TS 24.327

Source: 	Orange

Discussion:

Status:	REVISED TO C1-082582 which is revised to C1-082647 which is AGREED

C1-082457	Attach for I-WLAN mobility: Home agent discovery

Type:		Draft CR, TS 24.327

Source: 	Orange

Discussion:	It is proposed to agree on the text added to the home agent discovery subclause in the TS 24.327.

"The UE can discover the IPv6 and optionally the IPv4 address of the home agent in one of the three following ways:

-	Via DNS as defined in 3GPP TS 24.303 [3];

-	During the PDP context activation procedure in GERAN or UTRAN accesses via the Protocol Configuration Options (PCO) as defined in 3GPP TS 24.008 [x];

-	Via IKEv2 during tunnel setup to PDG for I-WLAN access as defined in 3GPP TS 24.234 [y]."

It was questioned whether it is mandatory to support all 3 ways above, or the support of some of them is optional. This is still for further study to clarify and it should be covered by editor's note for the time being.

Status:	REVISED TO C1-082583 which is revised to C1-082648 which is AGREED

C1-082458	Attach for I-WLAN mobility: Home link detection

Type:		Draft CR, TS 24.327

Source: 	Orange

Discussion:	It is proposed to add editor's note to mention that UE configuration will be clarified when SA2 specification becomes stabile.

Status:	REVISED TO C1-082584 which is revised to C1-082649 which is AGREED

C1-082459	Handover from GPRS systems to 3GPP I-WLAN: UE procedures

Type:		Draft CR, TS 24.327

Source: 	Orange, Ericsson

Discussion:	It is proposed to agree on the text added to the UE procedures from the handover from GPRS systems to the 3GPP I-WLAN subclause in the TS 24.327.

Status:	REVISED TO C1-082585 which is revised to C1-082650

When UE moves to I-WLAN another scenario is applied. Two procedures should be therefore explained.

C1-082650 is AGREED.

C1-082460	Handover from 3GPP I-WLAN to GPRS systems: UE procedures

Type:		Draft CR, TS 24.327

Source: 	Orange, Ericsson

Discussion:	"Shall" should not be used in following: When the home agent and the GGSN are collocated, the GGSN shall be the one that contains the home agent allocated in 3GPP I-WLAN.

On the other hand in the next sentence "shall" should be used instead of "should".

The use of "shall" should be checked throughout the document.

Status:	revised to C1-082651 which is AGREED.

Abbreviation HA or Home Agent should be used consistently in the document - to be applied by the rapporteur.

C1-082461	Handover from GPRS systems to 3GPP I-WLAN: Network procedures

Type:		Draft CR, TS 24.327

Source: 	Orange, Ericsson

Discussion:	The use of "shall" should be checked throughout the document.

Status:	revised to C1-082652 which is AGREED

C1-082462	Handover from 3GPP I-WLAN to GPRS systems: Network procedures

Type:		Draft CR, TS 24.327

Source: 	Orange, Ericsson

Discussion:

Status:	revised to C1-082653 which is AGREED

## 9.20	Work Item: IMS_Corp

C1-082324	Support of Direct Ethernet access as IP-CAN

Type:		CR, 24.229

Source: 	Orange

Discussion:

Status:	AGREED

C1-082325	Support of Direct Ethernet access as IP-CAN

Type:		CR, 24.503

Source:

Discussion:	See LS from TSG SA C1-082198 and TSG CT C1-082254.

Status:	POSTPONED

C1-082326	Delivering Request-URI to UE managing several terminals

Type:		CR, 24.503

Source:

Discussion:

Status:	POSTPONED

C1-082466	Summary and Planning for IMS_Corp/NGCN Workshop

Type:		Discussion

Source: 	Research in Motion

Discussion:	At the previous CT1 meeting it was agreed to send a LS to relevant 3GPP, TISPAN an ECMA WGs identifying issues of concern with IMS_Corp/NGCN work and proposing a Workshop between all the relevant stakeholders to make progress on these issues. CT1 has received a positive response in a Reply LS from SA2 (a key stakeholder in such a workshop) and we understand that a positive response will also be forthcoming from TISPAN (although at the time of drafting this contribution a reply wasn’t yet available according to the CT1 document list). ECMA also have informally discussed the proposal in the LS but due to the fact that their next meeting isn’t until August no official response is available yet. However it is understood that ECMA also intend to provide representation at the workshop.

It is proposed that CT1 send a LS to all the workshop invitees proposing a scope and agenda proposed in this document.

It was commented that bullet 4 and part of bullet 5 should be omitted from the scope of the workshop.

Workshop dates 25-26 of August were fine with CT1 which should focus on stage 2 CRs and stage 3 can be handled in future CT1 meetings.

Status:	NOTED, the conclusion will be done by e-mail correspondence. ECMA representatives shall be included in the discussion.

C1-082512	Core network handling of P-Preferred-Identity and P-Asserted-Identity header for business communication

Type:		CR, 24.229

Source: 	Alcatel-Lucent / Keith Drage

Discussion:

Status:	POSTPONED

C1-082513	NGCN site as a protocol entity

Type:		CR, 24.229

Source: 	Alcatel-Lucent / Keith Drage

Discussion:

Status:	POSTPONED

C1-082517	Handling of NGCN site as an entity in 24.229

Type:		Discussion

Source: 	Alcatel-Lucent / Keith Drage

Discussion:	Keith Drage volunteered to organize a conference call on NGCN issues between CT1, SA2, TISPAN and ECMA groups.

It was said, that a P-CSCF might need to be aware of whether (via Gm) a normal UE or a NGCN (complex system) is accessing the IMS, as the P-CSCF needs to handle the trust domain issues correctly.

One possibility to make the P-CSCF aware of the fact, that a NGCN is connected, would be to send this information within the registration state event notification. Note: this may require IETF work on extending the registration state event package.

Status:	NOTED

## 9.21	Work Item: ICSRA

C1-082463	Baseline 24.292 ICS skeleton v0.1.1

Type:		DRAFT TS

Source: 	Rapporteur/Sean

Discussion:

Status:	NOTED

C1-082130	Updates to ICS skeleton to include supplementary svcs and additional call flows

Type:		CR, 24.292

Source: 	Ericsson/Sean

Discussion:

Status:	AGREED

C1-082177	Example signalling flow for CS UE origination via an MSC enhanced d for ICS where the origation MSC server enhanced for ICS supports codec negotiation.

Type:		CR, 24.292

Source: 	LM Ericsson

Discussion:

Status:	REVISED TO C1-082591 which is revised to C1-082756.

The Contact header should not include a URI in this version of the CR, as the URI will be replaced by the GRUU later on. The feature tags and other parameters already in the Contact header will NOT be removed.

The following Editors Note should be added at top of every example flow:

"In this example flow, the values for the GRUU in the Contact header as well as the value of the Accept header needs to be added."

In some Accept-Contact headers a ";" is missing between the "*" and the "+" – this needs to be added.

C1-082756 is AGREED.

C1-082178	Example signalling flow for CS UE origination via an MSC enhanced d for ICS where the origation MSC server enhanced for ICS does not supports codec negotiation.

Type:		CR, 24.292

Source: 	LM Ericsson

Discussion:

Status:	REVISED TO C1-082592 which is revised to C1-082757. Same comments as for C1-082756 apply. C1-082757 is AGREED.

C1-082188	Example flow for CS UE termination via MSC Server enhanced for ICS (with codec negotiation)

Type:		CR, 24.292

Source: 	Mavenir

Discussion:

Status:	REVISED TO C1-082593 which is revised to C1-082758

C1-082758 is AGREED.

C1-082189	Example flow for CS UE termination via MSC Server enhanced for ICS (without codec negotiation)

Type:		CR, 24.292

Source: 	Mavenir

Discussion:

Status:	REVISED TO C1-082594 which is WITHDRAWN

C1-082190	Example flow for CS UE termination, not registered in IMS

Type:		CR, 24.292

Source: 	Mavenir

Discussion:	An Editors Note needs to be added indicating that the value of the contact header is for further study, as it is not clear whether the B2BUA can retain the Contact of the other call leg or should put its own address. In any case it needs to be evaluated how the GRUU-value and feature tags of the remote side can be retained. The text related to the Contact header needs to be removed.

Status:	REVISED TO C1-082595 which is revised to C1-082759 and AGREED

C1-082317	Flow for ICS Registration

Type:		Discussion

Source: 	Nokia Siemens Networks

Discussion:

Status:	REVISED TOC1-082596 which is further revised to C1-082760. Editors Note needs to be added that the reg-event information needs to include the ICSI values. The same comments as for C1-082756 apply. C1-082760 is AGREED.

C1-082318	Registration procedure for ICS

Type:		CR, 24.292

Source: 	Nokia Siemens Networks

Discussion:

Status:	REVISED TO C1-082597 which is revised to C1-082761 which is AGREED.

C1-082319	MSC as IMS functional entity

Type:		CR, 24.292

Source: 	Nokia Siemens Networks

Discussion:

Status:	REVISED TO C1-082598 which is AGREED

C1-082320	Subscription to the reg event package

Type:		CR, 24.292

Source: 	Nokia Siemens Networks

Discussion:

Status:	REVISED TO C1-082599 which is AGREED

C1-082321	Reregistration procedure for ICS

Type:		CR, 24.292

Source: 	Nokia Siemens Networks

Discussion:

Status:	REVISED TO C1-082600 which is AGREED

C1-082322	Deregistration procedures for ICS

Type:		CR, 24.292

Source: 	Nokia Siemens Networks

Discussion:

Status:	AGREED

C1-082441	Pseudo-CR on ICS UE termination with CS media using Gm reference point when using an enhanced MSC Server

Type:		CR, 24.292

Source: 	Nortel Networks

Discussion:

Status:	REVISED TO C1-082601. Coding in step 9 to be deleted.

C1-082601 is revised to C1-082762 which is AGREED.

C1-082450	Pseudo-CR on Signalling flows for ICS UE origination with CS media using Gm reference point when using an MSC server (not enhanced for ICS)

Type:		CR, 24.292

Source: 	Nortel Networks

Discussion:

Status:	REVISED TO C1-082602 which is revised to C1-082763.

C1-082763 is AGREED.

C1-082451	Pseudo-CR on Signalling flows for termination to an ICS UE with CS media using Gm reference point when using an MSC server (not enhanced for ICS)

Type:		CR, 24.292

Source: 	Nortel Networks

Discussion:

Status:	REVISED TO C1-082603 which is revised to C1-082764. C1-082764 is AGREED.

C1-082506	Signalling flow for Execution of IMS conferencing via Gm

Type:		CR, 24.292

Source: 	ZTE

Discussion:

Status:	REVISED TO C1-082604 which was not available

C1-082507	Discussion about ICS hold at MGCF

Type:		CR, 24.292

Source: 	ZTE

Discussion:

Status:	NOTED

C1-082521	TS Skeleton for ICS Protocol over USSD bearer

Type:		TS-skeleton

Source: 	Huawei

Discussion:	Moved from late documents.

Status:	REVISED TO C1-082673 which is revised to C1-082765. The only change is to replace the word "over" with the word "via" in the title of the TS.

C1-082765 is AGREED.

C1-082522	Scope for TS 24.293

Type:		CR, 24.293

Source: 	Huawei

Discussion:	Moved from late documents.

Status:	REVISED TO C1-082674 which is AGREED

C1-082523	Discussion on the way forward for I1 protocol specification

Type:		Discussion

Source: 	Huawei

Discussion:

Status:	NOTED

## 9.22	Work Item: IMS-Cont

C1-082391	TS 24.237 V0.1.1

Type:		TS

Source: 	Huawei

Discussion:

Status:	NOTED

C1-082184	Application level handover

Type:		CR, 24.237

Source: 	Alcatel-Lucent/Milo Orsic

Discussion:

Status:	REVISED TO C1-082454 which is revised to C1-082666.

C1-082666 is AGREED.

C1-082383	Role of UE in registration

Type:		CR, 24.237

Source: 	Qualcomm Europe

Discussion:

Status:	REVISED TO C1-082667 which is AGREED.

C1-082384	Role of UE in origination and termination

Type:		CR, 24.237

Source: 	Qualcomm Europe

Discussion:

Status:	REVISED TO C1-082668 which is AGREED

C1-082385	Role of UE in PS-PS session continuity

Type:		CR, 24.237

Source: 	Qualcomm Europe

Discussion:	The rapporteur was asked to remove the automatic bulleting.

Status:	REVISED TO C1-082669 which is AGREED

C1-082390	Updated WID for IMS Service Continuity Stage3

Type:		WID

Source: 	Huawei

Discussion:

Status:	REVISED TO C1-082670 which is AGREED

C1-082392	Cleanup of TS 24.237

Type:		CR, 24.237

Source: 	Huawei

Discussion:

Status:	REVISED TO C1-082671 which is AGREED

C1-082393	Roles for registration in IMS

Type:		CR, 24.237

Source: 	Huawei

Discussion:

Status:	REVISED TO C1-082672 which is AGREED

C1-082394	Introduction for signalling flows

Type:		CR, 24.237

Source: 	Huawei

Discussion:

Status:	AGREED

C1-082395	Signalling flows for CS call origination

Type:		CR, 24.237

Source: 	Huawei

Discussion:

Status:	REVISED TO C1-082676 which is further revised to C1-082766.

C1-082766 is AGREED.

C1-082396	Signalling flows for CS call termination

Type:		CR, 24.237

Source: 	Huawei

Discussion:

Status:	REVISED TO C1-082677 which is revised to C1-082767. C1-082767 is AGREED.

## 9.23

### 9.23.1	All other IMS-related WIs

C1-082128	Introduction of GIBA (Early IMS) procedures

Type:		CR, 24.229

Source: 	Ericsson/Sean

Discussion:	Several new subclauses were added and other subclauses were updated as needed to introduce the GIBA procedures into 24.229.

Abbreviations that are not used in the document should be removed from abbreviations section, or should be used where appropriate in the body of the TS.

Subclauses should be renumbered in appropriate way.

Fallback mechanism from IMS AKA to GIBA procedures exist and those fallback mechanisms should be mentioned here, although they are described in TR.

UE procedures should stay in the document, but editor's note in the table should be added related to UEs that do not support IPsec and IMS AKA procedures.

It was commented that if fallback to different procedures is required than SA3 should define them.

Status:	REVISED TO C1-082657 which is AGREED

C1-082464	Enhancement of Filter Criteria for third party registration

Type:		Discussion

Source: 	Research in Motion

Discussion:

Proposal:

It is proposed that the Filter Criteria is enhanced to include an <include-Register-request> element.

When the <include-Register-request> element is present for the AS that the third party SIP REGISTER request is to be sent to the S-CSCF:

- Includes the entire incoming SIP REGISTER request as a message/sip MIME body in the third party SIP REGISTER request if the AS is part of the trust domain

- Includes a subset of the incoming SIP REGISTER request (with the sensitive headers such as P-Access-Network-Info removed) as a message/sipfrag MIME body in the third party SIP REGISTER request if the AS is not part of the trust domain

- If the <Service-Info> element is present in the Filter Criteria then when the incoming SIP REGISTER request is include in a message/sip or message/sipfrag this is included along with the <service-info> in a multipart/mixed MIME body.

Comments:

It was commented by Qualcomm that this CR changed since previous version and it is seen that there are no clear requirements from SA2 point of view for this change. It was supported by Nokia that there is no clear requirement for this change and the change is not needed. Other alternative is to evaluate the requirement covered by this document based on some arguments.

Status:	NOTED

C1-082465	Enhancement of Filter Criteria to Include Incoming Register in Third Party Register

Type:		CR, 23.218

Source: 	Research in Motion

Discussion:

Consequences if not approved says that it will remain unresolved how to support the 3GPP2 VCC AS as part of Common IMS. It was commented that the better way to resolve this issue is to contribute to 3GPP2.

This is a proposal to enhance initial filter criteria in generic way.

It was commented that this is standalone enhancement of the feature which was found useful by some companies, but also a number of companies expressed a concern that there might be other solutions, as well as security issues and other issues with this solutions which have to be checked within companies.

It was also questioned what is the use case for this enhancement and when the use case is described companies may come with different proposal how to achieve it.

Status:	REVISED TO C1-082659

The issue was seen far more complicated as outlined by originator. Nokia is willing to study all possible implications and bring the solution for Rel-9. Ericsson supports bringing it in Rel-9 if more study is needed. Qualcomm also proposes to postpone this CR for the time being. Alcatel-Lucent commented that all usages of application server are not defined by 3GPP. Alcatel-Lucent find this feature useful and commented that there is no additional issue related to this change.

C1-082659 IS POSTPONED.

It was commented by Nokia that if there are no requirements for this feature for the time being, there is no big difference if it is introduced in Rel-8 or Rel-9.

### 9.23.2	All other Non-IMS-related WIs

C1-082285	Roaming restriction issue with causes #13 and #15

Type:		Discussion

Source: 	Alcatel-Lucent / Bruno Landais

Discussion:	It was proposed to see the related CRs first.

Summary:

3GPP CN#14 Plenary approved CR 24.008-521r4 (R99) (and the mirror ones 524r4 (Rel-4) and 527r4 (Rel-5)) (Tdoc NP-010700) on handling of Location Updating Reject causes #13 (‘roaming not allowed in this location area’) and #15 (‘no suitable cells in this location area’).

By this CR, in case of location update, routing area update and service request, upon reception of reject cause #13 or #15, LAI, TMSI and ciphering key sequence number, and RAI, P-TMSI, P-TMSI signature and GPRS ciphering key sequence number have not to be deleted (they were prior to the CR). The reason for that change is the possibility to maintain the activated PDP contexts, if any, and avoid new authentication and the signaling load due to their reactivation. This is out of the scope of this document.

Note: on receipt of cause #13 (respectively #15) the UE looks for a new cell to camp on in another (respectively the same) PLMN.

In CS domain, an issue of not deleting the LAI and TMSI in the UE is that the UE will not trigger immediately a location updating request when coming back in its previous Location Area (the one kept stored in the UE) and the MT calls will not be delivered until the next MO call or periodic location update.

In PS domain, a similar issue may exist. However further investigation is needed with regard to transfer of activated PDP-contexts between the old and new SGSN.

The document details the issue related to CS domain and proposes a solution to improve the MT call delivery.

It was commented that the change in Rel-8 would be more appropriate. PS domain aspects shall be addressed as well.

Status:	REVISED TO C1-082539 which is NOTED

C1-082308	Adding and extending AT-commands to support touch screen functions

Type:		CR, 27.007

Source: 	AT&T, LG, Spirent

Discussion:

Status:	REVISED TO C1-082681 which is AGREED

C1-082309	Setting of display resolution and scren orientation for touch screen functions

Type:		CR, 27.007

Source: 	AT&T, LG, Spirent

Discussion:

Status:	REVISED TO C1-082682 which is AGREED

C1-082428	Correction for IMSI detach procedure during dedicated mode

Type:		CR, 24.008

Source: 	NEC/Yannick

Discussion:

Status:	REVISED TO C1-082683 which is AGREED

C1-082429	Clarifications for RAT usage in manual network selection mode

Type:		CR, 23.122

Source: 	NEC/Yannick

Discussion:

Status:	AGREED

C1-082471	Incorporation 802.11u network discovery procedures

Type:		CR, 24.234

Source: 	Research in Motion

Discussion:	Interested parties are invited to provide feedback offline to RIM before the next meeting.

Status:	POSTPONED

C1-082477	CSG and Idle Mode Mobility for 3G Home NodeB

Type:		WID

Source: 	Huawei

Discussion:	With the deployment of CSGs on legacy technologies one of the main issue is to maintain backward compatibility of pre-Rel-8 terminals and/or non-capable CSG terminal. Because of this issue the expected work specific to 3G HNB would likely be limited and would reuse as much as possible legacy procedures.

CT is expected to look at the CSG concept and the terminal Idle Mode mobility to/from macro 3G cell from/to CSG i.e.

- Define network selection scheme (for CSG) e.g. manual network selection, this would enhance the existing PLMN manual Selection scheme.

- Provide signalling and network selection functionality (for CSG).

- Provide CSG list configuration and management e.g. CSG white list

- Define CSG Id.

It was commented that this WI should not be a feature, but should come under the SA1 WI. Stage 2 is covered in SA2.

It was commented that CT6 should be informed about requirements.

Status:	REVISED TO C1-082535 which is revised to C1-082684

C1-082684 is revised to C1-082798 and AGREED. The only changes is to mark core network impact.

C1-082478	CSG and Idle Mode Mobility for LTE Home eNodeB

Type:		WID

Source: 	Huawei

Discussion:	CSG handling/mobility and network access control procedures can benefit from the new EPC system being designed within the same release. The backward compatibility with legacy systems doesn’t apply and shouldn’t constraint the design of the solutions

CT work should consist of

- Define the Idle mode mobility procedure to/from macro LTE cell from/to LTE CSG.

- Provide signalling and network selection functionality (for LTE CSG).

Provide LTE CSG list configuration and management including UICC aspects e.g. LTE CSG white list

Status:	REVISED TO C1-082536 which is revised to C1-082685 which is AGREED.

C1-082496	Access Network Discovery and New IEEE 802.11u Interworking with External Networks

Type:		Discussion

Source: 	Research in Motion

Discussion:

Status:	NOTED without presentation

C1-082519	TMSI reallocation in a location area where the UE isnt updated

Type:		Discussion

Source: 	Ericsson

Discussion:

Status:	NOTED

# 10	Output Liaison Statements

C1-082418	LS on SDP Enhancements to support resource allocation

Type:		LS OUT

Source: 	CT1

Discussion:

Status:	REVISED TO C1-082631 which is revised to C1-082773.

C1-082773 is AGREED.

C1-082508	LS on Rel-8 UICC parameters

Type:		LS OUT

Source: 	CT1

Discussion:

Status:	REVISED TO C1-082713 which is AGREED

C1-082534	LS on 3GPP Namespace Identification (NID) administration

Type:		LS OUT

Source: 	CT1

Discussion:	Related to document C1-082533.

Status:	AGREED

C1-082540	LS on IMS Emergency Registration

Type:		LS OUT

SA2, CT4

Source: 	CT1

Discussion:	This is reply LS to C1-082214.

Status:	AGREED

C1-082541	Reply LS on request for recommendations (on IEEE 802.11u approach)

Type:		LS OUT

IEEE 8.011

Source: 	CT1

Discussion:	This is reply LS to C1-082215.

Status:	AGREED

C1-082542	SA1 answer to Relation between EPS Services and GPRS Services

Type:		LS OUT

Source: 	CT1

Discussion:	This is reply LS to C1-082221.

Status:	WITHDRAWN

C1-082544	LS on add/remove media

Type:		LS OUT

Source: 	CT1

Discussion:	This is reply LS to C1-082235.

Status:	REVISED TO C1-082772 which is AGREED.

C1-082545	LS on SDP connection information

Type:		LS OUT

Source: 	CT1

Discussion:	This is reply LS to C1-082236.

Status:	REVISED TO C1-082782 which is AGREED

C1-082546	LS on RTCP bandwidth modifiers for MTSI

Type:		LS OUT

Source: 	CT1

Discussion:	This is reply LS to C1-082237.

Status:	AGREED

C1-082547	LS on Enhancements for SRNS Relocation

Type:		LS OUT

CT4

Source: 	CT1

Discussion:	This is reply LS to C1-082239.

Status:	AGREED

C1-082548	LS on HSPA VoIP to WCDMA/GSM CS continuity

Type:		LS OUT

Source: 	CT1

Discussion:	This is reply LS to C1-082242.

SA has recommended a common solution, therefore the questions will not be answered.

Status:	AGREED

C1-082549	LS on UTRA R8 hNB requirements

Type:		LS OUT

Source: 	CT1

Discussion:	This is reply LS to C1-082243. Related document is in C1-082323.

The WID in C1-082798 should be attached to this LS.

Status:	REVISED TO C1-082799 which is AGREED.

C1-082550	Reply LS on NAS–AS interaction for dependent procedures

Type:		LS OUT

Source: 	CT1

Discussion:	This is reply LS to C1-082245. Related Tdoc is in C1-082422

Status:	POSTPONED

C1-082551	LS on Connection recovery by NAS

Type:		LS OUT

RAN2

Source: 	CT1

Discussion:	This is reply LS to C1-082246.

Status:	REVISED TO C1-082800 which is AGREED

C1-082552	Reply LS on Earthquake and Tsunami Warning System

Type:		LS OUT

Source: 	CT1

Discussion:	This is reply LS to C1-082249. Related documents are in C1-082194 - 97.

Status:	AGREED

C1-082553	LS on CAT in the 3GPP CS domain

Type:		LS OUT

Source: 	CT1

Discussion:	This is reply LS to C1-082257.

Status:	REVISED TO C1-082805 which is POSTPONED

C1-082554	LS on CS Fallback

Type:		LS OUT

Source: 	CT1

Discussion:

Status:	REVISED TO C1-082806 which is AGREED

C1-082558	Initiation of Security mode control procedure

Type:		LS OUT

SA3

Source: 	CT1

Discussion:	This LS is related to C1-082171.

Status:	REVISED TO C1-082801 which is AGREED

C1-082590	Reply LS on handling of local emergency calls numbers dialled whilst in IMS

Type:		LS OUT

Source: 	CT1

Discussion:	Related document is C1-082201.

Status:	REVISED TO C1-082675 which is revised to C1-082679.

C1-082679 is revised to C1-082730 and further revised to C1-082777.

C1-082777 is revised to C1-082783 which was finally AGREED.

C1-082691	Reply LS on "SAE interworking with Pre-REL8 system"

Type:		LS OUT

Source: 	CT1

Discussion:	This is reply LS to C1-082646. This LS should preferably have a common CT1/CT4 reply. The LS will be presented in CT1 for endorsement but will be sent from CT4.

Status:	POSTPONED

C1-082714	LS on UE behaviour when the network fails authentication

Type:		LS OUT

Source: 	CT1

Discussion:	This is related to C1-082573.

Status:	AGREED

# 11	Late and misplaced documents

C1-082314	Clarification of abnormal handling of de-registration

Type:		CR, 24.229

Source: 	LM Ericsson

Discussion:

Status:	REVISED TO C1-082629 and moved to agenda item 9.11

C1-082352	Architecture for Access Control Mechanisms for CSG Cells

Type:		Discussion

Source: 	Qualcomm Europe

Discussion:

Status:	late document, not handled

C1-082357	Update of security header

Type:		CR, 24.301

Source: 	Qualcomm Europe

Discussion:

Status:	late document, not handled

C1-082359	QoS parameters for the UE init ESM procedures

Type:		CR, 24.301

Source: 	Qualcomm Europe

Discussion:

Status:	late document, not handled

C1-082363	Normative annex for information elements in each signalling message

Type:		CR, 24.303

Source: 	Qualcomm Europe

Discussion:

Status:	late document, not handled

C1-082373	Removal of E-IMPU

Type:		CR, 24.229

Source: 	Qualcomm Europe

Discussion:

Status:	late document, not handled

C1-082414	Handling of NAS COUNT and NAS sequence number

Type:		CR, 24.301

Source: 	Nokia Siemens Networks

Discussion:

Status:	late document, not handled

C1-082438	Comparison of Communication Protocols

Type:		CR, 24.302

Source: 	Telcordia, Intel

Discussion:

Status:	late document, not handled

C1-082479	Clarification on SDF QoS Parameters

Type:		CR, 24.301

Source: 	Panasonic

Discussion:

Status:	late document, not handled

C1-082481	Service Type redefinition in Service request

Type:		CR, 24.301

Source: 	Panasonic

Discussion:

Status:	late document, not handled

C1-082482	Service Request usage in CS fallback procedures

Type:		CR, 24.301

Source: 	Panasonic

Discussion:

Status:	late document, not handled

C1-082483	Paging Type 2 support for CS fallback

Type:		CR, 24.301

Source: 	Panasonic

Discussion:

Status:	late document, not handled

C1-082509	Storage of EMM location information

Type:		CR, 24.301

Source: 	NTT DoCoMo, NEC

Discussion:

Status:	late document, not handled

C1-082516	Additional changes for private network indication

Type:		CR, 24.229

Source: 	Alcatel-Lucent / Keith Drage

Discussion:

Status:	late document, not handled

C1-082520	P-CR on update of EPS mobility management timer on the network side

Type:		CR, 24.301

Source: 	ZTE

Discussion:

Status:	late Tdoc request, not handled

# 12	A.O.B.

The Chairman introduced a new CT1 secretary Frederic Firmin and wished him a welcome on behalf of CT1.

The Chairman also thanked to Andrijana Brekalo for the support to CT1 group in recent years on his behalf and behalf of CT1 and handed to her a nice memory from CT1 delegates. Andrijana thanked to everybody for this kind attention and wished CT1 delegates all the best for the future and successful forthcoming meetings.

# 13	Closing

The meeting was closed on Friday at 15:30. The chairman thanked to delegates for one more successful meeting and the host for well organized meeting in a warm atmosphere of Zagreb.

## Annex A	Participants list

| TITLE | Lastname | Firstname | PHONE | Email | Organization Represented |
| --- | --- | --- | --- | --- | --- |
| Ms. | Agarwal | Anjana | 16 309 797 089 | anjana@alcatel-lucent.com | Alcatel-Lucent Telecom Limited |
| Mr. | Aghili | Behrouz | -6224995 | behrouz.aghili@interdigital.com | INTERDIGITAL COMMUNICATIONS |
| Mr. | Aikawa | Shinichiro | -6218 | saikawa@jp.fujitsu.com | Fujitsu Limited |
| Ms. | Al -Bakri | Ban | 33603602888 | ban.al-bakri@motorola.com | MOTOROLA Ltd |
| Mr. | Alfano | Frank | +1 630.979.7209 | falfano@alcatel-lucent.com | Alcatel-Lucent Deutschland AG |
| Mr. | Allen | Andrew | 18478098636 | aallen@rim.com | Research in Motion UK Limited |
| Mr. | Arreaga | Arturo | +1 (647) 747 4223 | arturo.arreaga@rci.rogers.com | Rogers Wireless Inc. |
| Mr. | Atarius | Roozbeh | 18 588 451 341 | Roozbeh@qualcomm.com | Qualcomm Incorporated |
| Mr. | Bakker | John-Luc | -3105 | jbakker@rim.com | Research in Motion UK Limited |
| Ms. | Brekalo | Andrijana | +33 4 92 94 43 09 | andrijana.brekalo@etsi.org | ETSI Secretariat |
| Mr. | Calme | Jim | 16 309 794 385 | calme@alcatel-lucent.com | Alcatel-Lucent |
| Mr. | Chadli | Youssef | +33 145 29 51 52 | youssef.chadli@orange-ftgroup.com | France Telecom |
| Miss | Chen | Ai | 8 613 910 630 873 | chenai@chinamobile.com | China Mobile Com. Corporation |
| Mr. | Chengzhi | Yu | +86 10 66006688-3075 | yuchengzhi@chinamobile.com | China Mobile Com. Corporation |
| Mr. | Chin | Chen-ho |  | chenho.chin@samsung.com | SAMSUNG Electronics |
| Mr. | Damle | Ameya | 40822223784 | adamle@marvell.com | Marvell Switzerland |
| Mr. | Das | Subir | 17 326 992 483 | subir@research.telcordia.com | Telcordia Technologies |
| Mr. | Dawes | Peter | 447 717 275 009 | peter.dawes@vodafone.com | VODAFONE LTD |
| Mr. | Drage | Keith | 441 793 897 312 | drage@alcatel-lucent.com | Alcatel-Lucent Telecom Limited |
| Mr. | Droste | Scott | 18 475 232 723 | scott.droste@motorola.com | MOTOROLA S.A.S |
| Mr. | Farhoumand | Rouzbeh | -7369 | rfarhoumand@huawei.com | HuaWei Technologies Co., Ltd |
| Mr. | Firmin | Frédéric | +33 4 92 94 43 09 |  | ETSI Secretariat |
| Dr. | Frascolla | Valerio | 4,90911E+13 | valerio.frascolla@comneon.com | INFINEON TECHNOLOGIES |
| Mr. | Giaretta | Gerardo | 393 476 801 733 | gerardog@qualcomm.com | QUALCOMM EUROPE S.A.R.L. |
| Mr. | Gulbani | Giorgi | 358 718 029 759 | giorgi.gulbani@nsn.com | Nokia Siemens Networks Oy |
| Mr. | Gupta | Vivek | 334 085 135 716 | vivek.g.gupta@intel.com | INTEL CORPORATION SAS |
| Mr. | Hodges | Phil | 61 404 069 546 | philip.hodges@ericsson.com | Ericsson Inc. |
| Mr. | Howell | Andrew | 441 452 612 833 | ahowell@rim.com | Research in Motion UK Limited |
| Ing. | Hülsemann | Martin | 4 961 516 282 765 | Martin.Huelsemann@telekom.de | T-Mobile Austria GmbH |
| Mr. | Hutton | David | 44 163 533 251 | David.Hutton@vodafone.com | VODAFONE Group Plc |
| Mr. | Ishikawa | Hiroshi | +81 422 59 4143 | ishikawa.hiroshi@lab.ntt.co.jp | NTT |
| Mr. | Izaguirre | Enrique | 34 616 710 887 | leig@tid.es | TELEFONICA S.A. |
| Mr. | Jacobsohn | Dieter | 4 922 893 618 445 | dieter.jacobsohn@t-mobile.net | T-Mobile International AG |
| Mrs. | Jactat | Caroline | 33149072839 | caroline.jactat@nectech.fr | NEC Corporation |
| Mr. | Jesske | Roland | 4 961 516 282 766 | r.jesske@telekom.de | Deutsche Telekom AG |
| Mr. | Jin | Haipeng | -7689 | haipengj@qualcomm.com | Qualcomm Japan Inc |
| Mr. | Kåll | Jan | 358 400 400 056 | jan.kall@nsn.com | Nokia Siemens Networks |
| Mr. | Karlsson | Magnus | 4646232816 | magnus.mk.karlsson@ericsson.com | Nanjing Ericsson Panda Com Ltd |
| Mr. | Kavanaugh | Tom | 16 198 041 920 | tkavanaugh@sierrawireless.com | Sierra Wireless UK Limited |
| Mr. | Khan | Asan | -3788 | asan.khan@sprint.com | SPRINT |
| Dr. | Laganier | Julien | -57095 | laganier@docomolab-euro.com | DoCoMo Communications Lab. |
| Mr. | Lair | Yannick | +33 1 49 07 20 75 | yannick.lair@nectech.fr | NEC Technologies (UK) LTD |
| Mr. | Landais | Bruno | +33 2 96 04 82 61 | bruno.landais@alcatel-lucent.fr | Alcatel-Lucent |
| Mr. | Lavasani | Shahab | +46 70 6360204 | shahab.lavasani@huawei.com | Huawei Technologies Sweden AB |
| Mr. | Leis | Peter | +49 89 636 75208 | peter.leis@nsn.com | Nokia Siemens Networks S.p.A |
| Mr. | Li | Shitao | +86 25 52877868 | li.shitao@zte.com.cn | CCSA |
| Mr. | Libunao | Gerry | 19085597561 | gerry.libunao@verizonwireless.com | Verizon Wireless |
| Dr. | Lu | Yang | 492 115 335 432 | yang.lu@vodafone.com | Vodafone D2 GmbH |
| Mr. | Mayer | Georg | 358 504 821 437 | georg.mayer@nokia.com | Nokia Japan Co, Ltd |
| Mr. | Monrad | Atle | +47 372 93 040 | atle.monrad@ericsson.com | Telefon AB LM Ericsson |
| Miss | NADER | Reina | 33145294605 | reina.nader@orange-ftgroup.com | ORANGE SA |
| Mr. | Niemi | Marko | 3,58718E+11 | marko.t.niemi@nokia.com | NOKIA UK Ltd |
| Mr. | NOGAMI | KEN | +81-3-3457-3975 | kazuo1.nogami@toshiba.co.jp | Toshiba Corporation |
| Mr. | Norreys | Steve | +44 1277 32 32 20 | steve.norreys@bt.com | BT Group Plc |
| Mr. | Oba | Takumi | -8148 | ohba.takumi@lab.ntt.co.jp | NTT |
| Dr. | Orsic | Milo | 16 307 135 161 | orsic@alcatel-lucent.com | Alcatel-Lucent |
| Mr. | Pandit | Krishna | -54014612 | Krishna.Pandit@qualcomm.com | QUALCOMM EUROPE S.A.R.L. |
| Dr. | Patel | Milan | 4,41628E+11 | milanpa@nortel.com | NORTEL NETWORKS (EUROPE) |
| Mr. | Procopio | Roberto | 390 112 285 061 | roberto.procopio@telecomitalia.it | TELECOM ITALIA S.p.A. |
| Mr. | Provost | Curtis | 19 726 855 406 | cprovost@nortel.com | Nortel Networks |
| Mr. | Punz | Gottfried | 435 170 721 568 | gottfried.punz@siemens.com | Nokia Siemens Networks |
| Mr. | Ramankutty | Rajesh | +1-(978) 851-1607 | rramankutty@starentnetworks.com | Starent Networks Corporation |
| Dr. | Ro | Kwanghyun | -7164 | khrho@etri.re.kr | ETRI |
| Mr. | S Kumar | Swaroop | -11967 | swaroop.kumar@sg.panasonic.com | Panasonic Mobile Communication |
| Mr. | Sasaki | Tetsuo | +81 43 211 3532 | t-sasaki@lab.ntt.co.jp | NTT |
| Mr. | Schneyer | Sean | 19 725 830 903 | sean.schneyer@ericsson.com | Ericsson Inc. |
| Mr. | Sharma | Manish | 8 613 905 151 285 | manish.sharma@zte.com.cn | ZTE Corporation |
| Mr. | Shimizu | Akihiro | 81468403545 | shimizuaki@s1.nttdocomo.co.jp | NTT DoCoMo Inc. |
| Mr. | Shin | Jongkeol | +82 31 279 5252 | thomas.shin@samsung.com | Samsung Electronics Co., Ltd |
| Dr. | Song | Osok | -14572 | osok.song@qualcomm.com | Qualcomm Korea |
| Mr. | Subramanian | Ramachandran | 18 586 512 350 | rsubrama@qualcomm.com | Flarion Technologies |
| Mr. | Suh | Kyung Joo | 823 427 796 818 | joo.suh@samsung.com | Samsung Electronics Co., Ltd |
| Mr. | Sun | Yang | -52818099 | sun.yang@zte.com.cn | ZTE Corporation |
| Mr. | Syrett | Mark | 33476141965 | mark.syrett@hp.com | Hewlett-Packard |
| Mr. | Takada | Terufumi | +81 45 938 2424 | takada.terufumi@jp.panasonic.com | Panasonic Mobile Communication |
| Mr. | Tamura | Toshiyuki | +81 44 455 8496 | tamurato@aj.jp.nec.com | NEC Corporation |
| Mr. | Velev | Genadi | 4 961 037 661 193 | genadi.velev@eu.panasonic.com | PANASONIC R&D Center Germany |
| Mr. | Wallis | Brett | +14699164393 x5048 | brett@mavenir.com | Mavenir |
| Mr. | Wass | Mikael | +46 31 7476928 | mikael.wass@ericsson.com | Nippon Ericsson K.K. |
| Dr. | Xiong | Chunshan | +86 10 58832096 | xiongchunshan@datangmobile.cn | CATT |
| Mr. | Xu | Peili | -287888438 | xupeili@huawei.com | HuaWei Technologies Co., Ltd |
| Mr. | Yamashita | Hideyuki | 81 422 515 618 | yamashitahi@s1.nttdocomo.co.jp | NTT DoCoMo Inc. |
| Miss | Yang | Lili | +86-755-2856-506 | kadyyang@huawei.com | Huawei Technologies Sweden AB |
| Mr. | Yu | Yijun | +86 2168644808-27779 | yuyijun@huawei.com | HuaWei Technologies Co., Ltd |
| Mr. | Yuan | Liping | -68663750 | lipingy@huawei.com | HuaWei Technologies Co., Ltd |
| Dr. | Zaus | Robert | +49 89 636 75206 | robert.zaus@nsn.com | Nokia Siemens Networks |
| Mr. | Zhang | Ying | -28422231 | zhangying67324@huawei.com | HuaWei Technologies Co., Ltd |
| Mr. | Zhang | Peng Sheng | +86 20 3863 9313 | zhangps@gsta.com | China Telecommunications |
| Mr. | Zhang | Peng | -82836368 | zhang.peng@huawei.com | HuaWei Technologies Co., Ltd |
| Mr. | Zhu | Chunhui | -52877836 | zhu.chunhui@zte.com.cn | ZTE Corporation |
| Mr. | Zhu | Chunhui | -52877836 | zhu.chunhui@zte.com.cn | ZTE Corporation |
| Mr. | Zu | Qiang | 15145941136 | zu.qiang@ericsson | Ericsson Inc. |
| Mr. | Heidermark | Alf |  |  | Ericsson JNR |

## Annex B	Output documents (Agreed CRs, WIDs, LS OUT)

AGREED CRs for specifications under the change control

| Tdoc # | Tdoc Title | Spec | CR # | Rev | Rel | WI | Source |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C1-082142 | Reference correction | 24.229 | 2302 |  | Rel-8 | IMSProtoc2 | LM Ericsson |
| C1-082267 | Addition of AVPF support and SDP capability negotiation mechanism | 24.229 | 2313 |  | Rel-7 | IMSProtoc | Alcatel-Lucent / Keith Drage |
| C1-082268 | Addition of AVPF support and SDP capability negotiation mechanism | 24.229 | 2314 |  | Rel-8 | IMSProtoc | Alcatel-Lucent / Keith Drage |
| C1-082269 | Profile corrections for outbound | 24.229 | 2315 |  | Rel-7 | FBI-pcbl | Alcatel-Lucent / Keith Drage |
| C1-082270 | Profile corrections for outbound | 24.229 | 2316 |  | Rel-8 | FBI-pcbl | Alcatel-Lucent / Keith Drage |
| C1-082284 | Removal of redundant references | 24.141 | 0094 |  | Rel-8 | REDOC_3GPP2 | Alcatel-Lucent / Keith Drage |
| C1-082298 | Correction of reference | 24.605 | 0001 |  | Rel-8 | REDOC_TIS-C1 | Ericsson / Atle |
| C1-082299 | Correction of minors mistakes in signalling flows | 24.606 | 0001 |  | Rel-8 | REDOC_TIS-C1 | Ericsson / Atle |
| C1-082300 | Removal of normative statements in NOTEs | 24.607 | 0001 |  | Rel-8 | REDOC_TIS-C1 | Ericsson / Atle |
| C1-082301 | Correction of Activation/deactivation of HOLD | 24.610 | 0001 |  | Rel-8 | REDOC_TIS-C1 | Ericsson / Atle |
| C1-082302 | Removal of text from voided subclause | 24.616 | 0001 |  | Rel-8 | REDOC_TIS-C1 | Ericsson / Atle |
| C1-082303 | Editorial fixes for the flows | 24.628 | 0001 |  | Rel-8 | REDOC_TIS-C1 | Ericsson / Atle |
| C1-082304 | Removal of normative statement in a NOTE | 24.629 | 0001 |  | Rel-8 | REDOC_TIS-C1 | Ericsson / Atle |
| C1-082324 | Support of Direct Ethernet access as IP-CAN | 24.229 | 2319 |  | Rel-8 | IMS_Corp | Orange |
| C1-082327 | Correction of terminology | 24.604 | 0002 |  | Rel-8 | REDOC_TIS-C1 | Research in Motion |
| C1-082341 | Deletion of unnecessary usage of announcement | 24.428 | 0002 | 1 | Rel-7 | MAINT_R1 | NTT |
| C1-082342 | Deletion of unnecessary usage of announcement | 24.528 | 0002 | 1 | Rel-8 | MAINT_R1 | NTT |
| C1-082343 | Deletion of unnecessary usage of announcement | 24.628 | 0002 |  | Rel-8 | MAINT_R1 | NTT |
| C1-082429 | Clarifications for RAT usage in manual network selection mode | 23.122 | 0121 |  | Rel-8 | TEI8 | NEC/Yannick |
| C1-082472 | Implementation error of CR 0052 | 24.234 | 0054 |  | Rel-8 | IWLANNSP | Research in Motion |
| C1-082605 | Correction on identifiers distinguishing the dialog | 24.229 | 2311 | 1 | Rel-5 | IMS-CCR | Alcatel-Lucent / Keith Drage |
| C1-082606 | Correction on identifiers distinguishing the dialog | 24.229 | 2312 | 1 | Rel-6 | IMS-CCR | Alcatel-Lucent / Keith Drage |
| C1-082609 | Annex A: Correction of SDP connection information | 24.229 | 2304 | 1 | Rel-6 | IMS2 | LM Ericsson |
| C1-082610 | Annex A: Correction of SDP connection information | 24.229 | 2305 | 1 | Rel-7 | IMS2 | LM Ericsson |
| C1-082611 | Annex A: Correction of SDP connection information | 24.229 | 2306 | 1 | Rel-8 | IMS2 | LM Ericsson |
| C1-082612 | Annex A: Correction of SDP connection information | 24.403 | 0010 |  | Rel-7 | IMS2 | Ericsson |
| C1-082613 | Annex A: Correction of SDP connection information | 24.503 | 0019 |  | Rel-8 | IMS2 | Ericsson |
| C1-082618 | Introduction of terms "multimedia telephony participant" and "multimedia telephony application server" | 24.173 | 0053 | 1 | Rel-7 | MTSI | Alcatel-Lucent / Keith Drage |
| C1-082619 | Introduction of terms "multimedia telephony participant" and "multimedia telephony application server" | 24.173 | 0054 | 1 | Rel-8 | MTSI | Alcatel-Lucent / Keith Drage |
| C1-082620 | Correction of DHCP reference | 24.229 | 2301 | 1 | Rel-8 | IMSProtoc2 | LM Ericsson |
| C1-082621 | Add reference to draft-dotson-sip-mutual-auth | 24.229 | 2299 | 1 | Rel-8 | PktCbl-Sec | Ericsson/Sean |
| C1-082622 | Annex K Updates | 24.229 | 2328 | 1 | Rel-8 | PktCbl-Sec | CableLabs |
| C1-082623 | Cleanup of P-CSCF procedures for inclusion of "tls-yes" and "tls-pending" | 24.229 | 2297 | 1 | Rel-8 | PktCbl-Sec | Ericsson/Sean |
| C1-082625 | Backward compatibility issue with P-Access-Network-Info ABNF extension | 24.229 | 2308 | 1 | Rel-8 | IMSProtoc2 | LM Ericsson |
| C1-082626 | Update outbound reference | 24.229 | 2323 | 1 | Rel-8 | FBI-Pcbl | Qualcomm Europe |
| C1-082627 | Update outbound reference | 24.229 | 2334 |  | Rel-7 | FBI-Pcbl | Qualcomm Europe |
| C1-082642 | “Latency Reduction support for non RTTI capable MSs” | 24.008 | 1202 | 1 | Rel-7 | TEI7 | Nortel |
| C1-082643 | “Latency Reduction support for non RTTI capable MSs” | 24.008 | 1203 | 1 | Rel-8 | TEI7 | Nortel |
| C1-082657 | Introduction of GIBA (Early IMS) procedures | 24.229 | 2298 | 1 | Rel-8 | SEC-IMS | Ericsson/Sean |
| C1-082681 | Adding and extending AT-commands to support touch screen functions | 27.007 | 0159 | 1 | Rel-8 | TEI8 | AT&T, LG, Spirent |
| C1-082682 | Setting of display resolution and scren orientation for touch screen functions | 27.007 | 0160 | 1 | Rel-8 | TEI8 | AT&T, LG, Spirent |
| C1-082683 | Correction for IMSI detach procedure during dedicated mode | 24.008 | 1201 | 1 | Rel-8 | TEI8 | NEC/Yannick |
| C1-082731 | Correction of notification service activation | 24.604 | 0003 | 1 | Rel-8 | REDOC_TIS-C1 | Research in Motion |
| C1-082732 | Correction of subscription options | 24.404 | 0005 | 1 | Rel-7 | MAINT_R1 | Research in Motion |
| C1-082733 | Correction of subscription options | 24.504 | 0005 | 1 | Rel-8 | MAINT_R1 | Research in Motion |
| C1-082734 | Correction of subscription options | 24.604 | 0004 | 1 | Rel-8 | MAINT_R1 | Research in Motion |
| C1-082735 | Value of "No reply timer" for CDIV | 24.404 | 0006 | 1 | Rel-7 | MAINT_R1 | NTT |
| C1-082736 | Value of "No reply timer" for CDIV | 24.504 | 0006 | 1 | Rel-8 | MAINT_R1 | NTT |
| C1-082737 | Value of "No reply timer" for CDIV | 24.604 | 0005 | 1 | Rel-8 | MAINT_R1 | NTT |
| C1-082738 | Correction to the communication diversion service | 24.404 | 0003 | 1 | Rel-7 | MAINT_R1 | LM Ericsson |
| C1-082739 | Correction to the communication diversion service | 24.504 | 0003 | 1 | Rel-8 | MAINT_R1 | LM Ericsson |
| C1-082741 | Alignment of user configuration | 24.654 | 0001 | 1 | Rel-8 | REDOC_TIS-C1 | Ericsson / Atle |
| C1-082742 | Network requirements for OIP and OIR | 24.607 | 0002 | 1 | Rel-8 | REDOC_TIS-C1 | Nokia Siemens Networks |
| C1-082743 | Tidyup xsd | 24.623 | 0001 | 1 | Rel-8 | REDOC_TIS-C1 | Nokia Siemens Networks |
| C1-082744 | Miscellaneous clean-up corrections | 24.610 | 0002 | 1 | Rel-8 | REDOC-TIS_C1 | Qualcomm Europe |
| C1-082748 | Allow SIP based user configuration mechanism for configuring supplementary services | 24.607 | 0003 | 1 | Rel-8 | REDOC_3GPP2 | Qualcomm Europe |
| C1-082749 | Allow SIP based user configuration mechanism for configuring supplementary services | 24.608 | 0001 | 1 | Rel-8 | REDOC_3GPP2 | Qualcomm Europe |
| C1-082750 | Allow SIP based user configuration mechanism for configuring supplementary services | 24.611 | 0001 | 1 | Rel-8 | REDOC_3GPP2 | Qualcomm Europe |
| C1-082751 | Allow SIP based user configuration mechanism for configuring supplementary services | 24.654 | 0002 | 1 | Rel-8 | REDOC_3GPP2 | Qualcomm Europe |
| C1-082752 | Adding P-Debug-ID to SIP Profile Tables | 24.229 | 2329 | 1 | Rel-8 | OAM8-Trace | Vodafone |
| C1-082768 | Allow SIP based user configuration mechanism for configuring supplementary services | 24.173 | 0055 | 2 | Rel-8 | REDOC_3GPP2 | Qualcomm Europe |
| C1-082769 | Allow SIP based user configuration mechanism for configuring supplementary services | 24.604 | 0006 | 2 | Rel-8 | REDOC_3GPP2 | Qualcomm Europe |
| C1-082770 | Error Response for Different S-CSCF Assignment | 24.229 | 2325 | 2 | Rel-8 | IMSProtoc2 | Huawei |
| C1-082778 | Alignment of IP-CAN specific annexes | 24.229 | 2333 | 2 | Rel-6 | IMSProtoc2 | Alcatel-Lucent |
| C1-082779 | Clarification of B2BUA and Proxy roles for AS | 24.604 | 0001 | 2 | Rel-8 | REDOC_TIS-C1 | Ericsson/Sean |
| C1-082781 | Subscribing to the debug event package | 24.229 | 2330 | 2 | Rel-8 | OAM8-Trace | Vodafone |
| C1-082810 | Add Timestamp in Register Request | 24.229 | 2178 | 6 | Rel-8 | REDOC_3GPP2 | Qualcomm Europe/Roozbeh |
| C1-082813 | Additions to the protocol aspects of CBS for the realisation of ETWS | 23.041 | 0019 | 2 | Rel-8 | ETWS | NTT DoCoMo |
| C1-082815 | Avoidance of mobility management signalling for eCall only terminals | 24.008 | 1189 | 4 | Rel-8 | EData | Qualcomm Europe |
| C1-082817 | Chages to CBS for the realisation of ETWS. | 23.041 | 0018 | 3 | Rel-8 | ETWS | NTT DoCoMo |
| C1-082818 | Changes to the radio message format aspect of CBS for the realisation of ETWS | 23.041 | 0020 | 3 | Rel-8 | ETWS | NTT DoCoMo |

AGREED WIDs under CT1 leadership

| Tdoc # | Tdoc Title | Type | Status |
| --- | --- | --- | --- |
| C1-082561 | Proposed WID for CT1 aspects of SRVCC | WID | Agreed |
| C1-082685 | CSG and Idle Mode Mobility for LTE Home eNodeB | WID | Agreed |
| C1-082670 | Updated WID for IMS Service Continuity Stage3 | WID | Agreed |
| C1-082709 | Updated WID on stage 3 for CS Fallback in EPS | WID | Agreed |
| C1-082798 | CSG and Idle Mode Mobility for 3G Home NodeB | WID | Agreed |

AGREED Outgoing Liaison Statements

| Tdoc # | Tdoc Title | Type | Comment |
| --- | --- | --- | --- |
| C1-082534 | LS on 3GPP Namespace Identification (NID) administration | LS out | To: SA3; CC: SA, SA2, SA4, CT, CT3, CT4, GSMA |
| C1-082540 | Reply LS on IMS Emergency Registration | LS out | To: SA3, CT4; CC: SA |
| C1-082541 | Reply LS on Requesting recommendations from IEEE 802.11, IEEE 802.11-08/0417r2 | LS out | To: SA2, IEEE 802.11u; CC:SA1, SA |
| C1-082546 | Reply LS on RTCP bandwidth modifiers for MTSI | LS out | To: RAN5; CC: SA4 |
| C1-082547 | LS on Enhancements for SRNS Relocation | LS out | To: RAN3; CC: CT4 |
| C1-082548 | Reply to LS on HSPA VoIP to WCDMA/GSM CS continuity | LS out | To: RAN2; CC: SA2 |
| C1-082552 | Reply LS on Earthquake and Tsunami Warning System | LS out | To: RAN2; CC: SA2 |
| C1-082713 | LS on Rel-8 UICC parameters | LS out | To: CT6, CC: SA1 |
| C1-082714 | LS on UE behaviour when the network fails authentication | LS out | To: RAN2 |
| C1-082772 | Reply LS on add/remove media | LS out | To: RAN5; CC: SA1, SA4 |
| C1-082773 | LS on SDP Enhancements to support resource allocation | LS out | To: CT3, SA4 |
| C1-082782 | Reply LS on SDP connection information | LS out | To: RAN5; CC: SA4 |
| C1-082783 | Reply LS on handling of local emergency calls numbers dialled whilst in IMS | LS out | To: SA2 |
| C1-082799 | Reply LS on UTRA R8 hNB requirements | LS out | To: RAN2; CC: SA1 |
| C1-082800 | Reply LS on Connection recovery by NAS | LS out | To: RAN2; CC:SA2, RAN3 |
| C1-082801 | LS on combination of SMC and Attach or TAU | LS out | To: SA2; CC: SA3 |
| C1-082806 | LS on CS Fallback | LS out | To: RAN2, SA1; CC:SA2, RAN3 |

## Annex C	Document List (CT1-54)

| Tdoc # | Tdoc Title | Source | Spec | CR | WI | Release | Type | Status |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| C1-082120 | CT1-54 Agenda | CT1 Chariman |  |  |  |  | Agenda | Noted |
| C1-082121 | Pseudo CR on PLMN selection, Introduction of TA | T-Mobile | 24.801 |  | SAES | Rel-8 | Draft CR | Revised in 2555 |
| C1-082122 | DSMIP6 Detach | Nortel Networks | 24.303 |  | SAES |  | Draft CR | Agreed |
| C1-082123 | Optimized Handover Impacts to NAS | Nortel Networks |  |  |  |  | Discussion | Noted |
| C1-082124 | S101 mode NAS Signalling Connection | Nortel Networks | 24.301 |  | SAES |  | Draft CR | Revised in 2571 |
| C1-082125 | Optimized Handover Execution | Nortel Networks | 24.301 |  | SAES |  | Draft CR | Agreed |
| C1-082126 | Using S101 NAS Signalling Connection | Nortel Networks | 24.301 |  | SAES |  | Draft CR | Agreed |
| C1-082127 | Cleanup of P-CSCF procedures for inclusion of "tls-yes" and "tls-pending" | Ericsson/Sean | 24.229 | 2297 | IMSProtoc2 | Rel-8 | CR | Revised in 2623 |
| C1-082128 | Introduction of GIBA (Early IMS) procedures | Ericsson/Sean | 24.229 | 2298 | SEC-IMS | Rel-8 | CR | Revised in 2657 |
| C1-082129 | Add reference to draft-dotson-sip-mutual-auth | Ericsson/Sean | 24.229 | 2299 | PktCbl-Sec | Rel-8 | CR | Revised in 2621 |
| C1-082130 | Updates to ICS skeleton to include supplementary svcs and additional call flows | Ericsson/Sean | 24.292 |  | ICSRA | Rel-8 | Draft CR | Agreed |
| C1-082131 | Clarification of B2BUA and Proxy roles for AS | Ericsson/Sean | 24.604 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Revised in 2740 |
| C1-082132 | EMM-DEREGISTERED when in HRPD | Nortel Networks | 24.301 |  | SAES |  | Draft CR | Revised in 2795 |
| C1-082133 | Baseline version of TS 24.302 v0.4.0 | Rapporteur |  |  |  |  | Draft TS | Noted |
| C1-082134 | Notes on conference call of 5th Jun 2008 on TS 24.302 | Samsung/Chen-Ho |  |  |  |  | Report | Noted |
| C1-082135 | P-CR: Restructuring and adding procedural text to subclause 5.1 for Access Network discovery and selection | Samsung/Chen-Ho | 24.302 |  | SAES | Rel-8 | Draft CR | Revised in 2562 |
| C1-082136 | P-CR: Restructuring subclause 6.8 and adding signalling procedure text | Samsung/Chen-Ho | 24.302 |  | SAES | Rel-8 | Draft CR | Revised in 2563 |
| C1-082137 | P-CR: Deciding if non-3GPP IP access is trusted or untrusted | Samsung/Chen-Ho | 24.302 |  | SAES | Rel-8 | Draft CR | Withdrawn |
| C1-082138 | Removal of draft-ietf-simple-common-policy-caps | LM Ericsson | 24.141 | 0092 | PRESNC | Rel-8 | CR | Revised in 2607 |
| C1-082139 | Removal of draft-ietf-simple-pres-policy-caps | LM Ericsson | 24.141 | 0093 | PRESNC | Rel-8 | CR | Withdrawn |
| C1-082140 | Correction of DHCP reference | LM Ericsson | 24.229 | 2300 | IMSProtoc | Rel-7 | CR | Withdrawn |
| C1-082141 | Correction of DHCP reference | LM Ericsson | 24.229 | 2301 | IMSProtoc | Rel-8 | CR | Revised in 2620 |
| C1-082142 | Reference correction | LM Ericsson | 24.229 | 2302 | IMSProtoc2 | Rel-8 | CR | Agreed |
| C1-082143 | Annex A: Correction of SDP connection information | LM Ericsson | 24.229 | 2303 | IMS-CCR | Rel-5 | CR | Withdrawn |
| C1-082144 | Annex A: Correction of SDP connection information | LM Ericsson | 24.229 | 2304 | IMS2 | Rel-6 | CR | Revised in 2609 |
| C1-082145 | Annex A: Correction of SDP connection information | LM Ericsson | 24.229 | 2305 | IMS2 | Rel-7 | CR | Revised in 2610 |
| C1-082146 | Annex A: Correction of SDP connection information | LM Ericsson | 24.229 | 2306 | IMS2 | Rel-8 | CR | Revised in 2611 |
| C1-082147 | Target refresh correction | LM Ericsson | 24.229 | 2307 | IMSProtoc2 | Rel-8 | CR | Revised in 2624 |
| C1-082148 | Backward compability issue with P-Access-Network-Info ABNF extension | LM Ericsson | 24.229 | 2308 | IMSProtoc2 | Rel-8 | CR | Revised in 2625 |
| C1-082149 | Discussion on indication of early dialog termination | LM Ericsson |  |  |  |  | Discussion | Noted |
| C1-082150 | Discussion on STUN/TURN server discovery | LM Ericsson |  |  |  |  | Discussion | Withdrawn |
| C1-082151 | Pseudo-CR on multi system PLMN selection | Nokia | 24.801 |  | SAE | Rel-8 | Draft CR | Revised in 2556 |
| C1-082152 | Detailed pseudo CR on multi system PLMN selection | Nokia | 24.801 |  | SAE | Rel-8 | Draft CR | Revised in 2557 |
| C1-082153 | Multiple authentications for DSMIPv6 bootstrapping | TeliaSonera | 24.303 |  | SAES | Rel-8 | Draft CR | Revised in 2693 |
| C1-082154 | Clarification of DSMIPv6 Handover Procedure | Ericsson | 24.303 |  | SAE | Rel-8 | Draft CR | Revised in 2694 |
| C1-082155 | Field and Message Details for Initial BU and BA | Ericsson | 24.303 |  | SAE | Rel-8 | Draft CR | Revised in 2695 |
| C1-082156 | Field and Message Details for Re-Registration | Ericsson | 24.303 |  | SAE | Rel-8 | Draft CR | Withdrawn |
| C1-082157 | Field and Message Details for Handover BU and BA | Ericsson | 24.303 |  | SAE | Rel-8 | Draft CR | Withdrawn |
| C1-082158 | Field and Message Details for DSMIPv6 Detach using BU and BA | Ericsson | 24.303 |  | SAE | Rel-8 | Draft CR | Withdrawn |
| C1-082159 | Field and Message Details for HA Switch | Ericsson | 24.303 |  | SAE | Rel-8 | Draft CR | Withdrawn |
| C1-082160 | Field and Message Details for BRI/ BRA and corrections | Ericsson | 24.303 |  | SAE | Rel-8 | Draft CR | Withdrawn |
| C1-082161 | Communication protocol between the UE and the ANDSF | Ericsson |  |  | SAE |  | Draft CR | Revised in 2565 |
| C1-082162 | EPS bearer context | Ericsson |  |  |  |  | Discussion | Noted |
| C1-082163 | Pseudo-CR on EPS bearer context | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Postponed |
| C1-082164 | Pseudo-CR on optional parameters in PDN connectivity request | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2572 |
| C1-082165 | Pseudo-CR on Authentication procedure abnormal cases | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2573 |
| C1-082166 | Pseudo-CR on IPv6 prefix delegation | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2574 |
| C1-082167 | EPS bearer context synchronization at service request | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Withdrawn |
| C1-082168 | Pseudo-CR on NAS Sequence Number Handling | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2575 |
| C1-082169 | Pseudo-CR on TAU in connected mode | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Postponed |
| C1-082170 | Pseudo-CR on Order of integrity protection and ciphering | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Withdrawn |
| C1-082171 | Initiation of Security mode control procedure | Ericsson | 24.801 |  | SAE | Rel-8 | Draft CR | Postponed |
| C1-082172 | Pseudo-CR on Mapping between GUTI and P-TMSI | Ericsson | 24.801 |  | SAE | Rel-8 | Draft CR | Withdrawn |
| C1-082173 | Stage 2 alignment related to Network bearer control | Ericsson | 24.008 | 1194 | TEI7 | Rel-7 | CR | Revised in 2640 |
| C1-082174 | Stage 2 alignment related to Network bearer control | Ericsson | 24.008 | 1195 | TEI7 | Rel-8 | CR | Revised in 2641 |
| C1-082175 | Coding of the TAI list IE | Nokia | 24.301 |  | SAE |  | Draft CR | Revised in 2576 |
| C1-082176 | ESM information in Attach messages | Nokia | 24.301 |  | SAE |  | Draft CR | Revised in 2577 |
| C1-082177 | Example signalling flow for CS UE origination via an MSC enhanced for ICS where the origation MSC server enhanced for ICS supports codec negotiation. | LM Ericsson | 24.292 |  | ICSRA | Rel-8 | Draft CR | Revised in 2591 |
| C1-082178 | Example signalling flow for CS UE origination via an MSC enhanced for ICS where the origation MSC server enhanced for ICS does not supports codec negotiation. | LM Ericsson | 24.292 |  | ICSRA | Rel-8 | Draft CR | Revised in 2592 |
| C1-082179 | Replacement of Emergency IMPU | LM Ericsson |  |  |  |  | Discussion | Noted |
| C1-082180 | Replacement of Emergency IMPU | LM Ericsson | 24.229 | 2309 | EMC1 | Rel-7 | CR | Postponed |
| C1-082181 | Replacement of Emergency IMPU | LM Ericsson | 24.229 | 2310 | EMC1 | Rel-8 | CR | Postponed |
| C1-082182 | Correction to the communication diversion service | LM Ericsson | 24.404 | 0003 | MAINT_R1 | Rel-7 | CR | Revised in 2738 |
| C1-082183 | IMS Emergency Services gap analysis | Alcatel-Lucent/Milo Orsic |  |  |  |  | Discussion | Noted |
| C1-082184 | Application level handover | Alcatel-Lucent/Milo Orsic | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Revised in 2454 |
| C1-082185 | UE Security Capabilities IE | Alcatel-Lucent / Frank Alfano | 24.301 |  | SAES-St3-CT1sec | Rel-8 | Draft CR | Revised in 2578 |
| C1-082186 | Tracking area request message update | Alcatel-Lucent / Frank Alfano | 24.301 |  | SAES-St3-CT1sec | Rel-8 | Draft CR | Postponed |
| C1-082187 | Update to 24.302 Clause 6.4 /Authentication | Alcatel-Lucent / Frank Alfano | 24.302 |  | SAES-St3-CT1sec | Rel-8 | Draft CR | Revised in 2567 |
| C1-082188 | Example flow for CS UE termination via MSC Server enhanced for ICS (with codec negotiation) | Mavenir | 24.292 |  | ICSRA | Rel-8 | Draft CR | Revised in 2593 |
| C1-082189 | Example flow for CS UE termination via MSC Server enhanced for ICS (without codec negotiation) | Mavenir | 24.292 |  | ICSRA | Rel-8 | Draft CR | Revised in 2594 |
| C1-082190 | Example flow for CS UE termination, not registered in IMS | Mavenir | 24.292 |  | ICSRA | Rel-8 | Draft CR | Revised in 2595 |
| C1-082191 | IP Mobility Mode selection | Marvell |  |  |  |  | Draft CR | Revised in 2568 |
| C1-082192 | On Multiple PDN support | Marvell |  |  |  |  | Draft CR | Revised in 2569 |
| C1-082193 | Update of UE requested PDN connectivity procedure | Marvell |  |  |  |  | Draft CR | Revised in 2579 |
| C1-082194 | Introduction to the solution for ETWS for UTRAN | NTT DoCoMo |  |  |  |  | Discussion | Noted |
| C1-082195 | Chages to CBS for the realisation of ETWS. | NTT DoCoMo | 23.041 | 0018 | ETWS | Rel-8 | CR | Revised in 2654 |
| C1-082196 | Additions to the protocol aspects of CBS for the realisation of ETWS | NTT DoCoMo | 23.041 | 0019 | ETWS | Rel-8 | CR | Revised in 2655 |
| C1-082197 | Changes to the radio message format aspect of CBS for the realisation of ETWS | NTT DoCoMo | 23.041 | 0020 | ETWS | Rel-8 | CR | Revised in 2656 |
| C1-082198 | LS on documentation of TISPAN Rel-2 in 3GPP | TSG SA |  |  |  |  | LS in | Noted |
| C1-082199 | Reply to LS from TSG-RAN on decision for NW interface option for ETWS support | TSG SA |  |  |  |  | LS in | Noted |
| C1-082200 | LS on multiple solutions for VoIP call continuity | TSG SA |  |  |  |  | LS in | Noted |
| C1-082201 | LS on handling of local emergency calls numbers dialled whilst in IMS | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082202 | LS on IM Credentials | TSG SA |  |  |  |  | LS in | Noted |
| C1-082203 | LS on “IMS initiated and controlled PSS and MBMS User Service” Architecture | TSG SA WG4 MBS S |  |  |  |  | LS in | Noted |
| C1-082204 | LS on CS fallback for 1xRTT CS domain access | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082205 | LS on Earthquake and Tsunami Warning System | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082206 | LS on Active mode paging in E-UTRAN | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082207 | Response LS on the need for TAU in connected mode | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082208 | Reply LS on Enhancements for SRNS Relocation | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082209 | Reply LS on adding UE Capability as a SPT | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082210 | Reply LS on working assumptions for the scope of responsibility for optimized handover specification | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082211 | Reply LS on Resource mapping at handover between EPS and 2G/3G | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082212 | Reply LS on NGCN issues and proposed workshop | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082213 | LS on UE Radio Capabilities | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082214 | LS on IMS Emergency Registration | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082215 | Reply LS on request for recommendations (on IEEE 802.11u approach) | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082216 | Pseudo-CR on Combined Attach for CS Fallback | NTT DoCoMo | 24.301 |  | CSFB | Rel-8 | Draft CR | Revised in 2701 |
| C1-082217 | Pseudo-CR on Update type for CS Fallback | NTT DoCoMo | 24.301 |  | CSFB | Rel-8 | Draft CR | Withdrawn |
| C1-082218 | Pseudo-CR on Combined TAU procedure for CS Fallback | NTT DoCoMo | 24.301 |  | CSFB | Rel-8 | Draft CR | Revised in 2703 |
| C1-082219 | Pseudo-CR on Service request procedure for CS Fallback | NTT DoCoMo | 24.301 |  | CSFB | Rel-8 | Draft CR | Revised in 2705 |
| C1-082220 | Pseudo-CR on Paging procedure for CS Fallback | NTT DoCoMo | 24.301 |  | CSFB | Rel-8 | Draft CR | Revised in 2706 |
| C1-082221 | SA1 answer to Relation between EPS Services and GPRS Services | TSG SA WG1 |  |  |  |  | LS in | Noted |
| C1-082222 | LS on Unauthenticated PS emergency calls | TSG SA WG1 |  |  |  |  | LS in | Noted |
| C1-082223 | Reply LS on CSG requirements for UTRA/E-UTRA | TSG SA WG1 |  |  |  |  | LS in | Noted |
| C1-082224 | SA1 answer on " SAE interworking with Pre-REL8 system " | TSG SA WG1 |  |  |  |  | LS in | Noted |
| C1-082225 | LS on ODB barring categories for EPS | TSG SA WG1 |  |  |  |  | LS in | Noted |
| C1-082226 | Reply LS on Progress of eCall requirements | TSG SA WG1 |  |  |  |  | LS in | Noted |
| C1-082227 | LS on "MSG Answer to Progress of eCall requirements" | TSG SA WG1 |  |  |  |  | LS in | Noted |
| C1-082228 | SA1 answer to Support of pre-Rel-8 USIMs in EPS | TSG SA WG1 |  |  |  |  | LS in | Noted |
| C1-082229 | Ls on Adding and removing media during a multimedia service session | TSG SA WG1 |  |  |  |  | LS in | Noted |
| C1-082230 | Reply LS on Applicability of Multimedia Priority Service | TSG SA WG1 |  |  |  |  | LS in | Noted |
| C1-082231 | LS on PPAC clarifications | TSG SA WG1 |  |  |  |  | LS in | Noted |
| C1-082232 | LS on HSPA VoIP Continuity Solution | TSG RAN |  |  |  |  | LS in | Noted |
| C1-082233 | LS on decision for NW interface option for ETWS support | TSG RAN |  |  |  |  | LS in | Noted |
| C1-082234 | Response LS on UE Radio Capabilities | TSG RAN |  |  |  |  | LS in | Noted |
| C1-082235 | LS on add/remove media | TSG RAN WG5 |  |  |  |  | LS in | Noted |
| C1-082236 | LS on SDP connection information | TSG RAN WG5 |  |  |  |  | LS in | Noted |
| C1-082237 | LS on RTCP bandwidth modifiers for MTSI | TSG RAN WG5 |  |  |  |  | LS in | Noted |
| C1-082238 | Reply LS on reply LS on Paging Permission with Access Control (PPAC) | TSG RAN WG3 |  |  |  |  | LS in | Noted |
| C1-082239 | LS on Enhancements for SRNS Relocation | TSG RAN WG3 |  |  |  |  | LS in | Noted |
| C1-082240 | Reply LS on the necessity of Location Reporting procedure in S1 | TSG RAN WG3 |  |  |  |  | LS in | Noted |
| C1-082241 | LS on Data forwarding for Inter 3GPP-RAT HO from E-UTRAN to UMTS/GERAN | TSG RAN WG3 |  |  |  |  | LS in | Noted |
| C1-082242 | LS on HSPA VoIP to WCDMA/GSM CS continuity | TSG RAN WG2 |  |  |  |  | LS in | Noted |
| C1-082243 | LS on UTRA R8 hNB requirements | TSG RAN WG2 |  |  |  |  | LS in | Noted |
| C1-082244 | LS on per UE frequency restriction | TSG RAN WG2 |  |  |  |  | LS in | Noted |
| C1-082245 | Reply LS on NAS–AS interaction for dependent procedures | TSG RAN WG2 |  |  |  |  | LS in | Forwarded to CT1-55 |
| C1-082246 | LS on Connection recovery by NAS | TSG RAN WG2 |  |  |  |  | LS in | Noted |
| C1-082247 | LS on reservation of an MMEC value | TSG RAN WG2 |  |  |  |  | LS in | Noted |
| C1-082248 | Reply LS on UE specific paging DRX | TSG RAN WG2 |  |  |  |  | LS in | Noted |
| C1-082249 | Reply LS on Earthquake and Tsunami Warning System | TSG RAN WG2 |  |  |  |  | LS in | Noted |
| C1-082250 | Reply LS on S1 Overload Control and on security for service request message | TSG RAN WG2 |  |  |  |  | LS in | Noted |
| C1-082251 | LS regarding GAN Iu mode security | TSG GERAN WG2 |  |  |  |  | LS in | Noted |
| C1-082252 | LS on Latency Reduction support for non RTTI capable MSs | TSG GERAN |  |  |  |  | LS in | Noted |
| C1-082253 | Response LS on replacement of in-band tones within Group Calls | TSG GERAN |  |  |  |  | LS in | Noted |
| C1-082254 | LS on documentation of TISPAN Rel-2 in 3GPP | TSG CT |  |  |  |  | LS in | Noted |
| C1-082255 | ReplyLS on UE Radio Capabilities | TSG CT |  |  |  |  | LS in | Noted |
| C1-082256 | Reply LS on Enhancements for SRNS Relocation | TSG CT WG4 |  |  |  |  | LS in | Noted |
| C1-082257 | LS on CAT in the 3GPP CS domain | TSG CT WG4 |  |  |  |  | LS in | Forwarded to CT1-55 |
| C1-082258 | LS on CT impacts for eCALL Data WI | TSG CT WG4 |  |  |  |  | LS in | Noted |
| C1-082259 | LS on “Changes to the format of TMGI” | TSG CT WG4 |  |  |  |  | LS in | Noted |
| C1-082260 | LS on CT-wide WID on enhancement of multimedia interworking between IM CN subsystem and Circuit Switched network | TSG CT WG3 |  |  |  |  | LS in | Noted |
| C1-082261 | LS on Rejection of TFT filters | TSG CT WG3 |  |  |  |  | LS in | Noted |
| C1-082262 | LS to 3GPP CT3, CT4, CT1, SA1 and SA2 status on Overlap Work | ETSI TISPAN WG3 |  |  |  |  | LS in | Noted |
| C1-082263 | Correction on identifiers distinguishing the dialog | Alcatel-Lucent / Keith Drage | 24.229 | 2311 | IMS-CCR | Rel-5 | CR | Revised in 2605 |
| C1-082264 | Correction on identifiers distinguishing the dialog | Alcatel-Lucent / Keith Drage | 24.229 | 2312 | IMS-CCR | Rel-6 | CR | Revised in 2606 |
| C1-082265 | Introduction of terms "multimedia telephony participant" and "multimedia telephony application server" | Alcatel-Lucent / Keith Drage | 24.173 | 0053 | MTSI | Rel-7 | CR | Revised in 2618 |
| C1-082266 | Introduction of terms "multimedia telephony participant" and "multimedia telephony application server" | Alcatel-Lucent / Keith Drage | 24.173 | 0054 | MTSI | Rel-8 | CR | Revised in 2619 |
| C1-082267 | Addition of AVPF support and SDP capability negotiation mechanism | Alcatel-Lucent / Keith Drage | 24.229 | 2313 | IMSProtoc | Rel-7 | CR | Agreed |
| C1-082268 | Addition of AVPF support and SDP capability negotiation mechanism | Alcatel-Lucent / Keith Drage | 24.229 | 2314 | IMSProtoc | Rel-8 | CR | Agreed |
| C1-082269 | Profile corrections for outbound | Alcatel-Lucent / Keith Drage | 24.229 | 2315 | FBI-pcbl | Rel-7 | CR | Agreed |
| C1-082270 | Profile corrections for outbound | Alcatel-Lucent / Keith Drage | 24.229 | 2316 | FBI-pcbl | Rel-8 | CR | Agreed |
| C1-082271 | Summary of current IETF documents on SIPPING | Alcatel-Lucent / Keith Drage |  |  |  |  | INFO | Noted |
| C1-082272 | Summary of current IETF documents on SIP | Alcatel-Lucent / Keith Drage |  |  |  |  | INFO | Noted |
| C1-082273 | Summary of current IETF documents on MMUSIC | Alcatel-Lucent / Keith Drage |  |  |  |  | INFO | Noted |
| C1-082274 | Summary of current IETF documents on SIMPLE | Alcatel-Lucent / Keith Drage |  |  |  |  | INFO | Noted |
| C1-082275 | Summary of current IETF documents on XCON | Alcatel-Lucent / Keith Drage |  |  |  |  | INFO | Noted |
| C1-082276 | Summary of current IETF documents on GEOPRIV | Alcatel-Lucent / Keith Drage |  |  |  |  | INFO | Noted |
| C1-082277 | Summary of current IETF documents on ECRIT | Alcatel-Lucent / Keith Drage |  |  |  |  | INFO | Noted |
| C1-082278 | Summary of current IETF documents on MEDIACTRL | Alcatel-Lucent / Keith Drage |  |  |  |  | INFO | Noted |
| C1-082279 | Summary of current IETF documents on BLISS | Alcatel-Lucent / Keith Drage |  |  |  |  | INFO | Noted |
| C1-082280 | CR to 24.301: Completion of timer T3402 procedures | Alcatel-Lucent / Keith Drage | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2580 |
| C1-082281 | CR to 24.301: Download of timer T3402 | Alcatel-Lucent / Keith Drage | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2581 |
| C1-082282 | CR to 24.301: Completion of timer T3411 procedures | Alcatel-Lucent / Keith Drage | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082283 | Annex K editorial changes | Alcatel-Lucent / Keith Drage | 24.229 | 2317 | IMSProtoc2 | Rel-8 | CR | Withdrawn |
| C1-082284 | Removal of redundant references | Alcatel-Lucent / Keith Drage | 24.141 | 0094 | REDOC_3GPP2 | Rel-8 | CR | Agreed |
| C1-082285 | Roaming restriction issue with causes #13 and #15 | Alcatel-Lucent / Bruno Landais |  |  |  |  | Discussion | Revised in 2539 |
| C1-082286 | PPAC_UE behaviour (For UTRAN) | NTT DoCoMo |  |  |  |  | Discussion | Noted |
| C1-082287 | PPAC for UTRAN:introduction | NTT DoCoMo | 24.008 | 1196 | PPACR-CT1 | Rel-8 | CR | Revised in 2645 |
| C1-082288 | PPAC for UTRAN:general_mobility_management | NTT DoCoMo | 24.008 | 1197 | PPACR-CT1 | Rel-8 | CR | Withdrawn |
| C1-082289 | PPAC for UTRAN:follow-on request parameters | NTT DoCoMo | 24.008 | 1198 | PPACR-CT1 | Rel-8 | CR | Withdrawn |
| C1-082290 | PPAC for UTRAN:abnormal_cases | NTT DoCoMo | 24.008 | 1199 | PPACR-CT1 | Rel-8 | CR | Withdrawn |
| C1-082291 | Discussion about re-connection problem(R2-082895) | NTT DoCoMo |  |  |  |  | Discussion | Noted |
| C1-082292 | Service Request Modification for Connection Recovery | NTT DoCoMo | 24.301 |  | SAES | Rel-8 | Draft CR | Postponed |
| C1-082293 | TAU with active flag for Connection Recovery | NTT DoCoMo | 24.301 |  | SAES | Rel-8 | Draft CR | Postponed |
| C1-082294 | Modification of Service Request for Connection Recovery | NTT DoCoMo | 24.008 | 1200 | TEI8/SAES | Rel-8 | CR | Postponed |
| C1-082295 | Discussion on requirements for USIM from CT1 point of view | NTT DoCoMo |  |  |  |  | Discussion | Noted |
| C1-082296 | Proposal of normative annex which describes about newly introduced EPS parameters | NTT DoCoMo | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2586 |
| C1-082297 | Pseudo-CR on miscellaneous cleanups and corrections to the reference version | Ericsson, Nortel | 24.647 |  | REDOC_TIS-C1 | Rel-8 | Draft CR | Agreed |
| C1-082298 | Correction of reference | Ericsson / Atle | 24.605 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082299 | Correction of minors mistakes in signalling flows | Ericsson / Atle | 24.606 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082300 | Removal of normative statements in NOTEs | Ericsson / Atle | 24.607 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082301 | Correction of Activation/deactivation of HOLD | Ericsson / Atle | 24.610 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082302 | Removal of text from voided subclause | Ericsson / Atle | 24.616 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082303 | Editorial fixes for the flows | Ericsson / Atle | 24.628 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082304 | Removal of normative statement in a NOTE | Ericsson / Atle | 24.629 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082305 | Alignment of user configuration | Ericsson / Atle | 24.654 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Revised in 2741 |
| C1-082306 | Pseudo-CR on miscellaneous cleanups and corrections to the reference version | Ericsson / Atle | 24.642 |  | CCBS-CCNR | Rel-8 | Draft CR | Revised in 2632 |
| C1-082307 | Pseudo-CR on miscellaneous cleanups and corrections to the reference version | Ericsson / Atle | 24.615 |  | CW-IMS | Rel-8 | Draft CR | Agreed |
| C1-082308 | Adding and extending AT-commands to support touch screen functions | AT&T, LG, Spirent | 27.007 | 0159 | TEI8 | Rel-8 | CR | Revised in 2681 |
| C1-082309 | Setting of display resolution and scren orientation for touch screen functions | AT&T, LG, Spirent | 27.007 | 0160 | TEI8 | Rel-8 | CR | Revised in 2682 |
| C1-082310 | Reference version TS 24.304 v0.4.0 | Motorola |  |  |  |  | TS | Noted |
| C1-082311 | MIPv4 Security Aspects | Motorola | 24.304 |  | SAES | Rel-8 | Draft CR | Revised in 2686 |
| C1-082312 | MIPv4 multiple PDN connectivity | Motorola | 24.304 |  | SAES | Rel-8 | Draft CR | Revised in 2687 |
| C1-082313 | Correction to the communication diversion service | LM Ericsson | 24.504 | 0003 | MAINT_R1 | Rel-8 | CR | Revised in 2739 |
| C1-082314 | Clarification of abnormal handling of de-registration | LM Ericsson | 24.229 | 2318 | IMSProtoc2 | Rel-8 | CR | Revised in 2629 |
| C1-082315 | Network requirements for OIP and OIR | Nokia Siemens Networks | 24.607 | 0002 | REDOC_TIS-C1 | Rel-8 | CR | Revised in 2742 |
| C1-082316 | Tidyup xsd | Nokia Siemens Networks | 24.623 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Revised in 2743 |
| C1-082317 | Flow for ICS Registration | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Revised in 2596 |
| C1-082318 | Registration procedure for ICS | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Revised in 2597 |
| C1-082319 | MSC as IMS functional entity | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Revised in 2598 |
| C1-082320 | Subscription to the reg event package | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Revised in 2599 |
| C1-082321 | Reregistration procedure for ICS | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Revised in 2600 |
| C1-082322 | Deregistration procedures for ICS | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Agreed |
| C1-082323 | Pseudo-CR on Option C for CSG deployments | Telecom Italia |  |  |  |  | Draft CR | Revised in 2559 |
| C1-082324 | Support of Direct Ethernet access as IP-CAN | Orange | 24.229 | 2319 | IMS_Corp | Rel-8 | CR | Agreed |
| C1-082325 | Support of Direct Ethernet access as IP-CAN |  | 24.503 | 0017 | IMS_Corp | Rel-8 | CR | Postponed |
| C1-082326 | Delivering Request-URI to UE managing several terminals |  | 24.503 | 0018 | IMS_Corp | Rel-8 | CR | Postponed |
| C1-082327 | Correction of terminology | Research in Motion | 24.604 | 0002 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082328 | Correction of notification service activation | Research in Motion | 24.404 | 0004 | MAINT_R1 | Rel-7 | CR | Postponed |
| C1-082329 | Correction of notification service activation | Research in Motion | 24.504 | 0004 | MAINT_R1 | Rel-8 | CR | Postponed |
| C1-082330 | Correction of notification service activation | Research in Motion | 24.604 | 0003 | MAINT_R1 | Rel-8 | CR | Revised in 2731 |
| C1-082331 | Correction of subscription options | Research in Motion | 24.404 | 0005 | MAINT_R1 | Rel-7 | CR | Revised in 2732 |
| C1-082332 | Correction of subscription options | Research in Motion | 24.504 | 0005 | MAINT_R1 | Rel-8 | CR | Revised in 2733 |
| C1-082333 | Correction of subscription options | Research in Motion | 24.604 | 0004 | MAINT_R1 | Rel-8 | CR | Revised in 2734 |
| C1-082334 | Correction to emergency service request | Research in Motion | 24.229 | 2320 | EMC1 | Rel-7 | CR | Postponed |
| C1-082335 | Correction to emergency service request | Research in Motion | 24.229 | 2321 | EMC1 | Rel-8 | CR | Postponed |
| C1-082336 | Flexible concatenation of ESM messages during attach | Panasonic |  |  |  |  | Discussion | Postponed |
| C1-082337 | P-CR: Flexible concatenation of ESM messages during attach | Panasonic | 24.301 |  | SAES | Rel-8 | Draft CR | not handled |
| C1-082338 | Access Network Identity in TS 24.302 | Nokia Siemens networks, Nokia |  |  |  |  | Draft CR | Revised in 2688 |
| C1-082339 | Clarification of UE requested PDN disconnection procedure | ETRI | 24.301 |  | SAES | Rel-8 | Draft CR | Withdrawn |
| C1-082340 | Clarification of UE requested bearer resource release procedure | ETRI | 24.301 |  | SAES | Rel-8 | Draft CR | Withdrawn |
| C1-082341 | Deletion of unnecessary usage of announcement | NTT | 24.428 | 0002 | MAINT_R1 | Rel-7 | CR | Agreed |
| C1-082342 | Deletion of unnecessary usage of announcement | NTT | 24.528 | 0002 | MAINT_R1 | Rel-8 | CR | Agreed |
| C1-082343 | Deletion of unnecessary usage of announcement | NTT | 24.628 | 0002 | MAINT_R1 | Rel-8 | CR | Agreed |
| C1-082344 | Value of "No reply timer" for CDIV | NTT | 24.404 | 0006 | MAINT_R1 | Rel-7 | CR | Revised in 2735 |
| C1-082345 | Value of "No reply timer" for CDIV | NTT | 24.504 | 0006 | MAINT_R1 | Rel-8 | CR | Revised in 2736 |
| C1-082346 | Value of "No reply timer" for CDIV | NTT | 24.604 | 0005 | MAINT_R1 | Rel-8 | CR | Revised in 2737 |
| C1-082347 | Avoidance of mobility management signalling for eCall only terminals | Qualcomm Europe | 24.008 | 1189 | EData | Rel-8 | CR | Revised in 2644 |
| C1-082348 | Support of expedited location updating for an eCall only UE | Qualcomm Europe | 24.008 | 1192 | EData | Rel-8 | CR | Postponed |
| C1-082349 | Allow Multiple Registrations in Rel 8 | Qualcomm Europe/Roozbeh | 24.229 | 2177 | IMSProtoc2 | Rel-8 | CR | Postponed |
| C1-082350 | Add Timestamp in Register Request | Qualcomm Europe/Roozbeh | 24.229 | 2178 | REDOC_3GPP2 | Rel-8 | CR | Revised in 2745 |
| C1-082351 | MTU signalling over NAS | Qualcomm Europe | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2587 |
| C1-082352 | Architecture for Access Control Mechanisms for CSG Cells | Qualcomm Europe |  |  |  |  | Discussion | late document |
| C1-082353 | Impact of CSG Access Control on NAS Procedures | Qualcomm Europe | 24.301 |  | SAE | Rel-8 | Draft CR | Postponed |
| C1-082354 | On mapping between PDP context and EPS bearer context | Qualcomm Europe | 24.301 |  | SAE | Rel-8 | Draft CR | Postponed |
| C1-082355 | Paging in Mixed Deployments | Qualcomm Europe | 24.301 |  | SAE | Rel-8 | Draft CR | Postponed |
| C1-082356 | Registration in Mixed Deployments | Qualcomm Europe | 24.301 |  | SAE | Rel-8 | Draft CR | Withdrawn |
| C1-082357 | Update of security header | Qualcomm Europe | 24.301 |  | SAE | Rel-8 | Draft CR | late document |
| C1-082358 | Inclusion of R8 QoS in ESM messages | Qualcomm Europe | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2588 |
| C1-082359 | QoS parameters for the UE init ESM procedures | Qualcomm Europe | 24.301 |  | SAE | Rel-8 | Draft CR | late document |
| C1-082360 | Use DNS for ANDSF selection | Qualcomm Europe | 24.302 |  | SAE | Rel-8 | Draft CR | Postponed |
| C1-082361 | Definition of HA APN for HA discovery | Qualcomm Europe | 24.303 |  | SAE | Rel-8 | Draft CR | Revised in 2697 |
| C1-082362 | Clarifications on values and error codes in BU and BA | Qualcomm Europe | 24.303 |  | SAE | Rel-8 | Draft CR | Revised in 2698 |
| C1-082363 | Normative annex for information elements in each signalling message | Qualcomm Europe | 24.303 |  | SAE | Rel-8 | Draft CR | late document |
| C1-082364 | Clarification on HoA and HNP assignment | Qualcomm Europe | 24.303 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082365 | Clarification on DSMIPv6 and PMIPv6 interactions | Qualcomm Europe | 24.303 |  | SAE | Rel-8 | Draft CR | Revised in 2699 |
| C1-082366 | HA discovery mechanisms and respective applicability scenarios | Qualcomm Europe | 24.303 |  | SAE | Rel-8 | Draft CR | Revised in 2700 |
| C1-082367 | Encoding of the target PDN information in IKEv2 | Qualcomm Europe | 24.303 |  | SAE | Rel-8 | Draft CR | Postponed |
| C1-082368 | Clarification on the usage of F flag in BA | Qualcomm Europe | 24.303 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082369 | Resource allocation based on session information in SDP offer at the terminating network | Qualcomm Europe |  |  |  |  | Discussion | Noted |
| C1-082370 | P-CSCF notification of non UE detectable emergency calls | Qualcomm Europe |  |  |  |  | Discussion | Noted |
| C1-082371 | Identifying PSAP callbacks | Qualcomm Europe |  |  |  |  | Discussion | Noted |
| C1-082372 | Multiple registration | Qualcomm Europe |  |  |  |  | Discussion | Noted |
| C1-082373 | Removal of E-IMPU | Qualcomm Europe | 24.229 | 2322 | IMSprotoc2 | Rel-8 | CR | late document |
| C1-082374 | Update outbound reference | Qualcomm Europe | 24.229 | 2323 | IMSprotoc2 | Rel-8 | CR | Revised in 2626 |
| C1-082375 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.173 | 0055 | REDOC_3GPP2 | Rel-8 | CR | Revised in 2746 |
| C1-082376 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.604 | 0006 | REDOC_3GPP2 | Rel-8 | CR | Revised in 2747 |
| C1-082377 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.607 | 0003 | REDOC_3GPP2 | Rel-8 | CR | Revised in 2748 |
| C1-082378 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.608 | 0001 | REDOC_3GPP2 | Rel-8 | CR | Revised in 2749 |
| C1-082379 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.611 | 0001 | REDOC_3GPP2 | Rel-8 | CR | Revised in 2750 |
| C1-082380 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.654 | 0002 | REDOC_3GPP2 | Rel-8 | CR | Revised in 2751 |
| C1-082381 | Miscellaneous clean-up corrections | Qualcomm Europe | 24.610 | 0002 | REDOC-TIS_C1 | Rel-8 | CR | Revised in 2744 |
| C1-082382 | Introduction of IMC in support of common IMS | Qualcomm Europe | 24.229 | 2324 | REDOC_3GPP2 | Rel-8 | CR | Postponed |
| C1-082383 | Role of UE in registration | Qualcomm Europe | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Revised in 2667 |
| C1-082384 | Role of UE in origination and termination | Qualcomm Europe | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Revised in 2668 |
| C1-082385 | Role of UE in PS-PS session continuity | Qualcomm Europe | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Revised in 2669 |
| C1-082386 | TS 24.642 CCBS/NR proposal for signalling flow | Deutsche Telekom |  |  |  |  | Draft CR | Revised in 2543 |
| C1-082387 | TS 24.615 CW proposal for signalling flow | Deutsche Telekom |  |  |  |  | Draft CR | Revised in 2661 |
| C1-082388 | Discussion on specific SIP error response for different S-CSCF assignment | Huawei |  |  |  |  | Discussion | Noted |
| C1-082389 | Error Response for Different S-CSCF Assignment | Huawei | 24.229 | 2325 | IMSProtoc2 | Rel-8 | CR | Revised in 2628 |
| C1-082390 | Updated WID for IMS Service Continuity Stage3 | Huawei |  |  |  |  | WID | Revised in 2670 |
| C1-082391 | TS 24.237 V0.1.1 | Huawei |  |  |  |  | TS | Noted |
| C1-082392 | Cleanup of TS 24.237 | Huawei | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Revised in 2671 |
| C1-082393 | Roles for registration in IMS | Huawei | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Revised in 2672 |
| C1-082394 | Introduction for signalling flows | Huawei | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Agreed |
| C1-082395 | Signalling flows for CS call origination | Huawei | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Revised in 2676 |
| C1-082396 | Signalling flows for CS call termination | Huawei | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Revised in 2677 |
| C1-082397 | On temporary mobile identity handling at Intersystem change to 2G/3G for supporting ISR | Vodafone |  |  |  |  | Discussion | Noted |
| C1-082398 | Temporary mobile identity handling at Intersystem change to 2G/3G for supporting ISR | Vodafone | 24.801 |  | SAES | Rel-8 | Draft CR | Revised in 2658 |
| C1-082399 | Sub-states update | Vodafone | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2589 |
| C1-082400 | Latest version of TS24.259 | Vodafone |  |  |  |  | INFO | Noted |
| C1-082401 | On using XCAP for PNM | Vodafone |  |  |  |  | Discussion | Noted |
| C1-082402 | PNM XML schema update | Vodafone | 24.259 |  | PNM | Rel-8 | Draft CR | Revised in 2637 |
| C1-082403 | XCAP for PN configuration | Vodafone | 24.259 |  | PNM | Rel-8 | Draft CR | Revised in 2638 |
| C1-082404 | Trust relationship detection | Ericsson | 24.302 |  | SAES | Rel-8 | Draft CR | Withdrawn |
| C1-082405 | Overview on Overlap signalling an the resuming changes | Deutsche Telekom, T-Mobile |  |  |  |  | TD | Noted |
| C1-082406 | ANNEX N for Overlap Signalling | Deutsche Telekom, T-Mobile | 24.229 | 2326 | Overlap | Rel-8 | CR | Postponed |
| C1-082407 | Reference version of TR 24.801, v 1.0.0 | Nokia Siemens Networks |  |  |  |  | TR | Noted |
| C1-082408 | Reference version of TS 24.301, v 0.3.0 | Nokia Siemens Networks |  |  |  |  | TS | Noted |
| C1-082409 | Definition of the Service Request message. | Nokia Siemens Networks | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2633 |
| C1-082410 | Coding of the Attach result and Attach type information element | Nokia Siemens Networks | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2634 |
| C1-082411 | Coding of the TAI information element | Nokia Siemens Networks | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2635 |
| C1-082412 | Coding of the PDN type and PDN address information element | Nokia Siemens Networks | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2636 |
| C1-082413 | Principles of NAS COUNT and NAS sequence number handling | Nokia Siemens Networks |  |  |  |  | Discussion | Noted |
| C1-082414 | Handling of NAS COUNT and NAS sequence number | Nokia Siemens Networks | 24.301 |  | SAE | Rel-8 | Draft CR | late document |
| C1-082415 | Correction of the Detach type IE | Nokia Siemens Networks | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082416 | Detection of trusted/untrusted non-3GPP access network | Panasonic | 24.302 |  | SAES | Rel-8 | Draft CR | Revised in 2564 |
| C1-082417 | Discussion document on SDP enhancements | CableLabs, Nortel |  |  |  |  | Discussion | Noted |
| C1-082418 | [DRAFT] LS on SDP Enhancements to support resource allocation | CableLabs, Nortel |  |  |  |  | LS out | Revised in 2631 |
| C1-082419 | SDP Enhancements to support resource allocation | CableLabs, Nortel | 24.229 | 2327 | IMSProtoc2 | Rel-8 | CR | Revised in 2630 |
| C1-082420 | Annex K Updates | CableLabs | 24.229 | 2328 | PktCbl-Sec | Rel-8 | CR | Revised in 2622 |
| C1-082421 | CR 24.301: TAU in connected mode | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Postponed |
| C1-082422 | CR 24.301 : Multiple EPS bearer contexts activation | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Postponed |
| C1-082423 | CR 24.301 : Attach or TAU combined with Security Mode Control procedure | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Postponed |
| C1-082424 | CR 24.301 : UE requested PDN connectivity procedure | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2689 |
| C1-082425 | CR 24.301 : Default EPS bearer context activation not accepted by the UE | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2690 |
| C1-082426 | CR 24.301 : Dedicated EPS bearer context activation not accepted by the UE | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2718 |
| C1-082427 | CR 24.301 : EPS bearer context modification not accepted by the UE | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2719 |
| C1-082428 | Correction for IMSI detach procedure during dedicated mode | NEC/Yannick | 24.008 | 1201 | TEI8 | Rel-8 | CR | Revised in 2683 |
| C1-082429 | Clarifications for RAT usage in manual network selection mode | NEC/Yannick | 23.122 | 0121 | TEI8 | Rel-8 | CR | Agreed |
| C1-082430 | Corrections and additions to interaction between EMM and GMM following GMM unsuccessful procedures | NEC/Yannick | 24.801 |  | SAES | Rel-8 | Draft CR | Revised in 2560 |
| C1-082431 | Clarification for network initiated detach with re-attach required | NEC/Yannick | 24.301 |  | SAES | Rel-8 | Draft CR | Postponed |
| C1-082432 | Definition for EMM cause IE and updates for the handling of EMM reject causes | NEC/Yannick | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082433 | SGs interface specification | NEC/Yannick | 24.801 |  | SAES-CSFB | Rel-8 | Draft CR | Revised in 2707 |
| C1-082434 | Updated WID on stage 3 for CS Fallback in EPS | NEC/Yannick |  |  |  |  | WID | Revised in 2709 |
| C1-082435 | Proposed skeleton for new TS "Mobility Management Entity (MME) - Visitors Location Register (VLR) SGs interface specification" | NEC/Yannick |  |  |  |  | TS | Agreed |
| C1-082436 | Proposed scope for new TS "Mobility Management Entity (MME) - Visitors Location Register (VLR) SGs interface specification" | NEC/Yannick | New TS 29. |  | SAES-CSFB |  | Draft CR | Revised in 2710 |
| C1-082437 | MIH Protocol for communication between UE and ANDSF | Intel | 24.302 |  | SAE | Rel-8 | Draft CR | Revised in 2566 |
| C1-082438 | Comparison of Communication Protocols | Telcordia, Intel | 24.302 |  | SAE | Rel-8 | Draft CR | late document |
| C1-082439 | Location Information during Network Discovery | Intel | 24.302 |  | SAE | Rel-8 | Draft CR | Postponed |
| C1-082440 | WiMAX System Information from ANDSF | Intel | 24.302 |  | SAE | Rel-8 | Draft CR | Revised in 2712 |
| C1-082441 | Pseudo-CR on ICS UE termination with CS media using Gm reference point when using an enhanced MSC Server | Nortel Networks |  |  | ICSRA |  | Draft CR | Revised in 2601 |
| C1-082442 | Proposed skeleton for new TS 24.182 "IP Multimedia Subsystem (IMS) Customized Alerting Tones (CAT); Protocol specification" | Nortel Networks |  |  |  |  | Draft TS | Noted |
| C1-082443 | Pseudo-CR on stage 3 CAT scope and general description | Nortel Networks |  |  | CAT-SS |  | Draft CR | Revised in 2663 |
| C1-082444 | Pseudo-CR on CAT operational requirements | Nortel Networks |  |  | CAT-SS |  | Draft CR | Revised in 2664 |
| C1-082445 | Pseudo-CR on CAT signalling procedures | Nortel Networks |  |  | CAT-SS |  | Draft CR | Revised in 2665 |
| C1-082446 | Pseudo-CR on CAT interactions with other services | Nortel Networks |  |  | CAT-SS |  | Draft CR | Agreed |
| C1-082447 | Pseudo-CR on miscellaneous cleanups and corrections to the reference version of 24.238. | Nortel Networks, Ericsson |  |  | REDOC_3GPP2 |  | Draft CR | Agreed |
| C1-082448 | Pseudo-CR on miscellaneous cleanups and corrections to the reference version of 24.239 | Nortel Networks, Ericsson |  |  | FA |  | Draft CR | Agreed |
| C1-082449 | Pseudo-CR on AS procedures for FA service | Nortel Networks |  |  | FA |  | Draft CR | Revised in 2662 |
| C1-082450 | Pseudo-CR on Signalling flows for ICS UE origination with CS media using Gm reference point when using an MSC server (not enhanced for ICS) | Nortel Networks |  |  | ICSRA |  | Draft CR | Revised in 2602 |
| C1-082451 | Pseudo-CR on Signalling flows for termination to an ICS UE with CS media using Gm reference point when using an MSC server (not enhanced for ICS) | Nortel Networks |  |  | ICSRA |  | Draft CR | Revised in 2603 |
| C1-082452 | DSMIPv6 back home | Ericsson | 24.303 |  | SAES | Rel-8 | Draft CR | Withdrawn |
| C1-082453 | Discussion document on Correction to emergency service request | Research in Motion |  |  |  |  | Discussion | Noted |
| C1-082454 | Application level handover | Alcatel-Lucent/Milo Orsic | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Revised in 2666 |
| C1-082455 | Reference version of the TS 24.327, v0.1.1 | Orange |  |  |  |  | TS | Noted |
| C1-082456 | Attach for I-WLAN mobility: UE procedures | Orange |  |  |  |  | Draft CR | Revised in 2582 |
| C1-082457 | Attach for I-WLAN mobility: Home agent discovery | Orange |  |  |  |  | Draft CR | Revised in 2583 |
| C1-082458 | Attach for I-WLAN mobility: Home link detection | Orange |  |  |  |  | Draft CR | Revised in 2584 |
| C1-082459 | Handover from GPRS systems to 3GPP I-WLAN: UE procedures | Orange |  |  |  |  | Draft CR | Revised in 2585 |
| C1-082460 | Handover from 3GPP I-WLAN to GPRS systems: UE procedures | Orange |  |  |  |  | Draft CR | Revised in 2651 |
| C1-082461 | Handover from GPRS systems to 3GPP I-WLAN: Network procedures | Orange |  |  |  |  | Draft CR | Revised in 2652 |
| C1-082462 | Handover from 3GPP I-WLAN to GPRS systems: Network procedures | Orange |  |  |  |  | Draft CR | Revised in 2653 |
| C1-082463 | Baseline 24.292 ICS skeleton v0.1.1 | Rapporteur/Sean |  |  |  |  | DRAFT TS | Noted |
| C1-082464 | Enhancement of Filter Criteria for third party registration | Research in Motion |  |  |  |  | Discussion | Noted |
| C1-082465 | Enhancement of Filter Criteria to Include Incoming Register in Third Party Register | Research in Motion | 23.218 | 0117 | TEI-8 | Rel-8 | CR | Revised in 2659 |
| C1-082466 | Summary and Planning for IMS_Corp/NGCN Workshop | Research in Motion |  |  |  |  | Discussion | Noted |
| C1-082467 | Correction of PN access control procedure | Research in Motion | 24.259 |  | PNM | Rel-8 | Draft CR | Agreed |
| C1-082468 | Some cleanup of PNM Signalling flows | Research in Motion | 24.259 |  | PNM | Rel-8 | Draft CR | Agreed |
| C1-082469 | ANDSF indication of services supported | Research in Motion | 24.302 |  | SAE | Rel-8 | Draft CR | Postponed |
| C1-082470 | ANDSF Operator differentiated text field | Research in Motion | 24.302 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082471 | Incorporation 802.11u network discovery procedures | Research in Motion | 24.234 | 0053 | TEI8 | Rel-8 | CR | Postponed |
| C1-082472 | Implementation error of CR 0052 | Research in Motion | 24.234 | 0054 | IWLANNSP | Rel-8 | CR | Agreed |
| C1-082473 | Adding P-Debug-ID to SIP Profile Tables | Vodafone | 24.229 | 2329 | OAM8-Trace | Rel-8 | CR | Revised in 2752 |
| C1-082474 | Subscribing to the debug event package | Vodafone | 24.229 | 2330 | OAM8-Trace | Rel-8 | CR | Revised in 2753 |
| C1-082475 | Parameters for IMS Service Level Trace | Vodafone | 24.323 |  | OAM8-Trace | Rel-8 | Draft CR | Revised in 2754 |
| C1-082476 | LS on CS Fallback | RAN2 |  |  |  |  | LS in | Noted |
| C1-082477 | CSG and Idle Mode Mobility for 3G Home NodeB | Huawei |  |  |  |  | WID | Revised in 2535 |
| C1-082478 | CSG and Idle Mode Mobility for LTE Home eNodeB | Huawei |  |  |  |  | WID | Revised in 2536 |
| C1-082479 | Clarification on SDF QoS Parameters | Panasonic | 24.301 |  | SAES | Rel-8 | Draft CR | late document |
| C1-082480 | EPS bearer QoS delivery on NAS level | Panasonic | 24.301 |  | SAES | Rel-8 | Draft CR | Withdrawn |
| C1-082481 | Service Type redefinition in Service request | Panasonic | 24.301 |  | SAES | Rel-8 | Draft CR | late document |
| C1-082482 | Service Request usage in CS fallback procedures | Panasonic | 24.301 |  | SAES | Rel-8 | Draft CR | late document |
| C1-082483 | Paging Type 2 support for CS fallback | Panasonic | 24.301 |  | SAES | Rel-8 | Draft CR | late document |
| C1-082484 | Discussion on the impact of multiple PLMN identities encoded in TAI list | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2720 |
| C1-082485 | remove the FFS about "EPS bearer context status" | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082486 | Discussion on the FFS of unsuccessful TAU procedure | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2721 |
| C1-082487 | Update the description for UE requested ESM procedure | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082488 | Discussion on the impacts of ISR function | Huawei |  |  |  |  | Discussion | Noted |
| C1-082489 | Update the description of the ISR function for TR24.801 | Huawei | 24.801 |  | SAE | Rel-8 | Draft CR | Revised in 2715 |
| C1-082490 | Update the description of the ISR function for TS24.301 | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2722 |
| C1-082491 | Removed FFS about mapping GUTI to P-TMSI/RAI | Huawei | 24.801 |  | SAE | Rel-8 | Draft CR | Revised in 2716 |
| C1-082492 | The abnormal case for PDN connection procedure | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2723 |
| C1-082493 | the abnormal case for service request procedure | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2724 |
| C1-082494 | Update the description of CS fallback | Huawei | 24.801 |  | SAE | Rel-8 | Draft CR | Revised in 2704 |
| C1-082495 | NAS message related to CS fallback | Huawei | 24.801 |  | SAE | Rel-8 | Draft CR | Postponed |
| C1-082496 | Access Network Discovery and New IEEE 802.11u Interworking with External Networks | Research in Motion |  |  |  |  | Discussion | Noted |
| C1-082497 | P-CR on Abnormal cases on the network side for attach procedure | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2726 |
| C1-082498 | P-CR on Abnormal cases on the network side for TAU procedure | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2725 |
| C1-082499 | P-CR on Abnormal cases on the network side for GUTI reallocation procedure | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2727 |
| C1-082500 | P-CR on PCO request procedure | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2728 |
| C1-082501 | P-CR on Ciphered PCO transfer flag | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2729 |
| C1-082502 | P-CR on Abnormal cases for UE requested PDN disconnection procedure | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | Postponed |
| C1-082503 | P-CR on Abnormal cases for Dedicated EPS bearer context activation procedure | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | Postponed |
| C1-082504 | P-CR on Trusted and Untrusted Accesses | ZTE | 24.302 |  | SAES | Rel-8 | Draft CR | Withdrawn |
| C1-082505 | PN UE Redirection Signalling flow Update | ZTE | 24.259 |  | PNM | Rel-8 | Draft CR | Revised in 2639 |
| C1-082506 | Signalling flow for Execution of IMS conferencing via Gm | ZTE | 24.292 |  | ICSRA | Rel-8 | Draft CR | Revised in 2604 |
| C1-082507 | Discussion about ICS hold at MGCF | ZTE | 24.292 |  | ICSRA | Rel-8 | Draft CR | Noted |
| C1-082508 | LS on Rel-8 UICC parameters | NTT DoCoMo |  |  |  |  | LS out | Revised in 2713 |
| C1-082509 | Storage of EMM location information | NTT DoCoMo, NEC | 24.301 |  | SAES | Rel-8 | Draft CR | late document |
| C1-082510 | Separate ESM messages for default and dedicated bearers | Motorola |  |  |  |  | Draft CR | Agreed |
| C1-082511 | Update result and Update type information element | NSN, Motorola |  |  |  |  | Draft CR | Revised in 2702 |
| C1-082512 | Core network handling of P-Preferred-Identity and P-Asserted-Identity header for business communication | Alcatel-Lucent / Keith Drage | 24.229 | 2191 | IMS_Corp | Rel-8 | CR | Postponed |
| C1-082513 | NGCN site as a protocol entity | Alcatel-Lucent / Keith Drage | 24.229 | 2241 | IMS_Corp | Rel-8 | CR | Postponed |
| C1-082514 | EPS as IP-CAN | Alcatel-Lucent / Keith Drage | 24.229 | 2331 | SAES | Rel-8 | CR | Revised in 2680 |
| C1-082515 | CR to 24.301: Download of timer T3412 | Alcatel-Lucent / Keith Drage | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2790 |
| C1-082516 | Additional changes for private network indication | Alcatel-Lucent / Keith Drage | 24.229 | 2332 | IMS_Corp | Rel-8 | CR | late document |
| C1-082517 | Handling of NGCN site as an entity in 24.229 | Alcatel-Lucent / Keith Drage |  |  |  |  | Discussion | Postponed |
| C1-082518 | IPMS Indication in Authentication | Nokia Siemens Networks, Nokia |  |  |  |  | Discussion | Revised in 2692 |
| C1-082519 | TMSI reallocation in a location area where the UE isnt updated | Ericsson |  |  |  |  | Discussion | Noted |
| C1-082520 | P-CR on update of EPS mobility management timer on the network side | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | not handled |
| C1-082521 | TS Skeleton for ICS Protocol over USSD bearer | Huawei |  |  |  |  | TS | Revised in 2673 |
| C1-082522 | Scope for TS 24.293 | Huawei | 24.293 |  | ICSRA | Rel-8 | Draft CR | Revised in 2674 |
| C1-082523 | Discussion on the way forward for I1 protocol specification | Huawei |  |  |  |  | Discussion | Noted |
| C1-082524 | Alignment of IP-CAN specific annexes | Alcatel-Lucent / Keith Drage | 24.229 | 2333 | IMSProtoc2 | Rel-8 | CR | Revised in 2755 |
| C1-082525 | Proposed WID for CT1 aspects of SRVCC | Nokia Siemens Networks |  |  |  |  | WID | Revised in 2561 |
| C1-082526 | Proposed Update to WID for CT4 aspects of Evolved Packet System | Nokia Siemens Networks |  |  |  |  | INFO | Noted |
| C1-082527 | LS on Tracking Area Update in RRC Connected | TSG RAN WG2 |  |  |  |  | LS in | Noted |
| C1-082528 | Latest version of the Work Plan | MCC |  |  |  |  | Work Plan | to be handled by e-mail |
| C1-082529 | NGCN issues and proposed workshop | TISPAN |  |  |  |  | LS in | Noted |
| C1-082530 | Discussion on indication of keep-alive support | Ericsson |  |  |  |  | Discussion | Noted |
| C1-082531 | “Latency Reduction support for non RTTI capable MSs” | Nortel | 24.008 | 1202 | TEI7 | Rel-7 | CR | Revised in 2642 |
| C1-082532 | “Latency Reduction support for non RTTI capable MSs” | Nortel | 24.008 | 1203 | TEI7 | Rel-8 | CR | Revised in 2643 |
| C1-082533 | DISC, Administration of 3GPP Namespace Identification (NID) | CT1 Chairman |  |  |  |  | Discussion | Noted |
| C1-082534 | LS on 3GPP Namespace Identification (NID) administration | CT1 Chairman |  |  |  |  | LS out | Agreed |
| C1-082535 | CSG and Idle Mode Mobility for 3G Home NodeB | Huawei |  |  |  |  | WID | Revised in 2684 |
| C1-082536 | CSG and Idle Mode Mobility for LTE Home eNodeB | Huawei |  |  |  |  | WID | Revised in 2685 |
| C1-082537 | LS on Reply to LS S3-080489 = C4-081222 on SAE interworking with Pre-REL8 system | TSG CT WG4 |  |  |  |  | LS in | For info |
| C1-082538 | LS on E-UTRAN Identifiers | TSG RAN WG3 |  |  |  |  | LS in | Noted |
| C1-082539 | Roaming restriction issue with causes #13 and #15 | Alcatel-Lucent / Bruno Landais |  |  |  |  | Discussion | Noted |
| C1-082540 | Reply LS on IMS Emergency Registration |  |  |  |  |  | LS out | Agreed |
| C1-082541 | Reply LS on Requesting recommendations from IEEE 802.11, IEEE 802.11-08/0417r2 |  |  |  |  |  | LS out | Agreed |
| C1-082542 | Reply LS to SA1 answer to Relation between EPS Services and GPRS Services |  |  |  |  |  | LS out | Withdrawn |
| C1-082543 | TS 24.642 CCBS/NR proposal for signalling flow | Deutsche Telekom |  |  |  |  | Draft CR | Revised in 2660 |
| C1-082544 | Reply LS on add/remove media |  |  |  |  |  | LS out | Revised in 2772 |
| C1-082545 | Reply LS on SDP connection information |  |  |  |  |  | LS out | Revised in 2782 |
| C1-082546 | Reply LS on RTCP bandwidth modifiers for MTSI |  |  |  |  |  | LS out | Agreed |
| C1-082547 | LS on Enhancements for SRNS Relocation |  |  |  |  |  | LS out | Agreed |
| C1-082548 | Reply to LS on HSPA VoIP to WCDMA/GSM CS continuity |  |  |  |  |  | LS out | Agreed |
| C1-082549 | Reply LS on UTRA R8 hNB requirements | CT1 |  |  |  |  | LS out | Revised in 2799 |
| C1-082550 | Reply LS on NAS–AS interaction for dependent procedures |  |  |  |  |  | LS out | Postponed |
| C1-082551 | Reply LS on Connection recovery by NAS |  |  |  |  |  | LS out | Revised in 2800 |
| C1-082552 | Reply LS on Earthquake and Tsunami Warning System |  |  |  |  |  | LS out | Agreed |
| C1-082553 | Reply to LS on CAT in the 3GPP CS domain |  |  |  |  |  | LS out | Revised in 2805 |
| C1-082554 | Reply to LS on CS Fallback |  |  |  |  |  | LS out | Revised in 2806 |
| C1-082555 | Pseudo CR on PLMN selection, Introduction of TA | T-Mobile | 24.801 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082556 | Pseudo-CR on multi system PLMN selection | Nokia | 24.801 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082557 | Detailed pseudo CR on multi system PLMN selection | Nokia | 24.801 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082558 | LS related to 2171 |  |  |  |  |  | LS out | Revised in 2801 |
| C1-082559 | Pseudo-CR on Option C for CSG deployments | Telecom Italia |  |  |  |  | Draft CR | Revised in 2792 |
| C1-082560 | Corrections and additions to interaction between EMM and GMM following GMM unsuccessful procedures | NEC/Yannick | 24.801 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082561 | Proposed WID for CT1 aspects of SRVCC | Nokia Siemens Networks |  |  |  |  | WID | Agreed |
| C1-082562 | P-CR: Restructuring and adding procedural text to subclause 5.1 for Access Network discovery and selection | Samsung/Chen-Ho | 24.302 |  | SAES | Rel-8 | Draft CR | Revised in 2804 |
| C1-082563 | P-CR: Restructuring subclause 6.8 and adding signalling procedure text | Samsung/Chen-Ho | 24.302 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082564 | Detection of trusted/untrusted non-3GPP access network | Panasonic | 24.302 |  | SAES | Rel-8 | Draft CR | Postponed |
| C1-082565 | Communication protocol between the UE and the ANDSF | Ericsson |  |  | SAE |  | Draft CR | Agreed |
| C1-082566 | MIH Protocol for communication between UE and ANDSF | Intel | 24.302 |  | SAE | Rel-8 | Draft CR | Revised in 2793 |
| C1-082567 | Update to 24.302 Clause 6.4 /Authentication | Alcatel-Lucent / Frank Alfano | 24.302 |  | SAES-St3-CT1sec | Rel-8 | Draft CR | Agreed |
| C1-082568 | IP Mobility Mode selection | Marvell |  |  |  |  | Draft CR | Postponed |
| C1-082569 | On Multiple PDN support | Marvell |  |  |  |  | Draft CR | Agreed |
| C1-082570 | LS on SAE interworking with Pre-Rel-8 system |  |  |  |  |  | LS in | for info |
| C1-082571 | S101 mode NAS Signalling Connection | Nortel Networks | 24.301 |  | SAES |  | Draft CR | Revised in 2794 |
| C1-082572 | Pseudo-CR on optional parameters in PDN connectivity request | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082573 | Pseudo-CR on Authentication procedure abnormal cases | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082574 | Pseudo-CR on IPv6 prefix delegation | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082575 | Pseudo-CR on NAS Sequence Number Handling | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2796 |
| C1-082576 | Coding of the TAI list IE | Nokia | 24.301 |  | SAE |  | Draft CR | Revised in 2797 |
| C1-082577 | ESM information in Attach messages | Nokia | 24.301 |  | SAE |  | Draft CR | Agreed |
| C1-082578 | UE Security Capabilities IE | Alcatel-Lucent / Frank Alfano | 24.301 |  | SAES-St3-CT1sec | Rel-8 | Draft CR | Agreed |
| C1-082579 | Update of UE requested PDN connectivity procedure | Marvell |  |  |  |  | Draft CR | Agreed |
| C1-082580 | CR to 24.301: Completion of timer T3402 procedures | Alcatel-Lucent / Keith Drage | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082581 | CR to 24.301: Download of timer T3402 | Alcatel-Lucent / Keith Drage | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2791 |
| C1-082582 | Attach for I-WLAN mobility: UE procedures | Orange |  |  |  |  | Draft CR | Revised in 2647 |
| C1-082583 | Attach for I-WLAN mobility: Home agent discovery | Orange |  |  |  |  | Draft CR | Revised in 2648 |
| C1-082584 | Attach for I-WLAN mobility: Home link detection | Orange |  |  |  |  | Draft CR | Revised in 2649 |
| C1-082585 | Handover from GPRS systems to 3GPP I-WLAN: UE procedures | Orange |  |  |  |  | Draft CR | Revised in 2650 |
| C1-082586 | Proposal of normative annex which describes about newly introduced EPS parameters | NTT DoCoMo | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082587 | MTU signalling over NAS | Qualcomm Europe | 24.301 |  | SAE | Rel-8 | Draft CR | Postponed |
| C1-082588 | Inclusion of R8 QoS in ESM messages | Qualcomm Europe | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082589 | Sub-states update | Vodafone | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082590 | Reply LS on handling of local emergency calls numbers dialled whilst in IMS |  |  |  |  |  | LS out | Revised in 2675 |
| C1-082591 | Example signalling flow for CS UE origination via an MSC enhanced d for ICS where the origation MSC server enhanced for ICS supports codec negotiation. | LM Ericsson | 24.292 |  | ICSRA | Rel-8 | Draft CR | Revised in 2756 |
| C1-082592 | Example signalling flow for CS UE origination via an MSC enhanced for ICS where the origation MSC server enhanced for ICS does not supports codec negotiation. | LM Ericsson | 24.292 |  | ICSRA | Rel-8 | Draft CR | Revised in 2757 |
| C1-082593 | Example flow for CS UE termination via MSC Server enhanced for ICS (with codec negotiation) | Mavenir | 24.292 |  | ICSRA | Rel-8 | Draft CR | Revised in 2758 |
| C1-082594 | Example flow for CS UE termination via MSC Server enhanced for ICS (without codec negotiation) | Mavenir | 24.292 |  | ICSRA | Rel-8 | Draft CR | Withdrawn |
| C1-082595 | Example flow for CS UE termination, not registered in IMS | Mavenir | 24.292 |  | ICSRA | Rel-8 | Draft CR | Revised in 2759 |
| C1-082596 | Flow for ICS Registration | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Revised in 2760 |
| C1-082597 | Registration procedure for ICS | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Revised in 2761 |
| C1-082598 | MSC as IMS functional entity | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Agreed |
| C1-082599 | Subscription to the reg event package | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Agreed |
| C1-082600 | Reregistration procedure for ICS | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Agreed |
| C1-082601 | Pseudo-CR on ICS UE termination with CS media using Gm reference point when using an enhanced MSC Server | Nortel Networks |  |  | ICSRA |  | Draft CR | Revised in 2762 |
| C1-082602 | Pseudo-CR on Signalling flows for ICS UE origination with CS media using Gm reference point when using an MSC server (not enhanced for ICS) | Nortel Networks |  |  | ICSRA |  | Draft CR | Revised in 2763 |
| C1-082603 | Pseudo-CR on Signalling flows for termination to an ICS UE with CS media using Gm reference point when using an MSC server (not enhanced for ICS) | Nortel Networks |  |  | ICSRA |  | Draft CR | Revised in 2764 |
| C1-082604 | Signalling flow for Execution of IMS conferencing via Gm | ZTE | 24.292 |  | ICSRA | Rel-8 | Draft CR | not handled |
| C1-082605 | Correction on identifiers distinguishing the dialog | Alcatel-Lucent / Keith Drage | 24.229 | 2311 | IMS-CCR | Rel-5 | CR | Agreed |
| C1-082606 | Correction on identifiers distinguishing the dialog | Alcatel-Lucent / Keith Drage | 24.229 | 2312 | IMS-CCR | Rel-6 | CR | Agreed |
| C1-082607 | Removal of draft-ietf-simple-common-policy-caps | LM Ericsson | 24.141 | 0092 | PRESNC | Rel-8 | CR | Revised in 2774 |
| C1-082608 | VOID |  |  |  |  |  | Information |  |
| C1-082609 | Annex A: Correction of SDP connection information | LM Ericsson | 24.229 | 2304 | IMS2 | Rel-6 | CR | Agreed |
| C1-082610 | Annex A: Correction of SDP connection information | LM Ericsson | 24.229 | 2305 | IMS2 | Rel-7 | CR | Agreed |
| C1-082611 | Annex A: Correction of SDP connection information | LM Ericsson | 24.229 | 2306 | IMS2 | Rel-8 | CR | Agreed |
| C1-082612 | Annex A: Correction of SDP connection information | Ericsson | 24.403 | 0010 | IMS2 | Rel-7 | CR | Agreed |
| C1-082613 | Annex A: Correction of SDP connection information | Ericsson | 24.503 | 0019 | IMS2 | Rel-8 | CR | Agreed |
| C1-082614 | Removal of draft-ietf-simple-pres-policy-caps | Ericsson | 24.430 | 0001 | IMS2 | Rel-7 | CR | Withdrawn |
| C1-082615 | Removal of draft-ietf-simple-pres-policy-caps | Ericsson | 24.430 | 0002 | PRESNC | Rel-8 | CR | Withdrawn |
| C1-082616 | Removal of draft-ietf-simple-pres-policy-caps | Ericsson | 24.141 | 0095 | PRESNC | Rel-6 | CR | Revised in 2775 |
| C1-082617 | Removal of draft-ietf-simple-pres-policy-caps | Ericsson | 24.141 | 0096 | PRESNC | Rel-7 | CR | Revised in 2776 |
| C1-082618 | Introduction of terms "multimedia telephony participant" and "multimedia telephony application server" | Alcatel-Lucent / Keith Drage | 24.173 | 0053 | MTSI | Rel-7 | CR | Agreed |
| C1-082619 | Introduction of terms "multimedia telephony participant" and "multimedia telephony application server" | Alcatel-Lucent / Keith Drage | 24.173 | 0054 | MTSI | Rel-8 | CR | Agreed |
| C1-082620 | Correction of DHCP reference | LM Ericsson | 24.229 | 2301 | IMSProtoc2 | Rel-8 | CR | Agreed |
| C1-082621 | Add reference to draft-dotson-sip-mutual-auth | Ericsson/Sean | 24.229 | 2299 | PktCbl-Sec | Rel-8 | CR | Agreed |
| C1-082622 | Annex K Updates | CableLabs | 24.229 | 2328 | PktCbl-Sec | Rel-8 | CR | Agreed |
| C1-082623 | Cleanup of P-CSCF procedures for inclusion of "tls-yes" and "tls-pending" | Ericsson/Sean | 24.229 | 2297 | PktCbl-Sec | Rel-8 | CR | Agreed |
| C1-082624 | Target refresh correction | LM Ericsson | 24.229 | 2307 | IMSProtoc2 | Rel-8 | CR | Postponed |
| C1-082625 | Backward compability issue with P-Access-Network-Info ABNF extension | LM Ericsson | 24.229 | 2308 | IMSProtoc2 | Rel-8 | CR | Agreed |
| C1-082626 | Update outbound reference | Qualcomm Europe | 24.229 | 2323 | FBI-Pcbl | Rel-8 | CR | Agreed |
| C1-082627 | Update outbound reference | Qualcomm Europe | 24.229 | 2334 | FBI-Pcbl | Rel-7 | CR | Agreed |
| C1-082628 | Error Response for Different S-CSCF Assignment | Huawei | 24.229 | 2325 | IMSProtoc2 | Rel-8 | CR | Revised in 2770 |
| C1-082629 | Clarification of abnormal handling of de-registration | LM Ericsson | 24.229 | 2318 | IMSProtoc2 | Rel-8 | CR | Postponed |
| C1-082630 | SDP Enhancements to support resource allocation | CableLabs, Nortel | 24.229 | 2327 | IMSProtoc2 | Rel-8 | CR | Postponed |
| C1-082631 | [DRAFT] LS on SDP Enhancements to support resource allocation | CableLabs, Nortel |  |  |  |  | LS out | Revised in 2773 |
| C1-082632 | Pseudo-CR on miscellaneous cleanups and corrections to the reference version | Ericsson / Atle | 24.642 |  | CCBS-CCNR | Rel-8 | Draft CR | Agreed |
| C1-082633 | Definition of the Service Request message. | Nokia Siemens Networks | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082634 | Coding of the Attach result and Attach type information element | Nokia Siemens Networks | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082635 | Coding of the TAI information element | Nokia Siemens Networks | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082636 | Coding of the PDN type and PDN address information element | Nokia Siemens Networks | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082637 | PNM XML schema update | Vodafone | 24.259 |  | PNM | Rel-8 | Draft CR | Agreed |
| C1-082638 | XCAP for PN configuration | Vodafone | 24.259 |  | PNM | Rel-8 | Draft CR | Agreed |
| C1-082639 | PN UE Redirection Signalling flow Update | ZTE | 24.259 |  | PNM | Rel-8 | Draft CR | not handled |
| C1-082640 | Stage 2 alignment related to Network bearer control | Ericsson | 24.008 | 1194 | TEI7 | Rel-7 | CR | Postponed |
| C1-082641 | Stage 2 alignment related to Network bearer control | Ericsson | 24.008 | 1195 | TEI7 | Rel-8 | CR | Postponed |
| C1-082642 | “Latency Reduction support for non RTTI capable MSs” | Nortel | 24.008 | 1202 | TEI7 | Rel-7 | CR | Agreed |
| C1-082643 | “Latency Reduction support for non RTTI capable MSs” | Nortel | 24.008 | 1203 | TEI7 | Rel-8 | CR | Agreed |
| C1-082644 | Avoidance of mobility management signalling for eCall only terminals | Qualcomm Europe | 24.008 | 1189 | EData | Rel-8 | CR | Revised in 2711 |
| C1-082645 | PPAC for UTRAN:introduction | NTT DoCoMo | 24.008 | 1196 | PPACR-CT1 | Rel-8 | CR | Withdrawn |
| C1-082646 | Reply LS on " SAE interworking with Pre-REL8 system " | TSG SA WG3 |  |  |  |  | LS in | Forwarded to CT1-55 |
| C1-082647 | Attach for I-WLAN mobility: UE procedures | Orange |  |  |  |  | Draft CR | Agreed |
| C1-082648 | Attach for I-WLAN mobility: Home agent discovery | Orange |  |  |  |  | Draft CR | Agreed |
| C1-082649 | Attach for I-WLAN mobility: Home link detection | Orange |  |  |  |  | Draft CR | Agreed |
| C1-082650 | Handover from GPRS systems to 3GPP I-WLAN: UE procedures | Orange |  |  |  |  | Draft CR | Agreed |
| C1-082651 | Handover from 3GPP I-WLAN to GPRS systems: UE procedures | Orange |  |  |  |  | Draft CR | Agreed |
| C1-082652 | Handover from GPRS systems to 3GPP I-WLAN: Network procedures | Orange |  |  |  |  | Draft CR | Agreed |
| C1-082653 | Handover from 3GPP I-WLAN to GPRS systems: Network procedures | Orange |  |  |  |  | Draft CR | Agreed |
| C1-082654 | Chages to CBS for the realisation of ETWS. | NTT DoCoMo | 23.041 | 0018 | ETWS | Rel-8 | CR | Revised in 2812 |
| C1-082655 | Additions to the protocol aspects of CBS for the realisation of ETWS | NTT DoCoMo | 23.041 | 0019 | ETWS | Rel-8 | CR | Revised in 2813 |
| C1-082656 | Changes to the radio message format aspect of CBS for the realisation of ETWS | NTT DoCoMo | 23.041 | 0020 | ETWS | Rel-8 | CR | Revised in 2814 |
| C1-082657 | Introduction of GIBA (Early IMS) procedures | Ericsson/Sean | 24.229 | 2298 | SEC-IMS | Rel-8 | CR | Agreed |
| C1-082658 | Temporary mobile identity handling at Intersystem change to 2G/3G for supporting ISR | Vodafone | 24.801 |  | SAES | Rel-8 | Draft CR | Revised in 2717 |
| C1-082659 | Enhancement of Filter Criteria to Include Incoming Register in Third Party Register | Research in Motion | 23.218 | 0117 | TEI-8 | Rel-8 | CR | Postponed |
| C1-082660 | TS 24.642 CCBS/NR proposal for signalling flow | Deutsche Telekom |  |  |  |  | Draft CR | Agreed |
| C1-082661 | TS 24.615 CW proposal for signalling flow | Deutsche Telekom |  |  |  |  | Draft CR | Revised in 2780 |
| C1-082662 | Pseudo-CR on AS procedures for FA service | Nortel Networks |  |  | FA |  | Draft CR | Agreed |
| C1-082663 | Pseudo-CR on stage 3 CAT scope and general description | Nortel Networks |  |  | CAT-SS |  | Draft CR | Agreed |
| C1-082664 | Pseudo-CR on CAT operational requirements | Nortel Networks |  |  | CAT-SS |  | Draft CR | Agreed |
| C1-082665 | Pseudo-CR on CAT signalling procedures | Nortel Networks |  |  | CAT-SS |  | Draft CR | Revised in 2771 |
| C1-082666 | Application level handover | Alcatel-Lucent/Milo Orsic | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Agreed |
| C1-082667 | Role of UE in registration | Qualcomm Europe | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Agreed |
| C1-082668 | Role of UE in origination and termination | Qualcomm Europe | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Agreed |
| C1-082669 | Role of UE in PS-PS session continuity | Qualcomm Europe | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Agreed |
| C1-082670 | Updated WID for IMS Service Continuity Stage3 | Huawei |  |  |  |  | WID | Agreed |
| C1-082671 | Cleanup of TS 24.237 | Huawei | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Agreed |
| C1-082672 | Roles for registration in IMS | Huawei | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Agreed |
| C1-082673 | TS Skeleton for ICS Protocol over USSD bearer | Huawei |  |  |  |  | TS | Revised in 2765 |
| C1-082674 | Scope for TS 24.293 | Huawei | 24.293 |  | ICSRA | Rel-8 | Draft CR | Agreed |
| C1-082675 | Reply LS on handling of local emergency calls numbers dialled whilst in IMS |  |  |  |  |  | LS out | Revised in 2679 |
| C1-082676 | Signalling flows for CS call origination | Huawei | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Revised in 2766 |
| C1-082677 | Signalling flows for CS call termination | Huawei | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Revised in 2767 |
| C1-082678 | Reply LS on “Security Issues with NGCN connection” and “NGCN issues and proposed workshop” | TSG SA WG3 |  |  |  |  | LS in | Noted |
| C1-082679 | Reply LS on handling of local emergency calls numbers dialled whilst in IMS |  |  |  |  |  | LS out | Revised in 2730 |
| C1-082680 | EPS as IP-CAN | Alcatel-Lucent / Keith Drage | 24.229 | 2331 | SAES | Rel-8 | CR | Postponed |
| C1-082681 | Adding and extending AT-commands to support touch screen functions | AT&T, LG, Spirent | 27.007 | 0159 | TEI8 | Rel-8 | CR | Agreed |
| C1-082682 | Setting of display resolution and scren orientation for touch screen functions | AT&T, LG, Spirent | 27.007 | 0160 | TEI8 | Rel-8 | CR | Agreed |
| C1-082683 | Correction for IMSI detach procedure during dedicated mode | NEC/Yannick | 24.008 | 1201 | TEI8 | Rel-8 | CR | Agreed |
| C1-082684 | CSG and Idle Mode Mobility for 3G Home NodeB | Huawei |  |  |  |  | WID | Revised in 2798 |
| C1-082685 | CSG and Idle Mode Mobility for LTE Home eNodeB | Huawei |  |  |  |  | WID | Agreed |
| C1-082686 | MIPv4 Security Aspects | Motorola | 24.304 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082687 | MIPv4 multiple PDN connectivity | Motorola | 24.304 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082688 | Access Network Identity in TS 24.302 | Nokia Siemens networks, Nokia |  |  |  |  | Draft CR | Agreed |
| C1-082689 | CR 24.301 : UE requested PDN connectivity procedure | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Postponed |
| C1-082690 | CR 24.301 : Default EPS bearer context activation not accepted by the UE | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2802 |
| C1-082691 | Reply LS to C1-082646 |  |  |  |  |  | LS out | Postponed |
| C1-082692 | IPMS Indication in Authentication | Nokia Siemens Networks, Nokia |  |  |  |  | Discussion | Revised in 2803 |
| C1-082693 | Multiple authentications for DSMIPv6 bootstrapping | TeliaSonera | 24.303 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082694 | Clarification of DSMIPv6 Handover Procedure | Ericsson | 24.303 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082695 | Field and Message Details for Initial BU and BA | Ericsson | 24.303 |  | SAE | Rel-8 | Draft CR | Revised in 2808 |
| C1-082696 | LS on Actions upon out of credit condition | TSG CT WG3 |  |  |  |  | LS in | Noted |
| C1-082697 | Definition of HA APN for HA discovery | Qualcomm |  |  |  |  | Draft CR | Agreed |
| C1-082698 | Clarifications on values and error codes in BU and BA | Qualcomm Europe | 24.303 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082699 | Clarification on DSMIPv6 and PMIPv6 interactions | Qualcomm Europe | 24.303 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082700 | HA discovery mechanisms and respective applicability scenarios | Qualcomm Europe | 24.303 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082701 | Pseudo-CR on Combined Attach for CS Fallback | NTT DoCoMo | 24.301 |  | CSFB | Rel-8 | Draft CR | Agreed |
| C1-082702 | Update result and Update type information element | NSN, Motorola |  |  |  |  | Draft CR | Agreed |
| C1-082703 | Pseudo-CR on Combined TAU procedure for CS Fallback | NTT DoCoMo | 24.301 |  | CSFB | Rel-8 | Draft CR | Agreed |
| C1-082704 | Update the description of CS fallback | Huawei | 24.801 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082705 | Pseudo-CR on Service request procedure for CS Fallback | NTT DoCoMo | 24.301 |  | CSFB | Rel-8 | Draft CR | Agreed |
| C1-082706 | Pseudo-CR on Paging procedure for CS Fallback | NTT DoCoMo | 24.301 |  | CSFB | Rel-8 | Draft CR | Revised in 2811 |
| C1-082707 | SGs interface specification | NEC | 24.801 |  | SAES-CSFB | Rel-8 | Draft CR | Agreed |
| C1-082708 | LS on IMS CAT | TSG SA WG2 |  |  |  |  | LS in | Noted |
| C1-082709 | Updated WID on stage 3 for CS Fallback in EPS | NEC/Yannick |  |  |  |  | WID | Agreed |
| C1-082710 | Proposed scope for new TS "Mobility Management Entity (MME) - Visitors Location Register (VLR) SGs interface specification" | NEC/Yannick | New TS 29. |  | SAES-CSFB |  | Draft CR | Agreed |
| C1-082711 | Avoidance of mobility management signalling for eCall only terminals | Qualcomm Europe | 24.008 | 1189 | EData | Rel-8 | CR | Revised in 2815 |
| C1-082712 | WiMAX System Information from ANDSF | Intel | 24.302 |  | SAE | Rel-8 | Draft CR | Revised in 2809 |
| C1-082713 | LS on Rel-8 UICC parameters | NTT DoCoMo |  |  |  |  | LS out | Agreed |
| C1-082714 | LS related to 2573 | Ericsson |  |  |  |  | LS out | Agreed |
| C1-082715 | Update the description of the ISR function for TR24.801 | Huawei | 24.801 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082716 | Removed FFS about mapping GUTI to P-TMSI/RAI | Huawei | 24.801 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082717 | Temporary mobile identity handling at Intersystem change to 2G/3G for supporting ISR | Vodafone | 24.801 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082718 | CR 24.301 : Dedicated EPS bearer context activation not accepted by the UE | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2819 |
| C1-082719 | CR 24.301 : EPS bearer context modification not accepted by the UE | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082720 | Discussion on the impact of multiple PLMN identities encoded in TAI list | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082721 | Discussion on the FFS of unsuccessful TAU procedure | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2820 |
| C1-082722 | Update the description of the ISR function for TS24.301 | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082723 | The abnormal case for PDN connection procedure | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082724 | the abnormal case for service request procedure | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082725 | P-CR on Abnormal cases on the network side for TAU procedure | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082726 | P-CR on Abnormal cases on the network side for attach procedure | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082727 | P-CR on Abnormal cases on the network side for GUTI reallocation procedure | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082728 | P-CR on PCO request procedure | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082729 | P-CR on Ciphered PCO transfer flag | ZTE | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082730 | Reply LS on handling of local emergency calls numbers dialled whilst in IMS |  |  |  |  |  | LS out | Revised in 2777 |
| C1-082731 | Correction of notification service activation | Research in Motion | 24.604 | 0003 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082732 | Correction of subscription options | Research in Motion | 24.404 | 0005 | MAINT_R1 | Rel-7 | CR | Agreed |
| C1-082733 | Correction of subscription options | Research in Motion | 24.504 | 0005 | MAINT_R1 | Rel-8 | CR | Agreed |
| C1-082734 | Correction of subscription options | Research in Motion | 24.604 | 0004 | MAINT_R1 | Rel-8 | CR | Agreed |
| C1-082735 | Value of "No reply timer" for CDIV | NTT | 24.404 | 0006 | MAINT_R1 | Rel-7 | CR | Agreed |
| C1-082736 | Value of "No reply timer" for CDIV | NTT | 24.504 | 0006 | MAINT_R1 | Rel-8 | CR | Agreed |
| C1-082737 | Value of "No reply timer" for CDIV | NTT | 24.604 | 0005 | MAINT_R1 | Rel-8 | CR | Agreed |
| C1-082738 | Correction to the communication diversion service | LM Ericsson | 24.404 | 0003 | MAINT_R1 | Rel-7 | CR | Agreed |
| C1-082739 | Correction to the communication diversion service | LM Ericsson | 24.504 | 0003 | MAINT_R1 | Rel-8 | CR | Agreed |
| C1-082740 | Clarification of B2BUA and Proxy roles for AS | Ericsson/Sean | 24.604 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Revised in 2779 |
| C1-082741 | Alignment of user configuration | Ericsson / Atle | 24.654 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082742 | Network requirements for OIP and OIR | Nokia Siemens Networks | 24.607 | 0002 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082743 | Tidyup xsd | Nokia Siemens Networks | 24.623 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082744 | Miscellaneous clean-up corrections | Qualcomm Europe | 24.610 | 0002 | REDOC-TIS_C1 | Rel-8 | CR | Agreed |
| C1-082745 | Add Timestamp in Register Request | Qualcomm Europe/Roozbeh | 24.229 | 2178 | REDOC_3GPP2 | Rel-8 | CR | Revised in 2810 |
| C1-082746 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.173 | 0055 | REDOC_3GPP2 | Rel-8 | CR | Revised in 2768 |
| C1-082747 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.604 | 0006 | REDOC_3GPP2 | Rel-8 | CR | Revised in 2769 |
| C1-082748 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.607 | 0003 | REDOC_3GPP2 | Rel-8 | CR | Agreed |
| C1-082749 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.608 | 0001 | REDOC_3GPP2 | Rel-8 | CR | Agreed |
| C1-082750 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.611 | 0001 | REDOC_3GPP2 | Rel-8 | CR | Agreed |
| C1-082751 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.654 | 0002 | REDOC_3GPP2 | Rel-8 | CR | Agreed |
| C1-082752 | Adding P-Debug-ID to SIP Profile Tables | Vodafone | 24.229 | 2329 | OAM8-Trace | Rel-8 | CR | Agreed |
| C1-082753 | Subscribing to the debug event package | Vodafone | 24.229 | 2330 | OAM8-Trace | Rel-8 | CR | Revised in 2781 |
| C1-082754 | Parameters for IMS Service Level Trace | Vodafone | 24.323 |  | OAM8-Trace | Rel-8 | Draft CR | Agreed |
| C1-082755 | Alignment of IP-CAN specific annexes | Alcatel-Lucent / Keith Drage | 24.229 | 2333 | IMSProtoc2 | Rel-8 | CR | Revised in |
| C1-082756 | Example signalling flow for CS UE origination via an MSC enhanced d forICS where the origation MSC server enhanced for ICS supports codec negotiation. | LM Ericsson | 24.292 |  | ICSRA | Rel-8 | Draft CR | Agreed |
| C1-082757 | Example signalling flow for CS UE origination via an MSC enhanced d forICS where the origation MSC server enhanced for ICS does not supports codec negotiation. | LM Ericsson | 24.292 |  | ICSRA | Rel-8 | Draft CR | Agreed |
| C1-082758 | Example flow for CS UE termination via MSC Server enhanced for ICS (with codec negotiation) | Mavenir | 24.292 |  | ICSRA | Rel-8 | Draft CR | Agreed |
| C1-082759 | Example flow for CS UE termination, not registered in IMS | Mavenir | 24.292 |  | ICSRA | Rel-8 | Draft CR | Agreed |
| C1-082760 | Flow for ICS Registration | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Agreed |
| C1-082761 | Registration procedure for ICS | Nokia Siemens Networks |  |  | ICSRA |  | Draft CR | Agreed |
| C1-082762 | Pseudo-CR on ICS UE termination with CS media using Gm reference point when using an enhanced MSC Server | Nortel Networks |  |  | ICSRA |  | Draft CR | Agreed |
| C1-082763 | Pseudo-CR on Signalling flows for ICS UE origination with CS media using Gm reference point when using an MSC server (not enhanced for ICS) | Nortel Networks |  |  | ICSRA |  | Draft CR | Agreed |
| C1-082764 | Pseudo-CR on Signalling flows for termination to an ICS UE with CS media using Gm reference point when using an MSC server (not enhanced for ICS) | Nortel Networks |  |  | ICSRA |  | Draft CR | Agreed |
| C1-082765 | TS Skeleton for ICS Protocol over USSD bearer | Huawei |  |  |  |  | TS | Agreed |
| C1-082766 | Signalling flows for CS call origination | Huawei | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Agreed |
| C1-082767 | Signalling flows for CS call termination | Huawei | 24.237 |  | IMS-Cont | Rel-8 | Draft CR | Agreed |
| C1-082768 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.173 | 0055 | REDOC_3GPP2 | Rel-8 | CR | Agreed |
| C1-082769 | Allow SIP based user configuration mechanism for configuring supplementary services | Qualcomm Europe | 24.604 | 0006 | REDOC_3GPP2 | Rel-8 | CR | Agreed |
| C1-082770 | Error Response for Different S-CSCF Assignment | Huawei | 24.229 | 2325 | IMSProtoc2 | Rel-8 | CR | Agreed |
| C1-082771 | Pseudo-CR on CAT signalling procedures | Nortel Networks |  |  | CAT-SS |  | Draft CR | Agreed |
| C1-082772 | Reply LS on add/remove media |  |  |  |  |  | LS out | Agreed |
| C1-082773 | LS on SDP Enhancements to support resource allocation | CableLabs, Nortel |  |  |  |  | LS out | Agreed |
| C1-082774 | Removal of draft-ietf-simple-common-policy-caps | LM Ericsson | 24.141 | 0092 | PRESNC | Rel-8 | CR | Postponed |
| C1-082775 | Removal of draft-ietf-simple-pres-policy-caps | Ericsson | 24.141 | 0095 | PRESNC | Rel-6 | CR | Postponed |
| C1-082776 | Removal of draft-ietf-simple-pres-policy-caps | Ericsson | 24.141 | 0096 | PRESNC | Rel-7 | CR | Postponed |
| C1-082777 | Reply LS on handling of local emergency calls numbers dialled whilst in IMS |  |  |  |  |  | LS out | Revised in 2783 |
| C1-082778 | Alignment of IP-CAN specific annexes | Alcatel-Lucent | 24.229 | 2333 | IMSProtoc2 | Rel-6 | CR | Agreed |
| C1-082779 | Clarification of B2BUA and Proxy roles for AS | Ericsson/Sean | 24.604 | 0001 | REDOC_TIS-C1 | Rel-8 | CR | Agreed |
| C1-082780 | TS 24.615 CW proposal for signalling flow | Deutsche Telekom |  |  |  |  | Draft CR | Agreed |
| C1-082781 | Subscribing to the debug event package | Vodafone | 24.229 | 2330 | OAM8-Trace | Rel-8 | CR | Agreed |
| C1-082782 | Reply LS on SDP connection information |  |  |  |  |  | LS out | Agreed |
| C1-082783 | Reply LS on handling of local emergency calls numbers dialled whilst in IMS |  |  |  |  |  | LS out | Agreed |
| C1-082784 | Void |  |  |  |  |  | Information |  |
| C1-082785 | Void |  |  |  |  |  | Information |  |
| C1-082786 | Void |  |  |  |  |  | Information |  |
| C1-082787 | Void |  |  |  |  |  | Information |  |
| C1-082788 | Void |  |  |  |  |  | Information |  |
| C1-082789 | Void |  |  |  |  |  | Information |  |
| C1-082790 | CR to 24.301: Download of timer T3412 | Alcatel-Lucent / Keith Drage | 24.301 |  | SAES | Rel-8 | Draft CR | Revised in 2816 |
| C1-082791 | CR to 24.301: Download of timer T3402 | Alcatel-Lucent / Keith Drage | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082792 | Pseudo-CR on Option C for CSG deployments | Telecom Italia |  |  |  |  | Draft CR | Agreed |
| C1-082793 | MIH Protocol for communication between UE and ANDSF | Intel | 24.302 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082794 | S101 mode NAS Signalling Connection | Nortel Networks | 24.301 |  | SAES |  | Draft CR | Agreed |
| C1-082795 | EMM-DEREGISTERED when in HRPD | Nortel Networks | 24.301 |  | SAES |  | Draft CR | Agreed |
| C1-082796 | Pseodo-CR on NAS Sequence Number Handling | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Revised in 2807 |
| C1-082797 | Coding of the TAI list IE | Nokia | 24.301 |  | SAE |  | Draft CR | Agreed |
| C1-082798 | CSG and Idle Mode Mobility for 3G Home NodeB | Huawei |  |  |  |  | WID | Agreed |
| C1-082799 | Reply LS on UTRA R8 hNB requirements | CT1 |  |  |  |  | LS out | Agreed |
| C1-082800 | Reply LS on Connection recovery by NAS |  |  |  |  |  | LS out | Agreed |
| C1-082801 | LS on combination of SMC and Attach or TAU |  |  |  |  |  | LS out | Agreed |
| C1-082802 | CR 24.301 : Default EPS bearer context activation not accepted by the UE | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082803 | IPMS Indication in Authentication | Nokia Siemens Networks, Nokia |  |  |  |  | Discussion | Agreed |
| C1-082804 | P-CR: Restructuring and adding procedural text to subclause 5.1 for Access Network discovery and selection | Samsung/Chen-Ho | 24.302 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082805 | Reply to LS on CAT in the 3GPP CS domain |  |  |  |  |  | LS out |  |
| C1-082806 | Reply to LS on CS Fallback |  |  |  |  |  | LS out | Agreed |
| C1-082807 | Pseodo-CR on NAS Sequence Number Handling | Ericsson | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082808 | Field and Message Details for Initial BU and BA | Ericsson | 24.303 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082809 | WiMAX System Information from ANDSF | Intel | 24.302 |  | SAE | Rel-8 | Draft CR | Agreed |
| C1-082810 | Add Timestamp in Register Request | Qualcomm Europe/Roozbeh | 24.229 | 2178 | REDOC_3GPP2 | Rel-8 | CR | Agreed |
| C1-082811 | Pseudo-CR on Paging procedure for CS Fallback | NTT DoCoMo | 24.301 |  | CSFB | Rel-8 | Draft CR | Agreed |
| C1-082812 | Chages to CBS for the realisation of ETWS. | NTT DoCoMo | 23.041 | 0018 | ETWS | Rel-8 | CR | Revised in 2817 |
| C1-082813 | Additions to the protocol aspects of CBS for the realisation of ETWS | NTT DoCoMo | 23.041 | 0019 | ETWS | Rel-8 | CR | Agreed |
| C1-082814 | Changes to the radio message format aspect of CBS for the realisation of ETWS | NTT DoCoMo | 23.041 | 0020 | ETWS | Rel-8 | CR | Revised in 2818 |
| C1-082815 | Avoidance of mobility management signalling for eCall only terminals | Qualcomm Europe | 24.008 | 1189 | EData | Rel-8 | CR | Agreed |
| C1-082816 | CR to 24.301: Download of timer T3412 | Alcatel-Lucent / Keith Drage | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082817 | Chages to CBS for the realisation of ETWS. | NTT DoCoMo | 23.041 | 0018 | ETWS | Rel-8 | CR | Agreed |
| C1-082818 | Changes to the radio message format aspect of CBS for the realisation of ETWS | NTT DoCoMo | 23.041 | 0020 | ETWS | Rel-8 | CR | Agreed |
| C1-082819 | CR 24.301 : Dedicated EPS bearer context activation not accepted by the UE | NEC/Caroline | 24.301 |  | SAES | Rel-8 | Draft CR | Agreed |
| C1-082820 | Discussion on the FFS of unsuccessful TAU procedure | Huawei | 24.301 |  | SAE | Rel-8 | Draft CR | Agreed |