Title

Updates to 44.060 §§ 1 to 3

Source

Lucent

Abstract

This contribution proposes a draft CR to incorporate GERAN updates in 44.060 §§ 1 to 3. The GERAN Ad Hoc previously adopted this contribution as GP-010509.

Editor's notes capture questions and comments. They are indicated by the prefix "ENote" or within angled brackets as follows: <editor's note>.

Recommendation

Adopt, as a working draft, the attached proposed CR.

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | 44.060 | CR |  | ( rev | - | ( Current version: | x.y.z | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE |  | Radio Access Network | X | Core Network |  |
| Title: ( | GERAN changes to 44.060 §§ 1 to 3 |
| Source: ( | GERAN Ad Hoc |
| Work item code: ( |  |  | Date: ( | 16 February 2001 |
| Category: ( | B |  | Release: ( | REL-5 |
|  | Use one of the following categories: F (essential correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | Add GERAN. |
| Summary of change: ( | • State that procedures apply to GERAN. • Introduce the A/Gb mode and the Iu mode. • Add a § 1 subsection on the use of logical traffic channels to parallel the subsection on use of logical control channels. • Delete duplicate information. • Break § 1 into subsections, similar to 44.018. • Update references to the latest 3GPP documents. • Add a reference to 43.051. • Incorporate an addition to point 3 of the § 2 introductory paragraph. This addition is recommended in GP-010031. • Add definitions to the existing definitions. • Add abbreviations. • Add symbols. • Partially update the format to comply with 3G TR 21.801. • Reword some of the strange English to comply with The Elements of Style by William Strunk Jr. and E.B. White. |
| Consequences if ( not approved: | No evolution path towards 3G core networks. |
| Clauses affected: ( | §§ 1, 2, and 3. |
| Other specs ( |  | Other core specifications ( |  |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( |  |

# 1.	Scope

## 1.1	General

This document specifies procedures for the following layers of the GSM/EDGE Radio Access Network (GERAN):

–	Radio Link Control (RLC).

–	Medium Access Control (MAC).

These layers span the GERAN radio interface (Um reference point).

The procedures apply in the following two modes:

–	A/Gb mode, where service is provided through A or Gb network interfaces.

–	Iu mode, where service is provided through an Iu network interface.

## 1.2	Related documents

The following documents provide information related to this document:

–	3GPP TS 43.064 contains an overview of the GPRS radio interface (Um reference point).

–	3GPP TS 44.003specifies channel types, access capabilities, and channel configurations at the Um reference point.

ENote:	44.003 may need changes.

–	3GPP TS 44.004  specifies services offered by the physical layer of the Um reference point. It also specifies control channels. RLC and MAC use these services and control channels.

–	3GPP TS24.007 specifies, in general terms, this protocol's structured functions, its procedures, and its relationship with other layers and entities. It also specifies the basic message format and error handling applied by layer-3 protocols.

–	3GPP TS 44.018 specifies GPRS procedures when operating on the Common Control Channel (CCCH).

–	3GPP TS 44.064 specifies the Logical Link Control (LLC) layer.

–	3GPP TS 43.051 is an overall description of the GSM/EDGE Radio Access Network (GERAN).

–	3GPP TS 51.010 and the 3GPP TS 51.02x series specify test procedures for radio-interface signalling.

## 1.3	Use of logical control channels

3GPP TS 55.002 defines three similar sets of logical control channels used by RLC and MAC.

ENote:	List of logical control channels may need to be updated when agreement is reached on use of all dedicated control channels for RLC/MAC procedures.

The first set consists of the following logical control channels:

–	Broadcast Control Channel (BCCH): downlink only, used to broadcast cell-specific information.

–	Paging Channel (PCH): downlink only, used to send page requests to mobile stations (MSs).

–	Random Access Channel (RACH): uplink only, used to request GPRS resources or a Dedicated Control Channel.

–	Access Grant Channel (AGCH): downlink only, used to allocate GPRS resources or a Dedicated Control Channel.

The second set consists of the following logical control channels (Packet Control Channels):

–	Packet Broadcast Control Channel (PBCCH): downlink only, used to broadcast cell-specific information.

–	Packet Paging Channel (PPCH): downlink only, used to send page requests to mobile stations.

–	Packet Random Access Channel (PRACH): uplink only, used to request GPRS resources.

–	Packet Access Grant Channel (PAGCH): downlink only, used to allocate GPRS resources.

–	Packet Associated Control Channel (PACCH): bidirectional, associated with a Temporary Block Flow (TBF).

–	Packet Timing-advance Control Channel Uplink (PTCCH/U): used to transmit random access bursts to allow estimation of the timing advance for one MS in transfer state.

–	Packet Timing-advance Control Channel Downlink (PTCCH/D): used to transmit timing-advance updates for several MSs. One PTCCH/D is paired with several PTCCH/Us.

The third set consists of the following logical control channels (COMPACT control channels):

–	COMPACT Packet Broadcast Control Channel (CPBCCH): downlink only, used to broadcast cell-specific information. This channel broadcasts the same information as the PBCCH, but has a different physical structure (see 3GPP TS 45.002).

–	COMPACT Packet Paging Channel (CPPCH): downlink only, used to send page requests to mobile stations on a COMPACT control channel.

–	COMPACT Packet Random Access Channel (CPRACH): uplink only, used to request GPRS resources on a COMPACT control channel.

–	COMPACT Packet Access Grant Channel (CPAGCH): downlink only, used to allocate GPRS resources on a COMPACT control channel.

–	Packet Associated Control Channel (PACCH): see above.

–	Packet Timing-advance Control Channel Uplink (PTCCH/U): see above.

–	Packet Timing-advance Control Channel Downlink (PTCCH/D): see above.

## 1.4	Use of logical traffic channels

3GPP TS 45.002 defines the following logical traffic channels used by RLC and MAC:

–	Traffic Channel (TCH): bidirectional, carries encoded speech or user data using GMSK on a dedicated physical subchannel (DPSCH). TCH can be full-rate (TCH/F) or half-rate (TCH/H).

–	Octal Traffic Channel (O-TCH): bidirectional, carries encoded speech using 8-PSK on a DPSCH. O-TCH can be full-rate (O-TCH/F) or half-rate (O-TCH/H).

–	Enhanced Traffic Channel (E-TCH): bidirectional, carries user data using 8-PSK on a DPSCH.

–	Packet Data Traffic Channel (PDTCH): downlink or uplink, carries user data using GMSK or 8-PSK on a shared physical subchannel (SPSCH) or a DPSCH. PDTCHs can be full-rate (PDTCH/F) or half-rate (PDTCH/H).

## 1.5	Conventions

Unless explicitly stated otherwise, the following conventions apply:

–	The notations "further study", "FS", or "FFS" indicate the annotated text is not normative.

–	"GPRS" refers to "GPRS and EGPRS".

–	"PBCCH" refers to "PBCCH and CPBCCH".

–	"PPCH" refers to "PPCH and CPPCH".

–	"PRACH" refers to "PRACH and CPRACH".

–	"PAGCH" refers to "PAGCH and CPAGCH".

–	Procedures apply in A/Gb mode and Iu mode.

# 2	References

The following documents contain provisions that, through reference in this text, constitute provisions of this document.

–	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

–	For a specific reference, subsequent revisions do not apply.

–	For a non-specific reference, the latest version applies. For a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of the referenced document in the same release as the referencing document.

[1]

3GPP TR 21.905: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Vocabulary for 3GPP Specifications".

[2]

3GPP TS 22.060: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; General Packet Radio Service (GPRS); Service description; Stage 1".

[3]

3GPP TS 23.003: "3rd Generation Partnership Project; Technical Specification Group Core Network; Numbering, addressing and identification".

[4]

3GPP TS 43.013: "3rd Generation Partnership Project; Technical Specification Group GSM EDGE Radio Access Network; Discontinuous Reception (DRX) in the GSM system".

[5]

3GPP TS 43.064: 3rd Generation Partnership Project; Technical Specification Group GSM EDGE Radio Access Network; General Packet Radio Service (GPRS); Overall description of the GPRS radio interface; Stage 2".

[6]

3GPP TS 24.002: "3rd Generation Partnership Project; Technical Specification Group Core Network; GSM – UMTS Public Land Mobile Network (PLMN) access reference configuration".

[7]

3GPP TS 44.003: "3rd Generation Partnership Project; Technical Specification Group GSM EDGE Radio Access Network; Mobile Station – Base Station System (MS – BSS) interface; Channel structures and access capabilities".

[8]

3GPP TS 44.004: "3rd Generation Partnership Project; Technical Specification Group GSM EDGE Radio Access Network; layer 1 General requirements".

[9]

3GPP TS 44.005: "3rd Generation Partnership Project; Technical Specification Group GSM EDGE Radio Access Network; Data Link (DL) layer General aspects".

[10]

3GPP TS 24.007: "3rd Generation Partnership Project; Technical Specification Group Core Network; Mobile radio interface signalling layer 3; General aspects".

[11]

3GPP TS 44.018: "3rd Generation Partnership Project; Technical Specification Group GSM EDGE Radio Access Network; Mobile radio interface layer 3 specification, Radio Resource Control Protocol".

[12]

3GPP TS 44.064: "3rd Generation Partnership Project; Technical Specification Group Core Network; General Packet Radio Service (GPRS); Mobile Station – Serving GPRS Support Node (MS-SGSN) Logical Link Control (LLC) layer specification".

[13]

3GPP TS 45.002: "3rd Generation Partnership Project; Technical Specification Group GSM EDGE Radio Access Network; Multiplexing and multiple access on the radio path".

[14]

3GPP TS 45.003: "3rd Generation Partnership Project; Technical Specification Group GSM EDGE Radio Access Network; Channel coding".

[15]

3GPP TS 45.008: "3rd Generation Partnership Project; Technical Specification Group GSM EDGE Radio Access Network; Radio subsystem link control".

[16]

3GPP TS 45.010: "3rd Generation Partnership Project; Technical Specification Group GSM EDGE Radio Access Network; Radio subsystem synchronization".

[17]

3GPP TS 51.010-1: "3rd Generation Partnership Project; Technical Specification Group GSM EDGE Radio Access Network; Mobile Station (MS) conformance specification; Part 1: Conformance specification".

3GPP TS 51.010-2: "3rd Generation Partnership Project; Technical Specification Group Terminals; Mobile Station (MS) conformance specification; Part 2: Protocol Implementation Conformance Statement (ICS); proforma specification".

3GPP TS 51.010-3: "3rd Generation Partnership Project; Technical Specification Group Terminals; Mobile Station (MS) conformance specification; Part 3: Layer 3 Abstract Test Suite (ATS)".

3GPP TS 51.010-4: "3rd Generation Partnership Project; Technical Specification Group Terminals; Mobile Station (MS) conformance specification; Part 4: SIM application toolkit conformance specification".

[18]

3GPP TS 51.021: "3rd Generation Partnership Project; Technical Specification Group GSM EDGE Radio Access Network; Base Station System (BSS) equipment specification; Radio aspects".

[19]

3GPP TS 23.060: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; General Packet Radio Service (GPRS); Service description; Stage 2".

[20]

3GPP TS 24.008: "3rd Generation Partnership Project; Universal Mobile Telecommunications System; Mobile radio interface layer 3 specification, Core Network Protocols – Stage 3".

[21]	3GPP TS 43.051: "3rd Generation Partnership Project; Technical Specification Group GERAN; GSM/EDGE Radio Access Network (GERAN); Overall Description – Stage 2"

# 3	Definitions, abbreviations, and symbols

## 3.1	Definitions

This document uses the following definitions:

A/Gb mode: For further study. For now, see 3GPP TS 44.018.

ENote:	a high-level operating mode at the mobile station and the GERAN where the GERAN provides service through an A network interface or a Gb network interface. Mode-specific protocol stacks, functional models, and procedures apply.

Block period: A block period is the sequence of four timeslots on a PDCH used to convey one radio block.

Dual transfer mode: In dual transfer mode, the mobile station is allocated radio resources providing an RR connection (3GPP TS 44.018) and a Temporary Block Flow on one or more packet data physical channels. The allocation of radio resource for the RR connection and the Temporary Block Flow is co-ordinated by the network in agreement with the capabilities of the mobile station in dual transfer mode.

EGPRS: Enhanced GPRS. enables higher data rates through usage of 8PSK modulation in addition to GMSK. EGPRS also enables incremental redundancyoperation.

EGPRS TBF mode: a TBF utilising EGPRS enhancements, e.g., 8PSK and incremental redundancy. This mode applies in A/Gb mode and Iu mode.

GPRS multislot class: The term GPRS multislot class refers to the different mobile station capabilities to transmit and receive on different combinations of multiple PDCHs. The multislot classes are defined in 3GPP TS 45.002. Note that the mobile station may indicate different multislot classes for circuit-mode services and for GPRS (see 3GPP TS 44.008). [stf note: not yet found in a CR!]Different multislot-class mobile stations are capable of supporting different medium access modes (see subclause 5.2.4).

GPRS TBF mode: a TBF not utilising EGPRS enhancements,. This mode applies in A/Gb mode and Iu mode.

IR: Incremental redundancy. enables higher data rates through combining information from different transmissions of RLC data blocks when decoding. Also known as Hybrid Type II/III ARQ.

# Iu mode: For further study. For now, see 3GPP TS 44.018.

ENote:	a high-level operating mode at the mobile station and the GERAN where the GERAN provides service through an Iu network interface. Mode-specific protocol stacks, functional models, and procedures apply.

# MAC dedicated state: a MAC-control-entity state where a dedicated physical subchannel is assigned and no shared physical subchannel is assigned. This state only applies in Iu mode.

# MAC DTM state: a MAC-control-entity state where at least one dedicated physical subchannel and one shared physical subchannel are assigned. This state only applies in Iu mode.

# MAC idle state: a MAC-control-entity state where no physical subchannels are assigned. This state only applies in Iu mode.

# MAC shared state: a MAC-control-entity state where at least one shared physical subchannel is assigned. This state only applies in Iu mode.

MCS: Modulation and Coding Scheme.

Packet flow context: Packet Flow Context (PFC) procedures are described in 3G TS 23.060. A Packet Flow Identifier (PFI) is used to identify a PFC.

Packet idle mode: a mobile station is prepared to transfer LLC PDUs on packet data physical channels (see subclause 5.3). The mobile station is not allocated any radio resource on a packet data physical channel; it listens to the PBCCH and PCCCH, or if those are not provided by the network, to the BCCH and the CCCH. This mode only applies in A/Gb mode.

Packet transfer mode: a mobile station is prepared to transfer LLC PDUs on packet data physical channels (see subclause 5.4). The mobile station is allocated radio resource on one or more packet data physical channels for the transfer of LLC PDUs. This mode only applies in A/Gb mode.

Radio block: A radio block is the sequence of four normal bursts carrying one RLC/MAC protocol data units (see 3GPP TS 44.004). (The one exception is a radio block occasionally used on PACCH consisting of a sequence of four access bursts, each carrying a repetition of one short RLC/MAC block.)

Random values: In a number of places in this Technical Specification, it is mentioned that some value must take a “random” value, in a given range, or more generally with some statistical distribution. For such random values refer to 3GPP TS 44.008.

RLC data block:A RLC data block is the part of a RLC/MAC block carrying user data or upper layers’ signalling data (see subclause 10.2).

RLC/MAC block: A RLC/MAC block is the protocol data unit exchanged between RLC/MAC entities (see clause 10 and 3GPP TS 44.004).

RLC/MAC control block: A RLC/MAC control block is the part of an RLC/MAC block carrying a control message between RLC/MAC entities (see subclause 10.3).

RR connection: An RR connection is a physical connection established between a mobile station and the network to support the upper layers’ exchange of information flows. An RR connection is maintained and released by the two peer entities. RR connections apply in A/Gb mode.

RRC connection: a point-to-point bidirectional connection between an RRC entity in the MS and its RRC peer in the GERAN. An MS has 0 or 1 RRC connections. An RRC connection may have, or may not have, a physical-layer connection. RRC connections apply in Iu mode.

TBF abort: The term “abort” as applied to TBF is used when the TBF is abruptly stopped without using the release-of-TBF procedures defined in clause 9.

TBF release: The term “release” as applied to TBF is used when the TBF is stopped using one of the release-of-TBF procedures defined in clause 9.

Temporary Block Flow (TBF): a connection offered by two MAC entities to support the unidirectional transfer of higher-layer PDUs on physical subchannels.

Timer Expiry: a started timer has run the time specified.

Timer Restart: a timer that may already be running is stopped and then started again to run the time specified.

Timer Start: a timer is started to run the time specified.

Timer Stop: a started timer is stopped and its value is then undefined.

Uplink State Flag (USF): The Uplink State Flag (USF) is used on PDCH channels to allow multiplexing of uplink radio blocks from different mobile stations (see subclause 5.2.3, clause 10 and 3GPP TS 45.002).

Upper-layer PDU: [A/Gb mode] an LLC PDU.

Upper-layer PDU: [Iu mode] an RRC message or a PDCP PDU.

## 3.2	Abbreviations

This document uses abbreviations from 3GPP TR 21.905 and 3GPP TS 43.064. It also uses the following abbreviations:

ENote:	It is bad form to refer the reader to multiple references for abbreviations.

ARI	Access Request Identifier

ARQ	Automatic Repeat reQuest

AS	Access Stratum

BCCH	Broadcast Control CHannel

BSS	Base Station Subsystem

CBCH	Cell Broadcast CHannel

CC	Call Control

CCCCH	Compact CCCH

CCCH	Common Control CHannel

CN	Core Network

CPBCCH	Compact PBCCH

CS-i	GPRS Coding Scheme i

DC	Dedicated Control

DLC	Data Link Control

DPSCH	Dedicated Physical Sub CHannel

ECSD	Enhanced Circuit Switched Data

EDGE	Enhanced Data rates for Global Evolution

E-FACCH	Enhanced FACCH

EGPRS	Enhanced General Packet Radio Service

E-TCH	Enhanced TCH

FACCH	Fast Associated Control CHannel

GC	General Control

GERAN	Gsm/Edge Radio Access Network

GPRS	General Packet Radio Service

GRA	Geran Registration Area

G-RNTI	Geran Radio Network Temporary Identity

GSM	Global System for Mobile communications

IETF	Internet Engineering Task Force

IMSI	International Mobile Subscriber Identity

IP	Internet Protocol

LCS	LoCation Services

LLC	Logical Link Control

MAC	Medium Access Control

MCS-i	EGPRS Modulation and Coding Scheme i

MM	Mobility Management

MS	Mobile Station

NAS	Non Access Stratum

NSAPI	Network-layer SAPI

Nt	Notification

O-FACCH	Octal FACCH

O-TCH	Octal TCH

PBCCH	Packet BCCH

PDCH	Packet Data CHannel

PDCP	Packet Data Convergence Protocol

PDP	Packet Data Protocol

PDTCH	Packet Data TCH

PDU	Protocol Data Unit

PFC	Packet Flow Context

PLMN	Public Land Mobile Network

PTCCH	Packet Timing-advance Control CHannel

P-TMSI	Packet TMSI

QoS	Quality of Service

RAB	Radio Access Bearer

RANAP	Radio Access Network Application Part

RB	Radio Bearer

RLC	Radio Link Control

RNC	Radio Network Controller

RNS	Radio Network Subsystem

RNSAP	Radio Network Subsystem Application Part

ROHC	Robust Header Compression

RR	Radio Resource

RRC	Radio Resource Control

RTP	Real Time Protocol

SACCH	Slow Associated Control CHannel

SAP	Service Access Point

SAPI	Service Access Point Identifier

SDCCH	Stand-alone Dedicated Control CHannel

SDU	Service Data Unit

SPSCH	Shared Physical Sub CHannel

TBF	Temporary Block Flow

TCH	Traffic Channel

TCP	Transmission Control Protocol

TLLI	Temporary Logical Link Identifier

TMSI	Temporary Mobile Subscriber Identity

UDP	User Datagram Protocol

UMTS	Universal Mobile Telecommunication System

USF	Uplink State Flag

UTRAN	UMTS Terrestrial Radio Access Network

## 3.3	Symbols

This document uses the following symbols:

A	Interface between BSS and 2G MSC

Gb	Interface between BSS and 2G SGSN

Iu-cs	Interface between BSS and 3G MSC

Iu-ps	Interface between BSS and 3G SGSN

Iur-g	Interface between GERAN BSSs
Interface between a BSS and an RNC is FFS.

Um	Interface between MS and BSS

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the lastest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. Work item acronyms are listed in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.