## Slide 1: Motivation for Study on Integrated Access and Backhaul for NR
RAN#75, DUBROVNIK, CROATIA, MARCH 6-9, 2017
AI 9.1
RP-17XXXX
AT&T

## Slide 2: Integrated Access and Backhaul Architecture for NR
A wireless multi-hop self-backhauling architecture is a critical feature for NR
    Backhaul (in-band or out of band) and access are integrated and multiplexed at Layer 2
    Allows for ultra-dense deployment of mmWave TP without having to densify the transport proportionately
    Due to usage of phased array access and backhaul can use the same radio (no need for full duplex interference cancellation)
Layer 3 Relay
Layer 2 Relay
Each TRP has its own cell ID
TRP switching (route switching) involves RRC signaling and is visible to core
Lower specification impact
Not suitable for mmWave since no fast switching to mitigate blocking
Shared cell ID
Fast TRP switching (route switching) by enabling this functionality at Layer 2
Higher specification impact
Suitable for mmWave since it can allow for fast L2-level switching to mitigate blocking
Donor TRP (Cell ID 1)
L2-nRT
L2-RT
-L
PHY
L2-RT
-L
PHY
L2-nRT
L2-RT
PHY
L2-RT
PHY
Relay TRP (Cell ID 2)
UE
L2-nRT
L2-nRT
Donor TRP (Cell ID 1)
L2-nRT
L2-RT
-L
PHY
L2-RT
-L
PHY
L2-nRT
L2-RT
PHY
L2-RT
PHY
Relay TRP (Cell ID 1)
UE

## Slide 3: Key Aspects of the Integrated Access and Backhaul for NR
    High spectral efficiency with dynamic resource allocation
    Fast route switching (much faster than RRC time scales) to mitigate blocking events in mmWave
    Allow for multi-hop scheduling and route optimization built in the scheduler
1 Topology Management
Happens on long time scales
Manages static hop order
Initial access
Changes every time a node is added or removed
2 Route Management
Happens over 10s or 100s of subframes
Routes are updated for load variance and blocking
3 Frame Structure and Scheduling
Optimizes the frame structure (DL, UL, DL+UL) at every node
Schedules backhaul and access traffic

## Slide 4: Topology Management
  Operating NR systems in mmWave spectrum presents some unique challenges including experiencing severe blocking that cannot be readily mitigated by RRC-based handovers due to the short time-scale.
  Architecture options which support multi-hop and multi-link connectivity between relay TRPs (rTRPs) enable dense deployments in a scalable manner while also remaining robust to short-term blocking events:
    Adhoc/mesh network based on Sidelink-like framework for resource allocation between rTRPs
      No hierarchy between TRPs and the network framework is scalable
      Very in-efficient and overhead heavy for an ultra dense network
    Hierarchical design where one entity schedules the links between a pair of rTRPs
      Topology relation based on a hop order (N) where N is the number of hops needed for a rTRP to reach a fiber backhaul.
      Multi-hop scheduling supported, with multiple candidate rTRPs per link
Hop Order 0 (donor)
Hop Order 1
Hop Order 2

## Slide 5: Route Management
Protocol stack and network architecture design considering operation of multiple relay hops between the anchor node and UE:
  S1/NG1 termination at anchor cell
  RAN-based L2 mobility between Relay TRPs (no RRC-based handover) that share a common cell ID
  Relay TRPs may be based on Option 2 (PDCP/RLC) or Option 3-1 (RLC-H/RLC-L) functional split
  Donor cell may be physically split into a virtualized central unit with L3+L2nRT and remote unit with L2RT+L1
NGC
S1/NG1 Termination
L2 RT
L3
L2 NRT
L1
Anchor Cell
L2 RT
L1
L2 RT
L1
Relay Hop-1
Relay Hop-1
Relay TRP 3
Relay TRP 1
L2 RT
L1
Relay Hop-2
Relay TRP 2
UE

## Slide 6: Frame structure and scheduling
  Efficient resource multiplexing between access and backhaul links
    Can consider dynamic resource sharing (e.g. TDM/FDM) subject to half-duplex constraints at the relay nodes
    Support MU-MIMO between access and backhaul as well as multi-site transmission of backhaul links
    Investigate over-the-air control (OTA) information exchange between nodes to coordinate resource allocation to mitigate interference and optimize end-to-end route selection
  Take the NR physical layer design as a baseline considering future enhancements
    Efficient multiplexing of eMBB/URLLC is beneficial for low latency control between backhaul nodes
    Support same or different numerology on access/backhaul links considering the support for increased spectral efficiency
    During initial access multiple backhaul links can be established and periodically maintained (e.g. RRM reports or other link quality metrics)
Duplexing Options Between
Access and Backhaul

## Slide 7: Network Architecture with IAB
  The study should consider protocol stack and interface design for relay nodes:
L3
L2-NRT
L2 RT
L1
L3
L2
L1
Xn
Uu
L2 RT
L1 RT
Xn
Uu
Uu
Xr
CU
DU
UE
UE
CU
DU
RU
  CU-DU split with wireless backhaul
  CU-DU split without wireless backhaul
L3
L2
L1
L2 RT
L1 RT
L3
L2-NRT
L2 RT
L1 RT