## Slide 1: 3GPP TSG RAN Meeting #75 Dubrovnik, Croatia, March 6 - 9, 2017 Agenda item: 10.1.1 Document for: Discussion
Motivation for even further enhancement of eMTC for LTE
RP-170686

## Slide 2: Justification
In Rel-14, two work items, eMTC and NB-IoT, were approved to address the requirements of cellular internet of things.
However , the scope of WID was reduced during the WID discussion as a result of limited TU time available.
Some features were further delayed in WG discussion
As the actual network deployment started, it is important to ensure that IoT devices and IoT traffic can be handled efficiently in the networks ,and service requirements can be satisfied

## Slide 3: Objectives
Power consumption and latency reduction enhancement
Spectrum efficiency and coverage enhancement

## Slide 4: Power consumption and latency reduction enhancement
Device power consumption is of paramount importance for IoT success. Currently, feedback from field deployment and actual comparison with competing technologies shows room for improvement and calls for immediate attention.
Latency reduction is beneficial for many IoT services.

## Slide 5: Power consumption and latency reduction enhancement (1)
Status | Ave power consumption (mA) | Ave time % | Ave usage
Actual TX period | 400 | 17% | 43%
Non TX RRC connected period | 180 | 50% | 56%
IDLE period | 3 | 33% | 1%
For IoT applications, lots of the traffic is characterized by small packet data transmission. Improving access and transmission efficiency for small data transmission will lower UE power consumtpion.
Objective:
  Specify enhancement to improve UE power consumption and efficiency of small packet transmission [RAN1, RAN2]

## Slide 6: Power consumption and latency reduction enhancement (2)
SI latency enhancement [RAN1, RAN2]
  SI transmission enhancement via IoT specific SIB to reduced UE monitoring requirement and network access latency
  Control channel enhancement in connected mode [RAN1]
    Reduce power consumption for control channel detection.
Chart: Expected Latency reduction for some SIB Transmission
 | 2560 | 5120 | 9560 | 29440

## Slide 7: Spectrum efficiency and coverage enhancement
With deployment of multiple PRBs , it is desirable for terminals to efficiently utilize available bandwidth .
  Resource allocation on subcarriers level will increase both spectrum efficiency and coverage ;
Standalone eMTC deployment scenario could be enhanced, for example, in the area of resource utilization.

## Slide 8: Spectrum efficiency and coverage enhancement
  Paging enhancement [RAN1, RAN2]
    Paging transmission enhancement via common PO to reduce resource utilization
    Potential paging reduction
Pagingcycle | 128 | 256 | 256
PO reduction | 512 | 512 | 512

## Slide 9: Thank you