## Slide 1: WF on RAR transmission
Huawei, HiSilicon, ALU, ASB, Ericsson, IDC, Intel, Panasonic
R1-153499
3GPP TSG RAN WG1 #81
Fukuoka, Japan, May 25-29, 2015
Agenda item 6.2.1.8

## Slide 2: Background
From Rel-12 (RAN1#74bis):
  FFS during initial random access procedure if repetition level associated with transmission of Msg2/3/4 can be semi-statically configured, dynamically signalled, or predefined
From Rel-13 (RAN1#79):
  RAR/paging message intended for Rel-13 low-complexity UE and/or UE operating CE can support PDSCH subframe bundling/repetition with multiple bundle sizes/repetition levels

## Slide 3: Background
Agreements from RAN1#80bis:
Options for paging/RAR transmission mechanism
  Option 1. M-PDCCH + PDSCH carrying paging/RAR messages
  Option 2. M-PDCCH carrying paging/RAR message
  Option 3. PDSCH carrying paging/RAR message

## Slide 4: Proposals
UE knows repetition level of transmission of RAR from the repetition level of its most recent PRACH
UE knows in which subframe(s) transmission of RAR can begin from its most recent PRACH resource set
UE knows in which frequency resource(s) transmission of RAR can occur from its most recent PRACH resource set
NOTE: “Transmission of RAR” includes Option 1,2,3 for RAR transmission mechanism.