## Slide 1: eMTC, cat-M1 RRM Test Tolerance analysis strategy
RAN5 #72, Gothenburg
R5-166102
Document for discussion and endorsement

## Slide 2: Overview of test cases
In the following slides the RRM test cases for eMTC are presented and discussed according to their type and clause.
For some clauses (5, 6, 7) we present suggestions on coming Test Tolerance analysis and for some (8, 9) we raise questions on how to handle the test tolerances.
The aim with the presentation is to agree (partly per clause or fully) on a way forward for the coming Test Tolerance work needed to complete the Work Item.
Note this analysis is only for CE mode A at this stage since RAN4 has not completed CE mode B.
This document captures the agreed way forward as an update of R5-165843, the agreements are written in red text below.

## Slide 3: EMTC Idle state mobility test cases, TS36.521-3, clause 4
There are three eMTC idle state mobility test cases, 4.2.12, 4.2.13 and 4.2.14. All have the same dB values as the legacy intra freq FDD/TDD test cases 4.2.1 & 4.2.2; all test cases are in AWGN.
  The only difference to legacy test cases is the antenna configuration 1x1.
Since the dB values are identical we suggest to apply the same Test Tolerance and hence no new analysis is needed.
Suggestion endorsed

## Slide 4: EMTC Handover test cases, TS36.521-3, clause 5
There are three eMTC cat-M1 handover test cases, 5.1.13, 5.1.14 and 5.1.15. All have the same dB values as the legacy intra freq FDD/TDD test cases 5.1.1 & 5.1.2 and all test cases are in AWGN.
Since the dB values are identical we suggest to apply the same Test Tolerance and hence no new analysis is needed.
Suggestion endorsed

## Slide 5: eMTC RRC Connection control test cases, TS36.521-3, clause 6
There are three eMTC RRC Re-establishment test cases (6.1.9, 6.1.10 and 6.1.11) and three eMTC Random Access test cases (6.2.10, 6.2.11 and 6.2.12) in clause 6.
All have the same dB values as the legacy intra freq FDD/TDD test cases 6.1.1 & 6.1.3 for RRC Re-establishment and 6.2.1 & 6.2.3 for Random Access.
All test cases are in AWGN.
All the dB values are identical, but there is a need to analyze if side conditions and PRACH parameters also are identical for eMTC. If so we suggest to apply the same Test Tolerance and hence no new analysis is needed.
Suggestion endorsed, NOTE! Test case writers must ensure that PRACH parameters are identical before concluding that no TT analysis is needed on a per test case basis.

## Slide 6: eMTC Timing and signaling characteristics test cases, TS36.521-3, clause 7
There are three Transmit Timing Accuracy test cases (7.1.10 - 12), three Timing Advance test cases (7.2.6 - 8) and 12 RLM test cases 7.3.48 - 7.3.59.
  The Transmit Timing test cases all have the same dB values and propagation conditions (AWGN) as the legacy test cases (7.1.1 & 7.1.2).
  The Timing Advance test cases all have the same dB values and propagation conditions (AWGN) as the legacy test cases (7.2.1 & 7.2.2).
  The RLM test cases still have the SNR values undefined in TS36.133. A way forward was agreed in RAN4 (R4-164905) and the values are to be further discussed in Gothenburg.
Conclusion and suggestion for clause 7: No new TT analysis needed for Transmit Timing and Timing Advance (given the UL timing requirements are the same). For RLM non of the SNR dB values are expected to be similar to any legacy test cases hence these test cases needs separate Test Tolerance analysis.
Suggestion endorsed

## Slide 7: eMTC RRM Measurement test cases, TS36.521-3, clause 8
There are 8 eMTC RRM Measurement test cases, 8.1.23 - 8.1.30. The test cases have identical dB values and fading conditions as the corresponding “legacy” test cases. Test cases are synchronous/asynchronous and with/without DRX. E.g. 8.1.23 same as 8.1.1(“legacy”)
Question: Is it possible to reuse any of the existing test tolerances? Note: For Cat-0 test cases it was found not possible since absolute RSRP is worse than for legacy. Similar conclusion for Cat-M1?
Endorsed Suggestion: Test case writers must ensure that RSRP requirements are identical before concluding that no TT analysis is needed. If RSRP requirements are different new Test Tolerance analysis is needed.

## Slide 8: eMTC RRM RSRP/RSRQ accuracy test cases, TS36.521-3, clause 9
There are three eMTC RRM RSRP accuracy test cases, 9.1.52 – 9.1.54
The test cases have identical dB values as the corresponding MTC cat-0 test cases. E.g. 9.1.52 same as 9.1.41
Question: Is it possible to re-use the TT analysis from the corresponding cat-0 test cases?
Endorsed Suggestion: Test case writers must ensure that RSRP requirements are identical before concluding that no TT analysis is needed. If RSRP requirements are different new Test Tolerance analysis is needed.