## Slide 1: Emergeny session identificaton
Carmen Catalano
Telecom Italia
Discussion Paper Emergency Session Identification WID
3GPP TSG-SA WG1 Meeting #61
Prague, 28 January -01 February 2013
Notes: 1

## Slide 2: Emergency session identification (1/3)
When a User dials an emergency number, the following scenarios need to be supported for the routing of the emergency sessions.
In order to guarantee all the scenarios described above the following problems need to be solved:
The emergency service invoked by the User needs to be identified unambiguously.
The emergency service indication needs to be carried through the operator’s network to the PSAP.
User
Opertaror CN
112
113
118
PSAP 2
Dedicated PSAP
PSAP 3
PSAP 1
112
113
118
User
Opertaror CN
112
113
118
PSAP 1
Shared PSAP
PSAP 2
112
113
118
User
Opertaror CN
112
113
118
Hierarchic PSAP
112
113
118
PSAP 2
PSAP 3
PSAP 1
PSAP
112
113
118

## Slide 3: Emergency session identification (2/3)
Status: RFC 5031 defines some URNs which can be used in IMS in order to identify a set of emergency sessions (sos; sos.ambulance; sos.animal-control; sos.fire; sos.gas; sos.marine; sos.mountain; sos.physician; sos.poison; sos.police). The dialled digits can be mapped into the previous emergency URNs
Problem 1: The emergency services invoked by the User needs to be identified unambiguously. If the dialled digit cannot be mapped on any emergency URN contained in the RFC 5031, how can the emergency services be identified?
Possible solutions:
New sub-service type definition.
From RFC 5031: Additional sub-services can be added after expert review and must be of general public interest and have a similar emergency nature. The expert is designated by the ECRIT working group, its successor, or, in their absence, the IESG. The expert review should only approve emergency services that are offered widely and in different countries, with approximately the same caller expectation in terms of services rendered.
Extention of existing sub-service type (e.g. sos.police.childprotection).
If this scenario is considered feasible, which entity/SDO can define this values? Can these values be defined autonomously in a country from the Regulation Authority?
Introduction of a general purpose sub-service type (sos.extension.114 where 114 are the dialled digits).
Regarding the listed possible solutions: This is only presented here for information and it’s up to stage 3 to try to find the right choice

## Slide 4: Emergency session identification (3/3)
Problem 2: When the User initiates an emergency session dialling the digits of the emergency number, the emergency service indication needs to be carried through the operator’s network to the PSAP.
Possible solutions: It’s up to stage 3 try to find the possible solution in order to cover the previous issue
Regarding the listed possible solutions: This is only presented here for information and it’s up to stage 3 to try to find the right choice