## Slide 1: UUAA/C2 Authorization in EPS by using protocol configuration options
Roozbeh Atarius
Lenovo, Motorola Mobility
ratarius@motorola.com

## Slide 2
Figure 5.3.2.1-1: Attach procedure – TS 23.401
Figure 5.3.2.1-1: Attach procedure – simplified

## Slide 3: Attach procedure with ePCO checking
Proposal:
  Attach Request (PDN CONNECTIVITY REQUEST message [PCO])
  Attach Response (ACTIVATE DEFAULT EPS BEARER CONTEXT REQUEST message [ePCO support])
  Attach complete (ACTIVATE DEFAULT EPS BEARER CONTEXT ACCEPT message [ePCO])
The proposal to the meeting has been that Modify Bearer Request message convey ePCO from ACTIVATE DEFAULT EPS BEARER CONTEXT ACCEPT message from MME via SGW to PGW-C+SMF.
  Modify Bearer Request message does not have PCO/ePCO capability according to TS 29.274.

## Slide 4: Solution 1 – ePCO Only
This assumption is currently very close to what we do, except we check by sending PCO.
MME support ePCO, the MME chooses:
  SGW due to network topology, load balancing, non-IP, ethernet capability, if supported UE assisted dedicated core network(DCN).
    There is no SA2 requirement for ePCO support, however if SGW supports inter system change with 5GS, it will support ePCO.
    I could not locate any such req. for MME/SGW and this may result in a change of MME to look for such capability but since it is not for UAS, then may be OK, however rel-17 will be first release, thus no legacy network and against SA2 requirement. Requirement for mobility and thus to find MME and SGW with this capability must also be added.
    If SGW does not support ePCO, the ePCO IE is dropped from passing along in create session request message.
  PGW due to UE’s subscribed APN or e.g. UE assisted DCN locates the PWG-C+SMF which supports inter system change with 5GS and always support ePCO.
MME does not support ePCO:
  The ePCO IE is dropped by the MME when populating create session message towards SGW and PGW-C+SMF.
  PGW-C+SMF may register the UE as a regular UE as a result even if it may realize the UE capability due to its subscription.
  The UE receives PCO support indicator back from the network, and thus should consider the network is not supporting UAS services.

## Slide 5: Solution 1 – ePCO only
Pros:
  Messages up to 65 K can be transmitted.
Cons:
  Only those network (MME, SGW) with inter system 5GS exchange capability which also have ePCO capability supports the UAS services. Thus rel-17 onwards and no legacy network.
  This is not clear how MME should locate another MME or SGW should locate another SGW without breaking “no MME/SGW impact” requirement. If support for intersystem 5GS change is required, then only a selected EPC can comply.
    If due to mobility MME and/or SGW change, the new MME and SGW must support ePCO since re-UUAA can be performed by the network. If the ePCO network support ceases, the PGW-C+SMF must release the UE.
  PGW-C+SMF behavior needs to be defined if a UAV UE preforms a regular registration.
  Even if ePCO is used, it is not clear that data is less than 65K, especially if the UE transmit data for both UUAA and C2 pairing authorization.

## Slide 6: Solution 2– UUAA data transmission
Follow the same procedure as for e.g.
  bearer resource allocation or
  bearer resource modification
to trigger
  Modify Bearer Command form MME to PGW-C + SMF

## Slide 7
Solution 2– UUAA result transmission

## Slide 8: Solution 2
Pros:
  Even PCO can be used thus the pre-release 13 MME and SGW will also work Or even newer ones which did not implement ePCO. What needs to be done is to send repetitively parts of the UUAA data on slide 4 and to receive repetitively parts o fthe UUAA results.
  Any size of message can be transferred since even if the messages are larger than 65K and ePCO is supported.
  SA2 requirement that MME does not have to be updated is fully upfilled.
Cons:
  New procedure needs to be defined for
    bearer modification concept for UUAA data and C2 authorization data transmission by PCO/ePCO in TS 24.301.
    update bearer request concept for UUAA and C2 Authorization results transmission by PCO/ePCO in TS 29.274.