## Slide 1: WF on spatial consistency
Intel, Ericsson, InterDigital, Nokia, ALU, ASB, Samsung, NTT DoCoMo
R1-161726
3GPP TSG RAN1 #AH Channel Model
Ljubljana, Slovenia, March 14 - 16, 2016
Agenda Item: 7

## Slide 2: Background
In R1-161150, below working assumption is agreed:
  The channel model in this SI should be based on the stochastic modeling methodology that is used for the 3D spatial channel model of TR 36.873, but with additional features >6GHz to fulfill the agreed requirements in R1-161142 and the agreed scenarios in R1-161145
In R1-161142, it was agreed:
  The model should be consistent in space, time and frequency
In R1-161622, three alternatives have been described to solve the spatial consistency issue:
  Alternative 1 (spatial consistent random variable based approach) has been verified in R1-160437, R1-161643, R1-161617, R1-161651, R1-161646
  Alternative 2 (Geometric Stochastic Approach) has been simulated in R1-161603
  Alternative 3 (Method using geometric locations of clusters) has been simulated in R1-161610
  The main merits of alternative 1 compared with alternative 2/3 is its implementation simplicity and compatibility with the existing 3GPP 3D channel model

## Slide 3: Proposals
  Alternative 1 (spatial consistent random variable based approach) in R1-161622 is set as working assumption for this SI:
    Proposal 1-1: Introduce spatial consistency to the channel cluster specific random variales in the 3GPP 3D channel model. The channel cluster specific random variables include:
      Cluster specific random delay in step 5.
      Cluster specific shadowing in step 6.
      Cluster specific offset for AoD/AoA/ZoD/ZoA in step 7.
      Apply to the nth cluster before sorting the delay
    Proposal 1-2: Generate below channel cluster specific random variables to be drop based:
      Cluster specific sign for AoD/AoA/ZoD/ZoA in step 7.
    Proposal 1-3: Introduce spatial consistency to the path specific random variables in the 3GPP 3D channel model. The path specific random variables include:
      Random coupling of rays in step 8.
      XPR in step 9.
      Random phase in step 10.
    Proposal 1-4: the correlation distance is FFS, e.g. according to corresponding LSP correlation distance

## Slide 4: Proposal (Continued)
    Proposal 2: Introduce spatial consistency to the LOS/NLOS and indoor/outdoor random variables in the 3GPP 3D channel model. LOS/NLOS state and indoor/outdoor state are determined by comparing the spatial consistent random variable with a distance dependent LOS probability or indoor probability.
      FFS: dcorr, e.g. dcorr=50m for LOS/NLOS and dcorr=30m for indoor/outdoor
    Proposal 3: Make the indoor distance to be spatially consistent if it is agreed that indoor pathloss (PLin in TR36.873) is a function of a uniform random indoor distance.
    Proposal 4: If soft LOS/NLOS and soft indoor/outdoor state is modelled, introduce soft LOS/NLOS state and soft indoor/outdoor state to describe the transition regions between LOS/NLOS and indoor/outdoor. Example of the soft LOS/NLOS state and soft indoor/outdoor state can be found in the appendix.
      Use soft LOS/NLOS and soft indoor/outdoor state to calculate the pathloss and fast fading channel.
    Note: examples to generate spatially consistent random variables for all the proposals can be found in the appendix

## Slide 5: Appendix: example 1 of generating spatially consistent uniform random number
Complex normal distribution is used for the corner of one correlation grid
  Uncorrelated Real/Imag
Interpolation is used to generate the complex normal random variable
Uniform distribution is generated from the phase of
ensures no abrupt change of between 0 and 1 spatially

## Slide 6: Appendix: example 2 of generating spatially consistent uniform random number
Generate spatially consistent normal random variable at specific location (x, y)
, this random variable could be generated based on the exponential decaying filtering scheme which is used for spatially consistent LSP generation in current 3GPP 3D channel model
Uniform distribution is generated based on

## Slide 7: Appendix: example 3 of generating spatially consistent uniform random number
Uniformly distributed random variables are used for the corner of one correlation grid
  Ai,j=Xj∈U(0,1), j=1,2,3,4
Interpolation is used to generate the complex normal random variable
Uniform distribution is generated from the X
is designed to ensure Y∈U(0,1)

## Slide 8: Appendix: example of generating soft LOS/NLOS and soft indoor/outdoor states
Soft LOS/NLOS state can be generated by filtering the binary LOS/NLOS state over space.
  FFS the average transition size

## Slide 9: Appendix: example of generating soft LOS/NLOS
A spatially consistent Gaussian number G with autocorrelation distance dLOS is generated. This is combined with a threshold value F determined via
  Here is the distance and is the LOS probability function. The soft LOS state is determined by a function approximating knife-edge diffraction: