## Slide 1: Way forward on antenna modelling for channel model calibration
Intel Corporation, Samsung
AGENDA: 8
3GPP TSG-RAN WG1 #AH Channel Model R1-161731
Ljubljana, Slovenia, 14th – 16th March, 2016

## Slide 2: Proposal
For calibration of the channel model TR captures the following antenna modelling for BS/MS
  For the BS/MS antenna model is uniform rectangular panel array, comprising MgNg panels, as illustrated below:
    Uniform rectangular element array with (M,N,P) and (dH, dV) as defined in TR36.873 is used as a single antenna panel.
    Mg is number of panels in a column
    Ng is number of panels in a row
    Antenna panels are uniformly spaced in the horizontal direction with a spacing of dg,H and in the vertical direction with a spacing of dg,V.
    FFS: MS may have two antenna panel arrays pointing to opposite directions
  The BS antenna element radiation pattern is the same as defined in TR 36.873
  The companies are encouraged to bring their proposal regarding modelling of the antenna element radiation patterns for the MS