## Slide 1: WF on Large Antenna Array Support
Huawei, HiSilicon, Samsung, Ericsson
R1-161732
3GPP TSG RAN WG1 Ad Hoc meeting for Channel Model
Ljubljana, Slovenia, March 14-16, 2016
Agenda Item: 5.2

## Slide 2: Background
In the Malta meeting, the agreed requirements (R1-161142) include:
  Support large antenna arrays
And the working assumption (R1-161150, further agreed in Ljubljana) says
  The spatial consistency which involves the evolutionary features and the correlation of channels between adjacent UEs or links on the large and small scale. This is useful for support of massive MIMO, mobility and beam trackings
  Support of 3D beamforming with large arrays
This contribution proposes a way forward for further study on these items.

## Slide 3: Proposal
Proposal 1: The SI should investigate if the angular distribution of clusters and paths within clusters can be modified from the 3GPP TR 36.873 assumptions to avoid non-physical behavior for large antenna arrays.
  An example solution to further investigate: use direct sampling method of Laplacian instead of uniform sampling of rays.
  Other solutions are not precluded
Proposal 2: The SI should consider if the phase error resulting from the plane wave assumption is acceptable. If not, modeling of spherical wave fronts should be considered.
Proposal 3: The SI should evaluate spatial consistency modeling proposals also from the aspect of supporting large antenna arrays.

## Slide 4: Appendix 1
The far field criterion allows 22 degrees phase error compared to plane wave. This may be too high for beam forming and interference cancellation.
Far field assumption can be assumed when the distance of an antenna array from a point source (transmitter or a nearest scattering/diffraction object) is

## Slide 5: Appendix 2
In the 3GPP 3D model the Laplacian power angular spectrum (PAS) is approximated by 20 sinusoids (randomly coupled between azimuth and elevation)
Large antenna array may see many sinusoids as individual specular waves. Additionally random coupling may lead to different correlation characteristics.
Instead of using the equal amplitude sinusoids, it is recommendable to use direct sampling method of Laplacian.

## Slide 6: Appendix 3
Very large arrays may see different propagation effects in two ends of the array.
This happens when the array size is larger than the consistency interval (or stationarity interval or correlation distance).
All small scale parameters such as angle of arrival, delay, Doppler, polarization, may be different along the array. Also large scale parameters such as shadowing may concern only a sub-set of antenna elements in the array.
This is also true with distributed antennas and cooperative networks.

## Slide 7: Appendix 4
Wideband array modeling
Implementation options:
Option 1: Channel is calculated separately for different frequency blocks
Option 2: To support large channel bandwidths and large antenna arrays, a wideband model which allocates a unique delay to each ray.