## Slide 1: WF on Atmosphere Attenuation
InterDigital, Samsung, Ericsson,……
3GPP TSG RAN1 #AH Channel Model
Ljubljana, Slovenia, March 14 - 16, 2016
Agenda Item: 7
R1-161747

## Slide 2
In R1-161150 and R1-161631, a list of additional features was agreed.
  One feature is “Foliage, atmosphere and rain attenuations as a function of frequency”
In R1-161694 and R1-161695, it is agreed
  Water vapor attenuation should not be considered for the UMi, UMa, and indoor office scenarios
  Subtract the impact of oxygen absorption from the measurement data before parameterizing the model
  Apply an oxygen loss to the generated channel impulse response on the form [dB]
  Rain attenuation should be considered with lower priority for the UMi and UMa scenarios, and not at all for the indoor office scenario
  Do not model foliage loss explicitly since it is already implicitly accounted for in the stochastic path loss models
How to model the oxygen loss ?
Background

## Slide 3
Reference [1] provides a method to calculate the oxygen loss
  The oxygen loss below 100 GHz is general low, except around 60 GHz
A simple look-up table on oxygen loss is provided around 60 GHz
  Oxygen loss at 52 GHz and 68 GHz is approximate
Oxygen loss can be modeled by this look-up table
  For carrier frequency beyond the range of this table, the oxygen loss is approximated by 0 dB
  For carrier frequency within the range of this table (52 GHz to 68 GHz), the oxygen loss is linearly interpolation based on this table
[1] ITU-R P.676-10, “Attenuation by atmospheric gases”, International Telecommunication Union Radiocommunication Sector ITU-R, 2013
Proposal
Carrier Frequency (GHz) | Oxygen loss (dB/km)
52 | 0
53 | 1.0
54 | 2.2
55 | 4
56 | 6.6
57 | 9.7
58 | 12.6
59 | 14.6
60 | 15
61 | 14.6
62 | 14.3
63 | 10.5
64 | 6.8
65 | 3.9
66 | 1.9
67 | 1.0
68 | 0