## Slide 1: WF on Transmission Gaps in NB-PUSCH Repetition
Sony, Intel, Panasonic, Sequans
R1-162002
3GPP TSG RAN WG1 NB-IoT Ad-Hoc Meeting
Sophia Antipolis, France, 22nd – 24th March 2016
Agenda item 2.3.1

## Slide 2: Background
The frequency of a HD-FDD UE’s transmission can drift beyond the tolerance of the eNodeB during a long uplink transmission, for example due to large number of NB-PUSCH repetitions

## Slide 3: Proposal
Introduce transmission gaps for long NB-PUSCH transmissions.
  During transmission gaps, the UE may switch to the DL and performs time/frequency synchronization
  Transmission gap is defined by a period and a gap length.
    Transmission gap is applied when the NB-PUSCH repetition is greater than the period
    RRC provides 4 bits to indicate period and gap in SIB
    FFS whether 2 bits for period and 2 bits for gap or joint indication of period and gap