## Slide 1: WF on PUSCH & PDSCH Repetitions
Sony, Panasonic, CATT, DoCoMo, …
R1-162003
3GPP TSG RAN WG1 NB-IoT Ad-Hoc Meeting
Sophia Antipolis, France, 22nd – 24th March 2016
Agenda item 2.2.3

## Slide 2: Proposal
A NB-PDSCH or NB-PUSCH encoded TB can be rate matched to one or more Resource Units
  For reference purpose, this one or more Resource Unit is called a Rate Matched Block
The size (number of Resource Units) of the Rate Matched Block is indicated in the DCI
The repetition pattern of the Rate Matched Block is realized by using Cyclic Subframe level repetition.
  In each cycle, each subframe in the Rate Matched Block is repeated consecutively for Z times
    Z = 4
  Different scrambling is used in each cycle
  NOTE: RV cycling is feasible under this repetition

## Slide 3: Example of Rate Matched Block & Cyclic Subframe Level Repetition (No RV Cycling)
TB
Coding
Rate Match
Resource Unit = 2 subframes
A
B
C
D
1 subframe
1 Resource Unit
Rate Matched Block
Repetition (8×)
A
A
A
A
B
B
B
B
C
C
C
C
D
D
D
D
Z=4
1 cycle
A
A
A
A
B
B
B
B
C
C
C
C
D
D
D
D

## Slide 4: Example of Rate Matched Block & Cyclic Subframe Level Repetition (RV Cycling)
TB
Coding
Rate Match
Resource unit = 2 subframes
A
B
C
D
1 subframe
1 Resource Unit
Rate Matched Block
Repetition (8×)
A
A
A
A
B
B
B
B
C
C
C
C
D
D
D
D
Z=4
RV1
A
A
A
A
B
B
B
B
C
C
C
C
D
D
D
D
RV1
RV2
RV2
RV1
RV2
1 cycle