## Slide 1: Way forward on RAN2 selection of TBS values for SI messages
Ericsson,…
R2-163293
3GPP TSG-RAN WG2 Meeting NB-IOT ad-hoc Sophia-Antipolis, France, 3-4 May, 2016

## Slide 2: Prerequisite – RAN1 agreements
From “RAN1 NB-IoT adhoc#2”
SI scheduling
  SI scheduling information is provided in NB-SIB1.
  One transport block of an SI message is transmitted over 8 consecutive valid DL subframes.
  SI scheduling information is given by –
    TBS (2 bits)
      Values to be decided by RAN2, possible values are {208, 256, 328, 440, 552, 680}

## Slide 3: RAN2 discussion
The TBS values that RAN1 informed RAN2 to choose from are considered too limiting as the lowest value is 208 bits.
Lower TBS values will be needed to reduce the padding if certain SIBs are sent alone inside an SI message (for example SIB-14-nb size is only ~20 bits)
The TBS numbers that we select now will also limit what could be done in future releases.

## Slide 4: Proposal
R2-163256 proposes the following:
  SI-message TBS is signalled by 3 bits in SIB1-NB and the range is {56, 120, 208, 256, 328, 440, 552, 680}. The number of subframes for transmission of TBS < 208 bits is up to RAN1 (an LS should be sent to RAN1).
The RAN2 assumption is that there is no impact to RAN1 specifications since
  the SI messages are processed like other NPDSCH transmissions
  entries from the existing TBS table for NPDSCH can be used also for SI messages
Proposed way forward is to agree in RAN2:
  the proposal above to include TBS=56 and TBS=120 and send an LS to RAN1
  a fallback of using 2 bits and make a selection of 4 values from the TBS values {208, 256, 328, 440, 552, 680} that can be used in case RAN1 responds with indication that extending the TBS for SI messages cannot be done
The LS to RAN1 should include the following content:
  Inform about the RAN2 assumption that smaller TBS values are possible to use for SI messages and that there is no RAN1 specification impact . Ask RAN1 to confirm this assumption
  Ask RAN1 to give feedback on what two entries (for TBS=56 and TBS=120) from Table 16.4.1.5.1-1 in 36.213 that should be used for SI messages as there are several options (see options in green in the TBS table on the next slide)

## Slide 5: NPDSCH TBS table
 | Subframes |  |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
0 | 16 | 32 | 56 | 88 | 120 | 152 | 176 | 208 | 224 | 256
1 | 24 | 56 | 88 | 144 | 176 | 208 | 224 | 256 | 328 | 344
2 | 32 | 72 | 144 | 176 | 208 | 256 | 296 | 328 | 376 | 424
3 | 40 | 104 | 176 | 208 | 256 | 328 | 392 | 440 | 504 | 568
4 | 56 | 120 | 208 | 256 | 328 | 408 | 488 | 552 | 632 | 696 680
5 | 72 | 144 | 224 | 328 | 424 | 504 | 600 | 680 | 776 | 872
6 | 328 88 | 176 | 256 | 392 | 504 | 600 | 712 | 808 | 936 | 1032
7 | 104 | 224 | 328 | 472 | 584 | 712 680 | 840 | 968 | 1096 | 1224
8 | 120 | 256 | 392 | 536 | 680 | 808 | 968 | 1096 | 1256 | 1384
9 | 136 | 296 | 456 | 616 | 776 | 936 | 1096 | 1256 | 1416 | 1544
10 | 144 | 328 | 504 | 680 | 872 | 1032 | 1224 | 1384 | 1544 | 1736
11 | 176 | 376 | 584 | 776 | 1000 | 1192 | 1384 | 1608 | 1800 | 2024
12 | 208 | 440 | 680 | 904 | 1128 | 1352 | 1608 | 1800 | 2024 | 2280
13 | 224 | 488 | 744 | 1000 | 1256 | 1544 | 1800 | 2024 | 2280 | 2536

## Slide 6: Stage 3 details
The signalling of this on SIB1-nb per SI-message (3 bits, value 0-7) is based on ITBS/ISF from 36.213:
The alternative if we stick with the restrictions of using ISF=6 (8 ms) would be:
ISI-TBS | ITBS | ISF | TBS
0 | 1 | 1 | 56
1 | 4 | 1 | 120
2 | 0 | 6 | 208
3 | 1 | 6 | 256
4 | 2 | 6 | 328
5 | 3 | 6 | 440
6 | 4 | 6 | 552
7 | 5 | 6 | 680
ISI-TBS | ITBS | TBS
0 | 0 | 208
1 | 1 | 256
2 | 3 | 440
3 | 5 | 680

## Slide 7: 36.213 tables Table 16.4.1.5.1-1 16.4.1.3-1
ISF | NSF
0 | 1
1 | 2
2 | 3
3 | 4
4 | 5
5 | 6
6 | 8
7 | 10
ITBS | ISF |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 16 | 32 | 56 | 88 | 120 | 152 | 208 | 256
1 | 24 | 56 | 88 | 144 | 176 | 208 | 256 | 344
2 | 32 | 72 | 144 | 176 | 208 | 256 | 328 | 424
3 | 40 | 104 | 176 | 208 | 256 | 328 | 440 | 568
4 | 56 | 120 | 208 | 256 | 328 | 408 | 552 | 680
5 | 72 | 144 | 224 | 328 | 424 | 504 | 680 | 
6 | 88 | 176 | 256 | 392 | 504 | 600 |  | 
7 | 104 | 224 | 328 | 472 | 584 | 680 |  | 
8 | 120 | 256 | 392 | 536 | 680 |  |  | 
9 | 136 | 296 | 456 | 616 |  |  |  | 
10 | 144 | 328 | 504 | 680 |  |  |  | 
11 | 176 | 376 | 584 |  |  |  |  | 
12 | 208 | 440 | 680 |  |  |  |  |