## Slide 1
RAN WG3 Chair: Yin Gao
RAN WG3 Vice-Chairs: Angelo Centonza, Gen Cao
RAN3 Secretary: Seonggu Shim
Status Report for RAN WG3
3GPP TSG RAN #105, Melbourne, Australia
Sep 9th – 12th, 2024
RP-241701

## Slide 2: Executive Summary
Total 606 Tdocs at submission deadline (excluding LSin received from other groups) in Q3
  6% LSs and related documents
  26% Maintenance: Rel-18 & earlier
  68% Documents to Rel-19 WIs
Updated endorsed guidelines for f2f meeting with 1-way remote access: R3-244003
TR30.531 Work Plan and Working Procedures - RAN WG3 was updated and approved in R3-244648
R19 AI/ML for NG-RAN SI and R19 Topology Enhancements SI are completed.
RAN3#125 | Aug 19th – 23th, 2024 Maastricht, NL
RAN #105 | Sep 9th – 12th, 2025 Melbourne, AU

## Slide 3: Tdoc submitted to RAN3
In R19, the total number of contributions around 610 (less than R18) for each RAN3 meeting seems reasonable.
Notes: w

## Slide 4: Tdocs for each Topic

## Slide 5: Overview of RAN3-led Rel-19 NR SI/WIs
UID | Name (acronym) | Acronym | Target completion | Old % (the same as in WI/SI SR) | WID | New % | Change or comments
1021092 | Data collection for SON (Self-Organising Networks)/MDT (Minimization of Drive Tests) in NR standalone and MR-DC (Multi-Radio Dual Connectivity) Phase 4 WI | NR_ENDC_SON_MDT_Ph4-Core | 25/09/2025 | 15% | WID: RP-234038 | 30% | 
1020083 | Study on enhancements for Artificial Intelligence (AI)/Machine Learning (ML) for NG-RAN SI | FS_NR_AIML_NGRAN_enh | 25/09/2024 | 80% | WID: RP-240323 | 100% | 
1020082 | Study on additional topological enhancements for NR SI | FS_NR_WAB_5GFemto | 25/09/2024 | 70% | WID: RP-240319 | 100% | 
WI: Black SI: Blue
Completed WI/SI: Red

## Slide 6: RAN3 CRs to RAN
List of RAN3 CRs to RAN in RP-241702, which includes:
  64 CRs were agreed in Q3.
    2 Rel-15: 2 Cat.F CRs
    4 Rel-16: 2 Cat.F CRs, 2 Cat.A CRs
    10 Rel-17: 7 Cat.F CRs, 3 Cat.A CRs
    48 Rel-18: 35 Cat.F CRs, 10 Cat.A CRs, 3 Cat.B CRs
      10 Non-Backwards-Compatible (NBC) CRs
        Rel-16 Cat.F(R3-244765)
        Rel-17 Cat.F(R3-244668)
        Rel-18 Cat.F(R3-244336, R3-244386, R3-244667, R3-244677, R3-244779, R3-244783, R3-244794), Rel-18 Cat.A(R3-244669)
        (Here is how 3GPP works with NBC changes)
    5 TEI18 CRs with TEI identifier
    * These two TEI identifiers were introduced at RAN#104 by RAN2(CR pack: RP-241543)
      Cat.B: [EM_Call_Exemption] R3-244651, R3-244786, R3-244787, linked RAN2 CRs (R2-2407829, R2-2407820)
      Cat.F: [Sub_1s_periodicity] R3-244656, R3-244657, linked RAN2 CR (R2-2403973)
      *Details of each agreed TEI18 CR and corresponding identifier are shown in p7 and p8.
  7 endorsed draftCRs to RAN2 specs.

## Slide 7: TEI 18 – RAN3 CRs
EM_Call_Exemption (Cat.B)
TDoc | Title | Source | Type | Spec | Version | Related WIs | CR | CR category | TSG CR Pack
R3-244651 | Introduction of Emergency call support in barred cells [EM_Call_Exemption] | Huawei, ZTE, China Telecom, China Unicom, Nokia, Qualcomm Incorporated, Ericson, CMCC, CATT | CR | 38.470 | 18.2.0 | TEI18 | 0153 | B | RP-241879
R3-244786 | Introduction of barring exemption for (e)RedCap and 2RX XR UEs [EM_Call_Exemption] | ZTE Corporation, China Telecom, China Unicom, Nokia, Qualcomm Incorporated, Ericson, Huawei, CMCC, CATT | CR | 38.423 | 18.2.0 | TEI18 | 1322 | B | RP-241879
R3-244787 | Introduction of barring exemption for (e)RedCap and 2RX XR UEs [EM_Call_Exemption] | China Telecom, ZTE, China Unicom, Nokia, Qualcomm Incorporated, Ericson, Huawei, CMCC, CATT | CR | 38.473 | 18.2.0 | TEI18 | 1415 | B | RP-241879

## Slide 8: TEI 18 – RAN3 Only CRs
Sub_1s_periodicity (Cat.F)
TDoc | Title | Source | Type | Spec | Version | Related WIs | CR | CR category | TSG CR Pack
R3-244656 | NRPPa support for sub 1s location information reporting periodicity [Sub_1s_periodicity] | Ericsson, ZTE, CATT | CR | 38.455 | 18.2.1 | TEI18 | 0156 | F | RP-241880
R3-244657 | F1AP support for sub 1s location information reporting periodicity [Sub_1s_periodicity] | ZTE Corporation, Ericsson, CATT | CR | 38.473 | 18.2.0 | TEI18 | 1446 | F | RP-241880

## Slide 9: Experience for GTW Usage in f2f meeting
RAN3 has 1 main meeting room and 1 breakout rooms in RAN3#125. GTW is provided for breakout room with best effort.
In general, the number of remote participants for main session is quite limited, less than 5. The audio device test for remote access was performed before daily session starts.
MCC and IT support during the meeting are sufficient.

## Slide 10: R19 SON/MDT WI
Progress in the last quarter
MRO Enhancements
  MRO for LTM:
    Reuse the existing connection failure definition.
    Take the existing detection mechanism descriptions as baseline.
    For failures due to inappropriate cell switch triggeringCU initiates analysis and may forwards the RLF report to the DU.
  MRO for CHO with Candidate SCG(s):
    MRO for Case 1a, 1b, 2a, 2b, 3a, 3b, 7a, 7b, 8a, 8b, 9 will be addressed.
    MRO for case 4/5/6 is in the scope.
    The RLF report include the type of the first fulfilled execution condition e.g. CPAC or CHO, fulfilment means all events of the type are met.
  MRO for S-CPAC:
    Reusing SCG FAILURE INFORMATION REPORT message over Xn for MN to report SCG failure of SCPAC to the concerned SN.

## Slide 11: R19 SON/MDT WI
Progress in the last quarter
MDT for NTN and Slicing
  Intra-NTN Mobility:
    Case 1 Too Late CHO Execution: RLF happens in the source cell before UE executes CHO (before or after T1 threshold starts), and the UE re-connects the cell other than the source cell.
      Distinguish if the RLF happens before or after T1
    Case 2 Too Early CHO Execution/CHO Execution to Wrong Cell: HOF happens or RLF happens shortly after successful CHO, and the UE re-connects in the source cell or a third cell.
      FFS on whether it matters if RLF happens within the duration or after the duration period.
  Network Slicing:
    For the immediate MDT, it is not needed to add measurements related to the slice unavailability and the lack of resources.
R18 Leftovers
  MRO for MR-DC SCG Failure:
    Take Stage 2 descriptions of PSCell change failure in TS37.340 as baseline for EN-DC and NGEN-DC SCG failure, and necessary updates can be added on top of it if needed.Take the existing detection mechanism descriptions as baseline.
    Introduce new SCG FAILURE INFORMATION REPORT message and SCG FAILURE TRANSFER message over X2 interface.
  RACH Optimization for SDT:
    The time from the start of RA-SDT to the reporting of RA report should be stored and reported in the RA report for SDT

## Slide 12: R19 SON/MDT WI
Impacts and dependencies on other WGs
LS to SA5 on SON for Network Slicing and enhanced area scope agreed in R3-244823.
Other important info
N/A

## Slide 13: R19 AI RAN SI
Progress in the last quarter
AI/ML assisted Network Slicing:
Slice UE performance needs to be introduced, while the granularity to support slice UE performance can be further checked in WI phase.
AI/ML assisted Coverage and Capacity Optimization:
Predicted CCO Issue (including predicted affected cells/beams) from CU to DU.
For split arch, gNB-CU sends the future coverage status to neighbour gNBs, together with an associated coverage modification cause.
For non-split arch, gNB sends the future coverage status to neighbour gNBs, together with an associated coverage modification cause.
Future CCO state and predicted CCO issue will be provided together with timing information.
Rel-18 Leftovers:
Energy Saving Enhancements:
  RAN3 agrees that enhancements to the node level EC granularity to a scope finer than a whole gNB could be beneficial, assuming that such enhancements enable network level energy saving.
Others:
  The following Rel-18 leftovers are recommended by RAN3 to be specified in Rel-19 normative phase:
    Mobility Optimization for NR-DC
    Split architecture support for Rel-18 use cases
    Continuous MDT collection targeting the same UE across RRC states

## Slide 14: R19 AI RAN SI
Impacts and dependencies on other WGs
N/A
Other important info
This SI is completed.

## Slide 15: R19 Topology Enh SI
Progress in the last quarter
WAB:
RAN3 recommends that a normative phase for WAB should be pursued.
The two logical gNB solution (as described in the LS from SA2) is feasible.
The single gNB solution including the options below shall be captured in the TR:
-Single gNB single cell using registration update due to TAC change
-Single gNB two cells with different TAC using NG HO
-Single gNB single cell without TAC change
In the TR conclude that solutions on mobility will be further analysed during normative phase. At study conclusion it is assessed that the two gNB solution is feasible. It remains to be verified whether the single gNB solution is feasible and acceptable.
Femto:
Conclusion on NG interface： direct connection of an NR Femto Node to the 5GC is already possible，an optional NR Femto GW is recommended for a normative phase.
Conclusion on Xn interface： direct connection of an NR Femto Node to other NR Femto Nodes / gNBs via the Xn interface, is already possible.
For Access control, NR Femto reuses the existing CAG functionalities, no stage3 impact has been identified.
Clarify the aspects to support local service via local UPF.
Impacts and dependencies on other WGs
WAB:Feedback from SA2 is needed concerning whether any of the options above of the single gNB solution is feasible and whether enhancements are needed.
Femto: RAN3 ask SA2/3 to take RAN3’s conclusion on NR Femto into account in future work.
Other important info
This SI is completed.

## Slide 16: R19 Mobility Enh WI
Progress in the last quarter
Introduce a new UE associated Class-1 XnAP procedure to update the LTM configurations for subsequent LTM.
Change the name of LTM Cell Switch Notification message to Cell Switch Notification message.
Reuse the Early Status Transfer and SN Status Transfer message for inter-CU LTM.
Adopt Class-2 procedure for candidate gNB-initiated LTM cancellation. Down select from Option1 and Option3 in the next meeting:
  Option 1: Reuse CHO Cancel
  Option 2: Rename CHO Cancel
  Option 3: Introduce new procedure
Impacts and dependencies on other WGs
N/A
Other important info
N/A

## Slide 17: R19 NR NTN WI
Progress in the last quarter
MBS broadcast service:
  Mapped Cell ID(s) could be used to describe the intended MBS service area for NTN.
Regenerative payload:
  Option 2 NG Removal/Setup can be used for Regenerative Payload NG interface management.
  RAN3 assumes that current mechanisms to support UEs performing RRC connection resume and RRC connection re-establishment may be reused in regenerative payload architecture, subject to implementation and deployment.
  RAN3 assumes that during the feeder link switch, AMF is not changed for the UEs. Whether there has any standard impact needs to be further checked.
Impacts and dependencies on other WGs
N/A
Other important info
N/A

## Slide 18: R19 IoT NTN WI
Progress in the last quarter
  RAN3 decides to work on Split MME architecture and Full CN on board architecture. Whether eNB only on board architecture is feasible or not can be discussed later.
Impacts and dependencies on other WGs
N/A
Other important info
N/A

## Slide 19: R19 Ambient IoT SI
Progress in the last quarter
System architecture figures agreed for Topology1 and Topology2.
RAN3 starts with inventory-only procedure.
For topology 1, AIoT RAN node ID can be considered as a location of AIoT device. For topology 2, UE ID of the AIoT-enabled UE can be considered as a location of AIoT device.
For Topology2, whether AIoT RAN needs to be revised as AIoT enabled gNB needs to be further checked in next meeting.
Three TPs (R3-244837, R3-244838, R3-244840) are agreed.
Impacts and dependencies on other WGs
N/A
Other important info
N/A

## Slide 20
Progress in the last quarter
On-demand SIB1:
  Case 2 can be supported with the below details:
    -UL WUS configuration is decided by NES Cell DU.
    -UL WUS configuration transmission from NES Cell DU to NES Cell CU. NES gNB-CU sends UL WUS configuration to Cell A gNB-CU over Xn Interface.
    -Upon the reception of the UL WUS configuration, Cell A can provide feedback to NES Cell on whether the WUS configuration Transmission for NES Cell is accepted in Cell A (e.g., confirm, reject). FFS if Cell A broadcasts it right away or not.
Impacts and dependencies on other WGs
N/A
Other important info
N/A
R19 Network ES WI

## Slide 21
Progress in the last quarter
New IEs should be introduced to support LP-WUS on NG, Xn and F1.
For RRC idle/inactive UEs, RAN3 to discuss the LP-SS and LP-WUS configuration is generated at the gNB-DU or the gNB-CU is FFS.
For RRC idle/inactive UEs, RAN3 to discuss whether Entry/exit condition is generated at the gNB-DU or the gNB-CU.
Impacts and dependencies on other WGs
N/A
Other important info
N/A
R19 LP-WUS WI

## Slide 22: R19 XR WI
Progress in the last quarter
From RAN3 perspective, the periodicity provided by QoS flow is sufficient for semi-static periodicity case. Other potential cases need to be clarified by SA2 if any.
For DL, MN/SN notifies SN/MN whether the DL PSI based discard is configured or not via XnAP signaling. New notification over F1AP and F1-U for DL PSI Discard.
SN reports the PDU Set based Handling Indicator in S-NG-RAN node Addition Preparation procedure and M-NG-RAN node initiated S-NG-RAN node Modification Preparation procedure for the MN-terminated SCG bearer, SN-terminated MCG bearer and SN-terminated SCG bearer.
Impacts and dependencies on other WGs
RAN3 sends reply LS to SA2 in R3-244844 with answers and wish to receive feedback if any.
Other important info
XR for NR-DC is completed in RAN3.

## Slide 23: TEI Corrections
Progress in the last quarter
Positioning:
  Alignment between stage 2 and stage 3 spec, and miscellaneous corrections for stage specs.
  Correction on Positioning SRS BW Aggregation and Tx Hopping.
  Corrections for the support of sub 1s location information reporting periodicity.
  The support of pre-configured SRS activation over XnAP and NRPPa.
(e)RedCap Emergency Call:
  RAN3 agreed the attached CRs to indicate the barring exemption bit in order to be used for the subsequent target node selection during emergency calls for outgoing connected mode mobility, according to new agreements in RAN2.
  The barring exemption bit in these agreed CRs is referring to TS 38.331, without mentioning the applicable UE types (i.e., the (e)RedCap, or 2Rx XR UEs) for future compatibility.
  The reply LS (R3-244788) is sent to RAN2.
SON/MDT:
  Stage 2 and Stage 3 corrections on triggering reporting of requested DL LBT information in UE Context Release procedure.
  Stage 2 clarification on detection mechanism of Too Early CPC/CPA Execution.
  Stage 2 correction on SPR retrieval and forwarding.

## Slide 24: TEI Corrections
Progress in the last quarter
Response to IETF:
  RAN3 responses IETF TEAS of overview on Annex part of Realization of Network Slices for 5G Networks Using Current IP/MPLS Technologies.
IAB:
  Corrections on stage 2 description on (m)IAB authorization when the MT is dual-connected and miscellaneous corrections.
MBS:
  Miscellaneous corrections on stage 2 description / ASN.1 / Stage 3 procedural texts.
Mobility Enhancement:
  LTM supports feature of MIMO with 2TA.
  Miscellaneous corrections on stage 2 and stage3 for LTM and S-CPAC.
  LS to RAN2 on Early TA acquisition for the inter-DU scenario agreed in R3-244793.

## Slide 25: My Heartfelt Thanks To:
Angelo Centonza, Gen Cao (RAN WG3 Vice-Chairs)
  For chairing the corresponding sessions and organizing social events during the meetings!
  Thanks Angelo for helping to organize the RAN3 social event!
Seonggu (RAN WG3 Secretary)
  For impressive hard work and continous support!
Tianyang, Jiajun, Xudong, Shankar, Lixiang, Nianshan...
  For their positive and hard work to complete R19 SIs!
  For moderating some tough email discussions and good support!
All Rapporteurs and moderators
  For their efforts to rapporteur updates and TEI corrections!
All RAN3 delegates
  For their positive, constructive and cooperative spirit and hard work!

## Slide 26: RAN3 Social Events in Maastricht
Details can be found in R3-244861 and thanks Pascal!
Notes: w