## Slide 1: Way forward for inter-gNB LTM
3GPP TSG RAN Meeting #105
Melbourne , AU
September 9-12, 2024
Agenda Item: 9.3.2.1
RP-241796
Qualcomm Incorporated, NTT DOCOMO, Vodafone , Sony

## Slide 2
Design principles of Rel-18 intra-gNB LTM
Observation: Rel-18 intra-gNB LTM offers numerous benefits, primarily reducing interruption time and signaling overhead during UE mobility.
Rel-18 LTM achieved the following:
  Enabled serving cell switch via L1/L2 signaling
  Reduced interruption time during serving cell switch
  Minimized configuration overhead with subsequent LTM support
  Avoided security updates due to cell switch
  Avoided PDCP reestablishment during cell switch
  Avoided CN impact
  Supported SA mobility, MCG mobility and SCG mobility
  Etc.

## Slide 3
Design principles of Rel-19 inter-gNB LTM
The justification of Rel-19 inter-gNB LTM in [RP-241515] states that enabling LTM operation between cells of different gNBs allows the network to gain the benefits of LTM for a significantly greater number of handovers.
The WID further states that “Rel. 18 intra-CU LTM procedure is considered as baseline for adding inter-CU support.”
Based on the above, the following is observed:
Observation: The design principles for Rel-19 inter-gNB LTM include:
  Extending LTM to inter-gNB cell switches
  Retaining the benefits of Rel-18 intra-gNB LTM
  Building upon the Rel-18 LTM procedure

## Slide 4
Candidate solutions for inter-gNB LTM
Observation: Many solutions have been proposed for inter-gNB LTM, including options for performing or skipping security updates, and various methods for configuring security updates.
gNB1
CU1
RLC
DU1
RRC + DRB
UE
gNB2
CU2
DU2
gNB2
CU2
RLC
DU2
RRC + DRB
UE
gNB1
CU1
DU1
gNB2
CU2
RLC
DU2
RRC + DRB
UE
gNB1
CU1
DU1
gNB1
CU1
RLC
DU1
RRC + DRB
UE
gNB2
CU2
DU2
Solution category 1: security change is required during inter-gNB cell switch
  Assumes the CU anchor for the UE’s RRC and DRBs changes with an inter-gNB cell switch
  Seven solution variants have been captured in an LS by RAN2 to SA3 [R2-2404037]
Solution category 2: security change is avoided during inter-gNB cell switch
  Assumes the CU anchor for the UE’s RRC and DRBs does not change with an inter-gNB cell switch

## Slide 5
Status of the candidate solutions in the RAN WGs (1/2)
The solution variants have been proposed by companies in both RAN2 and RAN3
All solution variants meet the primary use case, allowing a UE to move to a cell of a different gNB .
However, there is no proper discussion yet on which solution variant outweighs the others. Various solutions diverge from Rel-18 LTM in different ways, such as:
  Increasing the signaling overhead by transmitting RRC configuration messages b/w cell switches
  Increasing the interruption time by introducing extra processing steps on the UE
  Introducing complex handling of subsequent mobility
  Security complexity and Introducing CN impact
Observation: Rel-19 inter-gNB LTM still faces unsolved issues that necessitate further solution discussions in both RAN3 and RAN2.

## Slide 6
Status of the candidate solutions in the RAN WGs (2/2)
RAN2 sent an LS to SA3 to inquire about the security aspects of a subset of solution proposals
The LS prompted SA3 to start a WID on the matter.
  The target completion date for this WI is March 2025
  SA3 is not expected to provide a conclusive response before this date
Consequently, the down-selection among the inter-gNB LTM solutions, cannot occur until SA3 has replied.
In the meantime, this would be an opportunity for RAN3 and RAN2 to further discuss and gain a better understanding of the available solutions.
Observation: Before the SA3 WI [NRmobenh_sec_Ph1] concludes, RAN3/RAN2 cannot down-select among the inter-gNB LTM solutions. Until then, discussion of the available solutions should continue.

## Slide 7
Attempts for early down-selection of the inter-gNB LTM solutions
In the last RAN3 meeting (RAN3#125), individual companies requested to halt discussions on some of the Rel-19 LTM solution proposals and to perform an immediate pre-mature down-selection of these proposals.
Such down-selection is inappropriate under the present circumstances where:
  The WI still has at least 6 meetings to continue discussions.
  SA3 has not provided a reply on the security aspects of a subset of the available solution proposals.
  There was no proper technical discussion of available solutions.
Observation: During the RAN3#125 meeting, individual companies called for the immediate down-selection of the inter-gNB LTM solution proposals, which is not yet feasible.

## Slide 8
Proposal
Proposal: RAN3 [subsequently in RAN2] to allow further discussion on the proposed solutions to Rel-19 inter-gNB LTM based on the WI scope.
Conclude technical discussions by RAN#107 to make further progress with normative work.
Solution discussions in RAN3 and then in RAN2 should continue to address the remaining inter-gNB LTM issues.