## Slide 1
Source: | Spreadtrum Communications
Document for: | Discussion and decision
Agenda Item: | 9.2.5
3GPP TSG RAN Meeting #105 RP-241804
Views on AI mobility scope
Melbourne, Australia, September 9th-12th, 2024

## Slide 2
The status of R19 AI/ML for Mobility SI
  RAN2-led AI/ML for Mobility SID had been studied for the past three meetings. The cases, evaluation scenarios and goals that need to be studied for RRM measurement prediction are basically clear.
  RAN4 scope can be defined based on the achieved RAN2 progress.
For cell level measurement prediction model, at least consider the following cases: Case 1: To predict beam level results, then generate cell level results based on the predicted beam results; Case 2: To directly predict cell level results based on cell level results. Case 3: To directly predict cell level results based on beam level results
1st goal： Measurement reduction，e.g., measurement duration、measurement objectives
2nd goal：HO performance improvement
Case number | Prioritization | Evaluation scenario combination | target study goal | Methodology
1 | Low | FR1 to FR1 intra-frequency temporal domain case A | 2nd goal | TBD
2 | High | FR1 to FR1 intra-frequency temporal domain case B | 1st goal | Intra-cell
3 | High | FR1 to FR1 inter-frequency (frequency domain) | 1st goal | Inter-cell
4 | High | FR2 to FR2 intra-frequency temporal domain case A | 2nd goal | Intra-cell
5 | Low | FR2 to FR2 intra-frequency temporal domain case B | 1st goal | TBD
6 | Middle | FR2 to FR2 intra-frequency spatial domain | 1st goal | Intra-cell
L3 filtered beam level prediction cases are lower priority.
Case 1: To predict L1 filtered beam level results, then generate L3 filtered results based on the predicted L1 beam results.
Case 2: To directly predict L3 filtered beam level results based on the L3 beam level measurement results.
Case 3: To directly predict L3 filtered beam level results based on the L1 beam level measurement results.
For cell-level RRM measurement prediction
For beam-level RRM measurement prediction

## Slide 3
RAN4 scope of R19 AI/ML for Mobility SI
  As the RRM measurement prediction case has impact on existing RRM measurement requirements and performance which needs the evaluation from RAN4.
  We propose that RAN4 should study the potential impact on RRM measurement requirements and performance for different RRM measurement prediction cases and evaluation scenarios.
  Proposal 1：RAN4 should study the potential impact on RRM measurement requirements and performance for different RRM measurement prediction cases and evaluation scenarios.
  Additionally, the testability and interoperability of different AI mobility cases should be evaluated to guarantee its performance. The progress made in Rel-19 Air AI should be reused as much as possible.
  Proposal 2：RAN4 should study the testability and interoperability aspects for different AI mobility use cases, at least including：
    Relation to legacy requirements
    New testability aspects, e.g., FR1, inter-cell
    Other aspects are not precluded

## Slide 4: AI/ML for Mobility scope update
Evaluate testability, interoperability, and impacts on RRM requirements and performance [RAN4]
  Study the potential impact on RRM measurement requirements and performance based on RAN2 assumptions for the following use cases:
    Cell-level/beam-level measurement prediction
    RLF prediction
    Measurement Event prediction
  Study the testability and interoperability aspects, at least including：
    Relation to legacy requirements
    New testability aspects, e.g., FR1, inter-cell
    Other aspects are not precluded
  NOTE 2: RAN4 scope/work can be defined and confirmed by RAN#105 after some RAN2 discussions (within the RAN4 pre-allocated TUs)

## Slide 5
Thank you!