## Slide 1: Background on Intra-SAN Carrier Aggregation (CA) and fragmented carrier aspects for NR NTN
Source: Inmarsat, Viasat, Terrestar Corporation, Thuraya, Omnispace, Mediatek, Eutelsat Group, AccelerComm, ESA, JSAT, Novamint, SES, Lockheed Martin, Keysight Technologies
3GPP TSG RAN #105
September 9-13th, 2024, Melbourne Australia
Agenda: 9.1.4 - Proposals led by RAN4 (non-spectrum related)
TDOC: RP-241841
For: discussion
Public

## Slide 2: Rationale - DL Carrier Aggregation
Initial channel allocations may in certain regions be constrained by existing/legacy services, whereby channels may become available in non-contiguous areas of spectrum
With dual band satellites, in some cases the capacity and DL throughput could be significantly increased by aggregating carriers from different bands (e.g. n255 + n256) – in the same satellite (SAN)
Intra-band non-contiguous CA and inter-band CA would thus unlock increasing the channel BW (and thus cell throughput) to provide higher data rates
[n253]
n255
NR
NR
legacy services
n255
NR
legacy services
n256
NR
NR

## Slide 3: Rationale - UL Carrier Aggregation
Problem statement:
NR NTN smartphone is UL link-budget limited, thus limiting how many PRBs can realistically be allocated (typically 1-6)
Higher PRB allocations are practically limited by PA Max Out Power (MOP) which reduces the UL Power Spectral Density (PSD) as more PRB are allocated, especially for PC3 (23 dBm)
Proposed approach:
At least for inter-band, FFS for intra-band non-contiguous: By making use of multiple mid-band PAs available on the device, allocating PRBs to different Band Group PAs (e.g., 2GHz PA, 1.6GHz PA) we could increase the effective UL BW without compromising UL PSD. PA chain could be reused across TN-NTN bands, increasing number of available PAs.
Other 2TX configurations transmitting 2x # of PRB (same PRB) could also be included
Even stronger applicability to higher-class devices with higher power and higher-gain, such as non-smartphone devices (e.g. CPE/FWA, automotive/vehicular, UAV/UAS, VSAT-like directional/high-gain UE, satellite phone, etc)
PA1
PA2
L-band UL
CC1
L-band UL
CC2
Intermods/
suppression/
leakages?
PA1
PA2
L-band UL
CC1
S-band UL
CC2
Intra-band (FFS)
Inter-band 1
PA1
PA2
L-band UL
CC1
Ext L-band UL
CC2
Inter-band 2
e.g. 1-6PRB
e.g. 1-6PRB
e.g. 1-6PRB
e.g. 1-6PRB
e.g. 1-6PRB
e.g. 1-6PRB

## Slide 4: Rationale – UL CA with TX Band Switching
Required to support bands with common DL and different but very close UL segments, e.g. n250/n251, where UL is segmented by 7.5 MHz gap, and may be implemented with separate RF filter chains
Some UE may not support simultaneous 2TX UL CA in the same NTN band group
UE should thus be able to leverage both UL segments dynamically, to allow leveraging the wider bandwidth based on network scheduling. Another PA might also be in use either for TN or NTN in separate band group.
R16 UL TX switching can be leveraged
The UE can pre-configure both TX RF chains and dynamically assign UL transmission to the two bands depending on the requirement
PA1
L-band (n250) UL
CC1
Ext L-band (n251) UL
CC2
Inter-band 3
e.g. 1-6PRB
e.g. 1-6PRB
Combined L/Ext-L-band n250/n251 DL (1518-1559 MHz)
L-band (n250) UL (1626.5-1660.5 MHz)
CC1
Ext L-band (n251) UL
(1668-1675 MHz) CC2
+
+
OR

## Slide 5: Objectives and General Principles
Proposal 1: Identify and specify missing requirements to support NTN-NTN intra-SAN Carrier Aggergation (CA), for NR both intra-band and inter-band
  Both DL and UL CA must be supported  UL CA both leveraging 2 TX PAs independently on the UE and Single or multi-PA UL TX band switching
  The Carrier Aggregation (CA) framework for NR NTN should be band-agnostic at least starting with FR1-NTN, similar to TN
  The existing R16 Terrestrial CA framework should be the baseline (R17 NR NTN was understood to be baselined on R16)
  Assumptions from NTN single-carrier operation should not be changed, assuming all CC are on the same satellite payload (Intra-SAN) – i.e. same frequency error, timing error, etc
  Work should focus only on the delta to support NTN, the majority of the framework from TN should be reused to maximize feature parity/commonality.
  The framework could be later re-used as a baseline for FR2-NTN (e.g. Ka, FR2-Ku, etc)
  PC3 per-TX as a starting point, future applicability to HPUE

## Slide 6: Initial NR NTN CA combination Proposals
Initial propose combinations focus on L-band and S-band (n255, [n253], n256)
Actual combinations to be further discussed.
New or Modified Combination | Band combination configuration | UpLink configuration | Subclass | Power class of band X | Tx number of band X | Power class of band Y | Tx number of band Y | Total Power class
New | CA_n255(2A) | CA_n255(2A) | NR only | PC3 | 1TX/2Tx | - | - | PC3
New | CA_n256(2A) | CA_n256(2A) | NR only | PC3 | 1Tx/2Tx | - | - | PC3
New | CA_n253(2A) | CA_n253(2A) | NR only | PC3 | 1Tx/2Tx | - | - | PC3
New | CA_n255A-n256A | CA_n255A-n256A | NR only | PC3 | 1Tx | PC3 | 1Tx | PC3
New | CA_n255A-n253A | CA_n255A-n253A | NR only | PC3 | 1Tx | PC3 | 1Tx | PC3
New | CA_n256A-n253A | CA_n256A-n253A | NR only | PC3 | 1Tx | PC3 | 1Tx | PC3

## Slide 7: Fragmented Spectrum support
Background:
Current NTN spectrum often hosts some legacy services
The total potential available spectrum for NTN is quite significant, but in some areas it may be interrupted by some narrowband legacy services – re-farming will likely take place, but will take time
Some chunks may be available that are just slightly smaller than a full NR channel BW, and would work best aggregated with a parent channel
An NTN operator may specify a wider NR CHBW and schedule signalling and user data around existing legacy services, but currently this is mostly left to implementation, and there are no explicit mechanisms to facilitate this mode of operation
Total allocation is not expected to exceed 50 MHz
5-10 MHz CH
1-3 MHz block
SSB
1CC UE BW
1CC – Max 50 MHz
1-3 MHz block
Proposal 2: Include this minimum NTN objective as part of overall Fragmented Carriers SI for Terrestrial Networks, to maximize commonality with TN design and avoid dedicated effort
  Identify minimum enhancements needed (if any) for NR NTN, to facilitate aggregation of small intra-band non-contiguous fragmented spectrum blocks (smaller than the minimum NR Channel BW) interrupted by legacy services or other operator allocations through single wider Component Carrier of 50 MHz or less, with a single RF chain
legacy services