## Slide 1: Discussion on WI scope of Rel-19 XR
Melbourne, Australia, September 9-12, 2024
3GPP TSG RAN Meeting #105
RP-241928
Agenda Item: 9.3.2.3
Source: Xiaomi
Document for : Discussion and decision

## Slide 2: Background
  In WID RP-240791, a study phase of multi-modality is captured in Rel-19 XR WID which aims to facilitate effective support for multi-modal QoS requirements, e.g. synchronization and/or coordination. And efficiency enhancements for capacity or power consumption are also considered.
  The scope adjustment will be checked in RAN#105 as show below:

## Slide 3: Current progress of multi-modality awareness at RAN2 (1)
  In RAN2#126bis meeting, RAN2 has agreed that multi-modality awareness at RAN is supported for both UL and DL. And a LS is sent to SA2 to ask for the information (e.g., MMSID and/or synchronization thresholds) in order to allow coordinated handling of the flows at RAN;
  In RAN2#127 meeting, progress has been make on multi-modality awareness in RAN2.
      RAN2 has made it as WA that UAI can be extended for multi-modal awareness at least for uplink QoS flows in Rel-19 XR, by having the UE report existence of multi-modality application and association information among QFIs to gNB regardless of SA2 decision.
      RAN2 considers that based on multi-modal information, the gNB may perform joint admission control based. Details can be left up to RAN3 in potential WI phase. FFS if MMSID can be used for this purpose.
      =>Xiaomi’s view:
      Even though the LS from SA2 is still pending, RAN2 has decided to pursue multi-modal awareness for UL;
      RAN has envisioned the usage with multi-modality feature awareness (i.e., the foreseen NG-RAN behavior for coordinated handling of the flows at NG-RAN for access control);
      RAN has sufficient information to close the SI phase of multi-modality and move to WI phase.

## Slide 4: Current progress of multi-modality awareness at RAN2 (2)
  Other enhancements for multi-modal traffic not strictly related to multi-modality awareness, e.g. power saving, scheduling are also considered:
      For UL, RAN2 does not intend to perform LCP enhancements due to complexity vs gains concerns. However, for DL, whether traffic synchronization (on a per packet basis) can be achieved depends on whether packet level synchronization information can be provided from CN to RAN;
      RAN2 thinks PDU Set discard across QoS flows of the same multi-modal service based on the dependency information between the multi-modal flows can only be achieved in case the synchronization information can be available at the UE which is up to SA2/SA4.
      For power saving, RAN2 decides to support neither multiple active DRX configurations nor independent configuration of drx-StartOffset for the secondary DRX group.
      =>Xiaomi’s view:
      Traffic synchronization on a per packet basis can be deprioritized since it highly depends on SA2/SA4;
      PDU Set discard across QoS flows can be deprioritized since it highly depends on SA2/SA4;
      DRX enhancement will not be in Rel-19 XR WI phase.

## Slide 5: Summary
  Proposal 1: The study phase of multi-modality can be closed and move to Working Item phase.
  Proposal 2: RAN is suggested to consider the following objectives for Rel-19 XR WID for multi-modality:
Specify enhancements to facilitate efficient and effective support for XR application with Multiple QoS flows with multi-modal inter-dependencies, meeting multi-modal QoS requirements, e.g. synchronization and/or coordination. (RAN2, RAN3) For the UL, specify extension of UAI for multi-modal awareness at least for uplink QoS flows in Rel-19 XR; (RAN2) Signalling supports between nodes for multi-modal awareness, e.g., MMSID for joint admission control; (RAN3)

## Slide 6
THANKS!