## Slide 1
CMCC
Views on Scope of Rel-19 NR MIMO Phase 5
3GPP TSG RAN Meeting #105
Melbourne, Australia, September 9-12, 2024
Agenda item: 9.3.1.1
RP-241941

## Slide 2
Unified partial-coherent codebook
Motivation:
Antenna layout of partial-coherent UE: For 3/5/6/7 Tx UE with partial-coherent capability, the most possible antenna layout is to configure with multi-panel antennas. Ng≥1 antenna port groups (panels) can be considered where each group comprises coherent antennas, and across groups, antennas are non-coherent. Considering the practical implementation of 3Tx UE, it is most possible to be used in the foldable phones and applied with multi-panel antennas, where one of the panels is configured with two coherent antennas, and another panel is configured with one antenna.
Extendibility and forward compatibility: R15 supports 1/2/4Tx UL transmission, R18 supports 8Tx UL transmission, and R19 is discussing 3Tx UL transmission. We have separate discussion and different codebook for each release. We may need a unified codebook design principle that applies to any kinds of UEs in the future, such as 5/6/7Tx. It is beneficial for spec evolution and forward compatibility.
Observation 1: For partial-coherent 3/5/6/7 Tx UE, the most possible antenna layout is to configure with multi-panel antennas.
Observation 2: Unified codebook that applies to any kinds of UEs, such as 3/5/6/7Tx, is beneficial for forward compatibility.
3Tx UE
Antenna port group-1
Antenna port group-2
5Tx UE
Antenna port group-1
Antenna port group-3
Antenna port group-2
6Tx UE
Antenna port group-1
Antenna port group-2
7Tx UE
Antenna port group-1
Antenna port group-2
Antenna port group-3
Note: Other kinds of antenna port groups are not precluded.

## Slide 3
Partial-coherent UL codebook for 3Tx multi-panel
In RAN#104 meeting, additional objectives for Rel-19 NR MIMO Phase 5 have been discussed, with the following objectives for further discussion, including the partial-coherent UL codebook for 3Tx multi-panel.

## Slide 4
 | Partial-coherent UL codebook for 3Tx multi-panel
Codebook | No new codebook: Antenna port group 1 (2 coherent antennas): 2Tx full-coherent codebook Antenna port group 2 (1 antenna): Codebook is not needed
TPMI | TPMI: Antenna port group 1 (2 coherent antennas): 2Tx TPMI field can be reused Antenna port group 2 (1 antenna): TPMI is not needed The DCI field “SRS resource set indicator” is used for panel selection similar as Rel-18 STxMP
SRS | Follow Rel-19 agreements, disable port 1003 of 4 port SRS resource
Partial-coherent UL codebook for 3Tx multi-panel
3Tx UE
Antenna port group-1
Antenna port group-2
Proposal 1: Support partial-coherent UL codebook for 3Tx multi-panel in Rel-19.
Proposal 2: Define partial-coherent UL codebook for 3Tx multi-panel based on two antenna port groups.

## Slide 5
THANK YOU !