## Slide 1
CMCC
Views on Scope of Rel-19 ISAC
3GPP TSG RAN Meeting #105
Melbourne, Australia, September 9-12, 2024
Agenda item: 9.2.3
RP-241942

## Slide 2
Status of ISAC in RAN1
Check point at RAN#105: Whether to include additional study beyond channel modelling for ISAC will be discussed at RAN#105.
RAN1 status of ISAC:
  Based on rapporteur’s status report, the completion level is 35% for ISAC channel modelling, which is slightly behind the time schedule (40% TU). We still have many open issues need to be addressed, including RCS modelling, details of target channel, background channel, and spatial consistency. Furthermore, we still need time for calibration of ISAC channel model based on measurement results.
Observation 1: The time left for additional study beyond channel modelling for ISAC is limited.

## Slide 3
Evaluation of ISAC
Evaluation workload of ISAC: The study of ISAC should firstly consider the data type for evaluation. The data type is highly related to the interface and architecture. Three kinds of sensing architecture can be considered:
  Option1: CPRI-side. SF is a separate entity, sensing raw data is transmitted directly from CPRI to SF. In this case, the evaluation of ISAC is based on sensing raw data.
  Option2: BBU-side. SF is located at RAN side, sensing raw data is transmitted from AAU to BBU, sensing measurement (such as delay, velocity/Doppler, angle) is transmitted from BBU to SF, and sensing result (such as position and velocity of sensing target) is calculated at SF. In this case, the evaluation is based on sensing measurement.
  Option3: Core network-side. SF is located at core network side, sensing measurement is transmitted from RAN to core network, and sensing result is calculated at SF. In this case, the evaluation is also based on sensing measurement.
  Whether the evaluation of ISAC is based on sensing raw data or sensing measurement should be discussed.
  For BBU-side and core network-side sensing architecture, the sensing result calculated in SF is based on the sensing measurement, we may further consider the sensing data non-consistency and non-integrity caused by measurement error.
  For BBU-side and core network-side sensing architecture, we may further consider the additional transmission overhead. e.g. transmission overhead between BBU and core network.
  Proposal 1: If additional study beyond channel modelling for ISAC is included, both sensing raw data-based and sensing measurement-based evaluation should be considered in the study.

## Slide 4
THANK YOU !