## Slide 1
Considerations on R19 UAV
3GPP TSG RAN Meeting #105 RP-241945
Melbourne, Australia, September 9-12, 2024
Agenda: 9.1.2
Source: CMCC
Notes: 党的二十大报告44次提到科技，55次提到创新，36次提到人才。刚刚高总也提到了，党中央和国家，对中央企业勇担国家战略科技力量，强化企业创新主体地位的要求之高史无前例。

## Slide 2
Motivation: The Challenges of 5G-A Low-Altitude Network
Identification of UE
Fewer obstruction
More handovers and more HO failure
unordered handover due to fragmented cell
ordered handover
UAV-specific Identification
Interference Level
Propagation Model
Handover Complexity
generic identification
simple interference
Terrestrial Network
NLOS path dominated
Low-Altitude Network
LoS path dominated
complex interference
Reqiurement of trusted access and terminal authentication between NW and UTM
New interference: air-to-air, air-to-ground, and ground-to-air
Fig.1 China Mobile guarantees takeout deliveries in Shenzhen based on UAV
Fig.2 HELI-EASTERN 5G + aeromedical emergency rescue
CMCC has conducted testing and verification of low-altitude networking architecture, interference control, handover enhancement, trusted access, and service assurance in Shenzhen, Wuxi, Changzhou and other cities in China.
Flight Path Information Reporting
for Aerial UE Communication
Altitude-based Reporting/Configurations
for Aerial UE Communication
Subscription-based Identification
of Aerial UE
BRID and DAA Support via A2X Communication
R18 NR support for UAV

## Slide 3
Mobility Enhancement for UAV
Field Test Result: High HO Failure Ratio
(Subsequent) CHO Enhancements for UAV
Beam Type | DL |  |  |  |  | UL |  | Mobility | 
 | RSRP | SINR | THP | RI | BLER | THP | Txpower | HO Number | HO Failure
4.9G Main Lobe | -77 | 6 | 440 | 3 | 8 | 116 | 19.3 | 100 | 50%
2.6G Side lobe | -70 | 0 | 300 | 2.1 | 13.5 | 80 | 21 | 200 | 75%
In Rel-18, signalling of flight path information from UE to NG-RAN is supported;
Considering related fixed UAV flight path across large network areas, the CHO mechanism/Subsequent HO can help to minimize the required signalling and increase the robustness of the handover of the UAV；
This scenario is very similar to the terrestrial use cases such as high speed train scenario where the UE’s movement is predictable to some extent；
The NR Rel-16 CHO can be baseline for UAVs mobility solution, with the enhanced conditions, e.g., if the associated Height-, distance- or time-based condition is met respectively for one of the waypoints (location, time stamp)；
To specify the enhancement for UAV in Rel-19
    Mobility enhancement for UAV [RAN2, RAN3]
      CHO triggerred upon height-, distance- or time-based condition is met respectively for one of the waypoints (height, location, time stamp) height and flight path;
      Subsequent CHO based on flight path information

## Slide 4
Control on UE flying state for UAV Supervision
Motivation
Aerial vehicle devices are reqiured to be supervised by the UAV operator and regulatory department:
  The legacy device (i.e. a Rel-15/16/17 device and a non-UAV Rel-18 device) riding an aerial vehicle has to be considered for USS/UTM commercialization as well.
    For this scenario, the flying state information for the UEs could not be achieved since gNB cannot obtain actual measurement report of height and location from the legacy devices.
          However, the flying state information can be derived by gNB in implementation e.g. flying state detection through height-dependent serving cell distribution or RSRP/RSRQ as shown in the below figure.
  For Rel-18 UE, the gNB can have a accurate knowledge of the UAV mobile based on the authentification procedure or UE capability /measurement reporting for UAV
Consequently, the flying state information with the UE ID can be delivered to CN through Ng-interface from gNB.
Specify the provisioning method of flying state information delivered to 5GC from gNB, which information will help operator to provide proper solution to the both legacy devices (Rel-15/16/17 device and a non-UAV device in Rel-18) as riding in aerial vehicle and Rel-18 UAV UE [RAN3].
  Specify the NW signaling procedure and information exchange over NG interface (e.g. UAV identification request/response, related flying state information , etc.).
  Serving Cell distribution and Handover rate simulation data for drone UEs[R2-1713897, TR36.777]
Objectives

## Slide 5
  Thank you
Notes: 党的二十大报告44次提到科技，55次提到创新，36次提到人才。刚刚高总也提到了，党中央和国家，对中央企业勇担国家战略科技力量，强化企业创新主体地位的要求之高史无前例。