## Slide 1
Discussion on E-UTRAN TN to NR NTN Mobility
RP-241954
3GPP TSG RAN Meeting #105
Melbourne, 9th - 12th, September 2024
Source: ETRI, SK Telecom, Inmarsat, Viasat
Agenda item: 10.3.2
ETRI, SK Telecom, Inmarsat, Viasat

## Slide 2
Background
Mobility from E-UTRA TN to NR NTN has been approved as a new Work Item at RAN #102, with the scope limited to idle mode mobility only.
In Rel-17 and Rel-18, some solutions have been defined for NR NTN – NR NTN mobility and NR TN - NR NTN as well as NR NTN – NR TN mobility. However, mobility between E-UTRA TN and NR NTN and vice versa has not been defined yet. Based on current any foreseen TN deployments and capabilities of UEs it is valuable to also define the mobility between E-UTRA TN and NR NTN for idle mode mobility support.
Justification
The work item aims at specifying support for the following objectives: • idle mode mobility based on cell reselection from E-UTRA TN to NR NTN, where E-UTRA TN provides satellite information for NR NTN neighbor cells in a System Information Block. [RAN2] Note: • The solutions shall be reusing the existing signaling introduced for IoT-NTN and mobility procedures between NR TN and NR NTN to the maximum extent.
Objective
RP-XXXXXX

## Slide 3
Required Features for E-UTRA TN to NR NTN Mobility
Due to the limited scope of Rel-19 WI, the following legacy features for NR NTN cannot be supported for E-UTRA TN to NR NTN mobility cases
  Handover, RACH-less handover, Conditional handover, etc.
  Multiple SMTCs, NW-controlled adjustments of SMTCs, etc.
Support of at least one feature among above is important, given that the other features on LTE-NR interworking, such as dual connectivity, are NOT available for NTN scenarios
As of 2023, more than 50% of world population still has been being connected by E-UTRA
  Therefore, it is expected that E-UTRA TN to NR NTN mobility could be a common operation scenario, at least in some regions
Proposal 1: Support connected mode mobility/measurement from E-UTRA TN to NR NTN in Rel-19.
  To minimize the specification efforts, support of multiple SMTCs for connected mode mobility from E-UTRA TN to NR NTN may have high priority.
  This feature should have high priority in Rel-20, at least.
https://www.itu.int/itu-d/reports/statistics/2023/10/10/ff23-mobile-network-coverage/
RP-XXXXXX

## Slide 4
Conclusion
Proposal 1: Support connected mode mobility from E-UTRA TN to NR NTN in Rel-19.
  To minimize the specification efforts, support of multiple SMTCs for connected mode mobility from E-UTRA TN to NR NTN may have high priority.
  This feature should have high priority in Rel-20, at least.
RP-XXXXXX

## Slide 5
Appendix
The yellow highlighted features are not supported for IDLE mode LTE to NR NTN mobility
RAN2 agreements from RAN2#127:
…
6. RAN2 will not do further work to introduce multiple SMTCs in LTE
…
16.14.3.3 Measurements
The same principle as described in 9.2.4 applies to measurements in NTN unless hereunder specified.
The network can configure:
- multiple SMTCs in parallel per carrier and for a given set of cells depending on UE capabilities;
- measurement gaps based on multiple SMTCs;
- assistance information (e.g., ephemeris, Common TA parameters, ) provided in SIB19 for UE to perform measurement on neighbour cells in RRC_IDLE/RRC_INACTIVE/RRC_CONNECTED.
NW-controlled adjustment of SMTCs can be based on UE assistance information reported in RRC_CONNECTED. A UE in RRC_IDLE/RRC_INACTIVE can adjust SMTCs based on its location and assistance information in SIB19.
UE assistance information consists of the service link propagation delay difference(s) between serving the cell and neighbour cell(s).
TS38.300 V17.9.0