## Slide 1: Checkpoint on ISAC Study
Huawei, HiSilicon, China Telecom, Reliance Jio, China Unicom, CAICT, Turkcell, China Broadnet
3GPP TSG RAN Meeting #105
Melbourne, Australia, September 9-12, 2024
RP-242037

## Slide 2: Background and motivation
RAN Chair summary for Rel-19 workshop (RWS-234088) states:
  Very strong interest in channel modeling for integrated sensing and communication (ISAC), and also interest in other possible areas (e.g., use cases, scenarios, key performance metrics (KPIs), potential spec impact, etc.)
In TSG#102 SA sent question to RAN asking “RAN’s view whether the monostatic base station based sensing is feasible without any additional (dedicated) RAN WG(s) study/work”. RAN agreed to “discuss at RAN#105 whether to include additional study beyond channel modelling for ISAC”.
There is increasing interest from operators globally in network-based sensing for e.g. UAV detection and tracking.

## Slide 3: Sufficient progress was made in ISAC channel model, especially for UAV
Channel model:
  Target channel:
    For UAV RCS, an angle independent value or with random fluctuation is the common understanding, e.g., -20dB with fluctuation of normal distribution (0, 2dB), etc.
    RAN1 has agreed the crucial component of the channel response generation, i.e., direct path and indirect path generation.
    It is the common understanding to reuse the LOS and NLOS clusters for each link (Tx-ST or ST-Rx) and full concatenation of LOS+NLOS clusters of two links with complexity reduction not precluded for evaluations.
  Background channel:
    Background channel modelling for TRP-TRP bistatic and for TRP mono-static has been agreed with a couple of options for FFS.
    The options can be settled down in parallel discussion with evaluation once started.
Evaluation assumption:
  Key evaluation assumptions for UAV have been agreed.
    Possible down-selection among the options for assumptions can be fixed in the evaluation phase.
  Other assumptions, e.g., antenna configuration of TRP, etc. can be further discussed in evaluation phase once started.

## Slide 4: Proposal
Add a new objective to assess whether any specification work is needed for meeting the Rel-19 SA1 UAV sensing requirements with network-based sensing
Proposed new objective:
Evaluate sensing performance for UAV scenario with TRP monostatic sensing and TRP-TRP bistatic sensing
  Identify and define, if any, additional parameter values needed for the performance evaluations leveraging parameter values defined for channel model calibration
  Verify whether performance metrics defined in TS 22.137 for outdoor UAV detection and tracking can be fulfilled, assuming network implementations that require no change to NR waveform/reference signals/frame structure