## Slide 1
Huawei, HiSilicon
Checkpoint on NES on-demand SIB1
3GPP TSG RAN#105 RP-242038
Melbourne, Australia, 9-12 September, 2024
Agenda Item: 9.3.1.5

## Slide 2
Contents
Background
Key outcome from WGs
Observation and proposal

## Slide 3
Background
RAN1, RAN2 and RAN3 are tasked to study procedures and signaling method(s) to support on-demand SIB1 since RAN#102. And a checkpoint for normative work in RAN#105 for the study is set, as shown below (left part).
The following cases (right part) are defined for study purpose, with key outcome related to different cases from WGs are summarized in the next slides.
Study procedures and signaling method(s) to support on-demand SIB1 for UEs in idle/inactive mode, including: [RAN1/2/3]
  Triggering method by uplink wake-up-signal using an existing signal/channel.
  Wake-up-signal configuration provisioning to UE
    Note: No modification of SSB will be discussed under this objective
  Information exchange between gNBs at least for the configuration of wake-up signal, if necessary.
  Checkpoint for normative work in RAN#105
Agreement@RAN1#117
For the further study of on-demand SIB1 for idle/inactive mode UE, RAN1 focuses its studies on the following cases:
  Case 1: Option 1+A+X
  Case 2: Option 1+B+X
  Case 3: Option 2+B+Y
Where the options 1/2/A/B/X/Y are defined below:
  On target cell of UL WUS transmission:
    Option 1: UE transmits UL WUS to NES Cell
    Option 2: UE transmits UL WUS to Cell A
  On configuration provision for UL WUS transmission
    Option A: UE obtains the UL WUS configuration from NES Cell
    Option B: UE obtains the UL WUS configuration from Cell A
  On receiving of SIB1
    Option X: UE receives on-demand SIB1 from NES Cell
    Option Y: UE receives on-demand SIB1 from Cell A

## Slide 4
Key outcome from WGs - RAN1
Agreement @RAN1#117
For SIB1 in idle/inactive mode, prioritize RAN1 discussions on Case 2 and Case 3
Case 2 (Option 1+B+X) is feasible from RAN1 perspective.
Further study Case 3, focusing on the additional NES benefits over Case 2, feasibility, complexity, and spec impact.
Agreement @RAN1#118
For on-demand SIB1 in idle/inactive mode, Case 3 (Option 2+B+Y) is feasible from RAN1 perspective for some scenarios. Case 3 (Option 2+B+Y) is lower priority compared to Case 2 from RAN1 perspective.
RAN1 is inconclusive on whether the required specification support is justified by the observed NES gain for Case 3
Conclusion @RAN1#118
For on-demand SIB1 in idle/inactive mode, RAN1 was not able to achieve consensus to support Case 1 (Option 1+A+X) in Rel-19, while Case 1 is technically possible from RAN1’s perspective.
Agreement @RAN1#118
RAN1 recommends specifying on-demand SIB1 only for Case 2 (Option 1+B+X) in Rel-19.
Note: RAN1 strive to minimize impact to legacy UE.
Note: RAN1 specification impact to support this feature should be minimized.
(For illustration. See FL summary R1-2405370)
The following key agreements are achieved in RAN1:

## Slide 5
Key outcome from WGs - RAN2/3
Scenario 3 (case 1 in RAN1) @RAN2#126
RAN2 to wait for RAN1’s progress whether to support scenario 3
Scenarios @RAN2#127
No consensus for RAN1 case 3 in RAN2
OD-SIB1 SI conclusion @RAN2#127
RAN2 conclude that on-demand SIB1 is feasible from RAN2 perspective and recommend normative work of case 2 for on-demand SIB1
@RAN3#124
Focus on case2 in RAN3 first.
@RAN3#125
Case 2 can be supported with the below details:
UL WUS configuration is decided by NES Cell DU.
UL WUS configuration transmission from NES Cell DU to NES Cell CU. NES gNB-CU sends UL WUS configuration to Cell A gNB-CU over Xn Interface.
Upon the reception of the UL WUS configuration, Cell A can provide feedback to NES Cell on whether the WUS configuration Transmission for NES Cell is accepted in Cell A (e.g., confirm, reject). FFS if Cell A broadcasts it right away or not.
The following key agreements are achieved in RAN2:
The following key agreements are achieved in RAN3:

## Slide 6
Observation and proposal
The following can be observed based on outcome from WGs:
Proposal: Support normative work for on-demand SIB1 for UEs in idle/inactive mode based on Case 2 in Rel-19.
  Case 3 can also be included, striving for minimized additional specification impact.
With good and sufficient study from working groups, there is firm consensus to specify on-demand SIB1 for Case 2 (Option 1+B+X) for Rel-19 enhancements of network energy savings.
There is also large support of Case 3 to be included in Rel-19, which is feasible but lower priority than Case 2.
Based on RAN3 agreements, information exchange is not only between gNBs, but also between CU and DU within one gNB.
Huawei view on case 3: Networks energy savings can be achieved by Case 3 over Case 2 in some cases. Also, Case 3 brings limited additional standard impact, on top of the work for support of Case 2.

## Slide 7
Appendix: example of WID revision
SpecifyStudy procedures and signaling method(s) to support on-demand SIB1 for UEs in idle/inactive mode, including: [RAN1/2/3]
  Triggering method by uplink wake-up-signal using an existing signal/channel.
  Wake-up-signal configuration provisioning to UE
    Note: No modification of SSB will be discussed under this objective
  Information exchange between gNBs over network interfaces at least for the configuration of wake-up signal, if necessary.
  Checkpoint for normative work in RAN#105