## Slide 1
3GPP TSG RAN Meeting #105
Melbourne, Australia, September 9-12, 2024
RP-242043
Agenda Item: 9.2.7
Source: Baicells
Document for: Discussion and Decision
Views on 5G Femto

## Slide 2
Contents
Status of SI
Potential normative work
Objectives of WI

## Slide 3: Status of SI
“NR Femto node” is used, and an NR Femto node only supports NR.
4 architecture options for NG interface are studied and evaluated.
    Option 1, namely direct connection of an NR Femto node to the 5GC via the NG interface, is already possible.
    Option 2 with an optional NR Femto GW is recommended for a normative phase to maintain the existing infrastructure for an operator who has deployed LTE HeNBs.
2 architecture options for Xn interface are studied and evaluated.
    Option A, namely direct connection of an NR Femto node to other NR Femto nodes / gNBs via the Xn interface, is already possible.
Architecture
Access Control
Access to Local Services
Reuse the existing CAG functionalities, no stage3 impact has been identified.
LADN and edge computing functionality can be reused.
3 identified aspects (out of RAN3 scope) may require further analysis.
  Aspect #1: Scalability of local UPF discovery e.g. when using mobile edge computing solutions
  Aspect #2: N4 interface switch-on/off
  Aspect #3: N4 interface aggregation

## Slide 4: Potential normative work
Architecture
  Normative work for Stage 2
    Specify NR Femto Architecture Option 2 (NR Femto GW) for NG interface.
    Specify functions supported by the NR Femto which may be the same as those supported by an gNB (e.g. access control).
    Specify functions supported by the NR Femto GW (e.g., NG-Flex, NNSF).
  Normative work for Stage 3
    Signalling enhancements for NG interface in Architecture Option 2 may be needed to maintain consistency with LTE HeNBs specifications (e.g., INNITIAL UE MESSAGE, PATH SWITCH REQUEST etc.)
Access to Local Services
  RAN WG may need to send LS to SA WG to consider an update of the new WID on System aspects of 5G NR Femto to include further analysis of the three aspects in TR 38.799.

## Slide 5: Objectives of WI
    The objectives of the 5G Femto work are as follows:
    Specification to support NR Femto architecture option 2 as captured in TR 38.799 [Stage 2].
    Specification for functions supported by the NR Femto which may be the same as those supported by an gNB (e.g. access control) [Stage 2].
    Specification for functions supported by the NR Femto GW (e.g., NG-Flex, NNSF) [Stage 2].
    Specification of necessary signalling enhancements for NG interface of NR Femto architecture option 2 [Stage 3].