## Slide 1: Motivation of new WI proposal on HAPS additional operating Bands
SoftBank Corp.
3GPP TSG RAN Meeting #105 RP-242064
Melbourne, Australia, 9-12 September 2024
Source: SoftBank Corp.
Agenda Item: 9.1.5

## Slide 2: Background－Identification of Band n1 for HAPS
【Agreement to study HAPS bands】
To study identifying an operation band in FR1 for HAPS conducting coexistence study at 2 GHz [1] [2]
【Co-existence study between HAPS-TN and HAPS-HAPS】
ACLR & ACS requirements on HAPS BS have been determined based on a 5% throughput degradation in the victim network in HAPS and TN co-existence scenarios.[3]
Required values of HAPS BS were agreed for ACLR as 45dB and ACS as 46dB and were captured in TR38.863 with the simulation assumptions [4] [5]
【HAPS RF requirements】
HAPS BS requirements are captured in TS 38.104, and HAPS BS class would refer to Wide Area BS class which is specified in clause 4.4 of TS 38.104.[6]
NR band n1 is applied for HAPS operation considering that ITU Radio Regulations identified HAPS frequency band only in 2 GHz at that time, and UEs as defined by current TS 38.101-1 can support HAPS deployments with no additional changes needed in TS 38.101-1. [4]
The identification of band n1 to the HAPS operation in REL-17 was conducted in the following manner.

## Slide 3: Background－Objectives of HAPS agenda in WRC-23
HAPS is expected to be used as an efficient method to cover terrestrial networks, particularly in unserved and underserved areas, by utilizing the frequencies owned by existing MNOs themselves.
However, frequencies for HAPS use are strictly limited in the Radio Regulation (only 2 GHz band is available now). WRC-23 considered to enable flexibility use according to the circumstances of each country and MNO.
Additional HAPS frequencies identified as follows will allow complementary existing MNO’s networks to connect more people, helping to bridge the digital divide with the flexibility to select the frequency bands that best serve their particular connectivity and coverage needs.
HIBS: HAPS as IMT Base Stations

## Slide 4: Background－Result of WRC-23
As a result of WRC-23, it was decided that 1.7GHz-2.1GHz, and 2.6GHz bands will be available globally for HAPS. Additionally, 694-960MHz band will be available in many countries.
Since the Band n1 was defined for HAPS operation based on the existing RR, additional bands would be defined as well.
The 3GPP specification (TS38.104)
”NR operating band n1, which is defined in Table 5.2-1, can be applied for HAPS operation.”

## Slide 5: SoftBank’s HAPS aircraft development
4
© SoftBank Corp.2024 All Rights Reserved.
2019~2020
September
2020
March 2023
September
2023
Successful low altitude flight
PoC for large wingspan
fixed-win aircraft
Reaching the Stratosphere
World’s first 4G/LTE communication during Stratospheric Flight through zoom video call
World's First 5G Connectivity
from the Stratosphere
Zoom video call between Japan and Rwanda
Successfully Flight Test of Sub-scale Model of Next-generation HAPS

## Slide 6: Technological Progress in the HAPS industry (1)
＜Airbus/AALTO HAPS＞
Airbus’ Zephyr achieved:
  64 days of stratospheric flight, across two 2022 flights, proving Zephyr can operationalize the stratosphere
  4,000+ total flight hours and demonstrating precise stratospheric maneuverability and station-keeping over points on the ground
AALTO’s services, targeting launch in Japan and a global entry-into-service in 2026.
Source: https://www.aaltohaps.com/zephyr
＜Kraus Hamdani Aerospace＞
Kraus Hamdani Aerospace developed:
  HAPS which achieved 26 hours and 10 minutes airborne with the K1000P (group-2 fully electric UAS) running high power mil spec radios and a highly capable EO/IR ISR FMV payload
Source: https://krausaerospace.com/
The latest technological progress (solar cells, next-gen batteries, lightweight aircrafts and motor & propellers) have paved the way for HAPS.
As shown in the following slides, HAPS Alliance members are developing HAPS airframes and communication payloads for commercialization (See also HAPS Alliance Media Coverage: https://hapsalliance.org/media-coverage/)

## Slide 7: Technological Progress in the HAPS industry (2)
＜Prismatic＞
Prismatic’s PHASA-35:
  Maiden flight completed in 2020.
  First stratospheric flight achieved in 2023, reaching an altitude of 66,386 feet, with a total mission duration of over 24 hours.
Source: https://www.prismaticltd.co.uk/
＜Stratospheric Platforms Limited＞
Stratospheric Platforms Limited’s STRATOMAST provides:
  3G / 4G / 5G / 6G connectivity direct to user handsets across vast areas, opening up new 5G services and providing significant additional revenue opportunities for MNOs at up to 90% cheaper than rural terrestrial masts.
  1 HAP provides a service equivalent to ~450 terrestrial masts:
  Direct to user handset connectivity / 1ms latency
  Providing connectivity speeds of over 200MbpS
  With coverage at least 15,000km2
＜SoftBank/AeroVironment＞
SoftBank’s Sunglider:
  Succeeded in a stratospheric test flight in 2020 that lasted 20 hours and 16 minutes, with 5 hours and 38 minutes in the Stratosphere
  Demonstrated its high-performance capabilities under demanding conditions and strong wind
  Successfully completed multiple previous test flights
Source: https://www.softbank.jp/en/corp/philosophy/technology/special/ntn-solution/haps/

## Slide 8: Technological Progress in the HAPS industry (3)
＜Aerostar＞
Aerostar develops stratospheric balloons that:
  Successfully delivered LTE networks connections from an altitude of 20km in 2022
  Demonstrated linger over a certain area for weeks to months by using solar power
  More than 10,000 operational flights, 500 consecutive days presence, and 2 million flight hours in the stratosphere
Source: https://aerostar.com/news
＜SCEYE＞
SCEYE builds high-performance HAPS for stratospheric infrastructure that:
  Successfully provided an internet connection from stratosphere to the ground in 2021
  Demonstrated the airship’s ability to stay over a designated area for operation for months by using renewable energy in 2022
  Demonstrated high-resolution environmental mapping in 2023
Source: https://www.sceye.com/sceye-media/
＜Stratosyst＞
Stratosyst develops SkyRider as their stratospheric platform:
  To provide long-term commercial flights in order to provide connectivity, earth observation, natural disaster monitoring and more
  Designed for smaller payloads and global operation
Source: https://www.stratosyst.com/#press-and-news

## Slide 9: Conclusion and proposal
The objective of this WI is to identify additional bands for HAPS use in the 3GPP specification based on the results of WRC-23, with the same approach as in previous studies in Release-17.
WRC-23 concluded additional frequencies for use of HAPS that provide flexibility for existing MNO’s to select their own frequency bands that best serve their particular connectivity and coverage needs.
The latest technological progress contributes HAPS industry to accelerate its development and many players are currently involved in commercialization of HAPS.
The proposal of the addition of HAPS bands to the 3GPP specification aligns with the objectives of WRC-23 to provide flexibility in frequency utilization, and considering the technological progress in the HAPS industry, we believe that this WI should be started at this timing.

## Slide 10: Reference
[1] R4-2103877 WF for NTN General Part, Moderator (THALES)
[2] R4-2106103 WF on [307] NTN_Solutions_Part1 (NTN general part) , Moderator (THALES)
[3] R4-2103878 Way Forward for NTN Coexistence Study, Moderator (Samsung)
[4] R4-2207346 Way Forward on NTN_solutions_Part1, Moderator (THALES)
[5] R4-2205557 TP to TR 38.863 on HAPS simulation update (Nokia)
[6] R4-2203080 Way Forward on NTN_solutions_Part1, Moderator (THALES)