## Slide 1: Motivation on R19 UAV WI in RAN
Agenda Item: 9.1.2
Source: CATT, China Telecom, China Unicom, Kyocera, Lenovo, vivo, LG Electronics Inc., CMCC, NTT DOCOMO INC, Qualcomm Incorporated, Turkcell, Spreadtrum, LG Uplus, SK Telecom, CBN, China Broadnet, Reliance Jio
3GPP TSG RAN #105
Melbourne, Australia, September 9-12, 2024
RP-242134

## Slide 2
Background on R19 UAV in RAN
Proposed WID for R19 UAV in RAN
  Motivation
  Proposed Scope
  Proposal for Rel-19 UAV WI approval

## Slide 3: Background of R19 UAV discussion in RAN
      The current discussion status for R19 UAV is as follows according to the summary (RP-232627) in RAN#101, which should be considered as the baseline for further discussion.
Conclusions
Large operator support for UAV as one of the most important Rel-19 topics (within the items in this offline) from a commercial and mission critical perspective.
Architectural changes will not be part of the UAV work (i.e. any architectural enhancements can be considered under NTN)
Starting point of an acceptable objective:
  Mobility enhancements
    Specifying new CHO triggering events
    Studying/specifying LTM enhancements for UAV
  No transmit zone (if SA2 will also do work on this)
  Enhancements for RRC_IDLE/RRC_INACTIVE

## Slide 4
Background on R19 UAV in RAN
Proposed WID for R19 UAV in RAN
  Motivation
  Proposed Scope
  Proposal for Rel-19 UAV WI approval

## Slide 5: General Motivation
Need of a Rel-19 WI for NR UAV enhancement in RAN
Increasing interests in uncrewed aerial vehicles (UAV) based services have been witnessed globally in recent years
  In some regions, there are great interests from governments and operators to build a “Low-altitude” network to support “Low-altitude” economy by UAV communications, with strong industrial radiations (e.g. logistics, transportation, agriculture, meteorology, etc.) and expectation of trillion-level industrial and market scale.
  Great expansion and growth of commercial drone/UAV markets are witnessed in a variety of regions throughout the globe.
In Rel-18, UAV specific enhancements were introduced in NR, aiming at more effective support of UAV based services in NR RAN but with following limitations:
  Mobility Aspects: No consideration on UAV specific factors in those advanced mobility mechanisms in NR (e.g. CHO, LTM, etc.) and No consideration on IDLE/INACTIVE mobility enhancements. These make the current 5G NR probably insufficient/ineffective to support the mobility requirements of UAV communication thus far.
  UAV Supervision Aspects: No network based identification/detection of UAV motion status by the 5GS, making the supervision of UAV communication in 5G system (incl. both Rel-18 and pre-Rel-18 UAVs) ineffective or even unreliable today.
  To this end, further enhancements in NR to support UAV based service are needed in Rel-19, with the main objectives to support further UAV-specific mobility enhancements and UAV detection and supervision.

## Slide 6
Background on R19 UAV in RAN
Proposed WID for R19 UAV in RAN
  Motivation
  Proposed Scope
  Proposal for Rel-19 UAV WI approval

## Slide 7: CHO enhancements
High accuracy positioning in variable scenarios and use cases indoor/outdoor
-- Continue enhancements
Improving mobility performance of aerial UEs – CHO enh.
Motivation:
According to TR 36.777, the number of detectable cells and the range of the detected cells increase as UAV altitude increases. The distribution of reachable distance to serving cell demonstrated that aerial UEs can be served by a geographically far-away cell, compared to ground UEs. For CHO, this means there could be different candidate cells in different altitude ranges . So CHO needs to take UAV altitude/flight path into account for candidate cell preparation and CHO triggering, so to support CHO for UAVs at different altitudes effectively (e.g. executed to the cells in-sight with optimal radio conditions). Besides, in practical deployment, the gNBs deployed to support UAV based services in a given area are expected to be with an inter-site distance of several kilometres (e.g. 3 ~ 5 km) which typically assume no Xn deployment due to e.g. cost-saving consideration. The NG-based CHO (which has not been supported except for NTN) needs to be specified in NG-RAN to provide efficient CHO support for UAV.
Objective:
Specify CHO enhancements, considering height/flight-path related events and practical RAN deployment to support UAV communication:
Specify height-based/flight path based CHO trigger events. [RAN2]
Specify NG-based CHO in terrestrial network for UAV. [RAN3]
Field Trial results captured in TR 36.777

## Slide 8: LTM enhancements
Improving mobility performance of aerial UEs - LTM enh.
Motivation:
The detection of the LTM candidate cells may be varied with the height of the UAV. Following existing LTM mechanism to serve UAV, the L1 measurement may be wasted when the candidate cells become undetectable, and thus the dynamic selection of candidate cells in order to reduce the L1 measurement and reporting should be supported. Also, considering the much more in-sight cells detected by a UAV than a normal ground UE and thus the potentially more frequent handover performed by a UAV, support of subsequent LTM mechanism is beneficial to avoid signaling overhead for frequent candidate cell (re)configuration in UAV communication. This should take into account UAV specific factors regarding aspects on e.g. L1 measurement events, candidate cell activation/deactivation, etc.
Objective:
Specify support of LTM enhancement for UAV, taking height and flight path factors into consideration, including following objectives:
  Signalling reduction on L1 measurement report for undetectable candidate cells (e.g. UAV specific trigger event). [RAN2]
  Subsequent LTM with UE autonomous candidate cell activation/deactivation (based on planned flight path). [RAN2, RAN3]
  NOTE: This objective is to be carried out based on the outcome of related work in Mob Phase-4 WI.
7
Field Trial [5] results captured in TR 36.777

## Slide 9: IDLE/INACTIVE mobility enhancements
IDLE/INACTIVE mobility enhancements
Motivation:
Some UAV based services may not expect continuous large volume data transmissions. For example, periodic data transfer alongside a UAV’s flight path with low data volume or low frequency (e.g. monitoring data of atmosphere/logistics, etc.), or image/video capture with instantaneous data transfer by a hovering UAV before it flies away. In such scenarios, a UAV is not necessarily kept in CONNECTED mode, but can be sent to IDLE mode after it finishes data transmission or sent to INACTIVE mode for small data transmission. In practice, a gNB aiming to provide better support of UAV based service can deploy additional antenna with up-tilted angles, in order for a better coverage to the air than normal down-tilted gNBs serving only ground UEs (which can serve UAVs only by side lobes). Such gNBs may co-exist with the legacy gNBs only serving normal ground UEs in a typical deployment scenario. To enhance performance of UAVs in IDLE/INACTIVE as in above exemplary occasions, it is preferably for the IDLE/INACTIVE UAVs to camp on the gNBs that provide enhanced UAV communication support (e.g. with dedicated antenna deployment). Considering also that such gNB with dedicated antenna deployment may support not only UAVs but normal ground UEs as well, it may apply altitude based SSBs introduced in Rel-18. It is preferable for a UAV to measure the SSB at its altitude, and camp on the cell thereon quickly. With the limitation that Rel-18 altitude based SSB only applies to CONNECTED UEs, it is beneficial to extend its use to IDLE/INACTIVE also. Thus, enhancements on IDLE/INACTIVE mobility for UAV can be considered.
Objective:
Specify UAV-specific IDLE/INACTIVE mobility enhancement: [RAN2]
  Specify mechanisms prioritizing frequency(ies)/cell(s) with enhanced UAV-based service support for cell (re)selection.
  Extend the use of altitude based SSB to support IDLE/INACTIVE mobility.

## Slide 10: UAV Detection and Notification
UAV Detection and Notification
Motivation:
In practice, there is the need for the network to know the real-time motion status of a UAV, so as to carry out effective supervision in the network (e.g. detection/control on communication of spurious UAVs). For example, the network may need to be aware of whether a UAV is in the flying status, and thus start supervision on its communication (e.g. release of connectivity or de-registration, if needed) w.r.t. its dynamics in a timely and on-demand manner, based on the interaction with supervision platform. Such demand may apply to both pre-R18 and R18 UAVs. It is possible for NG-RAN to identify a UAV with related dynamics via implementation-specific manners (e.g. via measurements, interference detection, etc.). However, due to the lack of specification support, NG-RAN currently cannot send such information to 5GC, which thus cannot contact the supervisory platform to provide necessary control to the UAVs’ communication in the field as intended.
Objective:
Specify UAV motion status detection and notification from NG-RAN to 5GC: [RAN3]
  Specify the NW signaling procedure and information exchange over NG interface (e.g. UAV identification request/response, related motion status, etc.).

## Slide 11: Alignment with SA conclusion on NTZ
UAV Detection and Notification
Motivation:
For NTZ, the Final conclusion of SA2 UAS phase-3 SI is “The UAV UE(s) configured with the following NTZ assistance information is responsible to provide such assistance information to the modem and to perform NTZ enforcement in implementation dependent ways” (See S2-2409542). This conclusion is also in line with RAN plenary conclusion in the LS RP-241668 that the UE is responsible of following any applicable NTZ regulations. On the other hand, RAN WGs may still need to investigate whether some AS operations (e.g. cell (re)selection, connection control, etc.) in the current Spec prevents this implementation specific NTZ enforcement at the UE side. If necessary, clarification in RAN Specs may be needed to allow this UE implementation specific NTZ enforcement concluded by SA2. Note that this is not to introduce enhancement, but to align UE AS behaviors with SA2 conclusion.
Objective:
Align UE AS operations with SA2 conclusion on NTZ enforcement: [RAN2]
  Study if current Spec allows the implementation-specific NTZ enforcement, and introduce necessary spec change/clarifications to align with SA2 conclusion (if needed).

## Slide 12
Background on R19 UAV in RAN
Proposed WID for R19 UAV in RAN
  Motivation
  Proposed Scope
  Proposal for Rel-19 UAV WI approval

## Slide 13: Proposal for Rel-19 UAV WI approval
Proposal for WI approval
It is proposed to approve a WID for Rel-19 UAV in RAN, taking into account the objectives listed in Page 6 ~ 10 and with the following WG schedule and TU allocation.
Proposed TU allocation
  RAN2: Total 3 TUs (.5 TU per meeting)
  RAN3: Total 3 TUs (.5 TU per meeting or start later)
  RAN1/4: No TU

## Slide 14
Notes: 万物互联，无限沟通
Universal Connectivity, Infinite Communication.