## Slide 1: Discussion on Checkpoints for Rel-19 MOBILITY Phase4 WI

## Slide 2: Checkpoints for RAN#105
Checkpoint#1: Work on Conditional LTM (CLTM)
  While support of CLTM is included in WID, work on CLTM is not started yet until RAN#105 checkpoint, as specified in WID:
  At RAN#105, RAN group need to discuss the following :
    Whether to start work on CLTM since RAN#105
    Work scope of CLTM
Checkpoint#2: Harmonization to avoid any overlap between Event-triggered L1 report for LTM and Event-triggered L1 report for MIMO
  RAN2 has been making progress on event-triggered L1 report for LTM, independent of event-triggered L1 report for MIMO, as guided in WID:
  At RAN#105, RAN group need to discuss the following:
    Any scope reduction is required for Mobility WI, with the assumption that overlapped work, if any, is handled by MIMO WI
Specify support of conditional LTM [RAN2, RAN3, RAN1]
  …
  Checkpoint to review objective at RAN#105. RAN WG work to not start before this checkpoint
  Specify necessary components to support event triggered L1 measurement reporting [RAN2, RAN1]
    RAN1 and RAN2 to progress independently on the event triggered measurements objectives of their respective MIMO and Mobility enhancement WIs. Review progress at RAN#105 to see if any modification of objectives is required to avoid/manage any overlap in the work

## Slide 3: Initiation of CLTM work
Whether to start work on CLTM since RAN#105
  Our observations are as follows:
  Among the three main objectives in WID, two on-going objectives (inter-CU LTM and measurement related enhancements) are making reasonable progress in RAN2.
  Work load for the two objectives is considered manageable so far, because RAN2 has been restricting target scenarios with proper prioritization of essential functionalities and down-prioritization of over-optimization during discussion.
  Initiation of CLTM work from RAN#105 will increase work load in RAN2, RAN1, RAN3. But we believe this should not be the reason not to start CLTM work because
    a) this work is already included as objective in WID
    b) the work load until now is currently acceptable so far.
    c) If the scope of CLTM work is reasonably tailored and decided, we believe the overall work load with additional work to support CLTM remains manageable for entire Rel-19 timeline
Proposal 1: Work on CLTM is initiated since RAN#105.

## Slide 4: Work scope of CLTM
RACH-based Intra-CU CLTM
  CBRA based CLTM would require small specification work .
    Candidate cell preconfiguration is already supported in Rel-18 LTM. CLTM execution conditions can reuse Event LTMs introduced for R19 LTM. Security related aspects for intra-CU LTM are directly applicable to intra-CU CLTM.
  For CFRA based CLTM, discussion on network coordination for CFRA resources may be needed.
RACH-less intra-CU CLTM
  To enable RACH-less CLTM, same beam should be assumed by both UE and NW during RACH-less CLTM execution and Timing Advance to the CLTM candidate cell should be known by UE.
  Some discussion is needed on overall CLTM procedure to enable beam alignment between UE and NW and TA acquisition, which may impact Uu as well as F1.
  While RACH-less CLTM would require non-trivial discussion, it is important to support RACH-less cell switch for CLTM as the performance benefit is maximized by skipping RACH during cell switch.
Subsequent intra-CU CLTM
  (C)LTM is designed to utilize beam-level diversity for cell switch, which inherently requires configuration of multiple candidate cells (i.e., higher signaling overhead) and results in frequent cell switching (i.e., short time of stay). So, we believe that subsequent CLTM is worth getting supported.
Proposal 2: RAN WGs are tasked to support both intra-CU RACH-based CLTM and intra-CU RACH-less CLTM.
Proposal 3: RAN WGs are tasked to support subsequent intra-CU CLTM.

## Slide 5: Work scope of CLTM
Inter-CU CLTM
  Intra-CU CLTM is of higher priority, according to WID.
  In our view, the support of inter-CU CLTM needs not be precluded, and whether to support inter-CU CLTM or not should be decided by RAN WGs (mainly RAN3) based on specification impacts and work load.
  So, we suggest RAN WGs discuss whether inter-CU support in Rel-19 is feasible, and based on the discussion, RAN#106 make a final decision on the work scope of CLTM. Both RACH-based CLTM and RACH-less CLTM can be considered, and subsequent CLTM (for both RACH-based and RACH-less) is also considered as scope for inter-CU CLTM.
Proposal 4: RAN WGs discuss whether inter-CU CLTM support in Rel-19 is feasible for RACH-based CLTM, RACH-less CLTM, and subsequent CLTM. Then, RAN#106 makes a final decision on CLTM work scope.

## Slide 6: Harmonization between MOBILITY and MIMO
Observation
  Different use cases lead to deviated event kinds and event fulfillment conditions
    Event-triggered L1 report functionalities being introduced for R19 LTM are designed for cell switching use cases (and possibly relevant use cases such as early synchronization).
    Event-triggered L1 report functionalities being introduced for R19 MIMO are designed for beam management use cases.
    For cell switching use cases, more reliable/stable event fulfillment conditions are required, whereas for beam switching use cases, more dynamic event fulfillment conditions are beneficial. Due to their differences, the actual event kinds and their event fulfillment conditions are already deviated from each other.
    Given such deviation already introduced, harmonization between two WIs is neither meaningful nor motivated.
  Event-triggered L1 report for LTM is evaluated by MAC and transmitted via MAC CE, whereas event-triggered L1 report for MIMO is evaluated by PHY and transmitted via UCI.
    The responsible layer in evaluating events and report triggering is different between LTM and MIMO. This is huge difference
    Given such difference already introduced, harmonization between two WIs is neither meaningful nor motivated.
Proposal 5: No explicit harmonization effort is necessary between R19 MOBILITY WI and MIMO WI.

## Slide 7: Conclusion
Conditional CLTM
  Proposal 1: Work on CLTM is initiated since RAN#105.
  Proposal 2: RAN WGs are tasked to support both RACH-based intra-CU CLTM and RACH-less intra-CU CLTM
  Proposal 3: RAN WGs are tasked to support subsequent intra-CU CLTM.
  Proposal 4: RAN WGs discuss whether inter-CU CLTM support in Rel-19 is feasible for RACH-based CLTM, RACH-less CLTM, and subsequent CLTM. Then, RAN#106 makes a final decision on CLTM work scope.
Harmonization between R19 MOBILITY WI and R19 MIMO WI
  Proposal 5: No explicit harmonization effort is necessary between R19 MOBILITY WI and MIMO WI.