## Slide 1: LGE Views on Rel-20 Mobility Enhancements (Ph5)

## Slide 2: Justification of Rel-20 Mobility Enhancement
L1/L2 triggered Mobility (LTM)
  In Rel-18, a new mobility scheme, called LTM, was introduced with limited scope of intra-CU LTM.
    LTM aims to reduce mobility interruption, by introducing significant optimizations, such as RACH-less cell switching.
    LTM is applicable for both MCG and SCG.
  In Rel-19, enhancements to LTM are on the way to expand LTM scenarios and improve measurement related performance.
    LTM support is extended to inter-CU LTM, and conditional LTM is supported within intra-CU.
    Beam based event triggered measurement report and early CSI reporting are being introduced.
Market interest on LTM
  It is observed that infra-vendors and UE vendors consider LTM as to-be-popular feature due to its performance benefit and flexible network deployment options:
    LTM can be implemented on top of existing protocol structure with supplementary functionalities as building blocks.
    LTM enables a maximal link diversity gain by executing dynamic mobility based on beam-level condition with extremely low mobility interruption.
    Flexible network configuration and deployment options for LTM triggering are supported, such as LTM triggering based on L1 measurement report and/or L3 measurement report, and applicability of LTM for both MCG and SCG.
Our view
  Given the above performance benefit and flexible network deployment options that LTM provides, we believe that LTM is a compelling candidate technology for 5G-Advanced and 6G. This motivates further enhancements of LTM in Rel-20, so as to provide differentiated mobility experiences for 5G-A and 6G users.

## Slide 3: Potential Scope for Rel-20 Mobility Enhancement
Justification for support of multiple reference configuration
  Limitation of single reference configuration
    For both intra-CU LTM and inter-CU LTM, network can only configure a single reference configuration. Multiple reference configuration was proposed in RAN2 and RAN3 during Rel-19 but not adopted due to failure of consensus.
    For inter-CU LTM, single reference configuration requires interaction with all involved CUs to generate or update the reference configuration, which incurs a huge Xn signaling.
    When a reference configuration is updated, all candidate cell configurations should be reconfigured, which incurs a huge RRC signaling.
    Considering that a neighboring gNB could contain DUs and cells with completely different configurations, using a single reference configuration implies the following, which defeats the original intention of introducing the concept of reference configuration.
      the delta configuration for candidate cell configuration is almost a full configuration; and/or
      the reference configuration is efficient only for a subset of candidate cells belonging to a specific CU, and for other candidate cells, complete configuration is required.
  To reduce the overhead introduced by the single reference configuration, support of multiple reference configuration is strongly motivated.
Proposed scope: support of multiple reference configuration in order to minimize network signaling overhead [R2/R3]

## Slide 4: Potential Scope for Rel-20 Mobility Enhancement
Justification for overhead reduction in measurements and measurement reporting
  L1 measurement for candidate cells are essential for LTM. Considering that UE is configured with multiple beams (SSB and/or CSI-RS) for each candidate cell, UE measurement burden is proportional to the number of beams across all candidate cells.
  To reduce the measurement overhead, selective measurements among configured candidate cell beams can be considered. The selective measurements can be enabled as per network command (e.g., MAC CE) or UE-based decision.
  In Rel-19 LTM, event triggered L1 measurement report are introduced to reduce measurement reporting overhead. But, measurement reporting overhead may still be high, because
    The events introduced for L1 measurement report are only targeting cell switch decision. For other decisions related to LTM operations, such as candidate cell management, early DL/UL sync, network should still rely on periodic L1 reporting or more frequent event triggered L1 reporting, which increases measurement reporting overhead.
    Since event triggered L1 MR is performed per beam, multiple instances of L1 MR can be successively triggered by different beams of the same candidate cell, which increases measurement report overhead.
  To reduce the L1 measurement reporting overhead, schemes to omit triggering non-essential measurement report can be considered.
Proposed scope
  Reduction of candidate cell beam measurement overhead, by e.g.,
    Activation/deactivation of candidate cell beam measurements via MAC CE; and/or
    UE autonomous selective beam measurements via candidate cell selection/beam set selection
  Reduction of event triggered L1 measurement reporting overhead, by, e.g.,
    New events to facilitate candidate cell management and RACH-less LTM with minimal measurement reporting overhead.
    Reduction of successive but unnecessary L1 measurement report triggering

## Slide 5: Potential Scope for Rel-20 Mobility Enhancement
Justification for overhead reduction of CFRA/RACH-less cell (C)LTM
  In CLTM, each candidate cell should keep reserving (UL) resources for CLTM, upon being prepared as CLTM candidate. This may often lead to the case the candidate cell has to reserve the resources for long time without utilizing it.
  To alleviate the inefficient network resource utilization, on-demand (or on-the-fly) network resource reservation can be pursued. The resource reservation for CLTM is dynamically made/released based on UE indication telling whether CLTM is highly likely/unlikely to happen.
  For early UL synchronization for RACH-less cell switch, RACH-based early TA acquisition is applicable available, but RACH transmission to candidate cell for early TA acquisition introduces a interruption in a serving cell. The use of UE-based TA acquisition eliminates the interruption but UE-based TA acquisition is currently applicable only in case where serving cell and candidate cell are tightly synchronized with CA-level sync requirements.
  If UE-based TA acquisition becomes applicable in more cases, the serving cell interruption caused by RACH to candidate cell can be further reduced and thus serving cell throughput is less affected.
  To enable RACH-less (C)LTM, network needs to keep receiving L1 measurement report to select a candidate cell eligible for early TA acquisition and trigger early-TA RACH to the selected candidate cell, which increases UL/DL signaling overhead.
  To reduce the UL/DL signaling overhead required to trigger early-RA RACH for (C)LTM, UE autonomous triggering of early-TA RACH can be considered.
Proposed scope
  Minimization of network resource reservation for CFRA/RACH-less CLTM, by, e.g.
    UE indication for on-demand network resource reservation
  Reduction of early UL synchronization overhead by, e.g.
    Generalization of UE-based TA for less-synchronized candidate cell
    UE autonomous triggering early-TA RACH for (C)LTM

## Slide 6: Mobility Enhancement (Ph5)
Justification for support of inter-CU conditional LTM
  For the network triggered LTM, both intra-CU and inter-CU scenarios are supported. However, For conditional LTM (CLTM), only intra-CU CLTM is supported.
  Considering that LTM is a compelling candidate for 5G-Advanced and 6G mobility features, it is important that both network-triggered LTM and conditional LTM are equally ready for all possible scenarios.
  In Rel-19, essential functionalities for inter-CU LTM and intra-CU CLTM will be defined. The support of inter-CU CLTM can be easily built on top of the building blocks defined for inter-CU LTM and inter-CU LTM.
Proposed scope: support of inter-CU conditional LTM

## Slide 7: Summary
Justification of Rel-20 Mobility Enhancement WI (Ph5)
  Given the performance benefit and flexible network deployment options that LTM provides, we believe that LTM is a compelling candidate technology for 5G-Advanced and 6G. This motivates further enhancements of LTM in Rel-20, so as to provide differentiated mobility experiences for 5G-A and 6G users.
Preferred work scope
  LTM overhead reduction
    Support multiple reference configurations to minimize network signaling overhead
    Reduction of candidate cell beam measurement overhead
    Reduction of event triggered L1 measurement reporting overhead
    Reduction of early UL synchronization overhead
  Conditional LTM specific enhancements
    Minimization of network resource reservation for CFRA/RACH-less CLTM
    Support of inter-CU conditional LTM