## Slide 1: Scope discussion on Ambient IoT
Sources: Panasonic
3GPP TSG RAN #106
Madrid, Spain, December 9-12, 2024
Agenda: 9.1.1
TDOC: RP-242515
For: discussion

## Slide 2: Background
Related to Ambient IoT, RAN#112 concluded following as Rel-19 Package of RP-232745 in Dec 2023.
  Target 12-month for SI completion, check in Dec’24 for conversion to WI or if necessary, continuation of SI.
RAN1#119 concluded the text proposal for recommendation for a normative phase but it has the list for inclusion or non-inclusion as following.
  Device 1 and/or Device 2a (with or without large frequency shift) and/or Device 2b (with RF-ED and/or IF-ED and/or ZIF receiver architecture)
  D1T1 and/or D2T2
    Scenario A1 and/or A2 and/or B and/or C
  Line code(s) Manchester/PIE for R2D, and Manchester / Miller / no line code for D2R
  Multiple access by TDMA and/or FDMA and/or CDMA for D2R; FDMA for device 2b (IF-ED/ZIF receiver) in R2D
  OOK and/or BPSK and/or MSK modulation for D2R
  Carrier-wave waveform 1 and/or 2, and transmission case(s)
  Device (un)availability direction 1 and/or 2
  Proximity determination solution 1 and/or 2

## Slide 3: Device type
Study item requested "a harmonized air interface design with minimized differences (where necessary)". There can be different views on how much difference is called as "where necessary".

## Slide 4: Device type
We see following character difference between device 1 and device 2b.
  Device 1 bit rate is around 1 to 7 kbps order and distance is 10 to 30 m order in D1T1.
    The system design can be optimized for simplicity for low cost without so much consideration of inter-reader/device interference. Device availability can be based on the client to the reader via Direction 1. CP handling may be simplified by not retaining subcarrier orthogonality.
    Device 1 reader may be more proper as gNB as it requires no full duplex receiver because of back scattered D2R transmission and small frequency shift. i.e. D1T1 of Device indoors, basestation indoors and BS ↔ Ambient IoT device.
  Device 2b bit rate is around 1 to 7 kbps order and distance is 20 to 3000 m order in D2T2.
    The system design needs to take into account inter-reader/device interference for the efficiency. More power consumption means device availability should be more autonomous by Direction 2. CP handling would be required for subcarrier orthogonality.
    Device 2b reception by UE reader is simpler as no full duplex reader by not using back scattered D2R transmission and large frequency shift. i.e. D2T2 of Device indoors, basestation outdoors and BS ↔ intermediate node ↔ Ambient IoT device.
  Device 2a can be designed close to device 1 or designed to be close to device 2b based on RAN's preference.
Note: The bit rate and distance varies significantly depending on the multiple of conditions like sensitivity, EIRP power, FEC, modulation scheme and evaluation platforms. The numbers described is just our side observation from the link budget evaluation in TR38.769. Different companies may observe values differently.

## Slide 5: Device type
Multiple access
  TDMA is always supported.
  Device 1: No FDMA for R2D, FDMA for D2R.
  Device 2b: FDMA for R2D, FDMA and potentially CDMA for D2R.
Carrier-wave waveform:
  Device 1 for waveform 1(single tone). Device 2b for waveform 2(two single tone) for energy harvest.
Proximity determination:
  Device 1 for solution 1 (without reader side measurement). Device 2b for solution 2(with reader side measurement).

## Slide 6: Device type
 | Device 1 | Device 2b
Scenario/Topology | D1T1 | D2T2
Clock/frequency synchronization related design | Less optimized | More optimized
Interference handling | Less optimized | More optimized
Device availability design | Client to the reader | Device autonomous
Multiple access | TDMA, FDMA only for D2R | TDMA, FDMA for both Potential for CDMA
Carrier-wave waveform | Waveform 1(single tone) | Waveform 2(two single tone)
Proximity determination | Solution 1 (without reader side measurement). | Solution 2(with reader side measurement).
  Device 2a can be designed close to device 1 and/or designed to be close to device 2b based on RAN's preference.
Previous slides can be summarized as following.

## Slide 7: Device type
The basic design of protocol can be harmonized. On the other hand, especially following should be optimized/differently for device 1 and device 2b.
  The clock/frequency synchronization related design
  Interference handling
  Device availability design
Proposal: If work item is established, such device characteristics difference should be taken into account.

## Slide 8: Other points
Following should be determined in working level.
  Line code(s). R2D can be harmonized but not essential to have harmonized for D2R between device 1 and 2b.
  OOK and/or BPSK and/or MSK modulation for D2R

## Slide 9: Schedule
We see following possibilities. As either has pros and cons, we are fine with either option.
  Option 1: Initial work item focus on device type 1. Trying to finalize work item within release 19 time frame.
  Option 2: Initial work item starts all device types. The schedule is not limited to release 19 time frame.