## Slide 1: Views on Rel-20 5G-Advanced Items
Agenda Item: 15.1
Source: Fujitsu
Document for: Discussion
3GPP TSG RAN Meeting #106 RP-242641 Madrid, Spain, December 9-12, 2024

## Slide 2: General Aspects
Scope of 5G-Advanced in Rel-20
  Conversion from Rel-19 SI to Rel-20 WI
  No Study Items for new topics (i.e. study phase is OK)
  Enhancements on existing functionalities depending on actual market needs
  Completion of ongoing topics (i.e. AI/ML, ISAC, Ambient-IoT)
Differentiation between 5G-Advanced and 6G
  Overlap discussion of the same topic in 5G-Advanced and 6G should be avoided
Time allocation
  18-month would be sufficient
  Less TUs than 6G study

## Slide 3: Rel-20 5G-A candidate topics (RAN1)
MIMO(Supportive): Further enh. on UL MIMO, enhancement on UE initiated beam reporting, and enhanced mTRP operation can be the candidate objectives in Rel-20  See part 1 for more details
AI/ML for air interface (Supportive): At least normative phase for 2-sided model  See part 2 for more details
Coverage enhancement (Supportive): PRACH repetition with different beams, Mg5 repetition  Strong demand from operators are observed
ISAC (Supportive): Complete the feasibility study for all sensing modes (RAN1) Normative phase (gNB-gNB sensing – RAN3), if necessary  OK as a continuation item from Rel-19
Ambient-IoT (Supportive) : Depending on the outcome of Rel-19 SI/WI Support of outdoor scenario – start from Study Phase  See part 3 (views on Rel-19) and part 4 (views on Rel-20) for more details

## Slide 4: Rel-20 5G-A candidate topics (RAN1)
NR-NTN (Not positive) Potential objective: enhancements on mobility aspects incl. satellite switching with re-sync, Supplemental coverage from space (SCS), GNSS-less operation etc.  6G (i.e. NTN as native function) would be more appropriate rather than adding optional 5G functionalities for optimization
Network Energy Savings (Not positive) Potential Objective: On-demand(OD) SIB1/SSB without cell restriction, on-demand TRS  NES should be discussed as a 6G topic without any backward compatibility restriction
Multi-carrier enhancements (Not positive) Potential objective: Reduce carrier activation time  Rather than spending our time on optimization of 5G, designing 6G native multi-carrier functionality would be more attractive
SBFD (Not positive) Potential objective: supporting different UL bandwidth among cells, UE side SBFD  Technically difficult, actual benefit is unclear

## Slide 5: Rel-20 5G-A candidate topics (RAN2)
Mobility (Supportive) Leftover from LTM Rel-19: Inter-CU CHO, L1-SINR etc  It would be reasonable to conclude 5G LTM design first, and then it can be exported to 6G
AI/ML for mobility (Supportive) Continuation from the Rel-19 study  Basic 5G design for AI/ML should be concluded first
IoT-NTN (Neutral) Support for GEO voice call Mobility related enhancement (carrier redirection)  Depends on the market demand

## Slide 6: Rel-20 5G-A candidate topics (RAN3)
AI for NG-RAN (Supportive)
SON/MDT (Supportive)  Support of Rel-19 functionalities (business as usual)

## Slide 7: Part 1 MIMO in Rel-20

## Slide 8: Review on Rel-19 MIMO
Rel-19 MIMO includes the following topics
  UE-initiated beam reporting
  CSI enhancements
    Up to 128 CSI-RS ports
    Multi-CRI reporting
    CJT with non-ideal sync and backhaul
  3Tx uplink transmission
  UL-only mTRP operation
In Rel-20, it is also important to continue enhancements on MIMO

## Slide 9: Proposal for MIMO objective in Rel-20
Enhancement on uplink transmission
  Uplink precoding enhancement, e.g., sub-band precoding, precoding cycling
Enhancement on beam management
  UE-initiated beam reporting enhancement, e.g., mTRP, fast (UE-initiated) beam switching
Enhancement on mTRP
  Considering the importance of distributed MIMO in future, further CSI enhancement can be considered, e.g., to support more than four TRPs, unequal antenna ports for different TRPs

## Slide 10: Rel-20 MIMO: Uplink Enhancement
Enhancement on uplink transmission
  For MIMO, more enhancements are on downlink
  In Rel-20, enhancements on uplink MIMO can be considered to improve uplink capacity and reliability
    Uplink precoding can be enhanced, e.g., to support sub-band precoding, precoding cycling

## Slide 11: Rel-20 MIMO: Beam Management
Enhancement on beam management
  UE-initiated beam reporting for mTRP
    In Rel-19, UE-initiated beam reporting is only for sTRP
    Considering that distributed MIMO could become more popular in future, it can be considered to extend UE-initiated beam reporting to the mTRP scenario
  UE-initiated beam reporting with fast beam switching, e.g., UE-initiated beam switching
    In Rel-19, latency reduction is mainly on reducing the report latency
    In Rel-20, it can be extended to reduce the beam switching latency. For example, UE-initiated beam switching can be considered, if it is not supported in Rel-19

## Slide 12: Rel-20 MIMO: Enhancement on mTRP
Enhancement on mTRP
  Enhancements have been performed on mTRP for several releases
  Considering the importance of distributed MIMO in future, it is worth continuing to enhance mTRP
    CSI enhancement for mTRP can be considered, e.g., to support more than four TRPs, unequal antenna ports for different TRPs

## Slide 13: Part 2: AI/ML in PHY

## Slide 14: AI/ML for air interface in Rel-19
Rel-19 WI on AI/ML for air interface includes the following use cases according to WID update in RAN #105
  Normative work
    AI based beam management
    AI based positioning
    AI based CSI prediction
  Further study
    CSI compression
It’s important to continue the work on AI/ML for 5G-Advanced in Rel-20

## Slide 15: Use cases in PHY for 5G-A Rel-20
The following AI/ML use cases could be considered in physical layer for 5G-Advanced Rel-20
  High priority: AI/ML based CSI compression
  Med priority: AI/ML based beam failure recovery
  Med priority: AI/ML based SRS antenna switching
  Low priority: AI/ML based positioning

## Slide 16: AI/ML based CSI compression
As representative case for two-sided model, AI/ML based CSI compression has been studied in Rel-18 and Rel-19
Normative work could be considered for 5G-Advanced Rel-20 depending on the outcome of Rel-19 study, including
  Inference
  Training data collection
  Performance monitoring
  Inter-vendor collaboration option(s)

## Slide 17: AI/ML based beam failure recovery
Beam failure recovery was designed to mitigate the blockage, especially in FR2
  UE needs to detect beam failure event and identify the new candidate beam
In Rel-19, the AI/ML based beam management is specified aiming at beam prediction in spatial domain (BM Case-1) and temporal domain (BM Case-2)
The AI/ML based beam prediction with UE side model could be extended to the new candidate beam identification in beam failure recovery operation
AI/ML could also be considered for potential beam failure event prediction with UE side model

## Slide 18: AI/ML based SRS antenna switching
SRS antenna switching has been supported for multiple xTyR configurations
  In Rel-18, x={1, 2, 4}, y={1, 2, 4, 6, 8} and x<=y, excluding 4T6R
Some xTyR configuration may need many SRS resources and uplink time slots
  For example, for 1T8R, 8 SRS resources are required and up to 4 slots are needed
  There could be performance degradation considering the SRS resources spans over long time interval
AI/ML with NW-side model could be considered to reduce the required SRS resources and uplink time slots

## Slide 19: AI/ML based positioning
In Rel-19 WI, the following cases for positioning enhancement were deprioritized
  (2nd priority) Case 2b: UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning
  (2nd priority) Case 2a: UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning
If Case-2a and Case-2b are not specified in Rel-19 and there is sufficient TU allocation in Rel-20, these two cases could be considered for positioning enhancement

## Slide 20: Part 3 Ambient IoT Rel-19

## Slide 21: Observations on AIoT
Ambient IoT is one of the items which may have a chance of commercial launch in the coming-up few years.
The AIoT devices should be carefully designed for a reasonable price and good performance.
  Ambient IoT business could be promising, if the AIoT devices can be really competitive with RFID tags.
    AIoT devices could be disposal devices, like RFID tags.
    The scale of the potential AIoT market should be very large, otherwise it could be very difficult to profit from operating AIoT business because the price of single device is very cheap.

## Slide 22: Observations on AIoT SI in Rel-19
Some considerations/proposals in WG discussions more considered how to make AIoT devices better than RFID tags and less consider the additional cost required for the extra advantage.
There are some redundant features/candidate solutions in TR.

## Slide 23: Consideration on AIoT WI in Rel-19
Proposal 1: Support an AIoT WI from 2025 Q1.
Proposal 2: The scopes of AIoT WI should be very limited,
  To guarantee that the first batch of AIoT devices have very reasonable price, and
  To match the very limited time units (only 3 WG meetings).
Proposal 3: Consider device 1 only.

## Slide 24: Part 4 Ambient IoT in Rel-20

## Slide 25: Ambient IoT in Rel-19
Ambient IoT SI was wrapped up in Nov. WG meetings.
We support a WI staring from 2025 Q1 with carefully selected scopes.
  The scopes should be very limited.
    To guarantee that the first batch of AIoT devices have very reasonable price, and
    To match the very limited time units (only 3 WG meetings).

## Slide 26: Ambient IoT in Rel-20
Support a continuation item in Rel-20:
  A normative phase for some reasonable left-over for indoor deployment.
    Considering the very limited time units for Rel-19 AIoT WI, if approved, there must be some reasonable left-over there for indoor deployment. The normative work for this part should be prioritized for a better support of indoor deployment.
  A study phase for outdoor deployment may be necessary, followed by a normative phase
    The study on the interference between AIoT system and other systems for outdoor deployment is different from the interference study done in Rel-19 for indoor deployment.
    The AIoT devices which are not finalized in Rel-19 WI are necessary, such as device 2b with ZIF/IF receivers or some more powerful new types of AIoT devices.
    The energy source other than the RF harvesting needs to consider, because only RF energy harvesting may not be able to support the routine operations of device 2b or more powerful devices.

## Slide 27
Thank you