## Slide 1: ETRI’s views on Rel-20 NTN
Electronics and Telecommunications Research Institute
RP-242775
3GPP TSG RAN Meeting #106
Madrid, Spain, December 9-12, 2024
Source: ETRI
Agenda item: 15.2

## Slide 2: On-Going NTN R&D Projects in Korea
Until 2030, South Korea will build 5G/6G LEO satellite communication system through three national R&D projects
  Project #1 (led by ETRI): ground station (GW) development
  Project #2 (led by Intellian): UE development
  Project #3 (TBD): 3GPP based payload development + system optimization  launch
P#1: Development of Ground Station Core Technology for Low Earth Orbit Cluster Satellite Communications
Period: 2024~2026
Budget: ~$14M
Objective: Ground station system to operate transparent & regenerative payloads
P#3: Development of Low Earth Orbit Cluster Satellite Communication System
Period: 2025~2030
Budget: ~$22M
Targets: (at least) two LEO in orbits + 5G/6G NTN testbed (ground station & UE)
P#2: Development of Core Technology for Low Earth Orbit Satellite Communication based on 3GPP standards
Period: 2024~2026
Budget: ~$17M
Objective: Ka-band VSAT Terminal based on 3GPP NTN standards
Service link
Feeder link
5GC
NG
Notes: https://www.korea.kr/news/policyNewsView.do?newsId=148929490#policyNews

## Slide 3: 3GPP NTN Specifications
Basic NTN features had been studied and specified through 2 SIs and 3 WIs
  Need to revisit fundamental assumptions, including GNSS capability/accuracy or multi-carrier support
01
Rel-15
02
Rel-16
TR 38.821 (2019-12)
NTN reference scenarios
NG-RAN impacts & solutions
L1 impacts & solutions
Protocol impacts & solutions
TR 38.811 (2018-06)
NTN use cases
NTN architectures
NTN scenarios
NTN channel model
Potential impacts
03
Rel-17
NR NTN phase 1 (transparent payload, FR1)
Ephemeris, TA, scheduling/timing offset
Multiple TACs & cell barring
TN-NTN HO (handover)
RRM/time/location-based CHO
Multiple SMTCs & measurement gaps
Coarse UE location reporting
OAM, switch over, NG-RAN signalling, etc.
04
Rel-18
NR NTN phase 2 (FR2, earth-moving cell)
UL coverage Enh. (Msg4 repetition, PUSCH DMRS bundling over timing drift)
RACH-less HO
Satellite switch with re-synchronization (w/ unchanged PCI)
Verification of UE location (Rx-Tx time difference report, etc.)
Mobility enhancement & power saving (via TN coverage area)
05
Rel-19
NR NTN phase 3 (regenerative payload)
DL coverage Enh. (SSB periodicity)
OCC for PUSCH, NPRACH & NPUSCH
Half duplex FDD UE support
On-board gNB support
Store & forward support
MBS intended service area signalling
LTE-to-NR NTN mobility (IDLE)

## Slide 4: Non-Terrestrial Networks Phase 4
Motivation for NTN phase 4 specifications
  Fundamental studies are required to enable NTN to everything
  Some of leftovers from NTN phase 1~3 due to limited TUs need to be specified
Potential objectives
  Specify E-UTRA TN to NR NTN mobility for CONNECTED mode UEs [RAN2]
    NTN phase 3 only supports E-UTRA TN to NR NTN mobility for IDLE mode UEs
    Need to avoid unnecessary cell reselection, e.g., via enabling multiple SMTCs
  Study on NTN supports for non-GNSS capable UEs [RAN1, RAN4]
  Multi-polarization support for NR NTN [RAN1, RAN4]
    Currently, the network broadcasts the polarization type of satellite (circular or linear)
    Further enhance NTN coverage by satellite-UE polarization alignment
  Study and specify CA/DC for NTN [RAN1, RAN2, RAN4]
    Specify intra-satellite CA and intra-orbit CA/DC (e.g., LEO-LEO CA/DC)
    Study TN-NTN DC, inter-orbit CA/DC (e.g., LEO-GEO DC)
  Leftovers from Rel-19 NTN, including further optimizations on SSB hopping [RAN1, RAN2]

## Slide 5: E-UTRA TN to NR NTN mobility for CONNECTED mode UEs
Motivation
  About 50% of world population still has been being connected by E-UTRA
  Even in 2030, up to 42% of users may rely on E-UTRA in some regions [Ericsson mobility report, Nov. 2024]
  However, E-UTRA TN to NR NTN mobility feature from Rel-19 is very limited
    Only support cell (re-)selection via single SMTC for RRC-IDLE UEs
Objectives [RAN2]
  Enable multiple SMTCs for E-UTRA TN to NR NTN mobility
  Enable handover and conditional handover for E-UTRA TN to NR NTN mobility

## Slide 6: NTN supports for non-GNSS capable UEs
Motivation
  Reliable GNSS cannot be guaranteed
    Blockage
    Inaccuracy: multipath, jamming, and spoofing
  Always-ON GNSS may cause high energy consumption and latency from UE side
Objectives
  Study and specify solutions to support non-GNSS capable UEs
    Uplink time and frequency synchronization (for both RRC idle/connected UEs) [RAN1]
    Enhancements for HO [RAN2]
    Study other impacts and solutions [RAN1, RAN2]

## Slide 7: Multi-polarization support for NR NTN
Motivation: NTN {Coverage, Spectrum Efficiency, Interference} Enhancement
  In multi-layer NTN, various polarizations might be mixed due to the diverse nature of communication platform.
    {Circular: satellite, VSAT UE} ↔ {Linear (or X-pol): UAV, Handheld UE}
  Currently, the network broadcasts the polarization type of satellite in SIB19
    no explicit specification about polarization alignment/multiplexing
  Further, the support of multi-polarizations might help
    to enhance coverage
      polarization mismatch (e.g. satellite: circular, UE: linear): 3 dB loss (current) ↔ 0 dB loss (by polarization alignment)
    to optimize spectrum utilization
      repetition resources for similar reliability: R repetitions (current) ↔ ½ R repetitions (by polarization alignment)
      minimum granularity for polarization : currently, polarization per satellite
        a satellite might support multi-polarizations within the resource grid (or channel bandwidth)
    to reduce interference/leakage
      explicit resource separation between circular and linear
Objectives: support of multi-polarizations (RH, LH, Linear) [RAN1, RAN4]
  E.g., semi-static and/or dynamic polarization alignment/multipelxing
  E.g., RB-level and/or BWP-level polarization alignment/multiplexing
  E.g., Requirements and capabilities for polarization alignment/multiplexing
polarization alignment
polarization multiplexing

## Slide 8: CA/DC for NTN
Motivation
  Currently, NR NTN does not support any multi-connection features, such as CA, DC, and DAPS
  Given that a basic set of NTN features are having been finalized until Rel-19, Rel-20 would be a good checkpoint to examine multi-connection features for NTN
Objectives
  Specify intra-satellite CA and intra-orbit CA/DC (e.g., LEO-LEO CA/DC) [RAN1, RAN2, RAN4]
  Study TN-NTN DC, inter-orbit CA/DC (e.g., LEO-GEO DC) [RAN1]
Rel-20 TN-NTN or NTN-NTN aggregation
TN-NTN interworking
Rel-19 TN-NTN / NTN-NTN interworking

## Slide 9: Leftovers from Rel-19 NTN
DL coverage enhancements (if issues remain)
  E.g., further system level enhancements based on network energy saving techniques [RAN1, RAN2]
  E.g., wider beam for SSB/ transmitting the DL common channels, while using narrow beam DL/UL dedicated channels [RAN1, RAN2]

## Slide 10: Conclusion
Consider the following objectives for Rel-20 NR NTN
  Specify E-UTRA TN to NR NTN mobility for CONNECTED mode UEs [RAN2]
    NTN phase 3 only supports E-UTRA TN to NR NTN mobility for IDLE mode UEs
    Need to avoid unnecessary cell reselection, e.g., via enabling multiple SMTCs
  Study on NTN supports for non-GNSS capable UEs [RAN1, RAN4]
  Multi-polarization support for NR NTN [RAN1, RAN4]
    Currently, the network broadcasts the polarization type of satellite (circular or linear)
    Further enhance NTN coverage by satellite-UE polarization alignment
  Study and specify CA/DC for NTN [RAN1, RAN2, RAN4]
    Specify intra-satellite CA and intra-orbit CA/DC (e.g., LEO-LEO CA/DC)
    Study TN-NTN DC, inter-orbit CA/DC (e.g., LEO-GEO DC)
  Leftovers from Rel-19 NTN, including further optimizations on SSB hopping [RAN1, RAN2]