## Slide 1: Views on AI/ML in Rel-20 CMCC
3GPP TSG RAN Meeting#106 RP-242971
Madrid, Spain, December 9-12, 2024
Agenda: 15.2
Document for: Discussion

## Slide 2: AI for Air Interface for two-sided model
Performance:
  Up to ~29% UPT gain can be achieved at high RU and rank 2 for Case 2 (spatial/temporal/frequency compression for present slot) compared with Rel-16 eType-II codebook;
  Up to ~22% UPT gain can be achieved at high RU and rank 2 for Case 3 (spatial/temporal/frequency compression for future slots) compared with Rel-18 eType-II codebook
Inter-vendor training collaboration:
  3 candidate directions, including their options/sub-options, have been identified to alleviate/resolve inter-vendor training collaboration complexity; while the feasibility of standardizing model/model structure and model/dataset transfer are still ongoing in Rel-19.
    Direction A: Sharing model parameters/model/dataset with UE-side offline engineering
    Direction B: Sharing NW side encoder model parameter to UE side inference directly with on-device operation
    Direction C: Fully standardized model, including model structure and parameter
Other aspects:
  Data collection: CSI-RS/SRS measurement enhancement for higher accuracy measurement, ground truth CSI content and the signaling for triggering data collection have been studied in Rel-18/19
  Monitoring: monitoring metric, and related report signaling for NW-side and UE-side monitoring methods have been studied in Rel-18/19
  Inference: data type for model input/output, CSI report configuration, CQI calculation, CPU, model paring, etc., have been studied in Rel-18
Testability study in RAN4:
  Candidate testing options for two-sided model have been identified, while the feasibility study of option 3 (fully specified decoder) is ongoing in RAN4
  The study on feasibility of standardizing model/model structure and model/dataset transfer are ongoing in Rel-19
The LCM procedure for CSI compression can lay the framework for two-sided model use case in 6G
Study status in Rel-18/19

## Slide 3: AI for Air Interface for two-sided model
Motivation
  Evaluation results till RAN1#119 shows spatial/temporal/frequency compression for present slot achieves further performance gain compared to the Rel-18 spatial/frequency compression, and spatial/temporal/frequency compression for future slot also shows performance gain over the Rel-18 Doppler eType-II codebook
  The LCM procedure for CSI compression can lay the framework for two-sided model use case in 6G
Main objectives
  Specify necessary signaling/mechanism(s) to facilitate LCM operations specific to the CSI compression
    Data collection: enhancements of RS measurement and reporting
    Inference: enhancements of CSI report configuration, including input/output quantization, CQI calculation
    Monitoring: monitoring metric calculation and signalling to enable monitoring
Support CSI compression into Rel-20 normative work

## Slide 4: AI/ML for Mobility
Overview
Justification
  Number of simulation results on RRM measurement prediction have been shown in RAN2, and simulations on measurement event prediction, RLF prediction and system level are ongoing
    the feasibility and benefits of RRM measurement prediction can be expected
    the feasibility and benefits of measurement event prediction and RLF prediction will be further justified
Potential scope
  Specify AI/ML aided mobility for network-triggered L3 handover for the following use cases, based on outcome of Rel-19 SI:
    RRM measurement prediction
      including temporal domain, spatial domain, frequency domain
      both UE-sided model and NW-sided model are considered
    Measurement event prediction and RLF prediction (depends on the progress of SI)
      only UE-sided model is considered
  Necessary signalling/mechanism(s) for LCM to facilitate model training, inference, performance monitoring, data collection
  AI/ML general framework for one-sided AI/ML model specified in AI/ML for Air Interface is reused
  No further study on new use cases in Rel-20

## Slide 5: AI/ML for Mobility
RRM measurement prediction
  Specify necessary signalling/mechanism(s) for LCM to facilitate model training, inference, performance monitoring, data collection for both NW-sided model and UE-sided model
  Temporal domain prediction, based on L1/L3 historical measurements with/without measurement reduction
    FR1 intra-frequency case B, FR2 intra-frequency case A
  Frequency domain prediction, based on measurements of a frequency
  Spatial domain prediction, based on measurement results of Set B
For NW-sided model, specify the input/output/performance metrics
  Input: actual L1/L3 measurement results, UE assistance information, e.g. UE location, speed, trajectory
  Output: predicted measurement results
  Performance metrics: average RSRP difference, last RSRP difference, etc.
For UE-sided model, specify the input/output/performance metrics
  Input: actual L1/L3 measurement results
  Output: predicted measurement results
  Performance metrics: average RSRP difference, last RSRP difference, etc.
case A (without measurement reduction)
case B (with measurement reduction)

## Slide 6: AI/ML for Mobility
Measurement event prediction/RLF prediction
  Specify necessary signalling/mechanism(s) for LCM to facilitate model training, inference, performance monitoring, data collection for UE-sided model (depends on the progress of SI)
  Indirect prediction
    Input: actual L1/L3 measurement results
    Immediate output: predicted measurement results
    Final output: the expected occurrence time of a certain event (ex. event A3, RLF)
    Performance metrics: true event prediction, false event detection, missed event detection, F1 score
  Direct prediction
    Input: actual L1/L3 measurement results, event configuration (e.g. threshold, timer)
    Output: the probability of event occurrence within a time window
    Performance metrics: true event prediction, false event detection, missed event detection, F1 score
An example of indirect prediction for measurement event
An example of direct prediction for measurement event

## Slide 7: AI/ML for NG-RAN
Justification
  RAN3 has already studied the benefits, solutions, and potential standard impacts of AI/ML-based Energy Saving, Load Balancing, Mobility Optimization, Network Slicing, Coverage and Capacity Optimization (CCO) and NR-DC
  Some new use cases were mentioned in Rel-19 discussion, but were not included in the Rel-19 WI scope due to the limited time, including QoE Optimization and Multi-hops UE Trajectory across gNBs
  The normative work of Rel-20 should taken these use cases into account
Objectives
  Study and specify data collection enhancements and signaling support within the existing NG-RAN interfaces and architecture for new use cases, including:
    QoE Optimization
    Multi-hops UE trajectory across gNBs
    Note: considering non-split architecture and split architecture
  Support of Rel-19 leftovers, if any
Rel-20 normative work

## Slide 8: AI/ML for NG-RAN
QoE Optimization
AI-based QoE performance guarantee during mobility: (focus on RVQoE)
  QoE prediction for resource allocation, e.g. whether more resources are needed to guarantee enough buffer and prepare in advance
  Maintain user experience during handover
QoE measurements collection for prediction validation
  Collect QoE related measurements/metrics after handover to evaluate AI/ML model
  Resource reallocation after handver
  Analyze whether more RVQoE metrics need to be introduced and collected for AI, if needed
RAN-visible QoE information reporting
Signalling procedure for AI-based QoE Optimization

## Slide 9: AI/ML for NG-RAN
Multi-hops UE trajectory prediction
UE trajectory prediction transmission:
  UE Trajectory prediction (including prediction of multi-hops) transmission across gNBs, e.g. from one node to the next hop node in order
  UE trajectory prediction validity information, to avoid confusion caused by outdated prediction information
Measured UE trajectory collection
  Node/Cell level measured UE trajectory
  Measured UE Trajectory collection mechanism, e.g. from one node to the previous hop node in order
Multi-hop UE trajectory across gNBs
Signalling procedure for multi-hop UE trajectory

## Slide 10: 谢 谢