## Slide 1: Consideration on UAV in 5G-A Rel-20
Agenda Item: 15.2
Source: CATT
3GPP TSG RAN #106
Madrid, Spain, December 9 - 12, 2024
RP-243125

## Slide 2
General Motivation
Potential scope of NR UAV enh. in 5G-A Rel-20
Proposals

## Slide 3: General Motivation
Need of NR UAV enhancement in 5G-A Rel-20
Increasing interests in uncrewed aerial vehicles (UAV) based services have been witnessed globally in recent years:
  In some regions, there are great interests from governments and operators to build a “Low-altitude” network to support “Low-altitude” economy by UAV communications, with strong industrial radiations (e.g. logistics, transportation, agriculture, meteorology, etc.) and expectation of trillion-level industrial and market scale.
  Great expansion and growth of commercial drone/UAV markets are witnessed in a variety of regions throughout the globe.
In Rel-18, UAV specific enhancements were introduced in NR, aiming at more effective support of UAV based services in NR RAN but still with some limitations on mobility aspects. Specifically, there were no consideration on UAV specific factors in those advanced mobility mechanisms in NR (e.g. CHO, LTM, etc.) and no consideration on IDLE/INACTIVE mobility enhancements. These make the current 5G NR probably insufficient/ineffective to support the mobility requirements of UAV communication thus far.
  In Rel-19, there were a large number of operators’ interests/supports on an NR UAV enhancement work item, due to urgent commercial needs (See RP-242134). Unfortunately, no corresponding WI was approved in Rel-19 somehow.
  To this end, further enhancements in NR to support UAV based service are needed in 5G-A Rel-20 , with the main objectives to support further UAV-specific mobility enhancements.

## Slide 4
General Motivation
Potential scope of NR UAV enh. in 5G-A Rel-20
Proposals

## Slide 5: CHO enhancements
High accuracy positioning in variable scenarios and use cases indoor/outdoor
-- Continue enhancements
Improving mobility performance of aerial UEs – CHO enh.
Motivation:
According to TR 36.777, the number of detectable cells and the range of the detected cells increase as UAV altitude increases. The distribution of reachable distance to serving cell demonstrated that aerial UEs can be served by a geographically far-away cell, compared to ground UEs. For CHO, this means there could be different candidate cells in different altitude ranges . So CHO needs to take UAV altitude/flight path into account for candidate cell preparation and CHO triggering, so to support CHO for UAVs at different altitudes effectively (e.g. executed to the cells in-sight with optimal radio conditions). Besides, in practical deployment, the gNBs deployed to support UAV based services in a given area are expected to be with an inter-site distance of several kilometres (e.g. 3 ~ 5 km) which typically assume no Xn deployment due to e.g. cost-saving consideration. The NG-based CHO (which has not been supported except for NTN) needs to be specified in NG-RAN to provide efficient CHO support for UAV.
Objective:
Specify CHO enhancements, considering height/flight-path related events and practical RAN deployment to support UAV communication:
Specify height-based/flight path based CHO trigger events. [RAN2]
Specify NG-based CHO in terrestrial network for UAV. [RAN3]
Field Trial results captured in TR 36.777

## Slide 6: LTM enhancements
Improving mobility performance of aerial UEs - LTM enh.
Motivation:
The detection of the LTM candidate cells may be varied with the height of the UAV. Following existing LTM mechanism to serve UAV, the L1 measurement may be wasted when the candidate cells become undetectable, and thus the dynamic selection of candidate cells in order to reduce the L1 measurement and reporting should be supported. Also, considering the much more in-sight cells detected by a UAV than a normal ground UE and thus the potentially more frequent handover performed by a UAV, support of subsequent LTM mechanism is beneficial to avoid signaling overhead for frequent candidate cell (re)configuration in UAV communication. This should take into account UAV specific factors regarding aspects on e.g. L1 measurement events, candidate cell activation/deactivation, etc.
Objective:
Specify support of LTM enhancement for UAV, taking height and flight path factors into consideration, including following objectives:
  Signalling reduction on L1 measurement report for undetectable candidate cells (e.g. UAV specific trigger event). [RAN2]
  Subsequent LTM with UE autonomous candidate cell activation/deactivation (based on planned flight path). [RAN2, RAN3]
5
Field Trial [5] results captured in TR 36.777

## Slide 7: IDLE/INACTIVE mobility enhancements
IDLE/INACTIVE mobility enhancements
Motivation:
Some UAV based services may not expect continuous large volume data transmissions. For example, periodic data transfer alongside a UAV’s flight path with low data volume or low frequency (e.g. monitoring data of atmosphere/logistics, etc.), or image/video capture with instantaneous data transfer by a hovering UAV before it flies away. In such scenarios, a UAV is not necessarily kept in CONNECTED mode, but can be sent to IDLE mode after it finishes data transmission or sent to INACTIVE mode for small data transmission. In practice, a gNB aiming to provide better support of UAV based service can deploy additional antenna with up-tilted angles, in order for a better coverage to the air than normal down-tilted gNBs serving only ground UEs (which can serve UAVs only by side lobes). Such gNBs may co-exist with the legacy gNBs only serving normal ground UEs in a typical deployment scenario. To enhance performance of UAVs in IDLE/INACTIVE as in above exemplary occasions, it is preferably for the IDLE/INACTIVE UAVs to camp on the gNBs that provide enhanced UAV communication support (e.g. with dedicated antenna deployment). Considering also that such gNB with dedicated antenna deployment may support not only UAVs but normal ground UEs as well, it may apply altitude based SSBs introduced in Rel-18. It is preferable for a UAV to measure the SSB at its altitude, and camp on the cell thereon quickly. With the limitation that Rel-18 altitude based SSB only applies to CONNECTED UEs, it is beneficial to extend its use to IDLE/INACTIVE also. Thus, enhancements on IDLE/INACTIVE mobility for UAV can be considered.
Objective:
Specify UAV-specific IDLE/INACTIVE mobility enhancement: [RAN2]
  Specify mechanisms prioritizing frequency(ies)/cell(s) with enhanced UAV-based service support for cell (re)selection.
  Extend the use of altitude based SSB to support IDLE/INACTIVE mobility.

## Slide 8
General Motivation
Potential scope of NR UAV enh. in 5G-A Rel-20
Proposals

## Slide 9: Proposals
Proposal for WI approval
Considering the great operators’ interests/support, it is proposed to further enhance the NR support for UAV as a work item within 5G-A Rel-20.
Proposal 1: Support NR UAV enhancement and approve a work item for 5G-A Rel-20 in RAN, with UAV specific mobility enhancements as listed in Page 4 ~ 6, including:
  CHO enh. (e.g. new trigger events, NG based CHO)
  LTM enh. (e.g. new L1 meas event, autonomous LTM candidate (de)activation)
  IDLE mode mobility enh. (e.g. altitude based SSB, frequency/cell prioritization).
Considering the potential time budget and work load in RAN1/4 for 5G-A in Rel-20 , it is proposed to avoid RAN1/4 impact as much as possible for NR UAV enhancements.
Proposal 2: Try to avoid RAN1/4 impact as much as possible in the potential NR UAV enhancement work item, if approved in 5G-A Rel-20.

## Slide 10
Notes: 万物互联，无限沟通
Universal Connectivity, Infinite Communication.