## Slide 1: Consideration on Positioning in 5G-A Rel-20
Agenda item: 15.2
Source: CATT
3GPP TSG RAN Meeting #106 RP-243129
Madrid, Spain, 9th -12th December, 2024

## Slide 2: Positioning in 5G-A Rel-20
  Address the impact of error sources, e.g., antenna reference point (ARP) error, phase center offset (PCO), for highly reliable and accurate positioning
NR Positioning enhancements
  Introduce A-IoT Positioning for supporting the use cases and KPI defined in TS 22.369/TR 38.848
  Study and evaluate the performance of potential A-IoT positioning solutions
  Study and specify architecture, reference signals, measurements, signaling and procedure for A-IoT positioning.
A-IoT Positioning
  Study and specify measurements, procedures, and higher layer signaling to enable:
    Positioning related information (coarse location, angle, etc.) used for beamforming, at least for downlink positioning.
    DL CSI related information (e.g., DL CSI) as positioning assistant information for positioning
Position-aided communication and communication-aided positioning
Unleashing extreme
5G-A capabilities
Achieving universal
business success
Deployment | Positioning accuracy | Communication range | Pos. service availability
Indoor | 1 m - 3 m, 90% availability | 10 m | 90%
Outdoor | several 10 m | 500 m | 95%

## Slide 3: A-IoT Positioning

## Slide 4: A-IoT Positioning Use Case
Enterprise Service Scenarios:
Asset tracking and management
Logistics
Retail，smart manufacturing
Intelligent parking
Personal and Home Scenarios:
Personal safety and convenience
Use cases related to family care and smart home environments
Retail positioning deployment in a shopping mall
Finding things at home
Source：GTI 5G-A Ambient power-enabled IoT Positioning Technology White Paper. CMCC

## Slide 5: A-IoT Positioning Application
A-IoT device attached to goods are increasingly required not only for identification but also for Tracking.
Merchandise Display Inspection
Mobile Robot Searching Object
Flat Warehouse Positioning Solution
High-Bay Warehouse Positioning Solution
Achieve shelf-level positioning with an accuracy rate close to 90%
Achieve centimeter-level positioning in lab
Supporting mobile robot navigation for object searching
Achieve storage-slot-level positioning
Saving 1-2 man-years of labor
Achieve meter-level positioning
Improve picking efficiency by 80%
A-IoT Reader
A-IoT device Integrated with Clothing Label
attached on Storage Area
A-IoT Reader
A-IoT device attached on Trolley
A-IoT Reader
A-IoT Device Attached on Cargo
A-IoT Reader
A-IoT device
Mobile Robot
Source：GTI 5G-A Ambient power-enabled IoT Positioning Technology White Paper. CMCC

## Slide 6: A-IoT Positioning KPI
KPI:
  Positioning accuracy (TS 22.369 and TR 38.848):
    1~3 meters @90% for indoor location
    Several tens of meters @90% for outdoor location
  Positioning latency (TS 22.369):
    1 second for sensor data collection and tracking
    Several seconds for inventory and actuator control
Scenarios | End-to-end latency | Message size | Device density | Positioning accuracy | Communication range | Positioning service availability
Inventory or asset management | Typically, seconds level | 96/256 bits | <1.5 million devices/km² indoor only | 3 m indoor, cell-level outdoor | 30 m – 50 m indoor, 200 m - 400 m outdoor | NA
Table 6.2-1 KPIs for inventory (TS 22.369)
Scenarios | End-to-end latency | Message size | Device density | Positioning accuracy | Communication range | Positioning service availability
Indoor tracking | 1 s | <1 kbits | 25 - 250 devices /100 m² | 1 m - 3 m, 90% availability | 10 m | 90%
Outdoor tracking | 1s | <1 kbits | ≤10 devices/ 100 m² | several 10 m | 500 m | 95%
Table 6.4-1 KPIs for tracking (TS 22.369)

## Slide 7: A-IoT Positioning Objective
Motivation:
  Challenges for A-IoT positioning include: low hearability due to poor received RF signal quality, low device complexity.
  Existing 5G NR positioning procedures and methods cannot be reused for A-IoT positioning.
  A-IoT Proximity determination to be introduced in Rel-19 cannot meet above A-IoT positioning requirements.
Objective:
  Evaluate performance and potential solutions for A-IoT Positioning for KPI in TS 22.369 and TR 38.848, targeting all devices types and topologies in Rel-19 WI.
  Study and specify architecture, reference signals, measurements, signaling and procedure for A-IoT positioning.
Topology 2
Topology 1

## Slide 8: Positioning enhancements to address error sources

## Slide 9: Positioning enhancements to address error sources
Motivation:
  Industry IoT (e.g., AGV pos., Smart Manufacturing) requires <10cm positioning accuracy
    AGV pos. market in Global may reach 73 billion RMB in 2030 (Source: Chinabgao)
    Existing AGV pos. with laser, and camera etc. suffer from high maintenance cost.
  Rel-18 evaluations show that cm-level positioning accuracy cannot be achieved if the error sources, such as ARP location errors, antenna PCO, are not properly addressed.
Objective:
  Positioning enhancements to address the error sources, including at least:
    ARP location error
    Antenna PCO
Smart Manufacturing
  Note: the above evaluation considers all the UEs which are evenly distributed in the cell
AGV

## Slide 10: Position-aided communication and communication-aided positioning

## Slide 11: Position-aided communication and communication-aided positioning
Motivation:
  5G NR positioning and communication have been developed separately.
  Positioning-aided communication and communication-aided positioning may bring significant benefits on
    Improving the accuracy, latency, etc. for positioning;
    Improving spectrum efficiency, reducing power consumption, etc. for communication.
  Use cases: commercial, smart factory and intelligent transportation.
Objective:
  Study and if agreed, specify measurements, procedures, and higher layer signaling to enable:
    Positioning related information (coarse location, angle, etc.) used for beamforming, at least for downlink positioning.
    DL CSI related information (e.g., DL CSI) as positioning assistant information for positioning.
Physical Layer:
Beam management,
Channel estimation
Higher Layer:
Initial access,
Mobility,
Resource scheduling
UE positioning measurements
(RSTD, RTOA, AoA, AoD, RSRP, Carrier Phase, etc. in DL-TDOA, UL-TDOA, Multi-RTT, CPP, etc.)
NR communication
NR positioning
Positioning-aided
Data communication
Communication-aided
positioning

## Slide 12: Summary
Proposal 1: Support A-IoT Positioning in 5G-A Rel-20.
  Study and evaluate the performance of potential A-IoT positioning solutions.
  Study and specify architecture, reference signals, measurements, signaling and procedure for A-IoT positioning.
Proposal 2: Support NR Positioning enhancements in 5G-A Rel-20.
  Support positioning enhancements to address the impact of error sources, e.g., antenna reference point (ARP) error, phase center offset (PCO), for highly reliable and accurate positioning.
Proposal 3: Support Position-aided communication and communication-aided positioning in 5G-A Rel-20.
  Study and specify the procedures, and higher layer signaling to enable:
    Positioning related information (coarse location, angle, etc.) used for beamforming, at least for downlink positioning.
    DL CSI related information (e.g., DL CSI) as positioning assistant information for positioning.