## Slide 1: Technical analysis relating to PC8 FR2
Ericsson, Rogers, US Cellular, T-Mobile USA
3GPP TSG-RAN Meeting #106
Madrid, Spain, 9-12 December 2024
RP-243180

## Slide 2: Concerns on the proposed FR2 PC8
PC8 UEs would deteriorate further FR2 coverage and DL/UL coverage and performance overall in stadium and hot-spot scenarios; these scenarios are already challenging for PC3
PC8 with its simpler antenna arrangement might become the “default” power class at the expense of PC3 support needed for adequate FR2 performance in the deployment scenarios considered
  or create device fragmentation

## Slide 3
Impact on UL/DL performance
PC8, a handheld UE type with
  Single panel
  Lower TX power
  2x1 array
  Min peak EIRP of 16.4 dBm
Compared with PC3
  No multi-panel, no diversity
  6 dB loss in UL (peak)
  Up to 9 dB worse UL
    spherical coverage
  3 dB loss in DL (peak)
End-to-end performance consequences
  Higher probability of blockage both DL&UL
  Dramatically worse UL coverage
    UL signaling and data on lower band
    Congestion in UL will result in lower DL capacity
  Shrinkage of FR2 DL coverage and throughput
   Additional capex investments due to lower UE capabilities
Impact across all markets/regions: PC8 risks PC3 availability
Negative impact on FR2 ecosystem

## Slide 4
Field observations
Stadium scenario
  Significant amount traffic is on FR2 compared with FR1 – both DL and UL
Urban dense scenario
  UL and overall system coverage has been steadily improved
  Lower capability UEs will undermine these achievements
Overall increasing UL traffic by user generated content
Constrained UL link budget with PC3
UL on FR1  interference limited scenario
DL capacity will be reduced due to UL congestion
  HARQ ACK/NACK
  CSI feedback for beam management
  CSI feedback for link adaptation
  UL feedback for various protocols (TCP, Video streaming etc.)

## Slide 5: Stadium scenario with surrounding hot spots
Super Bowl LVIII (2024) and hot-spots around the arena
  FR2 deployed in an NSA arrangement with an FR1 anchor in band n77. Besides the FR2 sites, FR1 sites were also deployed inside the stadium, often with LOS
  the FR1 link budget significantly better, but generally, FR1 spectrum blocks are more limited in spectrum and UL capacity as compared to FR2
  commercial deployment with commercial devices
Data from the event showed a 50/50 split of FR2/FR1 total UL traffic using PC3. For the stadium scenario, the FR2 link budget is still constrained for PC3
  PC8 devices would reduce the FR2 part of the traffic split
PC8 is not a solution to improve E2E performance for the stadium scenario

## Slide 6: References
R4-2418873, “Reconsidering the proposed new FR2 power class 8 and its specification”, Ericsson, Telecom Italia, US Cellular