## Slide 1
3GPP TSG RAN meeting #106 RP-243301 Madrid, Spain, December 9th-12th, 2024 Agenda Item: 9.4.1.6 Source: Intelsat, Thales, Eutelsat Group,
European Space Agency, FirstNet, Bosch,
Novamint, SyncTechno Inc, Fraunhofer HHI,
Fraunhofer IIS, BMW, Gilat, CHTTL, SES, Airbus,
EDF, Sharp, Hispasat, Lockheed Martin, UIC
Title: Way Forward on Ku band numerology Document for: Approval

## Slide 2: Background
RAN4 was tasked at RAN #104 to down select the numerology for Ku band to either FR1 or FR2
A thorough analysis at RAN 4 #113 of the feasibility of both options and concluded:
Overall observation is that both FR1 numerology and FR2 numerology are feasible.
There are use cases that favour either FR1 numerology or FR2 numerology
Some of the disadvantages of numerology combinations can be mitigated with implementation choices
The WF at RAN4 #113 was:
Agree to define two sets of bands, one for FR1 numerology and the other for FR2 numerology.
RAN4 will further discuss SCS options.
An LS on Ku band numerology to RAN1 and RAN 2 cc RAN was approved in R4-2419902

## Slide 3: Explanation of the RAN4 decision
RAN4 did not find a strong technical reason to down-select to one numerology
The range of NTN use cases is broad: low-cost enterprise (fixed) services through mobile automotive, maritime and airborne platforms
The commercial use case can favour one numerology over another
There are some use cases that are poorly served by one numerology but well-served by the other
In these circumstances RAN4 did not consider it had a mandate to make a down-selection decision that would disenfranchise one part of the industry over another
RAN has asked for the commercial justification to specify both FR1 and FR2 numerologies
This WF captures the views of interested companies towards specifying both

## Slide 4: Way Forward on Ku WID
Down scoping agreements for the revised WID in RP-242981
Remove VSAT type 1 (Fixed VSAT mechanically steered)
Remove VSAT type 2 (Fixed VSAT electrically steered)
  Assumes NGSO support added to type 5 such that type 2 is covered by type 5*
Remove VSAT type 3 (Fixed VSAT to LEO – small electrically steered)
Remove conducted requirements – only do radiated
Up scoping agreements for the revised WID in RP-242981
For mobile VSAT served by NGSO and GSO in Ku bands only:
  Specify NGSO and GSO connectivity based on existing type 5 RF requirements
  Specify the RRM timing requirements for the considered numerologies.
Note: There are no new regulatory requirements for mobile VSAT served by NGSO in Ku band that impact RAN4 coexistence studies or RF requirements.

## Slide 5: Annex. Company commercial views on numerology

## Slide 6: Gilat
In case we must choose between the two numerologies, it makes more sense to select FR1-SCS first and then move, later, to include FR2-SCS.
The reasons:
Commercial availability – Chip companies have demoed FR1-SCS modems with NTN support. The time-to-market based on these chips will be shorter than with FR2 chips (TDD-based).
Mass market adoption – A critical drive for the adoption of 5G-NTN is vehicular connection. The 5G chips will have to support FR1 for TN, so it makes sense that the same FR1 chip will be used as the basis for NTN connectivity.
FR1-SCS is closer to maturity and has the support of chip companies. Moving with FR2 first runs the risk losing this support

## Slide 7: Thales
The “Ku band” satellite market is divided between two kinds of satellites:
The ones with narrowband payload transponders: 36 MHz, 72 MHz (mostly in orbit satellites)
The ones with wideband payload transponders > 100 MHz (all GSO and NGSO satellites currently in development and future)
The feasibility for both FR1 and FR2 numerology in FDD mode in Ku band has been demonstrated. However one numerology does not perform optimally with both types of transponder.
Therefore, we request 3GPP to define two NTN bands to address these two distinct market segments.

## Slide 8: BMW
Commercial arguments for using FR1 and FR2 numerology for KU-Band:
Using FR1 numerology would speed up the introduction of Ku-Band services in the automotive industry because existing terrestrial FR1 modem chips could be used for narrowband data rate and wideband data rate NTN services in FDD bands.
Later on (next releases), FR2 numerology with higher carrier bandwidths would enable broadband data rate services in the automotive industry as soon as FR2 modem chips supporting FDD, are available.
Therefore, from BMW perspective, both numerologies (FR1 and FR2) would be favorable.

## Slide 9: CHTTL
Observations: FR1 numerology can fit the support of the legacy Ku band satellite transponders (36, 54, 72MHz) for GSO
FR2 numerology can fit the support considering satellite operating both Ku and Ka-band.

## Slide 10: Hispasat
Hispasat's operates different types of satellites, legacy ones which are equipped with old transponders (36 MHz and 72 MHz) while the new HTS satellites hosting higher bandwidth transponders (250 and 500 MHz)
Given that we are committed to transitioning from DVB waveform to 5G NTN, we need the flexibility of FR1 numerology to accommodate the signal bandwidth to the legacy satellites, while we also require FR2 numerology to cover high throughput scenarios using the HTS satellites.

## Slide 11: Eutelsat Group
The NTN services in Ku-band that will benefit from adoption of 5G will be GEO and LEO constellations with wideband transponders (e.g. 250MHz), as well as GEO satellite with "legacy" narrowband transponders (e.g. 36MHz). It is important that 5G-NTN delivers optimal performance over both wideband and narrowband transponders, while at the same time allowing reuse at the maximum extent of technology available for TN.
In this respect, defining Ku as FR1 will help in addressing narrowband use cases as well as providing a quick access to market for wideband use cases using CA.
Defining Ku as FR2 (120 kHz) creates synergies with Ka-band for satellites constellations that support both bands.
For this reason, both FR1 and FR2 are recommended.
One possible roadmap is to start from FR1, with a clear agreement that FR2 will be added later.

## Slide 12: SES
Use case Remote site connectivity using Ku-band High Throughput Satellite:
To connect remote sites, static terminals or mobile terminals on board moving platforms, it is necessary to reach data rates compatible with aggregated traffic of multiple users. These platforms and remote sites aggregating traffic require high data rate in both directions (e.g. up to 1 Gbps per terminal). This requires 120kHz SCS and up to 400MHz channel bandwidth allocation, corresponding to FR2 numerology.
To provide such performances, satellites (GSO and NGSO) currently in development and future are increasingly featuring wideband transponders (hundreds of MHz) able to support large channel bandwidth.
Therefore, FR2 numerology is useful for such Ku-band high throughput satellite applications (GSO and NGSO).

## Slide 13: Airbus 1/2
FR1 numerology arguments:
With current satellite systems and networks already existing and in orbit, small BW transponders (much lower than 100MHz) are being used. So having FR1 numerologies can help to address the existing market and facilitate and accelerate the time to market and the adoption of 5G NR in the very short term. In addition to that, some tests proving the feasibility of FR1 subcarrier spacing were already done, proving that the chipsets are ready to support this FR1 SCS market. All in all, having FR1 numerology will help an rapid and gradual adoption of 5G NR NTN standard in very short term
FR2 numerology arguments:
FR2 numerologies will allow the full capacity needs on new planned broadband satellite networks. In such cases the targeting bandwidth requirements can can be larger than 100 MHz bandwidth. However, as per our knowledge, we are not aware of any chipset currently available supporting NR NTN FR2 subcarrier spacing in FDD mode.

## Slide 14: Airbus 2/2
It is also important to remark, that if both numerologies are not accepted, the decision could push some SNO to rely on proprietary solutions, since the 5G NR NTN promises of flexibility and ease of deployment will not be met, thus having a real market fragmentation with multiple proprietary solutions. The promises of 5G NR NTN of having a single unified standard for TN and NTN and having a seamless integration between satellite and terrestrial networks could not be reached.

## Slide 15: Echostar
Defining FR1 and FR2 for the Ku-band will unlock the full potential of spectrum usage, driving innovation and meeting the diverse demands of commercial deployments

## Slide 16: Bosch
5G NR NTN paves the way to a standardized (and non-proprietary) connected mobility covering the unconnected situations. To increase connectivity resilience for existing use cases, 5G NR NTN requires operation in wider bandwidth. For smooth expansion to newer frequency bands, we propose:
First, utilize only one FR1 numerology (exploiting current satellite systems on network and UEs) to meet essential BW requirements.
Second, for the more data-rate demanding use cases, evolve to one FR2 numerology to enable wider bandwidth operation > 100 MHz.

## Slide 17: Intelsat
FR1 supports low data rate use cases for GEO for backward compatibility with non-3GPP platforms but also, higher data rates all the way to 500 MHz for advanced GEO and NGSO can be supported with future carrier aggregation.
FR1 chipset can be commercially available for NTN in the short term and demonstrated in multiple proof of concept demonstrations. We have commercial need for deployment in the short term.
FR2 can be supported possibly in a phase approach.

## Slide 18: FirstNet
Defining FR1 and FR2 for the Ku-band will unlock the full potential of spectrum usage, helping the First Responders to save human lives!

## Slide 19: JSAT
JSAT is currently evaluating plans to offer commercial services using 5G NTN in Ku-band.
FR1's small channel bandwidth is necessary not only for legacy GEO satellites but also for upcoming SDS/HTS GEO satellites.
In the case of SDS/HTS GEO satellites, the limited bandwidth of the Ku-band leads to an increase in the number of frequency divisions (reuse). This results in the satellite channel bandwidth allocated to a single beam becoming smaller.
Moreover, it is not always possible for satellite operators to allocate more than 100 MHz of bandwidth contiguously to NR. This is because these satellite channel bandwidths must also be allocated to other use cases, such as DVB services.
FR1 has several advantages that make it a strong candidate for early deployment. NTN-compatible chipsets for FR1 are already available, and only minimal modifications are needed for Ku-band support. Additionally, infrastructure such as gNBs and emulators are compatible with FR1 for NTN, while compatibility for FR2 remains limited. From a technical development and validation perspective, FR1 is a more practical choice.

## Slide 20
Considering the diverse commercial deployments in the maritime domain, which include vessels of various sizes (e.g., a few meters to a few hundreds meters) and aids to navigation systems such as fixed or floating buoys, it is recommended that both FR1 and FR2 numerologies for the Ku-band be considered within 3GPP. Depending on the available time units within the 3GPP RAN WGs, we may consider addressing FR1 first, followed by FR2.
SyncTechno Inc.

## Slide 21
We acknowledge the very different requirements of different systems
Legacy satellites with 36MHz (or similar) transponders)
Modern satellites with >100MHz transponders
There is a desire for legacy satellites which are typically using proprietary systems to move to standards-based systems sooner rather than later.
This is enabled by FR1 + CA
Future satellites need FR2 numerology
We support the dual numerology approach
  We would also support a phased approach with FR1 + CA (now) & FR2 (next)
Viasat

## Slide 22
From ESA point of view, both FR1 and FR2 numerologies are essential for supporting today and future commercial broadband satellite systems operating in Ku-band. This will allow the deployments of multiple services for the benefits of the European citizens.
European Space Agency