## Slide 1: Discussion on UE to satellite propagation delay
yaochuting@huawei.com

## Slide 2: Discussion history for UE to satellite propagation delay
Rel16 TR22.822
Rel16 TS22.261-remove with alignment/Rel17 TS 22.261
Evaluation angle = 90° , Altitude = 800km
Evaluation angle = 10°, Altitude = 1400km
Evaluation angle = 90°, Altitude = 8000km
Evaluation angle = 0°, Altitude = 8000km
Evaluation angle = 90°, Altitude = 35786km
Evaluation angle = 0°, Altitude = 35786km, +1ms
Rel18/Rel19/Rel20 TS22.261
Clarify inter satellite link is not considered
Clarify for the satellite access
The definition of satellite gives the typical altitude of the LEO is 500km to 2000km
The definition of satellite gives the typical altitude of the LEO is 300km to 2000km

## Slide 3: Calculation for UE to satellite propagation delay
Earth Radius: R
Satellite altitude: h
Elevation Angle: α
Distance between UE and satellite: d
According to the cosine formula, we have:
Then we can obtain the distance between UE and satellite as:
 | Altitude(km) | evaluation angle=10° |  | evaluation angle=90° | 
 |  | Distance(km) | delay(ms) | distance | delay
LEO | 300.00 | 1160.08 | 3.87 | 300.00 | 1.00
 | 500.00 | 1694.57 | 5.65 | 500.00 | 1.67
 | 600.00 | 1931.64 | 6.44 | 600.00 | 2.00
 | 800.00 | 2366.08 | 7.89 | 800.00 | 2.67
 | 1200.00 | 3131.10 | 10.44 | 1200.00 | 4.00
 | 1400.00 | 3478.74 | 11.60 | 1400.00 | 4.67
 | 2000.00 | 4435.16 | 14.78 | 2000.00 | 6.67
MEO | 8000.00 | 11822.72 | 39.41 | 8000.00 | 26.67
 | 20000.00 | 24507.43 | 81.69 | 20000.00 | 66.67
GEO | 35786.00 | 40581.18 | 135.27 | 35786.00 | 119.29
satellite: a space-borne vehicle embarking a bent pipe payload or a regenerative payload telecommunication transmitter, placed into Low-Earth Orbit (LEO) typically at an altitude between 300 km to 2 000 km, Medium-Earth Orbit (MEO) typically at an altitude between 8 000 to 20 000 k m, or Geostationary satellite Earth Orbit (GEO) at 35 786 km altitude.
Definition of satellite in TS 22.261:

## Slide 4: Correction on UE to satellite propagation delay on Description
Revise the propagation delay corresponding to the satellite altitude and indicate the range of the evaluation angle of UE.
Suggest having the mirror CR on Rel17/18/19/20.
The impact on the latency KPI can be FFS.
Current version
Correction