## Slide 1
Google
Nov. 08, 2024
Study on
Priority Messaging Services for Third-Party User
3GPP TSG WG-SA2 Meeting #166 S2-2412304
Orlando, United States, 18th-22nd Nov 2024
Notes: Thanks for joining techTalk.
I am Ellen in Google’s 3GPP standard team at Pixel.
In 3GPP, I am delegate of System architecture WG (SA2) of 3GPP network.
- provides updates on 6G status
- You might already hear 6G here and there a lot.
- after this talk, you can learn enough background knowledge to catch up on going 6G news and discussion.
Please feel free to raise your hand if questions

## Slide 2: Justification (1/2)
Currently, there are many Over-The-Top (OTT) messaging application for urgent events in the field provided by third-party service providers. These solutions employ methods such as SMS over NAS, SMS over IP, or NIDD-based messaging for UEs or IoT devices. These solutions use normal sessions over the 3GPP system (including TN and NTN) or for proprietary devices using non-3GPP compliant access. However, lacking of standardized priority treatment within the 3GPP system limits their effectiveness in delivering urgent messages promptly.
For example, application#O provides OTT based emergency services for in-vehicle security based on third-party’s subscription-based communications.
For example, application#G provides OTT based emergency messaging services at a UE using satellite access to access IoT NTN for alerting urgent event through a third party application server based on user configured emergency contacts.
Observations#1: Non-IP Data Delivery (NIDD) Mechanism is an existing 3GPP technology developed for NB-IOT devices since R13. Due to its lightweight nature, efficiency, and reliability, it is a feasible option for messaging services, especially when using satellite access given its energy constraints and broader coverage.
Observations#2: in TS 23.554, Application architecture for MSGin5G Service, already enables the Legacy 3GPP Message Gateway to interact with MSGin5G Server on behalf of Legacy 3GPP UE or IoT device (e.g., SMS, NIDD). The support of NIDD is in readiness for supporting messaging services with enhancement of priority treatment.

## Slide 3: Justification (2/2)
In R19, SA2 WG has enabled architecture enhancement for MPS for messaging (MPS4msg) for Service User (authorized by a regional/national authority) utilizing SMS or MMS, IMS Messaging in periods of network congestion during which normal commercial messaging services are degraded.
Per TS 22.153: "The system shall support MPS priority for messaging services supported using IMS Messaging, SMS and/or MMS, or MSGin5G for an authorized Service User using a UE with a subscription for MPS.
NOTE 1: MPS for Messaging may make use of commercial messaging service offerings provided by the operator. However, the messaging service applications are not in scope.
Observation#3: MPS for messaging services are operator’s services in EPS/5GS for authorized Service Users. However, architectural enhancements can enable differential priority treatment for third-party users. This allows a third-party user with a UE or IoT device to access messaging services with prioritized treatment during urgent events, even within the 3GPP system. Examples of such enhancements include: e.g. network exposure functionalities enhancement to support third-party AF, differential priority treatment between authorized Service Users and authorized third-party users, and charging aspects, etc.
Observations#4: In SA1, R20 miniWID – Priority messaging service for third party user has been proposed for approval in Orlando, FL, USA meeting.

## Slide 4: Objective (1/3)
The objective is to study solutions addressing gaps for enabling priority messaging services (PMS) in the EPC and 5GC interfaces and procedures to support third-party users using UE/IoT device for SMS and NIDD based messaging with priority treatment within 3GPP system including TN and NTN/IoT NTN.
The following aspects will be studied:
WT-1: Study how priority messaging service is requested and authorized to third-party user using a UE or IoT device.
WT-1.1: study how to enhance the authentication and authorization procedure for the case that third-party user’s PMS subscription information (e.g., credentials) is not always associated with the UE’s/IoT device’s Home Network subscription.
WT-1.2: study how the third-party service provider sponsors the PMS usage for their third-party users when the UE/IoT device is not associated with third-party user’s PMS subscription.
NOTE 1: Charging Aspects will be coordinated with SA5.

## Slide 5: Objective (2/3)
WT-2: Study what and how PMS priority treatment is provided in EPC and 5GC for messaging services including MO/MT SMS over NAS and MO/MT NIDD-based messaging.
WT-2.1: study how to provide PMS priority treatment in signalling invocation/revocation and messaging delivery, and how to ensure PMS is with lower priority than MPS priority for messaging.
WT-2.2: study how to assign PMS priority level for the third-party user and enforce the PMS priority level in accessing, invocation signalling, and delivering messaging services.
NOTE 2: The enhancement of NIDD-based messaging for PMS is in the scope. The NIDD-based messaging platforms and inter system aspects are outside 3GPP scope.
NOTE 3: Priority treatment in access aspects will need coordination with RAN2.

## Slide 6: Objective (3/3)
WT-3: Study how to support a third-party user using UE/IoT devices for PMS when the UE/IoT device is roaming within home country or out of country.
NOTE 4: The Home network can configure the UE to discover and select a network supporting PMS when roaming outside of the home country.
WT-4: study what enhancements are needed for the network exposure functionalities to interact with the third-party AF, e.g. network configuration parameters provisioning, sponsor charging for PMS, authentication and authorization of UE/IoT device for PMS used by authorized third-party user, etc.

## Slide 8
Thank You