## Slide 1: VFL issues 3 and 4
Ericsson
3GPP SA2#166
Orlando, FL, USA, 18 – 22 November, 2024
S2-2411671

## Slide 2: -Whether the VFL server capability needs to be registered in NRF -Interaction between the consumer and the VFL Server
Issues to Discuss

## Slide 3: Issue 3:Whether the VFL server capability is to be registered in NRF
Based on the above ENs, the following question has been proposed by the rapporteurs:
  Whether and which info should be registered to NRF by the VFL server, e.g. only supported analytics ID like other normal AnLF, or VFL capability info of VFL server?
Current status:
  The following editor’s notes are captured in the CRs agreed at SA2#165:
    Editor’s Note：Whether NWDAF as VFL server registers to NRF with VFL capability information is needed is FFS. (CR: 2411193 – vivo; Clause: 5.2)
  Editor’s Note：Whether AF as VFL server registers to NRF with VFL capability information is needed is FFS. (CR: 2411193 – vivo; Clause: 5.X)
  Editor’s Note：Whether a discovery of an AF acting as VFL server is required and how it can be done is FFS. (CR: 2411193 – vivo; Clause: 6.2H.2.1.2)
  Editor’s note: whether to register and discover VFL server is FFS. (CR: 2410096 – ICS; Clause: 6.3.13, TS 23.501)

## Slide 4: Issue 4: Interaction between the VFL server and the consumer
Current status:
  The following editor’s notes are captured in the CRs agreed at SA2#165:
    Editor's note: Whether the case that the AnLF can not generathe the analytics output but can determines the VFL server for the requested analytics is exist is FFS. Whether and how such NWDAF is capable to determine the NWDAF as VFL server is FFS. (CR: 2411192 – OPPO; Clause: 6.2H.2.4.1)
    Editor’s Note: Further extensions are needed to show the interaction between consumer and VFL server. For example, how the consumer (i.e., NWDAF containing AnLF) sends a subscription request to VFL server (CR: 2411194 – CMCC; Clause: 6.2H.2.3.1)
Based on the above Ens (the first one for the inference and the second one for the training), the following question has been proposed by the rapporteurs:
  Who can be the consumer of VFL server?
  Under which condition the consumer will interact with the VFL server?
  What (e.g. analytics output, ML model or other new info) and how to interact with VFL server by the consumer?

## Slide 5: Training – Interactions between consumer and VFL Server
For training a VFL server is either an NWDAF containing MTLF or an AF.
Option 1: The AnLF may retrieve a ML Model from MTLF.
  The MTLF knows that the AF does not provide QoE but it knows that AF will do VFL. VFL Server capability of the AF needs to be registered to NRF.
  The MTLF is a VFL Server. No VFL Server capability needs to be registered in NRF.
Option 2: The consumer request Analytics from AnLF, then the AnLF is also MTLF and VFL Server. Everything is internal. No need to register VFL Server to NRF. Same as b) above, but AnLF and MTLF collocated.

## Slide 6: Training – Interactions between consumer and VFL Server
Option 3: The consumer finds the provider of AnalyticID and support for the AnalyticsSubscription/request service via NRF. No discovery of VFL Server is required. See slide 12 NWDAF as Sever and AF as server option 1)
  The AF may need to train the ML Model. The AF is the VFL Server
  The NWDAF/AnLF/MTLF may need to train the MLModel, the NWDAF is a VFL Server. This is the same as option 2.
Option 4: The consumer finds the provider of AnalyticID and support for the AnalyticsSubscription/request Analytics via NRF. The AnLF knows that the AnalyticsId is provided by an AF. No need to discover the VFL Server, the AnalyticsID and support for AnalyticsSubscription service is used instead. See slide 12 AF as VFL Server option 2)

## Slide 7: Inference – Interactions between consumer and VFL Server
Option 1: AnLF knows that the AF or NWDAF/AnLF/MTLF supports AnalyticsID, it learned it during training. No VFL Server discovery.
Option 2: AnLF is the VFL Server. No need to discover a VFL Server, this is internal to NWDAF.

## Slide 8: Inference – Interactions between consumer and VFL Server
Option 3: The consumer requests Analytics from the Analytics provider. AF or NWDAF/AnLF/MTLF in the figure. Same as option 3 when training. Discovery via NRF.
Option 4: The consumer requests Analytics from the AnLF, as the consumer is not authorized to contact the AF. Same as option 4 when training. Discovery via NRF.

## Slide 9: Companies views for Options.
Companies | Option 1 | Option 2 | Option 3 | Option 4 | Comments
Ericsson | Yes | Yes | No impact on Analytics consumer preferred | No impact on NWDAF(AnLF) preferred | The different options do not rule out each other, can exists in parallel.
Interdigital | Yes | Yes | Analytics consumer should not need to know about VFL capability. No impact on Analytics consumer is preferred | No impact on AnLF is preferred. | We assume that when AnLF request Analytics from AF, AF is acting a NF consumer and as such does not need to know the VFL capability of the AF
Vivo | No | Yes | Yes | Yes | Opt 3 and 4 are either one or the other, final only one will be choose 1) does not work, because no such MTLF (between AnLF and AF ) exists without supporting model provision for analytics ID but only the agent
Lenovo | Yes |  | No |  | Option 2 is too restrictive. Option 4 use case unclear.
ZTE | Neutral | Yes | Preferred | Preferred | AF can register whether it support analytics to NRF, which is simpler.
Huawei | Yes | Yes (with the assumption that the Consumer does not need to know that NWDAF is the VFL Server) | unclear | unclear | It seems option 3 and 4 are implying AF will be able to provide output of an Analytic ID when AF is the VFL Server.

## Slide 10: Way forward
Depending on the outcome for the companies views in previous slide(s).
Is the decision on which NF type to produce the result better suited by the consumer of Analytics or NWDAF?
Propose to define option 1 and option 2, given that normal procedure uses MLModelprovisioning today, so this keeps the design based. Then option 3 and 4 can also be added.
NWDAF as VFL server registering into NRF seems not to have any use case, and can be kept open, and discuss in the meeting.
Question on whether option 4 is included or a simplification of option 1?
Option 2 and Option 3 (with MTLF) are the same.

## Slide 11
Other info provided by companies offline

## Slide 12: 4. Interaction between the VFL server and the consumer(vivo’s view)
  Background: According to the Nnrf_NFDiscovery service as defined in TS 23.502, the consumer should find a NWDAF for an analytics results with NF type = NWDAF, target NF service name = Nnwdaf_AnalyticsInfo_Request, analytics ID, etc.
  For the NWDAF as VFL Server case, the NF consumer (e.g. PCF) could possibly discover the NWDAF from NRF directly, as the NWDAF registers its profile and supported analytics ID and supported NF service name = Nnwdaf_AnalyticsInfo_Request in its NF profile before the discovery procedure. Then, NF consumer requests the NWDAF as VFL server to provide analytics by invoking Nnwdaf_AnalyticsInfo_Request with a specific analytics ID.
  For the AF as VFL Server case:
    1) besides NWDAF type, if NF consumer is allowed by MNO to be extended to discover AF type, from whom to get analytics result, then similar things happen as the above 2nd bullet, i.e. NF consumer can discovers AF, then interacts with AF to get analytics result (may via NEF);
    2) If that is not allowed by the MNO, then as usual in background, the NF consumer can only find an NWDAF (i.e. AnLF) to get analytics ID from NRF, this AnLF is acting as the delegate of AF, it registers to NRF declaring supports of specific analytics ID, however, the output is actually generated by the behind AF as VFL server. IMO, why the AnLF can play a role like this , because there is some agreement negotiated between AnLF and AF. in other words, the inference output from an AF can be shared and used by some AnLF(s), just like model interoperatorlilty rationale.
consumer
NRF
NWDAF
NF type = NWDAF, target NF service name = Nnwdaf_AnalyticsInfo_Request, analytics ID
NWDAF ID, profile..
Nnwdaf_AnalyticsInfo_Request ..
NWDAF as VFL Server
consumer
NRF
NF type = NWDAF, target NF service name = Nnwdaf_AnalyticsInfo_Request, analytics ID
NWDAF ID, profile..
AnLF acts as a delegate of AF
AnLF
Nnwdaf_AnalyticsInfo_Request ..
NF type = AF, target NF service name = Naf_AnalyticsInfo_Request, analytics ID
AF
Naf_AnalyticsInfo_Request ..
We don’t have strong preference between 1) and 2).