## Slide 1: Discussion on ATSSS for IMS service
China Telecom

## Slide 2: Background
ATSSS feature enables a multi-access PDU Connectivity Service, which can exchange PDUs between the UE and a data network by simultaneously using one 3GPP access network and one non-3GPP access network (both connected to 5GC) when both accesses are allowed.
IMS services can get benefit from the ATSSS feature: when the network conditions change, some user traffic related to dedicated IMS services can be offloaded from 3GPP access to non-3GPP access path, while other types of IMS services remain on the 3GPP access path.

## Slide 3: Use cases
#1: traffic is transmitted via different access according to their data type characteristics, e.g., data rate requirement.
#2: traffic is transmitted via different access according to their “sponsor”, e.g., service #2 is offloaded to non-3GPP access as service #1 might have higher priority.
  Suppose all IMS traffic is transmitted via 3GPP access at the beginning. When network conditions change, some user traffic related to dedicated IMS services can be offloaded from 3GPP access to non-3GPP access path, while other types of IMS services remain on the 3GPP access path:

## Slide 4: Gap analysis
ATSSS rule use traffic descriptor to differentiate different services. However, the PCF fails to provide suitable policy for the use case in the previous slide because it cannot configure the target traffic in the current format of Traffic descriptor for IMS services:
  Application descriptors:
  The Application descriptor used in the SIP procedure can only identify the TYPE of the service not the application/service name.
  So the PCF cannot match the traffic with the target prioritized service.
  IP 5-tuples:
  The same IP address but DYNAMIC assigned port numbers for DC services from the same IMS AS.
  So the PCF cannot provide the until the traffic is up.

## Slide 5: Summary
It is proposed to study the enhancement in Rel-20:
  To optimize the traffic descriptor of ATSSS rule to identify the IMS services in finer granularities
  To enhance IMS services related procedures for agility in 3GPP/non-3GPP access selection
  To improve the mechanism for PCF’s awareness/matching of subscription data and traffic data