## Slide 1: Discussion on Detailed content and the parameters during VFL process
SA2#166
Huawei, HiSilicon
S2-2411827

## Slide 2: Working Plan - Point 5: Detailed content and the parameters during VFL process
The Key Points to be discussed:
  5.1: Discovery
    Whether the following parameters are needed in the discovery request to NRF for VFL?
  5.2: Training
    Whether the following parameters are needed to be interact between VFL server and VFL client during VFL training?
For Discovery and Training there is a set of ENs that need to be solved
  See the summary from rapporteur: https://www.3gpp.org/ftp/tsg_sa/WG2_Arch/TSGS2_166_Orlando_2024-11/INBOX/DRAFTS/R19%20AIML_CN/Left%20issues%20list%20of%20VFL%20to%20be%20resovled%20in%20S2%23166%20meeting-r5.docx

## Slide 3: Point 5.1: Discovery (1/2)
Editor’s Notes
  Editor’s note: additional VFL learning related discovery parameters are FFS. (CR: 2410096 – ICS; Clause: 6.3.13, TS 23.501)
List of Parameters to be discussed
Name of parameters | Support for “Not needed” | Support for “needed” | neutral | Proposed Way forward
feature information | ZTE Ericsson: can live with Feature ID without detailing the features InterDigital: Feature ID is sufficient Huawei : Transferring feature information will have privacy issue. Solution direction assuming pre-establish agreements among VFL participants. The feature information can be considered as statically defined for the VFL participants that can collaborate for a given analytics ID and a sample space (i.e., supported list of sample IDs) ETRI: same view as Ericsson and InterDigital | Nokia: It is basic for VFL that different clients handle different features. It is thus essential to enable a server to discover clients supporting the desired features. Support of features will likely require specific code and is therefore likely relatively static and well-suited from that perspective for NRF discovery Discovering more clients and subsequently using feature negotiation to pick clients for specific features is not efficient but can be allowed in addition to address security / privacy concerns and for more dynamic features (if they exist) | OPPO：If feature info can be static e.g., based on the historic data, it can be register to the NRF with the feature ID. What the granularity of the info can be represent by the feature ID need further discussion | Not Needed(?) It seems the majority think feature information shall not be detailed.
vendor information | Ericsson: We can live it as optional, and discuss together with the VFL interoperabilityInformationIt needs to be discussed how it will work when untrusted AF is participant Huawei: Does not properly represent the case of AFs participating in the VFL process, as AFs would require yet another information, not vendor. This information can be enclosed as part of the VFL interoperability information. | Nokia: The split of already standardized analytics into standardized features is not realistic to achieve in this release. Also the intermediate results to be exchanged between server and client will depend on the featurresw, but also on the models (which are also supposed to be vendor specific). For AF as a server even the Analytics themselves will be vendor-specific. For those reasons VFL will only work between entities of the same vendors or between vendors that agree on additional unstandardized aspects to enable interoperability. OPPO: should be together with the interoperability information. | ZTE: This should be renamed into MLModelinteroperabilityIndicator | Need to discuss which kind of information should be used when untrusted AF is involved.

## Slide 4: Point 5.1: Discovery (2/2)
Editor’s Notes
  Editor’s note: additional VFL learning related discovery parameters are FFS. (CR: 2410096 – ICS; Clause: 6.3.13, TS 23.501)
List of Parameters to be discussed
Name of parameters | Support for “Not needed” | Support for “needed” | neutral | Proposed Way forward
VFL interoperability information |  | Ericsson InterDigital Nokia: Depends on contents. OK to place vendor IDs and vendor specific feature information within. Also OK to allow for additional vendor-specific information Huawei: Allows a simple way to enclose all the parametrization agreed among VFL participants that agreed to collaborate in the VFL process (e.g., vendor information, fixed feature space of each VFL participant for the same analytics ID). OPPO: feature info and vender info should be in the VFL interoperation information | ZTE | Needed No other view so far.
New parameter? |  |  |  | 

## Slide 5: Point 5.2: Training (1/5)
Name of parameters | support for “Not Needed” | Arguments for “Needed” | Neutral | Proposed Way forward
feature information | ZTE Ericsson: can live with Feature ID without detailing the features InterDigital: Feature ID is sufficient Huawei OPPO: if feature ID supported in the NRF, then using feature ID in the training is enough | Nokia: Server needs to indicate to client for which feature it should perform training (a client could support several features) AS a compromise also agreeable tp allow for a feature negotiation in preparation phase if feature registration in NRF is also supported |  | Not Needed(?) It seems the majority think feature information shall not be detailed.
ID(s) of sample(s) corresponding to the intermediate training result | Nokia Ericsson: It is part of the intermediate results, for NN is part of the intermediate matrix Huawei: do not need to specify every parameter in intermediate results | ZTE: At every iteration of training, help server to identify corresponding sample and compute loss information (applicable to batch gradient descent and stochastic gradient descent) InterDigital: Needed, but think it may not be needed every iteration ETRI: needed, but open to discuss detailed options, such as interaction based on part of the intermediate results or on every iteration OPPO: needed, it will let server know for this iteration, which samples related intermedia result the server need to compute the loss. |  | ?? It seems the controversial part is whether it is out of intermediate results or not.
VFL interoperability information | Nokia | ZTE: At the start of training or when conducting client re-selection Ericsson: It is needed at least at the preparation phase Huawei: should be used at the preparation phase OPPO: same view |  | ?? It seems the controversial part is whether preparation phase is part of training procedure
… |  |  |  | 
List of Parameters in rapporteur’s report

## Slide 6: Point 5.2: Training (2/5)
Name of parameters | Support for “Not Needed” | Support for “Needed” | Neutral | Proposed Way forward
VFL correlation ID |  | ZTE: At the start of training only Ericsson InterDigital Nokia Huawei ETRI OPPO |  | Needed No other view so far.
Convergence report | ZTE: VFL server can determine to terminate the process Nokia: Server is the one to determine termination | Ericsson: Helps VFL clients to determine how to converge the training. InterDigital | Huawei: It depends on the exact information in Convergence report. OPPO: is it also related to the accuracy monitoring? | ?? It seems the controversial part is whether client can determine to stop VFL training.
Initial model from VFL server to VFL clients | Nokia Ericsson: The initial model should be provisioned by OAM or any other means but I is not part of the training phase. OPPO: We should align with this principle in different case. If model can not shared, then even for the model stored in the ADRF should also not supported. | ZTE: only applicable between NWDAF and trust AF, at the training phase ETRI: The initial model should be provisioned by any means, as it is no possible for the VFL server to interpret intermediate results from VFL clients without it. Considering scenarios where model in use may change (e.g., due to poor model performance), we prefer including it as part of the training phase. | Huawei: It depends on the algorithms. | ?? It seems the controversial part is whether initial model provisioning is part of training.
Maximum response time: maximum response time(i.e. the maximum time between VFL clients receive backward local model information and send back intermediate training result). |  | ZTE: at start of training ETRI | Huawei: See P8, VFL Requirements | ?? Wait for more input

## Slide 7: Point 5.2: Training (3/5) – Parameters related to Start or Preparation Phase
Name of parameters | Support for “Not Needed” | Support for “Needed” | Neutral | Proposed Way forward
Analytics ID |  | Huawei: In the preparation phase or at the start of the training. Only the VFL correlation ID is not enough to indicate to the VFL Participants what is the target of the VFL training. The Analytics ID is a core information |  | ?? Wait for more input
ID(s) of sample(s) during preparation/start of training |  | Huawei: Required either during the conclusion of the preparation phase or at the start of the training phase. VFL participants must receive from the VFL Server the final list of sample IDs to be used for a specific training to start, as each VFL server makes the final decision on the list based on the input from VFL participants. OPPO: needed. When one iteration start, the server need to indicate to each client for this iteration, which samples will be used |  | ?? Wait for more input

## Slide 8: Point 5.2: Training (4/5) – New Parameters – Compatibility with existing services
Name of parameters | Support for “Not Needed” | Support for “Needed” | Neutral | Proposed Way forward
VFL Requirements | OPPO: Seems overlap with the interoperability information |  | Huawei: Could be used to standardize some high level parameters from the AI process, such as convergency rate, class of AI process (regression - i.e., model with real output - or classification – i.e., model with integer output) | ?? Wait for more input
VFL Data Availability requirement |  |  | Huawei: Keeps the compatibility with the parameters already defined in the model training services. | ?? Wait for more input Needs to discuss whether to use existing parameter or add “VFL” specific parameter
VFL Availability Time requirements |  |  | Huawei: Keeps the compatibility with the parameters already defined in the model training services. | ?? Wait for more input Needs to discuss whether to use existing parameter or add “VFL” specific parameter

## Slide 9: Point 5.2: Training (5/5) - New Parameters – Linking VFL Training to Other VFL Processes (inference, accuracy monitoring)
Name of parameters | Support for “Not Needed” | Support for “Needed” | Neutral | Proposed Way forward
VFL Server NF ID | OPPO: This is depend on the issue 4 discussion | Huawei: This information is required to allow the an NWDAF AnLF (with VFL Client) role receiving a subscription for analytics generation to determine the VFL server (e.g., as per agreed procedure in Clause 6.2H.2.4.1 paper S2-2411192) during VFL inference for a given VFL correlation ID for an analytics ID |  | ?? Wait for more input
VFL Client NF ID |  | Huawei: This information is required to allow the an NWDAF AnLF (with VFL Server) role receiving a subscription for analytics generation to determine the VFL Clients (e.g., as per agreed procedure in Clause 6.2H.2.4.1 paper S2-2411192) during VFL inference for a given VFL correlation ID for an analytics ID. |  | ?? Wait for more input
VFL Training DataSet Tag | OPPO: samples and feature info is enough | Huawei: Each VFL participant collects its own data for the training of their local ML model. In order to enable the proper separation of data samples for training and retraining of the same models associated with a VFL correlation ID (as per R18), each VFL participant shall have the same dataset tag to allow alignment of used information. |  | ?? Wait for more input

## Slide 10: Annex： Mapping between ENs and parameters
List of Editor’s Notes:
EN | Parameter related to EN
Editor's note: It is FFS additional parameters are needed to send from the VFL server to VFL client. (CR: 2411192 – OPPO; Clause: 6.2H.2.4.1) -> VFL Inference | general
Editor's note: It is FFS additional parameters are needed to send from the VFL client to VFL server. (CR: 2411192 – OPPO; Clause: 6.2H.2.4.1) -> VFL Inference | general
Editor’s Note: It is FFS whether sample/feature information is required to be provided in each training. (CR: 2411194 – CMCC; Clause: 6.2H.2.3.1) | ID(s) of sample(s) corresponding to the intermediate training result
Editor’s note: The report may include ID(s) of sample(s) corresponding to the intermediate training result. (CR: 2411194 – CMCC; Clause: 6.2H.2.3.1) | ID(s) of sample(s) corresponding to the intermediate training result
Editor´s Note: Whether and how to include interoperability information in the VFL training procedure is FFS. (CR: 2411194 – CMCC; Clause: 6.2H.2.3.1) | VFL interoperability information VFL Group ID
Editor´s Note: Additional Parameters to be provided in the request are FFS. (CR: 2411194 – CMCC; Clause: 6.2H.2.3.1) | VFL interoperability information Maximum response time Analytics ID VFL Group ID Sample Alignment Information VFL Requirements VFL Data Availability requirement VFL Availability Time requirements VFL Server NF ID VFL Client NF ID VFL Training DataSet Tag
Editor´s note: The following is FFS and may depend on the service design: When the clients reports the client intermediate training result, it also includes the corresponding VFL correlation ID. (CR: 2411194 – CMCC; Clause: 6.2H.2.3.1) | VFL correlation ID
Editor’s Note: Whether VFL server and VFL clients share feature information is FFS. (CR: 2411194 – CMCC; Clause: 6.2H.2.3.1) | feature information
Editor’s Note: The content of the VFL status report is FFS. (CR: 2411194 – CMCC; Clause: 6.2H.2.3.1) | ID(s) of sample(s) corresponding to the intermediate training result VFL correlation ID Convergence report
Editor’s Note: Whether VFL server sending convergence report to the VFL client and what is convergence report are FFS (CR: 2411194 – CMCC; Clause: 6.2H.2.3.1) | Convergence report
Editor's note: Whether and how to provide initial model from VFL server to VFL clients based on VFL client request is FFS. (CR: 2411195 – KDDI; Clause 5.4) | Initial model from VFL server to VFL clients

## Slide 11: Thank you.