## Slide 1: SoH Questions for NG_RTC_Ph2 way forward
China Mobile (Rapporteur)

## Slide 2: KI#4: Extensible IMS framework to support authorization and authentication of third-party identities in IMS sessions
This key issue is to study how to enhance the IMS architecture and procedures to support third party identities in IMS sessions
It is concluded in the TR that either S-CSCF or IMS AS supports authorization of usage of third party identities. However, some issues need to be discussed and decided during normative phase
  Issue 1: whether the authorization information should be stored in transparent data or service profile
    Option 1.1: If IMS AS authorizes the subscriber (S2-2412132), the authorization information should be stored as transparent data in HSS and not standardized
    Option 1.2: If S-CSCF authorizes the subscriber (S2-2412085), the authorization information should be stored as service profile and be standardized over Cx/N70
    If both options are supported, whether supporting co-existence of both option in one network need to be considered
It is concluded in the TR that RCD information may be provisioned in the HSS repository data via the NEF, however it seems there is different proposals
  Issue 2: how to support provisioning of RCD information
    option 2.1: RCD information is provisioned via OAM, thus provisiong of RCD information via NEF is not supported in this release (S2-2412132)
    Option 2.2: Provisioning of RCD information via NEF is supported (S2-2412085, S2-2412092)

## Slide 3: SoH for KI#4: Extensible IMS framework to support authorization and authentication of third-party identities in IMS sessions
Q1: whether the authorization information should be stored in transparent data or service profile
  only Option 1.1 is supported:
    Yes:
    No:
  only Option 1.2 is supported
    Yes:
    No:
  Both option 1.1 and 1.2 are supported
    Yes:
    No:
Q2: whether supporting co-existence of both option 1.1 and 1.2 in one network
    Yes:
    No:
Q3: how to support provisioning of RCD information
  Option 2.1: via NEF not supported in this release OAM
    Yes:
    No:
  Option 2.2: via NEF
    Yes:
    No:

## Slide 4: KI#8: Support of IMS Avatar Communication
This key issue aims to study enhancements of IMS architecture, interfaces, and procedures to support IMS based Avatar communication
It has been concluded in #165 that the Avatar ID list is stored in BAR per application and is downloaded via DC AS to DCSF, but the following aspects are to be decided
  issue 1: whether the service of DCAS and DCSF, interface between DCSF and DC AS are to be standardized
    Option 1.1: standardized in 3GPP (S2-2412170)
    Option 1.2: not standardized in 3GPP (S2-2411743)
  Issue 2: how the DCSF discovers the DC AS who handles the requested Avatar ID list
    Option 2.1: via DC service data in HSS (S2-2411332)
    Option 2.2: via NRF
Regarding to the Avatar communication procedure, there are fidderent proposals for the interaction between DC AS and IMS AS for media instructions
  issue 4: how DC AS sends media instructions to MF
    Option 4.1: DCAS send instruction to DCSF through IMS AS, and then via DCSF reusing R18
    Option 4.2: directly using R19 (S2-2412170)

## Slide 5: SoH for KI#8: Support of IMS Avatar Communication
Q1: whether the service of DCAS and DCSF, interface between DCSF and DC AS are to be standardized
  Option 1.1: standardized in 3GPP
    Yes:
    No:
  Option 1.2: not standardized in 3GPP
    Yes:
    No:
Q2: how the DCSF discovers the DC AS who handles the requested Avatar ID list
  Option 3.1: via DC service data in HSS
    Yes:
    No:
  Option 3.2: via NRF
    Yes:
    No:
Q4: how DC AS sends media instructions to MF
  Option 4.1: DCAS send instruction to DCSF through IMS AS, and then via DCSF reusing R18
    Yes:
    No:
  Option 4.2: directly using R19
    Yes:
    No:

## Slide 6: KI#2: Impact on IMS architecture, interfaces and procedures to support IMS capability exposure in the context of IMS data channel session
This key issue studies enhancements to IMS architecture, interfaces and procedures to expose IMS services in the following IMS data channel related scenarios
The general procedures and related service enhancements to support this feature have been agreed in #165
There are different proposals regarding to how the DC AS get immediate response when creating or modifying DC in a session using Nimsas_SessionManagement service.
  Option 1: define a new service operation Nimsas_SessionManagement_Notify to notify DC AS (S2-2411469, S2-2411562)
  Option 2: using existing Nimsas_ImsEE_Notify service operation (S2-2412164, S2-2412166)

## Slide 7: SoH for KI#2: Impact on IMS architecture, interfaces and procedures to support IMS capability exposure in the context of IMS data channel session
Q1: how the DC AS get immediate response when creating or modifying DC in a session
  Option 1: define a new service operation Nimsas_SessionManagement_Notify
    Yes:
    No:
  Option 2: using existing Nimsas_ImsEE_Notify service operation
    Yes:
    No:

## Slide 8: KI#6: standalone DC session Issues need to be resolved
Non-trivial
  Whether to remove BDC+ADC non-simultaneous way (S2-2410447 for removing)?
    Proposal: keep the scenario, the terminating user is alert when receiving INVITE with only BDC
  Whether to change the alerting criteria (S2-2410356 changes the alerting)?
    Proposal: besides alert before running APP, the UE can be configured to alert user before downloading APP
  Whether to describe P-Early-Media handling (S2-2409985 triggers the handling of P-Early-Media)?
    Proposal: P-Early-Media is sent to originating side and terminating side to enable both UEs to download APP
  Whether to remove the handling of setting ADC port to zero for BDC+ADC simultaneous way when APP not available in terminating UE? (S2-2410447 removes the related part)
    Proposal: see next slides on how to inform originating UE application is not downloaded but desired
Trivial
  Whether to change the term of "Standalone IMS DC Session“ (S2-2410356 change the term)?
    Proposal: next meeting D category CR for update
  Whether to redraw the BDC+ADC simultaneous way procedure (S2-2409985 redraw the flow)?
    Proposal: redraw the figures to reflect downloading before answer and alert

## Slide 9: KI#6: standalone DC session, SoH

## Slide 10: BACKUP