## Slide 1: Discussion on using satellites for limited backhaul in IOPS
Mythri Hunukumbure, Sivasubramaniam Ramanan –
UK Home Office

## Slide 2: Limited backhaul provision for IOPS
Satellites (especially LEO Sat’s) are a prime candidate for the provision of limited backhaul in IOPS operations.
  The satellite backhaul will be set-up (immediately) after the IOPS cell(s) is/are configured.
  The PCRF/PCF of the 5GS or EPS that provides the MC connectivity can inform the MC service server the capacity and QoS that can be supported in this limited backhaul. For LEO Sat’s these qualities can also vary over time.
As the backhaul link is constrained, only selective IOPS users can use this link to gain services from the MC service server.
  These selective users will be pre-configured and will need to notify their presence inside the IOPS cell, when the IOPS cell(s) is/are configured.
Example from ESN where this connectivity is highly useful
  Incident commander handling firefighter team in a remote wildfire need to request more resources.

## Slide 3: Current IOPS Architecture
SIP based IOPS signalling (for IOPS discovery, subscription and notification events) occurs between the signalling application server and signalling user agent client.
  The reference point is MC-IOPS-X1.
There is no signalling between the IOPS 5GS/EPS and the signalling application server or signalling user agent client currently defined.
  Only Application layer reference points between IOPS MC connectivity function and the IOPS EPS are defined. These support the allocation of unicast or multicast bearers.
Also the IOPS MC connectivity function and the IOPS EPS identifies users through IOPS MC ID’s or IOPS MC service ID’s (no global MC ID’s are recognized).

## Slide 4: Envisaged limited backhaul connectivity
MC UE1 is a selective user and requests the use of backhaul connectivity from IOPS MC connectivity function and IOPS EPS.
The limited backhaul is set-up and the PCRF indicates available QoS to the MC service server.
MC service server receives MC UE1’s request and after authentication:
  Allows MCPTT private and group calls and MCData SDS services through the respective service servers.
  MC UE2 and MC UE3 do not gain access to services through this limited backhaul usage.
* This diagram is for illustration only. Information flows going through boxes indicate these functions are involved.

## Slide 5: Proposed solution
The selective users within the IOPS cell(s) would indicate their presence to the IOPS MC connectivity function during device discovery.
The IOPS MC connectivity function shall be able to:
  Indicate to the IOPS 5GS/EPS that selective users UEs/users within the IOPS cell(s) are present and are requesting MC services through limited backhaul.
We propose to define a new reference point, MC-IOPS-X2 between the signalling application server and the IOPS 5GS/EPS for the above purposes.
Also the IOPS MC connectivity function and IOPS EPS to handle the MC service ID’s of selective users, so they can be verified with the MC service server(s).
MC-IOPS-X2