## Slide 1: Thoughts on Release 19
DISH Network

## Slide 2: Outline: Our Theme !!!
Past: 5G SA design was motivated for the NFV Native Deployment
  Service Based Architecture (SBA)
  Data Storage architectures for better stateless operation
  SBA enhancement including SCP (Service Communication Proxy)
  Supporting Distributed Network Function
Present: For the Cloud Native Deployment, is current 5G system perfect?
  3GPP has been occupied with introducing new enablers and capabilities, but there are gaps what the operator wants
  During 5G deployment in a Cloud Native environment, issues such as scalability, observability, and cloud automation tools alignment with 5G CNF (e.g., AMF, UPF) were encountered
  Inefficiency has been observed in deployments/operations
  SBA is not fully supported (e.g., N2, N4)
Future: 5G System enhancement/re-design for Cloud Native Deployment
  Let’s study what is missing and updates are needed in the current 3GPP architecture for Cloud Native deployment
  Rel-19, Cloud Native OAM (SA WG5) for better inter-operability and operation
  Rel-19/Rel-20, we can study what is the paint points and potential enhancements of 5GS for the Cloud Native Deployment

## Slide 3: Overall View on Rel-19 Content (1/2)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Enough Time unit allocation for TEI regarding 5G deployments and urgent issue from Operators |  |  |  |  | 
2 | 5GS enhancement for Cloud Native Deployment | Service Based Interface for N2: - Fully Service Based interface for N2 |  | SA2 | Yes, Alignment | 
 |  | UPF enhancement for Exposure and SBA Phase 2 Modular design and deployment of user plane (UPF) Fully Service Based interface for N4 Enhanced UF event exposure |  | SA2 | No | 
3 |  |  |  |  |  | 
4 |  | SCP enhancement - SCP support for the inter-PLMN, further enhancement? |  | SA2 | No | 
5 |  | Cloud Native OAM interface - Interworking with alternative cloud platforms for management and orchestration (Generic) |  | SA5 | N/A | 
6 | Dual Access Dual Registration | Enhancing service continuity using Dual registration and dual access across two PLMNs Reliable communication with accessing multiple Networks (e.g., two PLMNs, PLMN & SNPN) | FS_DualSteer | SA2 | N/A | 
7 | Energy as a Service | Study architecture enhancements to facilitate efficient energy use and energy saving Enabler to provide energy as a service characteristics | FS_EnergyServ | SA2 | Yes, Alignment | SA5
8 | 5G enhancement for AI/ML | Study the coordination of cross-domain AI/ML functionalities Closed loop design for AI/ML |  | SA2 | N/A | SA5

## Slide 4: Overall View on Rel-19 Content (2/2)
Prioritize any bug fix/small enhancement for 5G deployment/operation
  Allocate enough buffer Time Unit for TEI19 for this issue
Let’s have a enough Study (Study only phase) time for bigger items, to have a consolidated view, no RUSH !!!
  Integrated Sensing and Communication
  Ambient IoT

## Slide 5: Cloud Native Deployment

## Slide 6: Cloud Native Deployment (Potential Areas)
Fully Service Based Architecture (for better observability and traceability) of 5G NFs
  Without SCP, due to TLS, probing the SBI interface is not possible
  With SCP, still N2/N4 can’t use the SCP
UPF enhancement (UPEAS phase 2)
  Modular (e.g., NAT, DPI, Firewall) design of the UPF
  Study any additional UPF exposure service
SCP enhancement
  Extending to SNPN
  Inter-PLMN
Cloud Native OAM (SA WG5)
  OAM (Orchestration) architecture enhancement for the Cloud Native Deployment
  Study whether/how to interwork with alternative cloud platforms (e.g. Cloud Native Orchestration)

## Slide 7: Dual Access/Dual Registration for Reliable Comm.
For Reliable communication:
  5GS supports 3GPP dual accesses with dual registrations
  Minimal impact to the Secondary PLMN
  RAN impact need to be investigated
UE accessing Multiple Networks:
  Remote control, Remote operations scenarios require Device accessing to multiple networks simultaneously (NR-NR, NR-LTE, TN-NTN) for service continuity and reliable communication

## Slide 8: Energy as a Service
Reducing Carbon Footprint is a common goal for operators and customers
Study how to introduce the Energy as a Service
  Per UE/ Group of UEs
  Per Slice
  Adding CDR for new type of Charring and/or policy change
    The amount of the energy consumption will be the new criteria for cellular plan