## Slide 1: OPPO views on Rel-19
Tricci So
Delegate, OPPO
ADVANCED

## Slide 2: Perspectives from OPPO on Rel-19
Study emerging mobile system & business applications towards 6G visions
Essential advanced feature enhancements to Rel-18 to warrant the value proposition offered by 5G Advanced system
Necessary capacity /coverage/ performance enhancements and charging support to safeguard ROI interests of MNOs and MVNOs
v
v
Exceptional high speed
Ultra-low latency
Significant boost of network capacity
Enhanced high reliability
Catalyst of transformative technology (i.e., XR/Metaverse & AI)
Efficient IoT Enablement
Rel-19 is the last frontier to deliver the promises of 5G Advanced System:
Furthermore, Rel-19 should also be the stepping-stone towards the 6G visions.

## Slide 3: Outline
Multi-domain AI/ML support over the 5G System
5G Architecture Enhancement support for Ambient IoT devices
Integrated Sensing & Communications
Extended Reality & Media Services – XRM_Ph2
Traffic Steering, Switching and Splitting over Dual 3GPP Accesses (DualSteer)
Proximity based services Phase-3
Additional References - Multi-domain AI/ML support over the 5G System
Additional References - 5G Architecture Enhancement support for Ambient IoT devices
Additional References - Traffic Steering, Switching and Splitting over Dual 3GPP Accesses (DualSteer)
Summary
Backup

## Slide 4: Overall View on Rel-19 Content (1/6)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Multi-domain AI/ML support over the 5G System (See slides 9-11 for more reference) | Study for the converged system solutions to support AI/ML operations across multiple domains (i.e. UE, RAN, 5GC, OAM and Application) over 5GS. Key Work Tasks includes defining - Study 5GS enhancements to enable AI/ML support for the RAN-1 use cases for AI assisted CSI feedback, beam management and positioning and to support the RAN-2 model distributions which consist of (a) Data Collection, (b) Model Training, (c) Model Management, (d) Model Inference and (e ) Model Storage. Model identification & registration to enable coordination among UE, RAN and 5GC for model transfer/delivery Data Collection from UE to assist the model training QoS and policy control to support RAN model transfer and delivery (including data collection) 5GC/LMF extensions (e.g. UE selection) to support AI training/inference/real-time performance monitoring of the positioning model Study 5GC enhancements to enable cross-domain (i.e. UE, 5GC and applications) Vertical Federated Learning (VFL) to support AI training and inference for verifying and/or predicting the (a) Application QoE performance, (b) Network Energy Saving and (C) Mobility Optimization Feature determination and alignment across domains according to the target label when applying the VFL operation NF(s) identification/selection of required NF(s) in 5GC domain corresponding to the local feature to collaborate on the VFL operation (i.e. training/inference) Transport and Policy configurations/QoS enhancement, if needed, to support the VFL operation Study 5GC assistance for the Transfer Learning to expedite the model training or inference operation Whether and what to extend the R18 Member UE selection to support the Transfer Learning Whether and what to extend the QoS & Policy control as well as for the service provisioning for the traffic to support the Transfer Learning What and how to transfer the AI model between the UE (e.g. via local routing through the 5G Core or via the sidelink). | Yes, TR 22.876/ TR (RAN1)/ TR (RAN2)/ TR (RAN3) | SA2/RAN | Yes, Major | SA5 for charging and management capabilities

## Slide 5: Overall View on Rel-19 Content (2/6)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
2 | 5G Architecture Enhancement support for Ambient IoT devices (See slides 12-15 for more reference) | 5G System Architecture is enhanced to support ambient power-enabled IoT devices under extremely constrained power consumption conditions. The study shall consider the scenarios for Ambient IoT devices connecting to gNB either directly (i.e. direct mode) or via intermedia UE (i.e. indirect mode). However, whether all Ambient IoT device types (i.e. A, B and C) support both modes are TBD. Key Work Tasks includes defining - 1. Study the following 5G system signalling extensions: Registration, Subscription, Identification management with or without the 3rd party assistance Mobility, paging and connection management support for Ambient IoT devices, if applicable to specific device type(s) Architecture requirements for authentication and authorization of the Ambient IoT devices and device privacy; 3rd party assistance via service provisioning and network exposure support for Identification, Mobility and/or Connection Management. Link management between the Ambient IoT devices and the intermediate UE (i.e. indirect mode); Group management of the Ambient IoT devices; 2. Study whether and how to perform Session Management for data transmission Connectivity establishment for data transmission vs. connection less communication; Data received or collected by the network exposed to the 3rd party for backend service; 3. Study QoS and Policy Enhancement to support the Ambient IoT devices; 4. Study access and congestion control mechanisms to support the ultra-high density deployment scenarios of Ambient IoT devices | Yes, TR 22.840/TS(?) | SA2 | Yes, Major | SA3 for security, SA5 for charging, CT1 for network selection

## Slide 6: Overall View on Rel-19 Content (3/6)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
3 | Integrated Sensing & Communications | 5G system support for NR-based sensing capabilities to get information about characteristics of the environment and/or objects within the environment (e.g., shape, size, orientation, speed, location, distances or relative motion between objects, etc.) using NR RF signals. In R19 study, it is recommended to first focus on the UE-involved sensing ( i.e., UE-gNB bistatic sensing (Uu DL/UL) , UE-UE bistatic sensing and UE monostatic sensing) to ensure sensing coverage. Key Work Tasks includes defining - Study what and how to extend the 5GS architecture to support UE involved sensing (i.e., user plane sensing can be used) for large amounts of sensing data. Study 5GC sensing service exposure to UE and to the AF and service provisioning Study discovery and selection of the sensing entities (e.g., UE, gNB, etc.) Study authorization and privacy requirements for different sensing targets. Study sensing quality/QoS control & management for sensing services to support high volume and resource consumption for sensing data transfer. Study sensing data/result handling within 5GS and data/result transfer between 5GS and application. Study different sensing deployment considerations: - possible different types of sensing functions to support multiple service types and data types. - possible multiple sensing function instances to address the high processing complexity. 7. Study the charging method for different sensing target. 8. Study UE configuration according to above quality management, authorization, charging, service type aspects. 9. Study whether and how to use the non-3GPP sensing data in the 5GS architecture. | Yes, TR 22.837/TS(?) | SA2/RAN | Yes, Major | SA3 for security, SA5 for charging

## Slide 7: Overall View on Rel-19 Content (4/6)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
4 | Extended Reality & Media Services – XRM_Ph2 | Study the XR enhancements to extend and to optimize the PDU Set handling for advanced media services and to support the localized mobile metaverse services. Key Work Tasks includes defining - Study the extensions of the QoS handling for the PDU Set across multiple PDU sessions and/or across multiple service flows. Study the support for the UL PDU Set handling Study the enhancement of the traffic handling of PDU Set identification and marking when carrying encrypted media traffic including the inter-PDU Set dependency handling Study the performance monitoring (e.g. E2E packet delay) and guarantee over XR traffic over N6 Study the efficient and optimized multi-modal service coordination transmission in local area for metaverse traffic - e.g. joint admission control, handover control, per packet level reordering and synchronization etc. Study the service continuity for AR/VR to support immersive user experience under high UE mobility Study the integrated handling of 3GPP and non-3GPP XRM services | Yes, TR 22.856/TS(?) | SA led | Yes, Major | SA3 for security, SA5 for charging

## Slide 8: Overall View on Rel-19 Content (5/6)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
5 | Traffic Steering, Switching and Splitting over Dual 3GPP Accesses (DualSteer) (See slide 16 for more reference) | Study the enablement of 5GS support for UE with dual radio for traffic steering, switching and splitting of a given PDU session across two 3GPP accesses across the same, different PLMNs or PLMN & NPN. Key Work Tasks includes defining - Study the 5GC extensions in term of registration, connection and mobility management to enable MA PDU session support over two 3GPP accesses (same or different RAT types) for a UE with a single subscription. Study the 5GC session management extensions in SMF to derive the N4 (MAR) for the UPF to include together with routing and QoS information (FAR, PDR, etc.), and to derive the ATSSS rules to the UE delivered via AMF together with the UE Route Selection Policy (URSP) rules via NAS (N1). Study the unified policy and charging control support Compatible policy control rule for MA-PDU session over different 3GPP access types or over 3GPP and non-3GPP access types Any possible extensions to NWDAF to assist PCF to derive the ATSSS policy decision Changes to the charging policy, if needed | Yes, TR 22.841/TS(?) | SA led | No | SA3 for security, SA5 for charging

## Slide 9: Overall View on Rel-19 Content (6/6)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
6 | Proximity based services Phase-3 | The study item aims at further investigating 5G System enhancements to support Proximity Services, based on what has been specified in Rel-17 and Rel-18. The detailed objectives are to investigate potential 5GS enhancements in order to support the work tasks as described below. Key Work Tasks includes defining - 1. Continued to extend the relay capabilities to support to support: The multi-path relay to enable network managed multi-path indirect network connection. Multi hop U2N Relay, U2U Relay. Group mobility for L2 U2N Relay. MBS support over U2N Relay. | Yes, TS 22.278, TS 22.261, TS 22.115 | SA led | Yes, Major | SA3 for security, SA5 for charging
Concepts of various Relay Configurations

## Slide 10
Application Server
5G NF
UE
Local Data in Network
(e.g. slice status, applied policy and QoS)
Local Data in Application Server
(e.g. applied Codec, user preference) and Label (QoE)
Local Data in UE
Local Data in NW
Local Data in APP
AI Model
Output
(Estimated QoE)
(For Target UE)
IDx – Identifying the common training/inference request across the 5GS domains
AI-enabled RAN Model Distribution
AI-assisted RAN Positioning
5GC Assistance for Transfer Learning
Cross-domain Vertical Federated Learning to support AI-training/inference and Performance Monitoring
Multi-domain AI/ML support over the 5G System
AI/ML Enabled RAN

## Slide 11: Opportunities for 5G Operators for Implementing Cross-domain AI/ML
Improved network performance: AI/ML algorithms can be used to optimize network performance by predicting traffic patterns and adjusting network resources accordingly. This leads to more efficient use of network resources, reduced latency and faster/higher data rates.
Enhanced user experience: With the support for AI/ML services, 5G operators can offer more personalized and targeted services to their vertical service customers. This can include things like personalized recommendations, real-time translations and augmented reality applications.
New revenue stream: Offering support for AI/ML services can open up new revenue streams for 5G operators, e.g. they can charge for accessing 5G System AI/ML assistance support, partnership with 3rd party providers to offer more sophisticated AI/ML powered applications,
Competitive advantages: By offering support for AI/ML services, 5G operators can differentiate themselves from competitors to retain customers and to attract new customers who value the benefits of the AI/ML-powered applications.
Future-proofing the Network: By supporting AI/ML services, 5G operators can future-proof their networks, preparing for the next wave of innovation and customer demand. As AI/ML algorithms become more sophisticated, they will become even more critical to deliver high-quality network services.

## Slide 12: Mobile Operator Charging Considerations for AI/ML-As-A-Services
Charging for data and network usage: 5G operators can charge ASPs for the data used and the network access by their AI/ML applications. They could include charging based on the amount of data transferred, the number of request processed (e.g. iterations of FL operation), the time window for data transfer, QoS performance during the data transfer or other similar metrics.
Offering value-added services: 5G operators can offer value-added services to ASPs to help them optimize their AI/ML applications, e.g. they could offer data processing, data analytics services or help with data storage and management.
Charging for technical consulting support services: 5G operators can charge ASPs for technical consulting services to help optimize the performance of their applications.
Offering custom pricing: 5G operators can offer custom pricing based on the specific needs of the ASP, e.g. allowing the application AI/ML operation to be operated at specific location(s) and/or time window(s); the volume of data being processed and the complexity level of the network data analytic support that it requires.
One of more of the above charging models could be included as part of the SLA.
How do I get my money?
NOTE: Charging methods 2., 3. and 4 are outside the scope of 3GPP.
MNO

## Slide 13
Considerations of Ambient IoT in 5G Advanced System Deployment
Direct Mode
Indirect Mode
  DL Initiated e.g in Inventory (Smart home, logistics and warehouse)
  UL Initiated e.g Sensor data reporting (Smart Agriculture.)
5G network
Ambient IoT AF
5G network
Ambient IoT AF
B
C
Device A: No energy storage, no independent signal generation, i.e. backscattering transmission
Device B: Has energy storage, no independent signal generation, i.e. backscattering transmission. Use of stored energy can include amplification for reflected signals
Device C: Has energy storage, has independent signal generation, i.e. active RF component for transmission
devices capability
  Ambient IoT devices capability: Indirect mode can be lower than direct mode
  Device A: Ideal for indirect
  Device B: Indirect and Direct mode
  Device C: Indirect and Direct mode

## Slide 14
Considerations of System Impacts for Direct vs. Indirect Mode
Direct Mode vs. Indirect Mode |  | 
 | Direct Mode | Indirect Mode
Device Categories and Capabilities Supported | Device B; Device C; | Device A (ideal for indirect mode) Device B; Device C; UE is involved, device capabilities, cost and power consumption can be reduced further.
5G network impacts & Operator role | More impacts than indirect mode New interface between gNB to the device Operator is aware of and can control devices. | Less impact to 5G network: UE is present between devices and gNB, then the existing 5G network can be reused as much as possible. Existing Uu interface with minimal impact is expected. New interface between the UE and the device Operator is aware of and can control devices.
Coverage | Few 10 meters indoor; up to 200 meters outdoor | Few 100 meters or kilo meters by reusing existing infrastructure
ID management of device | managed by operators with or without 3rd party assistance. | managed by operators with or without 3rd party assistance.
Authentication and Verification of Device | 5G network perform the authentication and verification of device | Authorized UE can perform the device verification

## Slide 15: Opportunities for 5G Operators for Supporting Ambient IoT Services
Deliver ubiquitous ambient IoT service coverage: With the widespread coverage of the 5G infrastructure, 5G operators can offer complete end-to-end network solutions to interconnect the Ambient IoT customers to the backend application server.
Increased revenue: The market capital investments for Ambient IoT services could be quite significant and should not be ignored. By supporting Ambient IoT services, 5G operators can generate additional revenue streams beyond traditional voice and data services. This can help to diversify the revenue base with new revenue opportunity.
Partnership opportunities: Offering the support for Ambient IoT services can open up opportunities for 5G operators to form partnerships with companies that specialize in IoT technology. This does not just benefit the environment but also creates opportunities for new revenue streams.
Differentiation from competitors: By offering the support for Ambient IoT services, 5G operators provide value-added services to new breed of customers and can differentiate themselves from their competitors with new classes of services.

## Slide 16: Mobile Operators Charging Considerations for AIoT-As-A-Services
Charging for device connectivity: 5G operators can charge a fee for supporting the number of Ambient IoT devices for its customer to their network. This could be one-time fee or recurring fee depending on the operators’ pricing model.
Charging for data usage: 5G operators can charge based on the amount of data used by the IoT devices. This could include charging based on the number of messages sent, the volume of data transferred, the QoS requirements or other similar metrics.
Offering value-added services: 5G operators can offer value-added services to customers to help them optimize their IoT devices (e.g. Identity/tag management, authentication/authorization, power saving, location detection, infrastructure connectivity to backend application, data storage etc.).
Charging for technical consulting services: 5G operators can charge customers for providing technical consulting services to help to recommend the tag reader supporting model (i.e. direct mode vs, indirect mode), to optimize the performance of the Ambient IoT devices and to manage the devices.
Offering custom pricing: 5G operators can offer custom pricing based on the specific needs of the ASP, e.g. supporting AIoT services to be operated at specific location(s), the type of AIoT device to support, the amount of AIoT devices to be supported and may be also at specific time window etc..
Revenue Sharing: 5G operators can enter into revenue sharing agreements with the Ambient IoT customers. In this model, the operator would receive a percentage of the revenue generated by the customers from their Ambient IoT devices.
One of more of the above charging models could be included as part of the SLA.
How do I get my money?
NOTE: Charging methods 3., 4., 5. and 6. are outside the scope of 3GPP.
MNO

## Slide 17: Traffic Steering, Switching and Splitting over Dual 3GPP Accesses (DualSteer)
5GS support of enhanced mechanisms for steering, splitting and switching (ATSSS) of user data, pertaining to a UE data session, across two 3GPP networks (intra or inter -PLMN), where only one single subscription is assumed.
Higher capacity
Better coverage
Higher reliability
Better QoE

## Slide 18: Summary – Factors Influencing OPPO’s Views on R19 Priority
With the consideration of tight Rel-19 timeline and the readiness of the AI/ML framework supported by 5GC, a consolidated study for AI/ML support across multiple domains is the right approach to ensure converged system solution for supporting multi-domain AI/ML operations over 5G system.
With the expected tremendous growth of passive IoT worldwide market, the offering of Ambient IoT services over 3GPP system could proliferate the deployment justifications of the 5G Advanced system. By offering not only the flexible passive IoT tag reading support, but also offering the valued added “IoT Backend As A Service” connectivity for the passive IoT backend services/applications, 5G operators could collect the same harvest of the success of Passive IoT market.
The generation of real-time integrated sensing communication is here. The high capacity, massive connectivity and low latency 5G Advanced system is best suited to accelerate such communication evolution while bringing new revenue opportunity for 5G mobile operators serving their vertical service customers.
The growth of legacy services has reached their limits. MNOs and MVNOs need to expand their market opportunities with their vertical customers to support XR/Metaverse services. Hence, performance and efficiency for new vertical services are the keys for success in such market.
Improvements to 5G Advanced system capacity, coverage and performance are the keys to ensure the success for the new business opportunities above. Hence, enhancing and leveraging the side link and multi-access connectivity support are important system capabilities to sustain the growth.

## Slide 20: R19 Priority from OPPO
Adv. Features Towards 6G
Ultra-Realtime Applications
System Capacity Expansions
Misc. & Cont’ from Rel-18
Multi-domain AI/ML (MDAIML)
Based on R18 AI/ML framework and leveraged data sets from multiple 5G AI domains to support cross-domain AI/ML operations in order to improve the efficiency and the performance among various system functions and components, and to enable new classes of 5G services to support vertical.
Ambient IoT (AIoT)
RAN Impact (Y)
Ambient IoT leverages new classes of battery-less 3GPP devices referred as ambient IoT devices that do not have USIM to support small data communications across the radio spectrum by harnessing the power from ambient energy.
RAN Impact (Y)
RAN Impact (Y)
Extending 5G system to provide sensing services (e.g., data collection, sensing exposure etc.) addressing different target verticals/applications like autonomous/assisted driving, V2X, UAVs, 3D map reconstruction, smart city, smart home, factories, healthcare, maritime sector.
Integrated Sensing & Communication
XR Enhancement with Metaverse
Continued from R18 baseline to enhance inter & intra frequency RRM scheduling support, application traffic awareness and identification, QoS support for very high UE data rate, rate control, nominal data rate, extended XR optimizations to sidelink and tethering scenarios. Also, further enhancement to 5G-enabled XR and media services to support the metaverse
RAN Impact (Y)
Multi-connectivity (DualSteer)
Based on the existing ATSSS mechanisms to be extended to support the similar functionalities for the two 3GPP accesses (e.g., non-terrestrial network (NTN) and non-public network (NPN)) corresponding to the same PDU session under the same MNO’s policy and control.
Based on the existing Satellite feature, extending 5GS to support IoT devices for storing and forward operations in discontinuous feeder links, positioning with GNSS, and communications between UEs under the same satellite coverage.
Satellite-Ph3
RAN Impact (Y)
Built on top of MOCN configuration, enabling 5G RAN sharing among multiple operators among which it may have no direct interconnections between the shared NG-RAN and Participating Operators’ core networks. .
Network Sharing (NetShare)
RAN Impact (Y)
Edge-Ph3
Enabling independent evolution of edge networks and public networks, making it easier to deploy and introduce new functions on MEC without the support from the centralized control plan to be upgraded to support new functions and interfaces.
High priority for OPPO
OPPO’s three main targets for Rel-19:
Study emerging use cases/business interests of some topics aiming for 6g;
Essential enhancements of existing R18 important topics;
Enhancement on some fundamental/advanced technologies, e.g., AI;
ProSe-Ph3
RAN Impact (Y),
Continued to extend the relay capabilities to support (a) the multi-path relay to enable network managed multi-path indirect network connection, (b) Multi hop U2N Relay, U2U Relay, (c) Group mobility for L2 U2N Relay, and (d) MBS support over U2N Relay
RAN Impact (N),
RAN Impact (N),
Lesser priority for OPPO

## Slide 21: Overall View on Rel-19 Contents
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
N (Max 10 items) | Title of Rel-19 Proposal (you may provide reference to slide for more details) | Brief description of the Feature. Optionally, you may provide the list of Objectives/Work Task. See definition below – Feature: New or substantially enhanced functionality which represents added value to the existing system. Building block: sub-division of a feature, representing a coherent set of technical functionality which would generally be expected to reside in a single system element. Work task: sub-division of a building block, representing a self-contained, well-scoped and well-scheduled item of work. | List if there are related stage-1 (SA1) requirement (Yes/No). If Yes, Please provide reference to SA1 TS 22.xxx | Please list the SA WG that will lead the work. If you don’t know then just say - Don’t Know | Please list if there are any RAN dependencies (Yes/No). May further elaborate if dependencies are Major or Minor/Alignment. | Please list if there any dependencies on other SA WG. E.g., SA3, SA4, SA5, SA6
1 | Integrated Sensing & Communications (See slide xx for more details) | 5G system support for NR-based sensing capabilities to get information about characteristics of the environment and/or objects within the environment (e.g., shape, size, orientation, speed, location, distances or relative motion between objects, etc.) using NR RF signals. Key Work Tasks includes defining - Overall architecture and function enhancement to support new sensing service. Basic functionality and E2E procedure for Sensing service exposure, Discovery and selection of the sensing entities, Authorization, Sensing control parameter generation and provisioning, related QoS/Policy enhancement. Enhancements for Non-3GPP sensing | Yes, TS 22.xxx | SA2 | Yes, Major | SA3 for security, SA5 for charging
2. |  |  |  |  |  | 
Example